Keck Adaptive Optics Note ___

# Next Generation Adaptive Optics:

# Preliminary Design Manual

Version 0.4

May 4, 2010

Author List

| Name | Function |
| --- | --- |
| Peter Wizinowich | Project Manager |
| Richard Dekany | Senior Manager (COO) |
| Don Gavel | Senior Manager (UCO) |
| Claire Max | Project Scientist (UCO) |
| Sean Adkins | Instrument Manager (WMKO) |
| From Caltech Optical Observatories (COO): Viswa Velur Alex Delacroix Antonin Bouchez | Optical system engineer Mechanical engineer AO scientist |
| From University California Observatories (UCO): Elizabeth McGrath Renate Kupke Marco Reinig Chris Lockwood | Astronomer Optical system engineer AO software engineer Mechanical engineer |
| From W. M. Keck Observatory (WMKO): Chris Neyman Kevin Tsubota Jason Chin Mike Pollard Drew Medeiros Doug Morrison Jimmy Johnson Ed Wetherell | AO system scientist AO software engineer Laser & electronics engineer Mechanical engineer Mechanical engineer Software engineer Software engineer Electronics engineer |

Approval Control

| Control | Name | Function |
| --- | --- | --- |
| Revised by: |  |  |
| Approved by: |  |  |
| Authorized by: |  |  |

Document Change Record

| Version | Date | Change Description |
| --- | --- | --- |
| 0.1 | April 14, 2009 | Initial update of the SDM by P. Wizinowich |
| 0.2 and 0.3 | July 15, 2009 | Updated by R. Dekany |

1	Introduction	1

2	References	1

3	Design Overview	1

3.1	AO System Overview	1

3.2	Telescope and Facilities	5

3.2.1	Telescope Model	5

3.2.2	Facilities	6

3.2.3	Interfaces	6

3.3	AO System Description	6

3.3.1	AO Opto-Mechanical Design	6

3.3.1.1	Rotator and Wide Field Relay	6

3.3.1.2	LGS Wavefront Sensor Assembly	8

3.3.1.3	Interferometer Pickoff	9

3.3.1.4	Acquisition Camera and Pickoff	9

3.3.1.5	Low-Order Wavefront Sensor Assembly	9

3.3.1.6	Narrow-Field Relay	9

3.3.1.7	Natural Guide Star Pickoff	11

3.3.1.8	Narrow Field Science Instrument Pickoffs	11

3.3.1.9	Summary of Required Dichroics and Mirrors	11

3.3.1.10	Atmospheric Dispersion Correctors	11

3.3.1.11	Optics Bench Structure	12

3.3.2	Wavefront Sensor Opto-Mechanical Design	12

3.3.2.1	Object Selection Mechanism	14

3.3.2.2	Tip-Tilt (Focus and Astigmatism) Sensors	18

3.3.2.3	Truth Wavefront Sensors	18

3.3.2.4	LGS Wavefront Sensor Object Selection Mechanism	19

3.3.2.5	LGS Wavefront Sensors	19

3.3.2.6	NGS Wavefront Sensors	21

3.3.3	AO Optical Performance	21

3.3.3.1	Wide Field Relay Optical Performance	22

3.3.3.1.1	Optical Performance to the Low Order Wavefront Sensors	22

3.3.3.1.2	Optical Performance to the Interferometer Field Selectors	22

3.3.3.1.3	Optical Performance to the Laser Guide Star Wavefront Sensors	22

3.3.3.2	Narrow Field Relay Optical Performance	22

3.3.3.3	Atmospheric Dispersion Correction	23

3.3.3.4	Pupil Distortion	23

3.3.4	AO Enclosure	24

3.3.5	Alignment, Calibration, Diagnostics, Metrology and Monitoring	24

3.3.5.1	Alignment	24

3.3.5.2	Calibrations	26

3.3.5.3	Calibration Unit	26

3.3.5.4	Atmospheric Simulator	26

3.3.5.5	Metrology	26

3.3.5.6	Atmospheric Profiler	26

3.4	Laser Facility Description	27

3.4.1	Laser Facility Optical Design	27

3.4.2	Lasers	27

3.4.3	Laser Enclosure and Beam Transport Mechanical Design	29

3.4.4	Laser Safety System	30

3.5	AO Controls	31

3.5.1	Controls Infrastructure	31

3.5.2	AO Control Loops	33

3.5.2.1	Devices	33

3.5.2.2	NGS AO Control Loops	34

3.5.2.3	LGS AO Control Loops	36

3.5.3	Motion / Device Control	39

3.5.3.1	Motion Control Electronics	39

3.5.3.1.1	Controllers and Actuators	40

3.5.3.1.2	PWM Drives & EMI	41

3.5.3.1.3	Room for Expansion	42

3.5.3.1.4	Support Equipment	42

3.5.3.1.5	Cabling	42

3.5.3.1.6	Location of Equipment	43

3.5.3.2	Motion Control Software	44

3.5.3.3	Device Control Electronics	45

3.5.3.4	Device Control Software	46

3.5.4	AO Control Software	46

3.5.4.1	AO Control Sequencer	47

3.5.4.1.1	Wide Field Relay	48

3.5.4.1.2	Acquisition System	49

3.5.4.1.3	LGS Wavefront Sensors	49

3.5.4.1.4	Low Order Wavefront Sensors	52

3.5.4.1.5	Narrow Field Relay	52

3.5.4.1.6	NGS Wavefront Sensor	53

3.5.4.1.7	Atmospheric Dispersion Corrector	53

3.5.4.1.8	RTC Interface	54

3.5.4.1.9	Offloading	54

3.5.4.1.10	Other Composites	56

3.5.5	Laser System Software	57

3.5.5.1	Laser Control Sequencer	57

3.5.5.1.1	Asterism Validation Control Loop	58

3.5.5.1.2	Laser Switchyard	59

3.5.5.1.3	Laser Beam Generation System	61

3.5.5.1.4	Laser Safety System Interface	62

3.5.5.1.5	Laser Service Enclosure	63

3.5.5.1.6	Laser Interface	64

3.5.6	Data Server	64

3.5.7	Real Time Control	65

3.5.7.1	Introduction	65

3.5.7.2	RTC Tasks	66

3.5.7.3	Parametric Input, Optimization, and Reconfigurability	68

3.5.7.3.1	Minimum Variance Reconstruction Optimization	68

3.5.7.3.2	Calibration Parameters	68

3.5.7.3.3	Reconfiguration	68

3.5.7.4	Interfaces	69

3.5.7.4.1	Offloading	69

3.5.7.4.2	Diagnostics and Telemetry	69

3.5.7.4.3	Command State	70

3.5.7.5	Implementation	70

3.5.7.5.1	Algorithms	70

3.5.7.5.2	Hardware	71

3.5.7.5.3	Hardware Interfaces	71

3.5.7.5.4	Programming and Design Process	71

3.5.7.5.5	Physical Implementation	71

3.6	Science Operations	72

3.6.1	Science Operation Model	72

3.6.1.1	Observing Model: classical with built-in flexibility tools	72

3.6.1.2	Science Operation Requirements: Observing Efficiency	73

3.6.2	Conceptual Design for System Operations	75

3.6.2.1	Operation Control Infrastructure	75

3.6.2.2	System Configurations Matrix	76

3.6.2.3	System Calibration: Routine and Maintenance Calibrations	77

3.6.2.4	System Operations: Acquisition	77

3.6.2.5	System Operations: Dithering and Offsetting	80

3.6.3	System Control	81

3.6.3.1	Multi-System Command Sequencer	81

3.6.3.2	Operation Control (Graphical) User Interfaces	82

3.6.4	Pre and Post-Observing Tools	83

3.6.4.1	Pre-Observing Tools	83

3.6.4.2	Post-observing Tools	86

3.7	Science Instruments	87

3.7.1	Science Passbands	87

3.7.2	DAVINCI	88

3.7.3	Interferometer	88

3.7.4	‘OHANA	88

3.7.5	Thermal NIR Imager	88

4	Performance Budgets	88

4.1	Background and Transmission	89

4.2	Wavefront Error and Ensquared Energy	90

4.2.1	Key Flowdowns from the Wavefront Error Budget	91

4.2.2	Laser Power considerations	92

4.2.3	Performance Summary	92

4.3	Photometric Precision	93

4.4	Astrometric Precision	94

4.5	Companion Sensitivity	95

4.6	Polarimetric Precision	96

4.7	Observing Efficiency and Uptime	96

5	Requirements Development and Compliance	97

6	Alternate System Architectures	100

7	Trade Studies	100

8	Glossary	101

9	Appendix: NGAO PD Phase Detailed Wavefront Error Budgets	103

Figure 1.  LGS “3+1” asterism for tomography of the science field, plus three patrolling lasers for image sharpening of the tip-tilt stars	2

Figure 2.  NGAO Block Diagram	3

Figure 3.  Telescope Solidworks model.	5

Figure 4.  View from below of the telescope Nasmyth platform.	6

Figure 5.  Mapping of Keck primary mirror onto a 22x22 actuator low order DM.	7

Figure 6.  The image rotator and low order “wide” field relay.	8

Figure 7.  Laser Guide Star Wavefront Sensor and Interferometer Pickoffs.	8

Figure 8.  Narrow Field Relay.	9

Figure 9.  Mapping of Keck primary mirror to a 64x64 actuator high order DM.	10

Figure 10.  Optics Bench Structure.	12

Figure 11.  The LOWFS assembly.	15

Figure 12.  LOWFS OSM probe arm.	15

Figure 13.  Four configurations of the LOWFS OSM arms.	16

Figure 14.  (a) Zemax model of LOWFS probe arm.  (b) Probe arm patrol field.	17

Figure 15.  Tip, tilt, focus and astigmatism (TTFA) sensor schematic.	18

Figure 16.  Mapping of Keck primary mirror to a 32x32 actuator LOWFS DM.	18

Figure 17.  Truth wavefront sensor (TWFS) schematic.	19

Figure 18.  Plan view of the LGS object selection (/φ pickoff scheme.	19

Figure 19.  LGS WFS assembly enclosure.	19

Figure 20: LGS WFS assembly.	20

Figure 21.  Schematic of a single LGS WFS channel.	20

Figure 22: NGS WFS assembly.	21

Figure 23.  Spot diagrams delivered to the LOWFS focal plane.	22

Figure 24.  Spot diagrams delivered to the LGS WFS at 180 km conjugate.	22

Figure 25.  Spots at the on-axis and extreme field angles to the NGS WFS.	23

Figure 26.  RMS wavefront error to the NGS WFS versus field.	23

Figure 27.  Grid distortion at the woofer DM location, magnified by 100.	23

Figure 28.  Spot diagrams for 5 locations on the primary mirror imaged onto the woofer DM.	23

Figure 29.  Pupil grid distortion at the tweeter DM position, magnified by 100.	23

Figure 30.  Spot diagrams for 5 positions on primary mirror imaged onto the tweeter DM.	23

Figure 31: Mauna Kea seeing monitor.	27

Figure 32.  TOPTICA/MPBC demonstrator laser head.	28

Figure 33.  Schematic diagram of the laser	29

Figure 34.  Existing Keck II Telescope and laser location case 1.	29

Figure 35: Safety system.	30

Figure 36: A Block diagram of the NGAO system viewed abstractly as a distributed controls system	31

Figure 37: A block diagram of the NGAO controls infrastructure	32

Figure 38: AO device overview.	33

Figure 39: NGS AO control loops for the science instrument.	35

Figure 40: NGS AO control loops for the interferometer.	35

Figure 41: LGS AO control loops for the science instrument.	37

Figure 42: LGS AO control loops for the interferometer.	39

Figure 43: AO Motion Control Layout	43

Figure 44: Laser Motion Control Layout	44

Figure 45: AO Control Sequencer Collaboration Diagram	47

Figure 46: Image Rotator Control Loop	48

Figure 47: Field Rotation Offset Control Loop	49

Figure 48: WFS Focus Control Loop	50

Figure 49: Tomography LGS WFS Offloading	51

Figure 50: Patrolling LGS WFS Offloading	51

Figure 51: ADC Tip-Tilt Error Correction Control Loop	53

Figure 52: KAT Tip-Tilt Error Correction Control Loop	53

Figure 53: ADC Tracking Control Loop	54

Figure 54: Telescope Offload Control Loop	55

Figure 55: DAR Offset Control Loop	56

Figure 56: Laser Control Sequencer Diagram	57

Figure 58: Asterism Validation Control Loop	58

Figure 59: Laser Steering Control Loop	60

Figure 60: Laser Polarization Control Loop	60

Figure 61: Laser Focus Tracking Control Loop	62

Figure 62: Asterism Rotator Tracking Control Loop	62

Figure 63: Flexure Compensation Control Loop	62

Figure 64: Laser Safety System Collaboration Diagram	63

Figure 65: Data Server Overview	65

Figure 66.  Multi-guide star tomography data flow and parallel processing.	67

Figure 67.  Tomography algorithm.	67

Figure 68.  Efficiency estimate for the high-z galaxies science case.	74

Figure 69.  Science operations tools block diagram.	76

Figure 70.  NGAO system configurations.	77

Figure 71.  AO guide star tool workflow.	84

Figure 72.  NGAO performance estimation tool and exposure time calculator workflow.	85

Figure 73.  Observation preparation tool workflow.	86

Figure 74: NGAO Passbands	87

Figure 75.  Science target wavefront error budget for the Kuiper Belt Object Companion Survey Key Science Case. (TBR)	92

Figure 76. LOWFS NGS wavefront error budget for the KBO Companion Survey Science Case.	92

Figure 77.  Simulated NGAO J-band science observations with secondary objects inserted.	95

Figure 78.  NGAO project V-diagram including the design and development process.	98

Figure 79. Science target wavefront error budget for Io Science Case. (TBR)	104

Figure 80. Science target wavefront error budget for Galactic Center Science Case. (TBR)	105

Figure 81.  Science target wavefront error budget for ExoJupiter LGS Case. (TBR)	106

Figure 82.  Science target wavefront error budget for Galaxy/Galaxy Lensing Science Case. (TBR)	107

Figure 83. LOWFS NGS wavefront error budget for the Galaxy / Galaxy Lensing Survey Science Case.	108

Figure 84. Science target Ensquared Energy error budget for High-Redshift Galaxies.	109

Table 1. Summary of Required Dichroics and Mirrors.	11

Table 2.  Baseline design parameters for the NGAO wavefront sensors.	12

Table 3.  Required WFS detector characteristics.	14

Table 4.  Performance to the narrow field instruments.	23

Table 5.  Characteristics of the pupil image on the deformable mirrors.	23

Table 7.  Acquisition conceptual design level specifications.	77

Table 8.  Generic NGAO Acquisition Scenario.	78

Table 10: NGAO system passband and observing band characteristics	87

Table 13.  NGAO error budget tool anchoring to Keck II AO performance.	91

Table 14.  The NGAO error budget tools accurately models the upgraded Keck II AO performance.	91

Table 15. Wavefront error budget summary for several NGAO science cases.	92

Table 16.  Science case mapping to NGAO configurations.	100

Table 17.  List of trade studies performed.	100

Table 18.  Glossary of Terms	101

# Introduction

This document describes the preliminary design for the Next Generation Adaptives Optics (NGAO) system to be built for the W. M. Keck Observatory (WMKO).  This document is one of the key preliminary design phase deliverables as discussed in the Preliminary Design Report (KAON ___).  It is intended to provide an overview of the preliminary design, while referencing the appropriate documents which contain the details.  This document replaces the system design phase manual (KAON 511) which was updated with the build-to-cost design changes (KAON 642).

We begin with an overview of the preliminary design that includes major sections on the AO system, laser facility, controls hardware and software and science operations.  An overview of the science instruments and their interface with NGAO is not provided in this document.  The system design of the NGAO imager and IFU science instrument is presented in KAON ___.

The performance budgets are addressed in Section 4.  Eight system performance metrics were identified in the Science Requirements Document.  For three of these metrics, background and transmission, wavefront error and ensquared energy, and high-contrast performance, we have produced associated quantitative performance budgets to identify key performance drivers.  For photometric precision, astrometric accuracy, polarimetry and observing efficiency we have identified key drivers and documented these in technical reports that have informed the NGAO design..

Section 5 provides an overview of the requirements flow down and a discussion of compliance.  Detailed requirements have largely not been included in the design discussions in this document because of the length of this information.  The detailed requirements can be found in most of the referenced design KAONs as well as in the Functional Requirements Document (KAON 573).

# References

A list of all Keck Adaptive Optics Notes for NGAO can be found in an Appendix to the Preliminary Design Report (KAON ___).  These documents are available at http://www.oir.caltech.edu/twiki_oir/bin/view/Keck/NGAO/NewKAONs.

# Design Overview

## AO System Overview

All of the NGAO science cases require essentially diffraction-limited performance (Strehl > 0.6) in the near-IR.  A number of Solar System and Galactic science cases have requirements for at least modest Strehl at visible wavelengths.  All of the science cases also require high sensitivity with most of the targets of interest being too faint to use as references for wavefront sensing in the AO system.  This high Strehl, faint object performance is required with reasonable (≥ 30%) sky coverage.

The requirements for sky coverage and high sensitivity are both met by using a laser of 589 nm wavelength to illuminate the mesospheric sodium layer, producing an artificial laser guide star (LGS) for AO wavefront sensing.  Achieving the desired level of Strehl performance leads directly to a requirement for an AO system that can overcome the effect of focus anisoplanatism (the “cone effect”), a requirement that is met through use of multiple laser beacons forming an  asterism of LGS as shown in Figure 1.  Wavefront information from four central LGS is combined to produce a three dimensional description of the atmospheric turbulence over the telescope aperture using tomographic reconstruction techniques.  We have concluded that a fixed diameter LGS asterism with one in the center and three equally spaced around a circle provides the optimal sampling of the atmosphere above the telescope with respect to tomography error for the science field.  The radius of the circle is set at 10".

Three additional LGS, WFS , and DM’s are utilized as three independently controlled AO systems to provide image sharpening for three natural guide stars (NGS), which are required to overcome limitations imposed by the science tomography sensing system.  In particular, the NGS provide measurement of the atmospheric tip and tilt modes, as well as modes unsensed by the multiple-LGS asterism.  Operating at near-IR wavelengths, two of NGS sensors measure tip and tilt (TT) only, while a third additionally measures focus and astigmatism (TTFA).  Each NGS sensor arm contains its own high-order DM to allow optimal sharpening of NGS spread over a wide field of view, thereby maximizing sky coverage.

Figure 1.  LGS “3+1” asterism for tomography of the science field, plus three patrolling lasers for image sharpening of the tip-tilt stars

The Solar System and Galactic science cases all require single object observations over modest to narrow fields of view, ranging from 2" to 30".  This single line of sight could be AO corrected using a single deformable mirror (DM).  Based on a combination of limiting magnitude and off-axis distance for natural tip-tilt stars, an object selection mechanism (OSM) is required for these stars.  A block diagram of the AO system architecture that we have selected to deliver both high Strehl and good sky coverage is shown in Figure 2.  We refer to this design as the “cascaded relay” because it uses two AO relays in series.

Starting at the lower left hand side of the figure, an enclosure on the elevation ring of the telescope is provided to house three ~25W CW format lasers.  Laser output is sent via a free space beam transfer system to a multiple beam pattern generator and controller located at the top end of the telescope.  The output of this beam pattern generator is projected onto the mesospheric sodium layer by a laser launch telescope located behind the telescope secondary mirror as shown just to the left of center in Figure 2.

Light collected by the Keck telescope is directed to the AO system shown in the lower right in Figure 2.  The AO system and instruments are located on the telescope’s left Nasmyth platform at the f/15 focus.  The AO system science path is enclosed in an enclosure cooled to about -15(C below ambient (~260 K) to reduce the thermal emissivity of the optical surfaces.  A window is provided to isolate the enclosure from the dome environment.  Another window is provided to feed the LGS WFS.  The science instrument forms a seal with the cooled enclosure.

Figure 2.  NGAO Block Diagram

Within the cooled enclosure, the light from the telescope passes through an image de-rotator.  A “wide” field, low-order AO relay incorporating a single DM provides moderate spatial order AO correction (comparable to the correction provided by the existing Keck AO systems).  This DM operates in a closed loop in conjunction with the LGS wavefront sensors.  Just after the DM, a dichroic beamsplitter is used to send the 589 nm light from the asterism of LGS to the LGS wavefront sensor assembly, which includes both a fixed sensor assembly and an object selection mechanism for the three patrolling LGS.  The light from the wide field relay is transmitted directly to the object selection mechanism for the low-order wavefront sensors (LOWFS; i.e., the near-IR TT and TTFA sensors and a visible truth wavefront sensor (TWFS)).  A dichroic can be inserted to feed light to the Keck interferometer.

The light then passes through a “narrow” field, high-order AO relay.  High-order corresponds to approximately ten times the DM actuator areal density of the low-order DM.    This relay provides AO corrected light to a visible light NGS wavefront sensor and a science instrument(s).  Another instrument port will be provided for a future instrument capability.

For NGS AO observations only the NGS WFS is required.  For LGS AO observations, the LGS wavefront sensors, three low-order NGS sensors, and the NGS TWFS are required.

The following is a brief summary of the key architectural features of NGAO and why they were selected (i.e., flowed down from the science requirements):

- Laser tomography to measure wavefronts and overcome the cone effect over the science field.  This is supported by the fixed “3+1” LGS asterism and LGS WFS.

- LGS projection from behind the telescope secondary mirror to minimize perspective elongation.

- Location of the AO system on the Keck II telescope left Nasmyth platform to have sufficient space for the AO system and science instruments in a gravity constant environment.

- A cooled AO system to meet the near-infrared background requirements.

- A K-mirror rotator at the input to the AO system to keep either the field or pupil fixed.  The AO system would need to be cooled even without a rotator and this approach allows the most stability for the AO system and instruments.

- A wide-field (120" diameter) relay to feed light to the LGS wavefront sensors and the three LOWFS.

- A conventional (5 mm pitch) DM was chosen to transmit a wide field in the wide-field relay.

- A low-order (20 actuators across the pupil) DM (LODM) was chosen for the wide-field relay to limit the size of the relay, to permit closed loop AO correction on the LGS wavefront sensors and to keep the LGS wavefront sensors in their linear range, reducing the requirement on downstream open loop correction.

- Open loop AO-corrected near-IR tip-tilt sensors to maximize sky coverage.  This is supported by three patrolling laser beacons and LGS WFS.

- Open loop AO-correction to the narrow field science instrument(s) in LGS mode.

- MEMS DM’s for the AO-correction.  These are very compact devices and have been lab demonstrated to accurately go where they are commanded.  Small, modest-cost 32x32 element MEMS DM’s provide the required correction for the tip-tilt sensors.  A 64x64 element MEMS, similar to that developed for GPI, is needed to provide the required AO correction to the narrow field science instrument(s).

- A high order, narrow-field (40"x60" diameter) AO relay to feed light to the narrow field science instrument(s) and NGS wavefront sensor.  The science instruments fed by this relay only require a narrow-field (32"x32") and the narrow field facilitates the use of a single MEMS DM for all narrow-field instruments.

## Telescope and Facilities

The NGAO systems must utilize and interface to the existing Observatory infrastructure.  This infrastructure includes the telescope and related control systems as well as mechanical and electrical services.  In some cases this existing infrastructure may need to be modified.

The NGAO design and plan currently assumes implementation on the Keck II telescope.  This replaces the older AO system and laser and takes advantage of existing laser infrastructure.  It would be relatively straightforward to modify the design for implementation on Keck I.  The design and plan also assume that the existing Keck II AO and laser systems will be removed from the summit facility to make room for the NGAO system.  In addition to providing physical space for the system this will also free up power and cooling capacity, as well as cable wrap space.

### Telescope Model

A Solidworks model of the Keck II telescope has been generated in order to clearly define the available space and interfaces for the NGAO system.  Views of this model are shown in Figure 3 and Figure 4, with a possible AO enclosure on the left Nasmyth platform.  This tool can be used to provide the details of areas like the Nasmyth platform or secondary mirror socket which the NGAO system will need for interface purposes.  The details of this model are suitable for preliminary design.  Critical dimensions will need to be field verified before detailed design.

Figure 3.  Telescope Solidworks model.

Figure 4.  View from below of the telescope Nasmyth platform.

### Facilities

The total required facility power and cooling is TBD, but several elements of these requirements have had some initial determination.

### Interfaces

The AO system must interface to the existing telescope Drive and Control System (DCS); for example, to offload pointing and focus corrections or to request a telescope move.

## AO System Description

### AO Opto-Mechanical Design

The opto-mechanical design for the cascaded relay (see KAON 685) is summarized in this section.

#### Rotator and Wide Field Relay

The rotator and first relay are shown in shown in Figure 6.  The rotator and first relay are intended to pass a wide field for the NGS and corresponding patrolling LGS.  The relay includes a DM to provide low order wavefront correction.

The rotator is a K-mirror that can be used to either keep the field or pupil fixed.  The Keck telescope’s f/15 Nasmyth focal plane is located ~270 mm past the telescope’s elevation bearing.  It is still to be determined to what degree having a focal plane close to these two mirrors will add thermal background effects or performance issues and how it would impact the high-contract science goals (for reference the first mirror of the existing Keck AO rotator is located 110 mm after the telescope focus).  The 3-mirror rotator is sized to accommodate a 120" diameter NGS field of view (FOV) and a 120" diameter LGS FOV (for the case of an LGS at 80 km).  The first and third mirrors are at 60º angles of incidence while the second mirror lies parallel to the rotation axis of the K-mirror with an incidence angle of 30º.

A fold mirror is located between the rotator and first OAP .

The third-order optical aberrations can be minimized by two approaches using a collimated beam between two identical OAPs.  Of these the off-centered pupil approach was chosen since it maintains a non-tilted focal plane (Korsch, Reflective Optics, p. 171, 1991).

The first relay is a one-to-one magnification relay consisting of an off-axis parabola (OAP) to collimate the light and reimage the primary mirror onto the DM, the DM and a second identical OAP to converge the light with the same focal ratio as the telescope and a telecentric pupil.  The focal length of the OAP was selected to map the primary mirror to a 5 mm (dDM) pitch DM with 22x22 actuators as shown in Figure 5.

Figure 5.  Mapping of Keck primary mirror onto a 22x22 actuator low order DM.

The (vertical, horizontal) mapping = (547.45, 555.90) mm/subaperture.  Keck drawing 1410-CM0010.

The DM is placed at an optical conjugate to the primary mirror and is mounted on a fast tip-tilt controllable mount.  The second OAP is located its focal length from the DM in order to project the pupil to infinity and hence generate a telecentric output beam.

The output of the first relay goes directly to the object selection mechanism (OSM) that feeds the low order wavefront sensors (LOWFS).  A fold mirror or a dichroic can be inserted into this beam to feed the NGS acquisition camera and the interferometer.

Some key design numbers:

- Telescope parameters (from KOTN 163 or KAON 107).

  - Telescope focal length, fTel = 149.583 m.

  - Telescope entrance pupil diameter DTel = 10.949 m.

  - Telescope exit pupil diameter, DEP = 1460 mm.

  - Distance from telescope exit pupil to focus, tEP = 19948 mm.

  - Telescope f/#Tel = fTel/DTel = 13.66.

  - Telescope plate scale, PS = 0.727 mm/".

- Chosen design parameters.

  - LOWFS NGS field of view diameter, ΦNGS = 120".

  - Rotator mirror angles of incidence are 60º for mirrors 1 and 3, and 30º for mirror 2.

  - Rotator mirror diameters (assuming a 90% clear aperture) are 250 mm, 160 mm and 270 mm.  The separation of mirrors is 243.5 mm.

  - 180 mm diameter fold mirror located 322.5 mm after the last mirror of the rotator at an incidence angle of 30(.

  - OAP1 and OAP2 off-axis angle = 20º (corresponding to a decenter of 481.8 mm from the parent parabola).

  - DM conjugate to the telescope primary mirror.

  - DM incidence angle, (DM = 10(.

  - DM subaperture size, dDM = 5 mm.

  - Primary mirror subaperture size = 547.45 mm.

  - Output pupil from 1st relay at infinity.

- 1st order calculated parameters.

  - OAP focal length, fOAP = (dDM/dPM) fTel = 1366.2 mm.

  - Required OAP diameter to accept the pupil and field, dOAP = (fOAP/tEP)DEP + (fOAP+tEP)ΦNGS*PS/tEP = 193.2 mm.

  - Distance of DM from OAP1 in order to be conjugate to the primary, tDM = [1/fOAP – 1/(tEP+fOAP)]-1 = 1459.7 mm.

  - Pupil distortion on the DM due to the angle of incidence, % distortion = [1-cos((DM)]*100% = 1.5%.

  - Distance of OAP2 from the DM in order to project the pupil to infinity, tOAP2 = fOAP = 1366.2 mm.

Figure 6.  The image rotator and low order “wide” field relay.

Light from the telescope enters from the left and travels through the rotator to OAP1, the flat fold, the “woofer” DM.  A dichroic splitter reflects the 589 nm light to the LGS WFS and transmits the remainder of the light to OAP2.  A retractable mirror to feed the NGS acquisition camera is shown just before the focus.

#### LGS Wavefront Sensor Assembly

A sodium wavelength reflective dichroic is located in the collimated beam between the DM and OAP2 to send the sodium wavelength light to the LGS wavefront sensor as shown in Figure 6.  Describe relay optics.  The LGS WFS must translate in focus to be conjugate to the sodium layer.

Figure 7.  Laser Guide Star Wavefront Sensor and Interferometer Pickoffs.

The LGS WFS assembly consists of four fixed and three patrolling LGS WFS.

#### Interferometer Pickoff

Figure 6 also shows a dichroic pickoff to the Keck interferometer.

The dichroic sends a 60" diameter field to a pair of field selector mirrors.  The first of these mirrors is located near the focus and has a hole in it to transmit a small on-axis field.  The first field selector steers the desired off-axis point to the center of the second field selector mirror, which in turn steers the off-axis field along the desired axis (parallel to the on-axis field).  Similar field steering mirrors are used in the existing Keck AO system and this approach has been selected for the ASTRA upgrade to the Interferometer (ASTRA-0017).

The on-axis and off-axis beams go to a dual star module where OAPs are used to collimate the light and fold mirrors are used to steer the beam to the existing coude train.

#### Acquisition Camera and Pickoff

A removable 45º incidence angle mirror folds the entire 120" diameter wide field relay output to the acquisition camera.  We have determined (KAON 567 and section 3.6.2.4) that a visible camera is adequate (versus a NIR camera) and that this camera can therefore be used for both NGS and LGS acquisition.  The camera is mounted on a focus translation stage to go between the NGS and LGS foci as is done with the acquisition camera for the current Keck AO system.  A simple focal reducer can be used to obtain the required plate scale on the new Keck standard MAGIQ acquisition camera.

#### Low-Order Wavefront Sensor Assembly

The light reflected by OAP2 goes directly to the low-order wavefront sensors (LOWFS) in the absence of the interferometer or acquisition camera folds.  The LOWFS assembly is located directly in front of the narrow-field relay and consists of an Object Selection Mechanism (OSM) and three LOWFS.  Two arms of the OSM feed tip-tilt (TT) sensors.  A third arm feeds a tip-tilt-focus-astigmatism (TTFA) sensor and a truth wavefront sensor (TWFS).  A dichroic beamsplitter splits the light between the TTFA and TWFS.

#### Narrow-Field Relay

The narrow-field relay is intended to provide a high order of correction for the narrow-field science instrument(s).  It also provides a magnification of ~3 in order to provide separation between the instruments and an optimal plate scale for the science instruments.

Figure 8.  Narrow Field Relay.

The light from the first relay is folded before passing through focus to OAP3 which collimates the light and reimages the telescope primary mirror onto a 64x64 MEMS DM as shown in . The DM is mounted on a slow, large-stroke tip-tilt stage in order to facilitate science instrument dithering (TBC).  OAP4 is chosen to provide a factor of three magnification and is located its focal length from the MEMS in order to project the pupil to infinity.

Figure 9.  Mapping of Keck primary mirror to a 64x64 actuator high order DM.

The (vertical, horizontal) mapping = (182.48, 185.30) mm/subaperture.  Keck drawing 1410-CM0010.

- Chosen design parameters.

  - NGS field of view diameter, ΦNGS,narrow = 40"x60" for NGS WFS and science instruments.

  - OAP3 off-axis angle = 13º.

  - Telescope primary mirror subaperture size, dPM2 = 182.48 mm.

  - MEMS angle of incidence, (MEMS = 10º.

  - MEMS conjugate to the telescope primary mirror.

  - MEMS subaperture size, dMEMS = 0.40 mm.

  - 3x magnification (f/15 input becomes f/45 out).

  - OAP4 off-axis angle = 43º.

  - Output pupil from 2nd relay at infinity.

- 1st order calculated parameters.

  - OAP focal length, fOAP3 = (dMEMS/dPM2) fTel = 327.9 mm

  - Required OAP3 diameter to accept the pupil and field, dOAP3 = fOAP3/f/#Tel + ΦNGS,narrow*PS = 67.6 mm.

  - Distance of MEMS from OAP3 in order to be conjugate to the primary, tDM = fOAP3.

  - Pupil distortion on the DM due to the angle of incidence, % distortion = [1–cos((MEMS)]*100% = 1.5%.

  - Focal length of OAP4 for a 3x magnification, fOAP4 = 3fOAP3 = 1020 mm.

  - Distance of OAP4 from the DM in order to project the pupil to infinity, tOAP4 = fOAP4.

  - Required OAP4 diameter to accept the pupil and field, dOAP4 = fOAP3/f/#Tel + ΦNGS,narrow*3PS = 134 mm.

#### Natural Guide Star Pickoff

The dichroic pickoff in the collimated space between the high order DM and OAP4 feeds the NGS WFS.  The dichroic is at an angle of incidence of __º.  The nominal 30" diameter field required for the science instruments was deemed to be scientifically inadequate for the NGS WFS.  The current design has a slightly offset field that extends 57" perpendicular to the bench and 54" parallel to the bench due to vignetting by the tweeter and OAP4.

A pair of field selector mirrors, similar in concept to those discussed in section 3.3.1.3 will be used.  In this case the first mirror will not have a hole in it.

#### Narrow Field Science Instrument Pickoffs

Two potential science instruments can be fed by the narrow field relay as shown in Figure 8.  The light reflected by a fold mirror just after OAP4 goes directly to the combined imager and IFU.  This fold can be motorized and tilted in the future to feed a future science instrument.

#### Summary of Required Dichroics and Mirrors

The above sections only described the location of the required pickoffs.  Table 1 provides a summary of the required dichroics and mirrors and their properties.  The numbers in the NGS and LGS columns refer to the system configurations that will be discussed in a later section.  The LGS acquisition camera and fold are not required due to our decision to use a single visible wavelength acquisition camera for both NGS and LGS acquisition.

Table 1. Summary of Required Dichroics and Mirrors.

#### Atmospheric Dispersion Correctors

An atmospheric dispersion corrector (ADC) is provided for the narrow field science instrument over the full wavelength range of this instrument.  Ideally the full wavelength range can be provided by a single ADC.  The ADC must be removal for science near the zenith or IFS science where the higher throughput or lower emissivity is preferred.

#### Optics Bench Structure

The optics bench structure is shown in Figure 10.  A typical honeycomb core optical table is used.  The optimal thickness is __.

Figure 10.  Optics Bench Structure.

Attachment of the optics bench to the Nasmyth platform is TBD, but will likely be similar to the mounting of the existing Keck AO benches.  The clearance between the bottom of the bench and the Nasmyth platform is ~ 500 mm less than for the existing AO benches, which will make access under the bench more challenging (than for the existing benches).

### Wavefront Sensor Opto-Mechanical Design

Two wavefront sensor assemblies are fed by the wide field optical relay: the LGS wavefront sensor assembly and the low-order wavefront sensor (LOWFS) assembly.  The NGS wavefront sensor assembly is fed by the narrow-field relay.  Each of these assemblies includes an object selection mechanism that selects the appropriate NGS or LGS and feeds the light to the appropriate wavefront sensor(s).  Two versions of the same multi-target mechanism have been chosen for the LGS and LOWFS object selection mechanisms, while a different single-object selection approach has been taken for the NGS wavefront sensor assembly as described in section 3.3.1.7. The LGS wavefront sensor assembly includes a total of seven LGS wavefront sensors.  The LOWFS assembly includes two NIR tip-tilt sensors, a NIR tip-tilt-focus-astigmatism sensor and a visible truth wavefront sensor.  The design reports for the multi-target object selection mechanism and the LGS WFS can be found in KAON 692.  The LOWFS design report can be found in KAON 730 and the NGS WFS design in KAON __.

The design parameters for the wavefront sensors and detectors are summarized in Table 2 and Table 3.

Table 2.  Baseline design parameters for the NGAO wavefront sensors.

| WFS type | Location | Sensing wavelength (µm) | Input PS (µm/") | # of sub-apertures | Detector PS ("/pixel) | Filters | Field of regard (") | Object Selection |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Fixed LGS WFS | in WF relay | 0.589 | 727 | 64x64 | 1.45 | none | __ | Fixed |
| Patrolling LGS WFS | in WF relay | 0.589 |  | 32x32 | TBD | None | ~120 (TBC) | (φ pickoff |
| TT | after WF relay | 1.16 – 1.33 |  | 1x1 | 0.03 | J+H | 120 | (φ pickoff |
| TTFA |  | 1.16 – 1.33 |  | 2x2 | 0.03 | J+H |  | shared (φ pickoff |
| TWFS |  | (0.40- or) 0.60-0.90 |  | 5x5 | 0.2 | none |  |  |
| NGS WFS | after NF relay | (0.40- or) 0.60-0.90 | 2254 | 32x32 64x64 | 1.5 | none | 50 | shared field steering mirrors |

Table 3.  Required WFS detector characteristics.

| Detector | Characteristics | # of units | Comments |
| --- | --- | --- | --- |
| CCD | 256x256 pixels. RON ≤ 3e- at 2 kHz frame rate & DN ≤ 500 e-/sec @ operating temp. | 8 | 7 LGS WFS + 1 NGS WFS |
| CCD | 240x240 pixels. RON ≤ 3e- at 0.01-200 Hz & DN ≤ 0.001 e-/pix/sec DN | 1 | WF TWFS |
| IR detector | Small regions. RON ≤ 7e- with 8 Fowler samples & 500 Hz data rate for the entire chip; DN ≤ 0.001 e-/sec @ 73K. | 3 | 2 TT and 1 TTFA sensors |

#### Object Selection Mechanism

A design for a LOWFS OSM has been developed in KAON 562.  The LOWFS assembly is located at the focus of the first relay and contains two TT WFS, one TTFA WFS and one TWFS WFS.  The NGAO LOWFS assembly is a critical part of the NGAO system as it provides the required centering accuracy and stability for acquisition and observing modes such as off-chip dithering and non-sidereal tracking.

The LOWFS assembly shown in Figure 11 attaches directly to the AO bench. The assembly can be viewed as two separate entities: the OSM consisting of a stable structural plate that supports the three roaming probe arms and the three beam-fed units located behind the structural plate that are fixed during an observation.

The LOWFS OSM probe arm is a compact 2-motor device shown in Figure 12. The 2 degrees of freedom probe arm consists of 2 individual arms: a crank arm and a lever arm, driven by 2 corresponding rotation motors: the crank and lever motors.  The crank motor is secured to the main structural plate. It rotates the crank arm, and all hardware attached to it that includes the lever arm and lever arm motor, precisely about the rotation axis of the crank motor (( rotation). The lever arm motor provides the necessary second degree of freedom by rotating the lever arm and all associated optics (φ rotation).

The lengths of the crank and lever arms were chosen to provide full coverage of the LOWFS OSM field of view. Any position in the LOWFS OSM field of view can be acquired by calculating appropriate values for ( and φ, noting that due to a mirror reflection there are always two possible solutions. Four basic configurations of the LOWFS OSM probe arms are shown in Figure 13, including (a) the non-LGS observing mode; (b) a probe arm at full range; (c) “home position” where all probe arms are outside the field and (d) a random configuration for LGS mode.  The probe arm tips can be designed to approach very closely; this design allows the positioning of two probe arms on two NGS with only 5" separation.

Figure 11.  The LOWFS assembly.

Figure 12.  LOWFS OSM probe arm.

Figure 13.  Four configurations of the LOWFS OSM arms.

(a) one TT on-axis with the remaining 3 probes unused; (b) one probe arm fully extended; (c) all probe arms at the home position at the edge of the 150" diameter field; and (d) a random field with all 4 probes in operation.

The telecentric feed from the AO system makes the LOWFS optical design relatively simple.  The immediate benefit of this to a focal surface probe arm design is that the probe arms can patrol a flat field and not require any tilt of the optics to compensate for changing angle.  [Comment: reword to not confuse a flat field and a telecentric pupil. RGD 7/7/09].

The LOWFS OSM focal surface is curved with a radius of -1320 mm. As the probe arm moves from the center to edge of the field, this results in a defocus of approximately 1 mm. The broadening of the beam at the probe arm is negligible however the focus position of the re-imaged star at the WFS unit will change by a corresponding amount.  Note that this focus change is a smaller issue than the ~7 mm of focus change when a dichroic is inserted or removed from in front of the LOWFS assembly.

A solution to the focus issue is to position all three LOWFS units on linear slides. The units are moved to the correct focus position at the start of an acquisition procedure and do not need to be tracking devices.  An alternative solution is to keep the LOWFS units completely fixed and to place the probe arm focusing lenses on linear stages. This may be preferable and will be evaluated during preliminary design.

Optically the probe arm could be a simple relay, as shown in Figure 14, with a collimator, to produce a pupil, and a focusing lens. The design to incorporate a MEMS DM, and possibly a pupil stop, at the reimaged pupil is TBD.

A 5" diameter field of view was chosen as a reasonable size of field to be large enough to always hit the target, but small enough to allow close positioning of the probe arms. The field can be stopped at the WFS if required.   The focal length of the focusing lens will be determined as part of the WFS design.

Figure 14.  (a) Zemax model of LOWFS probe arm.  (b) Probe arm patrol field.

The advantages of a (/φ probe arm design for this application are:

- The optical pathlength is naturally and accurately preserved as a function of field position.

- As only four pick-offs are required one can allow larger mechanisms than otherwise allowed, resulting in readily available off-the-shelf rotary mechanisms using conventional worm gears rather than custom piezo or hybrid devices.

- The theta/phi arm naturally allows for a fixed feed to the non-tracking WFS unit.

- The arms can be balanced about the center of mass for each arm if this is needed for fine positioning.

There are two disadvantages of a theta/phi mechanism:

- The pupil rotates as a function of field position, by ±180o. This creates a varying rotation of the woofer DM with respect to the DM and lenslet arrays inside the TTFA and TWFS unit. The TT and PSF monitor units contain no lenslet arrays and the effect can be calibrated in software. A solution to this is to include an extra non-tracking rotation mechanism in the WFS unit that rotates the entire unit about the z axis as a function of field position.  However, the low order nature of the TTFA and TWFS units is most likely sufficient that this mechanism is not required in the LOWFS assembly, and we therefore propose the effect to be calibrated in software.

- In general, linear motors are more accurate than rotary.

#### Tip-Tilt (Focus and Astigmatism) Sensors

The three LOWFS operate at near-IR wavelengths to improve the availability of suitable stars of sufficient brightness.  Optimal performance is obtained using combined J and H band light.  One sensor will have 2 x 2 subapertures to provide sensing of focus and astigmatism.  Each tip-tilt star will be AO corrected using a MEMS DM with a pointable LGS beacon positioned near each tip-tilt star to maximize this correction.

Figure 15.  Tip, tilt, focus and astigmatism (TTFA) sensor schematic.

The telescope pupil to LOWFS DM mapping is shown in .

Figure 16.  Mapping of Keck primary mirror to a 32x32 actuator LOWFS DM.

The (vertical, horizontal) mapping = (346.97, 370.60) mm/subaperture.  Keck drawing 1410-CM0010.

#### Truth Wavefront Sensors

The TWFS is used to calibrate biases that arise when using LGS in an AO system; in the existing Keck AO system we refer to this as the Low Bandwidth Wavefront Sensor.  The biases are principally caused by the elongated nature of the LGS when viewed by sub-apertures of the LGS wavefront sensor and the changing sodium layer density profile. The truth wavefront sensor measures these biases by sensing the time-average wavefront from a NGS. These biases are slowly varying and are of a low spatial order. So, a NGS WFS using long exposures and only measuring the lowest spatial wavefront error is sufficient.

The TWFS is a 5x5 visible sensor (Figure 17).

Figure 17.  Truth wavefront sensor (TWFS) schematic.

The TWFS will use the visible NGS light while the TTFA uses the NIR light from the same NGS, typically the brightest NGS in the field of regards. The plate scale for this TWFS is __"/pixel.

The visible TWFS plate scale was chosen based on a median seeing limited spot size of 0.65".  Current estimates suggest that the visible TWFS can go down to 21.5 mag with a 10 second integration time and achieve 35 nm of total TWFS error.

#### LGS Wavefront Sensor Object Selection Mechanism

There are a total of seven LGS wavefront sensors in the baseline NGAO design. The asterism is novel in the sense that there is a fixed component, consisting of four guide stars (three on the vertices of an equilateral triangle and one at the triangle’s center), and a patrolling component, consisting of three guide stars that can be pointed anywhere in the field of regard in order to MOAO sharpen the three TT(FA) stars. The movable asterism diameter can be varied between 30" and 120", and can accept guide stars separated from each other by as little as 10".

Figure 18 is a schematic view of one of the three LGS (/φ pickoff probe arms.  These pickoffs are intended to be very similar to the LOWFS object selection mechanisms described in section 3.3.2.1.  A conceptual mechanical enclosure for the LGS WFS is shown in Figure 19.

Figure 18.  Plan view of the LGS object selection (/φ pickoff scheme.

Figure 19.  LGS WFS assembly enclosure.

Note that the LGS are always maintained fixed with respect to the LGS WFS OSM.  When the AO rotator is used in fixed field mode this is accomplished by the laser launch facility maintaining the LGS asterism fixed on the sky via its own rotator.  When the AO rotator is used in fixed pupil mode this is accomplished by not having the LGS asterism rotate on the sky.

#### LGS Wavefront Sensors

The LGS WFS assembly is shown in Figure 20.

Figure 20: LGS WFS assembly.

The fixed asterism LGS wavefront sensors are Shack-Hartmann (SH) sensors with 64 x 64 subaperture sampling of the pupil.  For the LGS wavefront sensor detectors we plan to use a very low noise CCD based on the CCID-56 to minimize the laser power required in each beacon.  This detector has 256x256 pixels with 3 electrons read noise at 2 kHz frame rates and < 500 electrons/sec of dark current at the operating temperature.  A descope to an existing 240x240 pixel CCD and 60x60 subapertures is a potential fallback option.

The movable asterism LGS WFS are similar, but sample their lower photoflux return wavefronts using only 32 x 32 subapertures.

A single LGS WFS channel is shown schematically in Figure 21.  This is very similar to the existing Keck AO WFS design (the existing optical design is documented in KAONs 137 and 375) and a preliminary optical design has been performed.  The WFS is positioned such that the LGS image is located at the field stop.  The entire mechanism, including object selection mechanism, must translate in focus to remain conjugate to the sodium layer.  Pupil reimaging optics reimage the telescope pupil (i.e., LODM) onto the lenslet array and relay optics relay the images produced by the lenslet onto the camera with the required magnification.  A lenslet switching mechanism allows multiple pupil sampling scales and a translation stage allows the relay lens and camera to refocus for different lenslets.

Figure 21.  Schematic of a single LGS WFS channel.

#### NGS Wavefront Sensors

The light to the NGS WFS is picked off in collimated light with a dichroic that reflects the visible light below ~900 nm and transmits the light above this cutoff.

The NGS WFS pickoff is performed with a pair of field steering mirrors as discussed in section 3.3.1.7.  The opto-mechanical layout of the NGS WFS is shown in Figure 22.  The field is reflected to the NGS WFS assembly by a dichroic (not shown) to a pair of field steering mirrors which feed the NGS WFS mounted on a focus translation stage.  The NGS WFS will use the same CCD as the LGS WFS.

Figure 22: NGS WFS assembly.

### AO Optical Performance

To determine the performance of the optical system, several sources of optical degradation were analyzed using Zemax in the wavelength passbands used by the individual science instruments and wavefront sensors. The passbands are defined in KAON 530.

The optical relay was modeled in conjunction with the Keck primary and secondary mirrors, to ascertain the combined effects of the two optical systems.

Field points used were the maximum off-axis fields defined for each instrument. The wavefront errors and RMS spot radii quoted are the worst-case for the field points analyzed.

According to Zemax, the working f/# of the wide-field relay is f/13.66 and of the narrow-field relay is f/46.89.  Airy disk sizes are defined by

and the depth of focus (DOF ) is defined by.

In Zemax, both the woofer and tweeter DM’s were defined as “Zernike Fringe” surfaces. This allowed a placement of Zernike terms on the mirror surface, to mimic the correction capabilities of an actual DM and derive an “uncorrectable” wavefront error (errors which could not be corrected with a DM).  Examination of the Zernike Fringe Coefficients and spot diagrams indicated that the bulk of the wavefront error was due to astigmatism and coma, therefore the Zernike fringe surfaces were optimized only for those coefficients (optimizing in Zemax with too many variables is slow and sometimes fails to converge in a realistic fashion).

#### Wide Field Relay Optical Performance

##### Optical Performance to the Low Order Wavefront Sensors

Figure 23.  Spot diagrams delivered to the LOWFS focal plane.

##### Optical Performance to the Interferometer Field Selectors

##### Optical Performance to the Laser Guide Star Wavefront Sensors

The LGS WFS dichroic pick-off is located in the collimated space between the woofer DM and OAP2.  The current simple design reimages the LGS, over their 150" diameter field, using __.

Figure 24.  Spot diagrams delivered to the LGS WFS at 180 km conjugate.

#### Narrow Field Relay Optical Performance

It is assumed for the narrow-field instruments that the HODM applies correction across the entire 40"x60" diameter field of view.  The performance values in Table 7 assume that the NGS dichroic is in place.  RMS spot radius takes lateral color into account but this can be minimized by putting a wedge angle on the second surface of the NGS dichroic.

Table 4.  Performance to the narrow field instruments.

Figure 25.  Spots at the on-axis and extreme field angles to the NGS WFS.

Figure 26.  RMS wavefront error to the NGS WFS versus field.

#### Atmospheric Dispersion Correction

#### Pupil Distortion

Pupil distortion in the NGAO cascaded relay manifests itself in several ways. The first two of these are evaluated in this section: the degree to which a grid of points on the primary mirror maps to a square grid on the DM on axis and the field dependent pupil aberrations.

Two other factors are: pupil tilt on the DM’s (this manifests itself not only as an uncertainty in the conjugate height of the correction, but also in plate scale errors that can degrade the astrometric accuracy) and DM-to-lenslet misregistration and scale errors (these are dependent on the pupil reimaging optics chosen for the wavefront sensors).

In the analysis, the telescope primary became the “object”, and field points were defined on the edges of the primary mirror. Observed field angle was set by adjusting the “stop” size placed at the Nasmyth focus to accommodate a 120" diameter field for the woofer, and a 30" diameter field for the tweeter in the narrow-field relay.  Results are shown in Table 5.   Figure 27 and Figure 28 and display grid distortion and the pupil PSFs for the woofer DM.  Figure 29 and Figure 30 show the same things for the tweeter DM.

Table 5.  Characteristics of the pupil image on the deformable mirrors.

Figure 27.  Grid distortion at the woofer DM location, magnified by 100.

Figure 28.  Spot diagrams for 5 locations on the primary mirror imaged onto the woofer DM.

Field considered is 150" diameter. Chief rays from the on-axis field angles make up the point of the comatic pattern, while chief rays for75" off-axis field angles  make up the outer “radius” of comatic points.

Figure 29.  Pupil grid distortion at the tweeter DM position, magnified by 100.

Figure 30.  Spot diagrams for 5 positions on primary mirror imaged onto the tweeter DM.

### AO Enclosure

The AO enclosure conceptual design is documented in KAON __.  The 3D model shown in Figure 3 was developed to support this design.  The current design makes full use of the entire left Nasmyth platform and covers an area of 6.1 x 9.1 m.  A working height of 2.59 m is provided with an overall working height of 3.35 m.

The cold enclosure requirements include up to -20º C operating temperature, a normal operating temperature of -15 º C, class 10,000 clean room and humidity ≤ 50%.

Entrance to the main room will be via an ante-room (2.4x2.4x3.35m).

### Alignment, Calibration, Diagnostics, Metrology and Monitoring

#### Alignment

KAON 719 defines and describes the alignments that will need to be performed to assemble the AO subsystems into the overall AO system and to align this system to the telescope.  Subsystem alignments will be documented as detailed design phase deliverables for each subsystem.

The key axes to be co-aligned are the telescope elevation axis (assuming the telescope optical axis overlaps this), the AO rotator mechanical axis, the science instrument optical axis and the optical axes for each subsystem.  The key points along the telescope elevation axis are the telescope focal plane and the telescope pupil plane.  These points need to be co-located with the appropriate foci and pupil planes for the AO subsystems and science instrument.

The models used for alignment will include the Zemax optical prescription and tolerance analysis and the SolidWorks model of the AO bench and AO system on the Nasmyth platform.  If appropriate the SolidWorks model will be exported to coordinate measuring machine (CMM) software to allow the use of a probe arm or laser tracker to locate components.  The models will be produced at the lab and operating temperatures.

The alignment requirements to the telescope (SR-55) include making the NGAO bench’s optical axis coincident with the telescope elevation axis to within 1 mm at the telescope focal plane (2 mm in focus) and 30 mm at the telescope pupil at all telescope elevations from zenith to 70(, all rotator angles and all operating temperatures.  These requirements are flowed down to requirements on the alignment of AO subsystems and DAVINCI to the AO rotator in KAON 719.

The alignment of the NGAO system in the lab is broken into the following sequence in KAON 719.  Preliminary procedures are provided for each of the install and align steps:

- Install and level the AO bench.

- Mark out location of all components on the bench based on the SolidWorks model and the optical tolerances.

- Install and align the rotator.

- Install and align the low order relay.

- Install and align the high order relay.

- Install and align the LGS WFS feed optics.

- Install and align the acquisition camera.

- Install and align the calibration unit and its fold mirror.

- Install and align the NGS WFS assembly.

- Install and align the LOWFS assembly.

- Install and align the ADC.

- Install and align the LGS WFS cold enclosure exit window.

- Install and align the LGS WFS to the AO bench.

- Install and align DAVINCI to the AO bench.

- Install and align the interferometer exit windows.

- Install and align the AO bench entrance window.

- Install and align the AO bench alignment fiducial in front of the AO bench entrance window.  The fiducial is a partially reflective mirror to be aligned perpendicular to the rotator axis with a cross-hair centered on the rotator axis.

- Align the interferometer dual star module to the AO bench (summit only).

Lab alignment testing is performed with the bench at room temperature and at the cold enclosure temperature.

A key question is how much we will need to or want to disassemble the fully assembled lab I&T system for shipment to the summit.  The lowest risk shipment approach is to fully disassemble and pack the lab system.  The quickest and less error prone re-assembly approach is to leave the aligned AO bench and aligned LGS WFS fully assembled.  For the purpose of this alignment procedure we assumed that the AO bench and LGS WFS will be shipped fully assembled to the summit.  We are therefore assuming that the internal alignments will only need to be verified at the summit.

The installation process will require removal of the AO room and electronics vault roofs.  In order to ensure optics cleanliness during the summit shipment and installation the AO bench and LGS WFS will have been sealed in some manner (preferably with the cold enclosure) to prevent air/dust inflow.  These seals will not be removed until after all the required components (AO bench, LGS WFS assembly, science instrument, electronics in the AO room, etc.) have been installed, the AO room roof has been replaced, cables have been routed and connected to the extent possible and the AO room has been thoroughly cleaned.  At this point the AO room will become a clean room.

The AO bench will be aligned to the telescope using an autocollimating theodolite, cross-hairs on the elevation journals and the AO bench alignment fiducial.

#### Calibrations

#### Calibration Unit

#### Atmospheric Simulator

#### Metrology

A metrology system could potentially be needed to monitor and correct for the alignments between the NGAO system and the science instruments, especially given the tight tip/tilt requirements and the significant non-common path between the LOWFS and the narrow field science instruments.  A “metrology like” alignment system (KAON 35) was proposed originally for the Keck AO system.  Some parts were installed in the NIRC2 camera but it was later decided not to be needed.  A laser metrology system for the Palomar AO system was also considered but was not installed.

#### Atmospheric Profiler

The initial requirements and design for an atmospheric profiler are KAON 552.  A profiler was deemed to be useful for NGAO for the following reasons:

- Acceptance testing and performance verification (in order to know the performance versus the current conditions).

- Diagnostic tool during observing.

- Aid to planning observations.

- Improve accuracy or speed up the convergence of the laser tomography algorithm.

- Useful as an aid in estimating the AO PSF across the instrument field of view.

The highest level requirements were determined to be (detailed requirements can be found in the functional requirements):

- Measure atmospheric profile at low resolution in six or more altitude bins between 1 km and 20 km altitude.

- Measure the profile once every 2 minutes.

- Measurement accuracy of 10% or better for r0.

- Operate automatically when conditions are suitable for operating the Keck telescopes.

- Small physical size.

A MASS/DIMM system was recommended as the best system to meet the NGAO requirements (KAON 552).  The NGAO team has significant experience utilizing and interpreting the data from the TMT MASS/DIMM that was located on Mauna Kea (KAONs 415, 420 and 496).  A TMT MASS/DIMM was donated to WMKO and installed by CFHT and UH at the CFHT weather tower site between CFHT and Gemini as shown in Figure 31.  This facility is operational and the data are published throughout each night at http://mkwc.ifa.hawaii.edu/current/seeing/.

Figure 31: Mauna Kea seeing monitor.

## Laser Facility Description

### Laser Facility Optical Design

### Lasers

The laser we plan to use for NGAO is the result of two down-select processes (WMKO has been involved in both) based on technical, management and budget criteria.  The first down-select involved the review of 5 proposals (one of the proposers was LMCT, which recently provided lasers for Keck I and Gemini-South, but which was not found to be cost competitive).  Two laser vendors were selected and funded by ESO to produce preliminary designs, completed in December 2009, and firm fixed price quotations for 20 W lasers.  WMKO, on behalf of a consortium of U.S. observatories (AURA, GMT and TMT), also placed contracts with these two vendors to perform risk reduction activities in support of these preliminary designs; primarily using $300k of AURA-NSF funding intended to support the development of the next generation of commercial lasers suitable for the future needs of our communities.  As a result, all of our organizations participated in the vendor progress review meetings and preliminary design reviews.

In the second down-select, based on the preliminary designs and quotations, ESO has selected the “Laser Guide Star Alliance” of MPB Communications Inc. and TOPTICA Photonics to produce a final design, a pre-production laser and four lasers.  This laser strongly leverages the expertise and existing products of these two world-leading laser companies.  The TOPTICA/MPBC laser design also meets the WMKO/TMT requirements.

The proposed laser will have a minimum output power of 18 W within the sodium D2a line and 2 W within the D2b line.  This re-pumping concept is predicted to improve the sodium return by a factor of 2 or more.  A 40% improvement was demonstrated in a preliminary on-sky experiment at Starfire Optical Range.  During the preliminary design phase TOPTICA/MPBC produced a demonstrator laser that achieved output powers of up to 30 W at 589 nm wavelength.  This demonstrator was shown to operate under variable gravity (see Figure 32) which allows it to be mounted to the elevation ring, thereby lowering beam transport complexity and throughput loss.  An electro-optic modulator was also demonstrated to produce the required D2b line with good beam quality.

Figure 32.  TOPTICA/MPBC demonstrator laser head.

Tilt test carried out at a power level of 23W at 589 nm.

The demonstrator laser is based on the Raman Fiber Amplifier (RFA) approach first demonstrated by ESO at 1178 nm and high powers.  The TOPTICA/MPBC demonstrator included two RFAs, whose output signals are coherently combined in fiber.  Due to successful higher power RFA demonstrations the proposed laser will be simplified significantly by the use of a single RFA, as represented schematically in Figure 33.  A master oscillator provides a low power narrow-band signal at a wavelength of 1178 nm to the RFA.  The RFA is pumped by an ytterbium fiber pump laser.  The 1178 nm RFA output is frequency doubled to the sodium D2a wavelength in a resonant cavity using a lithium triborate crystal.  The sodium D2b line is then generated as a sideband when the beam passes through an electro-optic modulator.

The three lasers for WMKO will each consist of a laser head mounted on the telescope’s elevation ring and an electronics module, including the seed laser, pump lasers and controller, mounted in the existing Nasmyth platform AO electronics enclosure (thereby greatly easing the heat removal task).  A single heat exchanger cabinet for all three lasers will also be mounted at Nasmyth.

Figure 33.  Schematic diagram of the laser

### Laser Enclosure and Beam Transport Mechanical Design

For reference, the Keck II telescope including the existing AO and laser enclosures and laser launch tube are shown in Figure 34.

Figure 34.  Existing Keck II Telescope and laser location case 1.

### Laser Safety System

The safety system will assure the entire laser system and its components will operate to maintain a safe environment for personnel, as well as equipment.  The safety system is shown in Error! Reference source not found..   To make the determination to shutter laser light, the safety system will sense environmental changes or user commands from the Laser System Interface (see section Error! Reference source not found.).  Termination of laser radiation will be done at different locales depending on the threat of laser radiation.  At the laser, it will close the laser shutters prior to the beam relay system or turn off power to the entire laser system.  At the beam steering system, it will close a final shutter prior to launching of the beam into the beam telescope.  To make proper determination, the safety system will sense inputs from the laser, beam steering system, glycol system, laser enclosures, aircraft detection and spotter system, and user inputs via the Laser System Interface.

In addition to terminating laser radiation, the safety system will also provide laser status for personnel entering laser zones that may be hazardous.  This will ensure laser or summit personnel will not accidentally walk into exposed laser radiation.  The safety system controller will be a programmable logic device.  It will sense inputs from multiple subsystems on and off the telescope, as well as commands via the network from the Laser System interface.

Figure 35: Safety system.

The increase in power from current systems with 10-20 W to a system with three 25W lasers means that the potential for property damage and personnel injury by 589nm light is increased.  In addition, the power of IR pump beams will also be increased over corresponding beams in the current lasers, increasing the risk of invisible radiation.  Still, the NGAO lasers will be class 4 lasers, the same as the current Keck lasers.  As such, the laboratory engineering controls and procedures are the same as any class 4 laser controlled area.  Measures include door interlocks, lighted signs, laser protective eyewear, written procedures, and training.  For the large diameter beams leaving the laser launch telescope, the Nominal Hazard Zone (NHZ) for diffuse reflections is essential zero.  In contrast, specular reflections would have a very long Nominal Ocular Hazard Distance (NOHD) for the NGAO lasers.   As with any sodium Laser Guide Star in navigable airspace, the beam(s) are a threat to aircraft.  This will require safety observers and annual request to the FAA for a letter of no-objection.  These are currently the standard practices at the observatory for LGS operations.  A complete safety analysis would be completed as part of the planning for the laser installation.

Aircraft safety for Keck LGS AO observations is currently provided by aircraft spotters as recommended by the FAA.  WMKO has been working with the G10-T Laser Safety Hazards subcommittee of the Society of Automotive Engineers that sets the relevant aircraft safety standards used by the FAA.  This committee is addressing the issue of facilitating a consistent approach to approving control measures.  This opens the door to approval of automated aircraft detection systems that do not require spotters or radar.  Gemini Observatory is developing an all sky camera for aircraft detection that will be implemented as a shared resource on Mauna Kea.

We will use the same procedures for satellite avoidance and for not interfering with the observations of other Mauna Kea telescopes as are currently used for Keck LGS AO observations.  A discussion of the impact on observing efficiency of these items, and potential changes, are discussed in section 3.6.1.2.

## AO Controls

This part of the design manual covers all NGAO controls except for the real-time control (RTC) system.

### Controls Infrastructure

The entire NGAO system can be viewed as a distributed controls system, in which many different components communicate with each other in various client/server or master/slave relationships using possibly several communication networks and protocols. We have represented a high-level abstraction of the NGAO system in the block diagram shown in Figure 36.

Figure 36: A Block diagram of the NGAO system viewed abstractly as a distributed controls system

Each block in the diagram represents a set of control functions unique to a particular system or subsystem that can logically be grouped together. The grouping is an abstraction, as the various functions represented by each block are actually to be implemented using multiple software and hardware components that may also be distributed.

Figure 37: A block diagram of the NGAO controls infrastructure

Figure 37 depicts the controls system as a software hierarchy. At the top level are the main interfaces to the various subsystems (some of these interfaces are referred to as sequences in the diagram). All user commands to the subsystems pass through these top level interfaces. The middle level of the hierarchy represents an abstraction of more complex lower level control tasks, namely the basic control functions for that subsystem. Users do not access the system at this level except for engineering or troubleshooting purposes. Finally, at the bottom level of the hierarchy are the devices controlled by the control system themselves. The telescope, LTCS, instrument, and atmospheric profile are outside of the direct control of the NGAO system.

The current Keck telescope and AO software and controls infrastructure relies on the EPICS control system middleware, Sun workstations and VxWorks real-time CPUs in VME crates.  Since NGAO and an upgrade of the Telescope Control System (TCS) were both in the early design phase we took this opportunity to look at whether options to EPICS might provide a better match to our requirements including ease of development and maintenance.  We therefore began the NGAO architecture design process (see KAON 679) by looking at a number of communication middleware packages and software frameworks and also reviewed similar comparisons performed by groups working on the Australian Square Kilometre Array Pathfinder and the ESO E-ELT TCS.

The software architecture we have chosen to build the NGAO controls system uses a framework based on the Advance Technology Solar Telescope’s (ATST) Common Services Framework (CSF). We have dubbed this architecture the “Keck Common Services Framework”, or KCSF. The KCSF provides the base infrastructure needed to develop a distributed control system.  We will perform one more comparison of CSF versus EPICS to ensure that we have chosen the optimal path for NGAO and TCS by early in the NGAO detailed design.

In a distributed system, components will need to communicate with each other, perform certain actions, and work together in a pre-defined way to form a larger system. The KCSF framework enables this by providing common communications, common data types, common commands and common tools throughout. The solution uses a Component Based Development (CBD) model that supports methods, attributes and properties. The framework provides a kernel API which hides all the details of network access and provides object browsing, discovery and common services.  Refer to KAON 671 and KAON 679 for more details.

### AO Control Loops

KAON 705 provides a high level summary of the AO control loops used during night-time operation.

#### Devices

Figure 38 provides an overview of the devices used in closed loop operation.

Figure 38: AO device overview.

Here is a brief explanation of each of the devices, proceeding roughly from left to right in Figure 38:

- Telescope.  The telescope tracks the science object.

- Rotator.  The rotator tracks to keep the field or pupil fixed.

- Deformable Mirror 1 (DM1).  The Low Order DM in the wide field relay.

- Tip-Tilt Mount 1 (TTM1).  The high bandwidth TTM on which DM1 is mounted.

- Laser Guide Star (LGS) WaveFront Sensor (WFS).  There are seven laser guide star (LGS) WFS.  The LGS WFS corresponding to the central fixed asterism are labeled A1 through A4.  The LGS WFS corresponding to the three patrolling lasers are labeled P1 to P3.  Each patrolling LGS WFS is positioned on the corresponding patrolling LGS with a (( probe arm (non-tracking). All LGS WFS’s include a TTM and a WFS (as pictured in the lower left of Figure 38).  The LGS WFS’s are mounted on a single tracking focus camera stage (FCS) to maintain conjugation to the sodium layer.

- Interferometer.  A dichroic beamsplitter can be inserted into the beam to feed light to the interferometer.  The interferometer uses a pair of object field selector (OFS) mirrors (non-tracking) to transmit the on-axis object and acquire an off-axis object (these are controlled by the interferometer).

- Low order wavefront sensor (LOWFS).  There are three near-infrared LOWFS.  Each is positioned on a NGS using a (( probe arm (non-tracking).  All three LOWFS contain a MEMS deformable mirror and a fast tip-tilt mirror (MEMS/TT in the figure).  The first two, labeled 1 and 2 in Figure 38, have a tip-tilt (TT) sensor.  The third LOWFS, labeled 3 in Figure 38, contains a tip-tilt-focus-astigmatism (TTFA) sensor.  Co-mounted with the TTFA is a truth wavefront sensor (TWFS) that uses the visible light.  All three LOWFS have focus translation stages (non-tracking) to position them, as a function of field position, conjugate to the science instrument or interferometer focus.

- Deformable Mirror 2 (DM2).  The High Order DM in the narrow field relay.  This is higher order than DM1.

- Tip-Tilt Mount 2 (TTM2).  The low bandwidth TTM on which DM2 is mounted.  This is suitable for tracking but not for atmospheric correction.  See KAON 669 for more discussion.

- Natural Guide Star (NGS) WFS.  A dichroic beamsplitter can be inserted into the beam to feed light to the NGS WFS.  A pair of field selector mirrors (FSM) (non-tracking) is used to acquire the NGS.  The NGS WFS is mounted on a translation stage to position its focus, as a function of field position, conjugate to the science instrument or interferometer focus.  The NGS WFS can be used in a mode where it acts as a TTFA/TWFS type LOWFS.

- Atmospheric Dispersion Corrector (ADC).  The science instrument ADC that compensates for atmospheric dispersion as a function of zenith angle and direction.  It can be moved into or out of the science path with a translation stage.

- Science instrument.  Only one science instrument, DAVINCI is planned initially, although the NGAO system will be capable of feeding a second future instrument.  No tracking devices are currently planned in the instrument, but multiple devices (e.g., filter wheels, gratings) will be changeable between science exposures.

- Not shown are the sources that can be inserted on the telescope side of the rotator (via a fold mirror) for alignment, calibration and testing purposes.  These are not expected to be required during routine night-time operation.

#### NGS AO Control Loops

Figure 39 and Figure 40 show the control loops used in NGS AO mode with the science instrument and interferometer, respectively.

Figure 39: NGS AO control loops for the science instrument.

The real-time wavefront sensing is provided by the NGS WFS.  The NGS WFS camera data is fed to the real-time control (RTC) system.  The RTC computed tip-tilt is sent to TTM1 and the higher order commands are sent to DM1.  In the case of the science instrument the highest order corrections can be applied to DM2 (DM2 is fixed, nominally flat, for the interferometer); these are higher order terms than DM1 is capable of correcting.

Figure 40: NGS AO control loops for the interferometer.

The AO control system keeps track of the tip-tilt applied to TTM1 and the focus applied to DM1.  Tip-tilt and focus are then periodically offloaded to the telescope pointing and focus (secondary piston).  Telescope Az/El position information is used to make the transformation to telescope coordinates.

The AO control system provides tip-tilt offsets.  These are applied to the FSM when the tip-tilt loop is open.   For the science instrument case the offsets are used as centroid offsets by the RTC when the tip-tilt loop is closed.  For the interferometer case these offsets are applied to TTM2 when the tip-tilt loop is closed.  The AO control system computes differential atmospheric refraction (DAR) between the NGS WFS wavelength and the science instrument or interferometer wavelength.  Keck angle tracker (KAT) offsets are provided by the interferometer and are combined with DAR offsets in the case of the interferometer.  Any pre-measured tip-tilt errors from the ADC rotation can also be included as part of the AO control system provided offsets.  Differential tracking can also be handled with offsets.

The AO control system provides position and rotation control for the science instrument ADC when it is in the science path.  This control is based on the Az/El of the telescope, the rotator orientation and the science instrument wavelength band.   Any tip-tilt errors introduced by the ADC rotation should be corrected via AO control system offsets to TTM2 (based on a previously calibrated lookup table or algorithm).

#### LGS AO Control Loops

Figure 41 shows the control loops used in LGS AO mode with the science instrument.  Two “AO Control” boxes are used in the figures for drawing simplicity; these are the same system.  Two “RTC Tomo.” boxes were used for the same reason.  The real-time wavefront sensing is provided by a central set of four fixed LGS WFS, three patrolling LGS WFS and the three LOWFS.

Figure 41: LGS AO control loops for the science instrument.

Data from the central fixed asterism LGS WFS and LOWFS are used by the real-time control (RTC) tomography engine to compute the best correction to be applied to the science path.  Two options will exist as to how to distribute the science path correction between DM1 and DM2.  One option is to apply the ground layer turbulence to DM1 and the high altitude turbulence to DM2.  The second option is to apply the lower order corrections to DM1 and the higher order (higher than DM1 can handle) corrections to DM2.  In either case DM2 must deal with the highest order terms that cannot be handled by DM1.  In the interferometer case DM2 is nominally flat so all of the possible correction must be applied to DM1.

The real-time wavefront sensing data from each patrolling LGS WFS is used to control the MEMS in the corresponding LOWFS via a separate RTC control loop (labeled RTC1, RTC2 and RTC3 in the figures).

The tip-tilt information from the three LOWFS is used via the RTC tomography engine to control TTM1.  This information is also used by the AO control system to determine if there is any field rotation; which could be corrected with an offload to the rotator.

Offloading of tip-tilt and focus from TTM1 and DM1 to the telescope is done in the same way as for NGS AO mode.  Science instrument ADC control is also the same as for NGS AO mode.

The seven LGS WFS are mounted on a tracking focus camera stage (LGS FCS) to maintain conjugation to the sodium layer.  Fast focus information from the TTFA (via the RTC) is used by the AO controller, with appropriate time averaging, to provide a focus correction to the FCS.  On a slower time scale more accurate focus information from the TWFS is used by the AO controller to provide a focus correction to the FCS.

The AO control system provides tip-tilt offsets (for DAR, KAT offloads and differential tracking).  These are applied to the three LOWFS (( probe arms when the tip-tilt loop is open.  The offsets are applied to TTM2 when the tip-tilt loop is closed (this is different than for the NGS case).

Figure 42 show the control loops used in LGS AO mode with the interferometer.  The real-time wavefront sensing is provided by the four fixed LGS WFS and by the LOWFS/TWFS mode of the NGS WFS (the fold dichroic that feeds the interferometer does not transmit NIR light to the LOWFS).  Data from the central fixed asterism LGS WFS and single LOWFS are used by the real-time control (RTC) tomography engine to compute the best correction to be applied to the interferometer science path using DM1.  The tip-tilt information from the LOWFS is used via the RTC tomography engine to control TTM1.

Offloading of tip-tilt and focus from TTM1 and DM1 to the telescope is done in the same way as for NGS AO mode.

The LGS WFS are mounted on a tracking focus camera stage (LGS FCS) to maintain conjugation to the sodium layer.  Fast focus information from the single TTFA (via the RTC) is used by the AO controller, with appropriate time averaging, to provide a focus correction to the FCS.  On a slower time scale more accurate focus information from the TWFS is used by the AO controller to provide a focus correction to the FCS.

The AO control system provides tip-tilt offsets (for DAR and KAT offloads.  These are applied to the NGS WFS field steering mirrors when the tip-tilt loop is open.  The offsets are applied to TTM2 when the tip-tilt loop is closed (this is the same as for the NGS case).

Figure 42: LGS AO control loops for the interferometer.

### Motion / Device Control

#### Motion Control Electronics

Approximately 90 moving axes are needed to support the AO and Laser Guide Star systems. There are four primary areas NGAO devices will be located. The devices on the cooled AO bench and those outside of the AO bench (AO Room) will be located on the Left Nasmyth Platform. The devices for the Laser Switchyard will be on the elevation ring. The Beam Generation System (BGS) devices that control the fixed LGS asterism and steering of the patrolling LGS will be in the secondary socket on the telescope.

Components of the motion control system will be required to operate reliably and within specification in the designated environment: -15°C for cold enclosure components, -10°C in other locations, and operating specifications may require derating based on the 4200m elevation of the observatory. In order to preserve the environment, the motion control system must not create EMI, no light pollution is allowable, thermal dissipation must be managed, and the design should minimize vibration. Measures must be taken to protect personnel and equipment from injury or damage, including (but not limited to) e-stops, limit switches, software protections, thermal monitoring and diagnostics.

The motion control architecture will be distributed in nature. The number of devices has decreased significantly as the subsystems have matured, making centralized control more practical, but there are still benefits to a distributed approach.

The concept of a control category, first introduced in KAON 643 (Motion Control Architecture Study), has been used by the controls team to help partition the design. The four categories are described below.

- Low precision in/out

  - simple in/out devices

  - actuators other than motors (e.g., solenoid, pneumatic, etc.) may be considered

  - switches or hard stops may be used to define positions

  - knowledge of position and velocity while moving, although desirable, may not be required

  - a dichroic or fold, for example, that is either in beam or out of beam

  - moved during configuration, not during an observation

- Non tracking

  - moved during configuration, not during an observation

  - generally used to position an element for focus or alignment

  - some devices with tight position tolerances

- Tracking

  - position calculated from and synchronized to external information (telescope az/el, etc)

  - servo loops closed during an observation, update rates from 25ms to 100s of seconds

  - various levels of precision required

  - ADC, rotators

- Special Consideration

  - coordinated motion with other DOF(s)

  - may be constantly moving during an observation, update rates ( 1Hz

  - mechanical design may require the device to servo in position

  - may require a high precision actuator, not a servo motor

  - examples include steering mirrors, tip/tilt stages, and object selection arms

  - pickoff arms require spatial position constraints to avoid collision

##### Controllers and Actuators

Servo motors will be controlled via multi-axis motion controllers. Controllers should be capable of performing the conversion between engineering units and encoder units. The ability to define coordinate systems is highly desirable to reduce overhead on the control system. Although a vendor has not been selected, the Delta-Tau PowerPMAC looks to be a good candidate given its programmability and scalability. Equipment will be mounted in standard 19inch equipment racks. Rack mountable equipment is preferred, although equipment with non-standard chassis can be placed on shelves within the rack.

For the lower precision, type 1 devices with intermittent motion, smart motors are recommended. A smart motor is a servo motor with an integrated controller. These devices can be chained together on a single communication port and power supply, providing a significant reduction in cabling. These motors have a NEMA17 or NEMA23 frame, so stages will need to be selected with that in mind. For cases where a smart motor is not useable, a conventional DC servo with shaft encoder will be used. The motor could be either brushed or brushless and depending on the location, a PWM amplifier could be used.

Some type 2 devices may be grouped with the type 1 devices and controlled via smart motor. The remainder will likely be actuated with a conventional servo motor and shaft encoder. The motor could be either brushed or brushless. Assuming electrical noise from PWM amplifiers is managed, linear amplifiers may not be required. Servo loops will be tuned to achieve commanded position within reasonable settling time; performance while stage in motion (following error, damping) is less critical

Type 3 devices will be actuated with brushed or brushless servo motors with shaft encoders. Assuming electrical noise from PWM amplifiers is managed, linear amplifiers may not be required. However, the torque jitter present in PWM driven loops may not be acceptable and depending on the required performance, dictate the use of linear amplifiers. These devices have more stringent requirements on servo loop performance, including minimal following error.

Type 4 devices require special consideration due to one or more requirements on their performance. These DOF will be actuated with a combination of motors, piezo and voice-coil actuators. Some of these DOF are required to track in some observing modes. Motorized devices may require linear drive amplifiers. Piezo devices may not be suitable for use with a 3rd party controller. OEM controllers are available to match the specific actuator. These are provided with either a digital (serial/Ethernet) or analog interface. In general, these devices will not require a high control bandwidth; tracking is used for flexure compensation and the rates are slow. If higher bandwidth is required, the interface and update rates will need to be carefully considered once the devices have been chosen to ensure that the tracking performance requirements are met. Some of these devices require custom homing sequences to move two more axes in coordination.

##### PWM Drives & EMI

Manufactures of servo drives are increasingly making use of Pulse Width Modulation (PWM) to efficiently transmit power to motors. PWM has several advantages and a few disadvantages. Of primary concern to NGAO is the generation of electromagnetic interference (EMI). PWM signals have relatively fast rise times and may be required to switch high currents through long lengths of cable; a scenario that leads to noise. Detectors on the AO bench are extremely sensitive and will likely not tolerate the presence of electrical noise. EMI could also affect analog feedback signals from strain gauge type sensors commonly used on piezo motion stages. The MEMS deformable mirrors may also be susceptible to EMI.

Even with the good cabling design and careful routing with sufficient physical isolation, PWM drives must not be used, or any cabling routed near, any of the various detectors, deformable mirrors or devices with analog feedback.

The architecture does not prohibit the use of PWM drives. In the case of smart motors, the drive signals are extremely short (several cm) which significantly reduces the magnitude of EMI. Many motors are not located near a sensitive device and careful cable design and routing may allow use of a PWM drive. In addition, many DOF only move during bench setup when sensitive devices are idle or could tolerate a slight elevation in EMI without an impact on performance.

When selecting PWM drives, they must be matched to the motor characteristics and, whenever possible, a path for changing to a linear drive should be identified.

##### Room for Expansion

The baseline NGAO motion control architecture will budget space for a 10%, or nearest sensible incremental increase in the total number of servo motor axes, beyond what is outlined in the Master Device List. It is acknowledged that some of the devices listed may not be implemented during initial commissioning, however these are included in the design and not considered expansion. The intent is to provide rack space, or if available, crate space for the additional controllers and amplifiers. Depending on the power supply configuration, power will be available or space will be available for an additional power supply. Communication ports will be reserved as well. Given the difficulty of modifying the cold enclosure, the design will make provisions for at least five additional motion cables passing through the enclosure wall. This will likely be a blank panel that is not populated with connectors.

##### Support Equipment

The motion control system is required to halt all devices in response to the observatory emergency stop. Circuitry will be required to remove power from the motion control amplifiers. Recovery from the e-stop event will be faster if the encoders and limits remain powered; re-initializing the devices would not be necessary.

Some digital inputs and outputs will be required to control and monitor the status of the motion controllers. Inputs will be required to monitor the health of the controllers. Outputs will be required to reset a controller.

Controllers will be connected to the Ethernet, either directly or via a protocol converter if their native protocol is RS-232 or USB.

Some controllers will need an analog setpoint and provide analog position feedback. Depending on the required bandwidth, either an Ethernet ready analog I/O module, an analog output from a motion controller or PLC, or an analog card in a control computer will be required.

Remote control of the power feeding servo amplifiers and motion controllers will be included.

##### Cabling

For servo motors, a generic two DOF cable will be designed. This will provide the primary connection between the motion controller distribution panel and the motion axis. It is envisioned that the cable will have Mil-spec connectors on each end with conductors sized according to the demands of the motion axes. The length of this cable will be a function of the source and destination. The intent is to include cabling in the NGAO 3D model in order to avoid excess. Breakout cables will be required at each end of this cable to connect the distribution panel to the motion controllers and to convert the circular connector to the axis specific connector at the stage. This scheme will need to be adjusted for brushless motors to accommodate the additional phase and sensor conductors.

Non-servo stages will have different requirements that may not allow more than one DOF per cable. This will be evaluated on a case by case basis. The goal is to reduce the number of individual cables and connectors as much as possible, while maintaining reliability and serviceability.

##### Location of Equipment

The proposed architecture places controllers in the AO Electronics vault and the Laser Service Enclosure. The use of smart motors puts some control on the AO bench.

The planned layout of the AO Bench, AO room and Electronics vault is shown in Figure 43. Although a single block is shown for the servo controllers, this may not reflect the final hardware implementation with all DOF on a single controller.

Figure 43: AO Motion Control Layout

Controllers for devices in the laser switchyard and beam generation system will be located in the Laser Service Enclosure (LSE), as shown in Figure 44. This helps by shortening the cable run and does not require significant use of the elevation cable wrap. This approach will also simplify integration of the laser switchyard devices. Cabling between the LSE and secondary should be designed to include two or more devices per cable, where possible. This architecture is quite feasible. The present LSE design will accommodate the volume of the equipment and glycol cooling is already required.

Figure 44: Laser Motion Control Layout

For more details on the motion control hardware, refer to KAON 715 and KAON 643.

#### Motion Control Software

The low level motion control functions consist of one or more device drivers that implement an API for interacting with the motion control system to provide the most basic level of control. This device driver will most likely be supplied by the manufacturer of the motion control electronics. An abstraction layer will be added above the low level driver as part of AO Controls.   This layer would hide all the hardware specifications and implementation of the actual motion control hardware.  At the top of this control block is a generic state machine that implements the basic coordinated functions required for controlling a motion control device with an arbitrary number of degrees of freedom. This concept is used in the existing Keck AO and Interferometer systems.

KAON 715 identifies all of the current device types / categories required by NGAO. In order from least complicated to most demanding, they are:

- Shutters

- Low precision  non-tracking devices

- Medium precision non-tracking devices

- High precision non-tracking devices

- Tracking devices

- Extremely high precision tracking  and non-tracking devices

- Coordinated high precision tracking and non-tracking devices

From a software perspective, these are grouped into the following generic categories:

- discrete commanded devices

  - shutters

- non-tracking devices

  - low precision  non-tracking devices

  - medium precision non-tracking devices

  - high precision non-tracking devices

  - extremely high precision non-tracking devices

  - coordinated high precision non-tracking devices

- tracking devices

  - tracking devices

  - extremely high precision tracking devices

  - coordinated high precision tracking devices

The intent is to develop each type once and instantiate it for all the necessary devices.   This will simplify implementation and allow for quick and easy changes or addition of new devices. Each of these types is discussed in the following sections.

#### Device Control Electronics

Device control is, in general, low speed without tight timing constraints; the commands are frequently single events (e.g., GUI button press) and are expected to be executed on the timeframe of a second.  Ethernet will be the primary means of communicating with devices for control. If a device does not have an Ethernet interface, there may be simple Ethernet solutions which exist (e.g., terminal servers to communicate with RS-232 based devices, or digital I/O modules with an Ethernet interface to generate digital I/O signals). This approach has a number of benefits:

- Control can easily be distributed as needed

- Cabling issues associated with centralized control can be minimized

- Solutions based on an industrial computer and real-time operating system, e.g., VxWorks and VME crates, can be minimized to those areas requiring tight real-time control which do not fall under the device control architecture discussed in this document.

- Ethernet-based solutions are easily interfaced to the NGAO control system.

  - To reduce software integration efforts, Ethernet devices should support an industrial protocol (Modbus TCP/IP, Fieldbus, etc) rather than a web (HTTP) based interface whenever possible.

The following is a summary list of all of the common control methods/interface/signal types that will be needed to support the NGAO controls system.  For more details on each type refer to KAON 668

- Remote Power Control

- Camera / Detector Control

- Discrete (Digital) Input/Output

- Analog Input

- Analog Output

- COTS Controllers

- Remote Reset control

- Video

- RS-232 and USB

- Ethernet

- Time Distribution / Synchronization

#### Device Control Software

Under the KCSF infrastructure, the concept of a digital I/O acquisition (DAQ) controller would be built and any component needing to interface to a device would create a DAQ specific controller to match the IDaqDevice interface. In our case we would use the NIDAQ Device Controller. This device controller uses the NI-DAQmx API from Nation Instruments and supports the ICE IDaqDevice interface.  The NI-DAQMmx driver supports a number of device types:

- Multifunction DAQ

- Analog output

- Digital input/output

- Counter/timer

- High speed digitizer

- Dynamic signal acquisition

A DAQ Client will run as part of the application and will be responsible for setting up the IO, alarming and reading/writing to the devices via the ICE interface.

Serial and Ethernet interface device types, which are not supported by NI-DAQmx, as well as special camera or detector controls, will be handled independently under the existing KCSF iDevice infrastructure.  For more details refer to KAON 679: NGAO Control Software Architecture.

Non-motion device control not covered by the above IDaqDevice interface will be described case by case in the following sections.  However, they should all be able to fall under the KCSF device infrastructure and be designed with the generic IDevice interface. The IDevice interface allows a device to access the get, set, execute and xxxMonitor methods which should be able to support the full command set for each device.

### AO Control Software

KAON 714 should be referred to for more details for the following section.

#### AO Control Sequencer

The AO control sequence is implemented by the AOFacilityComposite, which is the main interface between the various AO controls functions and the rest of the NGAO system.  The AO Sequencer is responsible for the management and coordinated execution of the entire AO controls system. The Facility Composite implements the high-level device sequences that will perform the system configuration, target acquisition, and closed-loop observing. The Composite executes these sequences by directing commands to each of the dependent subsystems depicted in Figure 45, and discussed in the following sections.

Figure 45: AO Control Sequencer Collaboration Diagram

The AO control sequence covers everything from bringing up the software system to acquisition, and finally shutting down for the night. The sequence itself can be divided into phases each covering a specific state of the system during a typical night’s observing. These phases are (listed in order of execution):

- Startup

- Initialize

- Configure

- Acquire

- Observe

- Halt

- Power-down

For the most part these phases can be executed straight through to perform NGAO corrections for a science target. However there is flexibility allowing the sequence to return to a previous phase or jump forward to a latter phase. A detailed review of the AO sequences is described in KAON 735: NGAO AO Sequence.  The following sections briefly discuss the AO subsystem composites controlled by the AO Sequencer.

##### Wide Field Relay

The Wide Field Relay covers the low-order atmospheric correction hardware and miscellaneous first-relay and low-order devices, which includes the entrance hatch cover, the rotator, the low order deformable mirror (LODM) , the tip-tilt stage on which the LODM is mounted and the IF fold dichroic.

The Wide Field Relay subsystem is a logical grouping of these hardware devices, but is not actually implemented as a standard KCSF component due to the very different management and control requirements of the individual devices. Although other devices may also be considered part of the wide field relay, they are grouped and managed under other subsystems (see the LGS and LOWFS subsystems).

The following sections detail the NGAO controls loops implemented by the Wide Field Relay devices.

###### Rotator Control Loop

Due to the design of the Keck telescopes, as a target is tracked across the sky it will appear to rotate on the science instrument. Similarly, as the telescope elevation changes, additional rotation is added to the field and pupil due to the rotation of the telescope’s tertiary mirror (optical axis) of the telescope with respect to the Nasmyth platform. The image rotator is designed to correct for these rotations and keep either the field or pupil stable relative to the instrument.

Figure 46: Image Rotator Control Loop

In fixed-field observing we want the sky field to remain at a fixed orientation relative to the detector. In this mode the rotator should track the position angle of the target (the apparent angle of rotation on sky) which will be constantly changing as the telescope tracks the target. While in fixed-field the pupil is allowed to rotate freely.

In fixed-pupil we want the telescope pupil to remain at a fixed orientation relative to the detector. To maintain a stable pupil the rotator will track the telescope vertical angle. The vertical angle changes as the telescope slews in elevation. While in fixed-pupil mode the field is allowed to rotate freely.

###### LOWFS Rotation Correction Control Loop

During LGS observing the LOWFS sensors will be tracking the tip and tilt of the natural guide stars. From this information the system can determine the appropriate tip-tilt correction to apply to TTM1, and determine if there is any residual field rotation not corrected by the Image Rotation control loop.

Figure 47: Field Rotation Offset Control Loop

The NGAO RTC Interface Controller will calculate the residual rotation seen by the three LOWFS and make this information available as telemetry. The Image Rotator Controller will subscribe to this telemetry and correct for any residual field rotation.

##### Acquisition System

During the NGAO acquisition phase of the observing sequence, the operators, science tools, and controls system will need to be able to view the sky to determine the current pointing and alignment of the telescope. This is possible by imaging the field with the acquisition camera. With this device clients can determine the precise pointing of the telescope and the orientation and position of the laser asterism. The functionality for this capability is provided by the Acquisition Subsystem. The Subsystem is responsible for the management and control of the following devices: acquisition camera, acquisition fold mirror, filter wheel and focus stage.  The Acquisition Subsystem does not implement any control loops.

##### LGS Wavefront Sensors

The LGS Wavefront Sensor Subsystem is responsible for the management and control of the LGS wavefront sensors and related hardware. The subsystem provides the initialization and acquisition functionality to position the patrolling pickoffs; align the patrolling and tomography LGS beacons; configure the WFS RTC cameras; and manage the focus for the entire LGS assembly. The LGS WFS Subsystem also provides capabilities to perform background calibrations and respond to alignment errors by offloading to the laser facility global tip-tilt and asterism rotator.

The following sections detail the offload control loops of the LGS WFS subsystem. Each control loop is implemented in part or in full by one or more of the NGAO controllers.

###### LGS WFS Focus Control Loop

As a tracking device, the WFS Focus Stage Controller will be monitoring the state of the system and responding to events. Focus information is derived from the LOWFS calculated focus and the telescope zenith angle.

Figure 48: WFS Focus Control Loop

WFS focus tracking is an event driven control loop triggered by telemetry events from the RTC, the TWFS camera, and DCS telescope zenith angle keywords. The RTC provides time-averaged data from the Tip-Tilt Focus and Astigmatism (TTFA) WFS to determine the error in the LGS WFS focus position. More accurate focus information is provided at a slower rate (~1Hz) directly by the Truth Wavefront Sensor (TWFS). The TWFS images will be processed by the NGAO controls system to determine focus and centroid offsets and published as telemetry. When the controller receives input from these items it will recalculate the sodium layer altitude and apply the appropriate compensation to the stage.

As the focus position is driven by measurements calculated from LGS beacon information, disturbances in seeing, hardware obstructions, or device failures can cause the control loop to receive erroneous data from the WFS. To ensure the focus is tracking a real target and not noise or reflections, the controls system will monitor the sensor data quality. This may involve periodic checks of flux intensity or the rate of focus degradation. Extreme changes in the monitored properties can be used to automatically stop focus correction until the seeing improves.

###### LGS WFS Offloading Control Loop

During observing the LGS WFS will periodically have to offload tip-tilt errors to the Beam Generation System to maintain alignment of the LGS beacons. Two types of offload control loops are implemented: one for the tomography sensors, and another for the patrolling WFS. The offload control loop has been divided in this way based on the specific offloading hardware. As with the LGS WFS focus control loop, data quality monitoring will be performed to ensure the offloads are genuine and not a product of tracking noise or reflections.

Tomography WFS Offload

The Tomography WFS Controller uses a single offload task to manage the tip-tilt offload for all four WFS. Offloads are performed when the average of all the tomography tip-tilt stages exceeds a specified threshold. This task is responsible for maintaining a balanced tip-tilt average across the asterism.

Figure 49: Tomography LGS WFS Offloading

Tip-tilt information from each of the WFS TT mirrors is provided through the RTC telemetry, and is used to calculate average tip-tilt across the tomography sensors. The offload task will determine the offset to apply to the BGS up-link Tip-Tilt and Rotator for asterism shift and rotation, respectively. The BGS offsets will be seen by the WFS as rapid motion away from the increasing tip-tilt. This will result in the RTC compensating by moving the WFS TT mirrors towards their zero point.

Patrolling WFS Offload

Each of the patrolling WFS Controllers implements their own tip-tilt offload control loop. This loop is responsible for periodically offloading the accumulated tip-tilt of the WFS TT mirror (the mirror itself is controlled by RTC) to the BGS patrolling steering arm.

Figure 50: Patrolling LGS WFS Offloading

When the RTC WFS loop is closed the real-time system will be using the WFS tip-tilt mirror to keep the LGS spot stable on the sensor. Over time the tip-tilt will build up and if not offloaded can cause the TT mirror to reach its limit, and eventually loose the LGS beacon all together. When the tip-tilt exceeds a defined threshold, the LGS WFS Controller will calculate the offset required by the steering arm to bring the beacon closer to true center (zero tip-tilt). The WFS will see this as the beacon moving rapidly out of center in the opposite direction of drift, and will compensate by moving the TT mirror to bring the spot back to center. This should consequently return the TT mirror to near its center of range of motion.

##### Low Order Wavefront Sensors

The Low Order Wavefront Sensor subsystem is responsible for the management and configuration of the low order wavefront sensors (LOWFS) and related hardware. The LOWFS are responsible for providing tip-tilt and focus information to the RTC and AO Controls system. RTC will apply corrections to the low-order relay TTM1 to correct for full-field tip and tilt. Focus and rotation offloading will be managed by the AO Controls and will be applied to the LGS focus stage and AO rotator.

There are a total of three LOWFS assemblies, each with a dedicated deformable mirror, pickoff arm, focus stage, tip-tilt mirror and sensor. In addition to tip and tilt, one of the LOWFS sensors also provides focus and astigmatism information (TTFA) to the RTC. Co-mounted with the TTFA is a truth wavefront sensor (TWFS). This sensor provides more accurate focus information, but at a slower rate than the TTFA. The TWFS sensor is under the direct management and operation of the AO Control system.

All three LOWFS and the TWFS are managed by the LOWFSComposite. This NGAO component provides a simple interface to initialize, acquire, and manage the devices during observing.  The following detail the control loops managed by the LOWFS subsystem.

###### TWFS Focus and Centroiding Control Loop

The TWFS Controller will be responsible for processing images to determine high accuracy focus and centroiding errors. A Shack-Hartmann technique is used to estimate the wavefront and calculate the overall focus of the light and its average centroid. The focus information will be published to the LGS WFS focus stage, and centroid information will be sent to RTC to improve AO corrections.

If the controller detects that the NGS target has been lost or the flux is too low to track against, the focus and centroid calculations will be suspended until seeing improves.

##### Narrow Field Relay

There are two devices that comprise the Narrow Field Relay: the high-order DM (HODM) and high-order tip-tilt stage (TTM2) on which it is mounted. The DM is under the direct control and management of the RTC, and is used to correct for the remaining atmospheric distortion that could not be removed by the Wide-Field Relay DM.  TTM2 is under the direct control of the NGAO controls system.

As a low-bandwidth device, TTM2 is used primarily for tracking of differential atmospheric refraction (DAR); correcting ADC tip-tilt errors; and offloading for the Keck Angle Tracker (KAT). In addition, TTM2 will be able to execute science dithering routines, either as scripts or built in sequences, to move the field in a coordinated fashion.  The following sections identify the control loops defined for the Narrow Field Subsystem.

###### ADC Tip-Tilt Errors Control Loop

It is expected that the Atmospheric Dispersion Compensator (ADC) will cause position translation errors in the science image. Fortunately these errors can be compensated for by the High-Order Tip-Tilt device.

Figure 51: ADC Tip-Tilt Error Correction Control Loop

The High-Order Tip-Tilt Controller will listen to position events from the ADC (as orientation of the corrector stages), and using a table of premeasured tip-tilt error values find the appropriate compensation to apply to the stage.

###### KAT Offloads Control Loop

During IF observing the Keck Angle Tracker (KAT) will need to periodically offload target centroids while tracking. The TTM2 mirror will correct for KAT offloads.

Figure 52: KAT Tip-Tilt Error Correction Control Loop

The High-Order Tip-Tilt Controller will listen to offload events from KAT as an X / Y field offset. The controller will convert these offsets into the appropriate tip-tilt offsets which will be corrected up-stream by the NGS WFS.

##### NGS Wavefront Sensor

The NGS WFS Subsystem is implemented by the NGSWFSComposite, and is responsible for the management and operation of the NGS devices. This includes the NGS WFS, focus stage, lenslet array, and field steering mirrors. The Composite presents a simple high level interface to the client to initialize, configure, and acquire the guide star from the field. The NGS WFS Composite is managed directly by the AO Sequencer subsystem.

The NGS WFS camera is under the direct control of the real-time system. The NGAO controls system is responsible for the initialization and configuration of the sensor, and commanding RTC to open and close the WFS control loops. The other NGS devices are all under the direct control of the Controls System. Outside of the RTC NGS control loops, the NGS Subsystem does not implement any tracking or offload tasks. The majority of device control is performed during configuration and acquisition.

The NGS WFS subsystem does not currently implement any servo control loops.

##### Atmospheric Dispersion Corrector

The ADC is responsible for compensating for the effects of refraction caused by light travelling through the atmosphere. This system uses a set of adjustable prisms to converge the dispersed wavelengths to their original shape and position. The ADCComposite is responsible for the management and operation of the ADC subsystem. The subsystem comprises the ADC devices and in-out stage.  The following detail all of the tracking control loops implemented by the ADC subsystem.

###### ADC Tracking Control Loop

As a tracking device the ADC Controller will be listening to system event and responding automatically to changes. The ADC dispersion corrector control loop takes as input the telescope zenith angle and rotator orientation. (The science instrument wavelength is also needed, but this is set before the start of a sequence.)

Figure 53: ADC Tracking Control Loop

The input values are used to index a table of premeasured dispersion values and combined to determine the appropriate correction to apply with the ADC. The ADC correction loop is event driven and can potentially run at the rate of the fastest telemetry item. Decimation can be used to reduce the correction rate if appropriate.

##### RTC Interface

The Real-Time Controller (RTC) is responsible for calculating the atmospheric distortion and applying corrections to the NGAO system by controlling the operation of the deformable mirrors and various tip-tilt stages. Tomographic and atmospheric reconstruction calculations are performed at multiple kilohertz rates to provide fast real-time atmospheric correction of the science field.

The RTC Interface is implemented by the RTCController, and provides all of the AO controls functionality exposed by RTC.  The RTC Interface Controller does not implement any control loops.

##### Offloading

The Offloading Composite manages two stand-alone offload tasks: TelescopeOffloadController and DAROffsetController. These controllers are responsible for calculating and applying offsets to the associated devices.

The Telescope Offload task offloads the focus and tip-tilt build-up (as measured by DM1 and TTM1) to the telescope secondary and pointing, respectively. In open loop mode (during target acquisition) focus and tip-tilt information will be provided by the LOWFS and NGS WFS. The DAR Offset task is responsible for calculating the effects of DAR between the science instrument and WFS (either LOWFS or NGS), while taking into account the other optics and filters in the beamtrain. These offsets are applied to the High-Order Tip-Tilt stage, or as centroid offsets to RTC. Both tasks are event driven; where the telescope offload is based on focus and tip-tilt thresholds; and the DAR task is based on changes in telescope elevation.

The following control loops are managed by the Offloading Subsystem.

###### Telescope Offload Control Loop

The TelescopeOffloadController is responsible for offloading tip-tilt, focus, and coma from the low-order relay to the telescope. During observing, focus and field tip-tilt will be corrected by the low-order DM and TTM1 stage, respectively. Periodically these quantities will need to be offloaded to the telescope to ensure the AO devices have sufficient range to correct for the atmosphere. Tip-tilt is offloaded to the telescope AZ / EL position of the telescope, and focus / coma is offloaded to the secondary piston and tip-tilt.

Figure 54: Telescope Offload Control Loop

The Track action is responsible for starting the telescope offload task, and represents the bulk of the controller’s functionality. While tracking, the controller will be listening to events from the low-order relay DM and Tip-Tilt Mirror (TTM). If the controller determines that the focus applied to the DM or the position of the TTM exceed configurable thresholds, the controller will take action to offload the buildup to the telescope.

###### DAR Offsets Control Loop

The DAR Offset controller is responsible for calculating and compensating for the affects of DAR on the NGAO system. DAR is a measure of the refraction of light between two wavelengths caused by atmosphere at different elevations. From the perspective of the WFS it will appear as if the target is slightly offset from its expected position due to the wavelength of light the sensor can see. If the diffraction effects are not corrected the WFS alignment will suffer and the science target will not be on-axis for the science instrument. (See KAON 221 for more information on Differential Atmospheric Refraction.)

Figure 55: DAR Offset Control Loop

DAR is a relative calculation based on the wavelength of the science instrument, tip-tilt WFS (either LOWFS or NGS WFS), and the current telescope elevation and vertical angle. In NGS mode or LGS with the Interferometer the DAR calculation is performed relative to the NGS WFS, and is applied to the RTC as centroid offsets. During LGS with an instrument the DAR is calculated relative to the LOWFS wavelength and is applied directly to TTM2. The DAR calculation is triggered whenever the telescope elevation / vertical angle changes.

The DAR Offset Controller is not responsible for initializing, configuring or acquiring the device dependencies. The Offset Controller assumes the devices are in the proper operating state and capable of accepting offsets when tracking.

##### Other Composites

###### Calibration Simulation

The Calibration Subsystem is comprised of a number of devices responsible for the generation and propagation of simulated sources including: stimulus devices, tip-tilt fold mirrors, and focus stages. The Calibration System is implemented by the NGAO CalibrationComposite class.

The calibration subsystem is a loose collection of device controllers. The subsystem is primarily responsible for initializing the devices and catching run-time errors. Control and execution of calibration sequences will be performed by the MSCS or other high-level operator tools, which will interface directly with the devices (see KAON 739 for a summary of the calibration sequences).

###### AO Enclosure

The AO enclosure, which includes the cold-bench, AO room, and electronics vault, contain a number of diagnostic and environment sensors. These sensors will be distributed throughout the AO enclosure to obtain global and localized measurements of environmental conditions. The readings from these sensors will be used primarily to monitor these conditions and ensure the safe operating environment for the AO hardware.

Currently this subsystem does not manage any motion control devices, and as such has a very simple software design and limited functional requirements. Although the sensor information will be freely available to the NGAO Controls System, it is not actively used during regular observing.

Unlike other NGAO control subsystems, the AO Enclosure Subsystem will typically be left running at all times, even during shutdown at the end of an observing night. Information published by the enclosures should always be available so operators and technicians can monitor the well being of the system, even during down time.

### Laser System Software

KAON 714 should be referred to for more details for the following section.

#### Laser Control Sequencer

The Laser Control Sequencer is implemented by the LaserFacilityComposite, and is responsible for managing and configuring the entire laser facility, and executing the various sequences. The Composite sits above all of the other laser system components, and coordinates their state and task execution during observing. The Laser Sequencer is under the direct control of the MSCS, and is the primary interface to the laser system.

Figure 56: Laser Control Sequencer Diagram

The Laser Sequencer exposes a simple set of high level actions to the MSCS. These actions provide the Command Sequencer with the ability to initialize and configure the laser facility; acquire LGS targets; and shutdown the system. The composite in-turn takes the action data and distributes it among the relevant subcomponents; invoking their corresponding initialization, configuration, acquisition, and shutdown actions.

As with other composites, the Laser Sequencer will reflect the overall state of its subcomponents: effectively the health and state of the entire laser system. The MSCS will monitor the state of the composite to ensure its continued safe operation, and to respond to any errors that may occur.

A detailed review of the Laser sequences is described in KAON 736: NGAO Laser Sequence.  The following sections briefly discuss the AO subsystem composites controlled by the AO Sequencer.

The following sections detail the control loops of the Laser Control Sequencer. Each control loop is implemented in part or in full by one or more of the NGAO components.

##### Asterism Validation Control Loop

NGAO makes use of high-intensity lasers to produce the LGS beacons. If the lasers are not properly aligned they can cause significant damage to the laser facility hardware and injury to personnel. As such, the laser propagation must be periodically validated to ensure the proper alignment and performance of the system. An asynchronous task will be created to monitor the health of the laser system. If the task identifies any major changes to the asterism structure, such as the loss of an LGS beacon, an automated response will be taken to ensure the safety of the laser facility.

Figure 57: Asterism Validation Control Loop

The AsterismValidationController is designed to perform asterism validation and error handling during the acquisition and observing sequence. The control loop implements an image processing routine that takes images from the Asterism Imager Camera and compares the laser beacons against their expected positions in the field. These positions are based on the coordinates of the tip-tilt targets, position of the asterism tip-tilt mirror, and the orientation of the rotator. If there are any major changes to the asterism structure, such as the loss of an LGS beacon, the validation controller can take an automated response to ensure the safety of facility.

Three failure modes have been identified for the laser asterism and will be monitored by the validation controller. The failure modes are:

- Loss of a laser or beacon – If the asterism validation identifies that there are fewer than the expected LGS beacons in the image the sequence will be halted and the laser system will be put into a shuttered safe state.

- Additional beacons – Potentially the laser system could be configured incorrectly to produce additional beacons when a reduced subset is desired (e.g. fixed-pupil or a single TT target). If the validation task identifies more than the expected number of LGS beacons the sequence will be halted and the laser system will be put into a shuttered safe state.

- Incorrect beacon position – Potentially caused by a number of factors (offloading, flexure compensation, etc.) the laser beacons may drift over time. As all of the beacons are accounted for, only displaced, there is no imminent safety concern for the system. The validation task will assume the system is performing correctly, but will warn the operator that the asterism has changed and that performance could suffer.

The validation task is event driven and will be executed for each new frame produced by the asterism imager camera. The initial positions of the beacons will be calculated when the validation task is started based on the sky position of the tip-tilt targets. The positions of the beacons will be recalculated whenever the BGS rotator or tip-tilt mirror is moved, and should only require a translation and rotation matrix transformation. The validation task is started at the beginning of the science sequence and halted at the end of integrations.

As a high-level subsystem, the Composite relies on the low-level subsystems for the majority of hardware control. Although the Laser Control Sequencer is capable of directly interacting with any hardware in the laser facility, there are only a few hardware devices it manages directly. The following sections briefly discuss the laser subsystem composites controlled by the Laser Sequencer.

##### Laser Switchyard

The Laser Switchyard control system is implemented by the LaserSwitchyardComposite. This component is responsible for controlling the individual devices and distributed software controllers that implement the switchyard functionality. This includes the low-power fold mirror, steering mirrors, beam polarizers, and beam positioning sensors.

The Switchyard Composite is managed directly by the Laser Facility Composite, and presents a simple high-level interface to initialize, acquire, and halt the switchyard devices. The Composite’s primary responsibility is to prepare the switchyard devices for closed loop observing. The majority of the Switchyard Composite functionality exists as part of the configuration and acquisition sequence. During observing tracking components are independently controlled or run closed-loop with the rest of the system.

The following sections detail the tracking and offload control loops of the Switchyard subsystem. Each control loop is implemented in part or in full by one or more of the switchyard subsystem controllers.

###### Laser Transport Control Loop

The laser transport control loop is responsible for maintaining the proper alignment of the lasers from the laser enclosure to the BGS. This control loop is needed to compensate for flexure as the telescope tracks a target; and uses a combination of the telescope elevation and feedback from the beam positioning sensors to calculate the appropriate position of the laser steering mirrors.

Figure 58: Laser Steering Control Loop

Although the laser transport tracking loop (implemented by the Laser Steering Mirror controller) uses inputs from DCS and the positioning sensors, it does not use both of them at the same time. The laser facility can propagate the lasers in high-power and low-power modes, depending on the position of the low-power fold mirror. When the fold mirror is in the beam path, all but a small percentage of the laser light is diverted to a beam dump. The leakage is allowed to propagate through the system and can be used for alignment and tests with little risk to hardware or personnel. When the fold mirror is retracted the full beam is allowed to propagate.

The laser transport control loop will use the flux value from the beam positioning sensors to determine if the system is configured for low or high-power propagation. If the flux is below a certain threshold the control loop will use the current telescope elevation from DCS. The elevation will be used to index a simple table to determine the appropriate flexure compensation to apply to the steering mirrors. These values will have been derived from tests empirical tests and will be interpolated to find the appropriate tip-tilt to apply to the stage.

If the positioning sensor threshold reports sufficient laser light, centroid information will be obtained from the detector and will be used to calculate the compensation required to keep the laser aligned with the BGS.

###### Laser Polarization Control Loop

During observing the laser asterism needs to have the proper polarization as seen by the AO wavefront sensors.  Fortunately this polarization is directly related to the elevation of the telescope and incidence angle of the laser with the sodium layer. The control loop to maintain the desired polarization is implemented by each of the polarizer controllers.

Figure 59: Laser Polarization Control Loop

The polarizer controller tracking loop is event driven and responds to telescope elevation events from DCS. When an event is received the controller will lookup the required orientation of the polarizer in a table based on the current elevation. The table will be defined through empirical tests at regular telescope elevations. The actual polarizer orientation will be interpolated based on these values.

The Half and Quarter Polarizer tracking loop can be remain closed throughout a night’s observing.

##### Laser Beam Generation System

The BeamGenerationSystemComposite is a high-level multi-device manager that is responsible for acquiring and configuring the hardware on the BGS. These devices include the patrolling steering arms, beam splitters, asterism rotator, tip-tilt mirror, and beam expander focus.

The BGS Composite is managed directly by the Laser Facility Composite, and presents a simple high-level interface to initialize, acquire, and halt the BGS devices. The majority of the BGS Composite functionality exists as part of the configuration and acquisition sequence. During observing the majority of the subcomponents are independently controlled or run closed-loop with the rest of the system.

The BGS subsystem is responsible for configuring and positioning the hardware to obtain the desired laser constellation. The constellation is based on the number and position of the wide-field targets, the position of the telescope, and the desired image orientation as seen from the science detector. The BGS subsystem will take this information and calculate the required positions for each of the associated devices.

The BGS subsystem also manages the focus and propagation of the lasers and implements various safety processes to ensure the safety of the laser generation system.

The following sections detail the tracking and offload control loops of the BGS subsystem. Each control loop is implemented in part of in full by one or more of the NGAO controllers.

###### Focus Tracking Control Loop

During observing the BGS subsystem will have to track the changing focus of the LGS asterism. Focus is primarily based on the current telescope elevation and launch telescope temperature. As the telescope elevation changes, the beam length of the laser from the telescope to the sodium laser will fluctuate. As the distance to the sodium layer changes the beam expander will have to compensate to maintain LGS focus. The temperature of the launch telescope also affects the focus of the laser. This information is derived from the environmental sensors within the LLT.

Figure 60: Laser Focus Tracking Control Loop

Beam expander tracking is an event driven control loop triggered by telemetry events from the LLT environment sensors and DCS telescope elevation keywords. When the controller receives input from these items it will calculate the LGS asterism focus compensation and apply it to the stage. A lookup table should be sufficient to define focus compensation based on telescope elevation and temperature.

###### Rotator Tracking Control Loop

During observing the laser asterism will need to track the LGS targets as the telescope rotates. This is to ensure that the asterism maintains alignment with the LGS WFS detectors. In fixed field mode this is based on the position angle (PA). In fixed pupil mode the rotator will track the vertical angle (VA).

Figure 61: Asterism Rotator Tracking Control Loop

Rotator tracking and offloading is event drive. The Asterism Rotator Controller will receive the position and vertical angle from the AO rotator through a telemetry stream. The asterism rotator will process this information and track with telescope and field rotation.

###### Flexure Compensation Control Loop

Changes in telescope elevation will induce flexure on the BGS and launch optics. As the telescope tracks a target the asterism tip-tilt will need to compensate for flexure to keep the asterism stable on the sky..

Figure 62: Flexure Compensation Control Loop

The Asterism Tip-Tilt Controller implements an event driven tracking loop. Primary input to the control loop is the telescope elevation and is made available from DCS through the Channel Access service. A simple look-up table can be used to interpolate the required flexure compensation for the current elevation.

##### Laser Safety System Interface

The LSS Interface is implemented by the LaserSafetySystemController, and provides the operational interface to the laser control system. The LSS Controller provides clients with actions and attributes to set permissives, execute device commands, and read-back state information about the lasers.

Figure 63: Laser Safety System Collaboration Diagram

As shown in Figure 63, a number of facility components interact with the Safety System including the Laser Traffic Control, Aircraft and Satellite detection, laser service enclosure, E-Stop and the laser units. The LSS utilizes these connections for commanding and feedback. The NGAO Controls system does not need to be directly aware of the state of these components, and instead can rely on the LSS to provide telemetry information indicating the overall safety / health of the laser system. Other safety permissives such as spotter and OA acknowledgments must be provided by the NGAO LSS Controller.

The Safety System Interface subsystem does not directly manage any tracking control loops.

##### Laser Service Enclosure

The LaserEnclosureComposite manages the environmental sensors found in the laser unit enclosure. These sensors are responsible for providing the current temperature, humidity, and particulate level.

As sensors are simple on / off devices without motion control requirements, the composite itself is very simple, and provides the basic capabilities to initialize the system for observing. The composite will collect data from each of its sensors and will provide a summarized health status as telemetry and alarming.  The Laser Enclosure subsystem does not manage any control loops.

##### Laser Interface

The Laser Interface Subsystem is implemented by the LaserSystemComposite, and manages the three individual laser units and provides propagation control through the Laser Safety System.

This Laser System Interface provides a single unified command and status interface to all three lasers units. Clients can treat the laser sources as a single instance, allowing them to issue a single command in place of three. Additionally, health and status information for all three laser units will be consolidated and made available to the control system for easy reference.

The Laser System Composite is managed directly by the Laser Facility Composite.  The Laser SystemInterface does not implement any control loops.

### Data Server

The Data Handling System for the AO Controls has been called the “Data Server”. The NGAO Data Server is defined as a computer in the network, with associated software, that is dedicated to the data storage and retrieval needs required by the AO Controls System. It holds the database management system, the databases and is part file server capable of housing non-database files such as FITS. In addition to providing data persistence, retrieval and data management there will be a telemetry data recorder, an ad-hoc data recorder, an alarm recorder, general logger, and configuration. High speed RTC data will be stored in its own data recording system.

Figure 64: Data Server Overview

Figure 64 shows a high level overview of the data server. The data server hardware consists of expandable and reliable (RAID) hardware capable of supporting multiple databases.  More details of the Data Server design can be found in the separate document: KAON 732: NGAO Data Server Preliminary Design.

### Real Time Control

#### Introduction

The Real Time Controller (RTC) is a specialized computer system designed to perform all of the wavefront sensing, tomography calculations, and deformable mirror control processing at rates that keep up with atmospheric turbulence induced optical aberrations. The RTC data flow and computer architectures have been designed to achieve the tomography precision, noise suppression, and bandwidth requirements implied by the science-case driven wavefront error budgets.

An equally important consideration in the RTC design is the need to keep the cost and complexity manageable. Simply scaling earlier implementations of single conjugate AO RTC reconstructors using traditional central processing units (CPUs) is infeasible because of the multiplying effect of multi-guidestars and multiple deformable mirrors on computer speed requirements. To address this issue, we have taken advantage of the parallelizability of wavefront reconstruction and tomography algorithms and mapped them on to a massively-parallel processing (MPP) compute architecture. This architecture scales in size and complexity much more favorably than doing the same calculations on CPUs, and can be readily implemented with commercial off the shelf technology building blocks called field programmable gate arrays (FPGAs). Additional details of this design approach are given in a later section on implementation later in this report, and given in still greater detail in KAON 553.

We first describe the main line real-time tasks that the RTC must perform. Then we describe the essential ancillary support tasks relevant to the RTC such as communicating with the supervisory controller configuration and calibration information, providing offload signals, and providing diagnostic data. In the final section we explain the MPP implementation, describing processor hardware, interface hardware, and software development methodology.

#### RTC Tasks

The RTC, at the core, performs the following tasks in LGS mode:

- Accept digitized pixel data from the LGS WFS and LOWFS, and perform basic image processing (dark and bias subtraction, flat-fielding).

- Calculate wavefront tilts from the LGS WFS and LOWFS using a choice of noise-optimal centroiding algorithms, and compensate for non-linearities in the centroiding methods.

- Reconstruct wavefront phase at each sensor and transmit this information to the tomography processor.

- Use cone-beam projection tomography techniques to reconstruct the three-dimensional volume of atmospheric index-of-refraction variations above the telescope and over the field of view of interest, given the wavefronts from various directions as measured by each wavefront sensor. This algorithm also takes inputs from the tip/tilt and tip/tilt/focus/astigmatism sensors to break volume solution ambiguities inherent in laser wavefront measurements.

- Integrate through the volume of index estimates along the path to the science instrument  – either on-axis for the narrow field science modes, or across a modest FoV (sacrificing peak on-axis performance for more uniform AO correction.)

- Compensate for deformable mirror influence functions and nonlinearities, deriving voltage commands for the DM’s given desired wavefront distortion corrections to be placed on them. Split the control between commands to the tip/tilt mirror, moderate-order (woofer) DM, and high-order (tweeter) DMs.

- Incorporate control compensation dynamics to keep the system stable and achieving a given temporal bandwidth.

In LGS mode the RTC also computes high-order wavefront control commands for DMs in the tip/tilt sensors, sharpening the IR tip/tilt stars.

In NGS mode, the RTC acts as a traditional single conjugate AO system. It takes inputs from one NGS sensor, reconstructs the wavefront, and computes commands to be split up amongst the tip/tilt mirror, woofer DM, and tweeter DM in the narrow field science path.

All these RTC tasks take place at the frame rate of the fastest wavefront sensor camera, up to 2,000 frames per second.

As shown in the Figure 65 schematic, large chunks of compute tasks are associated with either wavefront sensors or DM’s and thus can be parallelized across them. Thus some of the dedicated processing units will be assigned specifically to hardware. Furthermore, algorithms within the subunits, as well as within the tomography unit itself (Figure 66), are highly parallelizable when implemented in the Fourier domain, and thus will each map onto an MPP architecture as described earlier.

Figure 65.  Multi-guide star tomography data flow and parallel processing.

Figure 66.  Tomography algorithm.

#### Parametric Input, Optimization, and Reconfigurability

##### Minimum Variance Reconstruction Optimization

The RTC algorithm computes the statistical minimum variance solutions for wavefronts at each science instrument, given the measured wavefront data from the guide stars. The minimum variance solution depends on certain a-priori data, which the RTC accepts as parametric input. These include:

- Volumetric turbulence strength (Cn2 profile, discretized at layers)

- Number of layers of turbulence

- Brightness of guide stars

- Wind speeds at layers

Cn2 can be provided either as a-priori input, or as derived from external measurements, for example, from a MASS/DIMM sensor. The preparation and processing of this data is left to the external supervisory control system; the RTC simply takes in a set of normalized Cn2 strength numbers, one per layer, at a rate that is slow (e.g. once per second) with respect to the real-time tasks. As an option, the RTC’s tomography engine will provide statistical average rms aberrations resolved by layer, which can be used to adjust Cn2 profile numbers dynamically.

Similarly, wind speeds can be incorporated from external data or deduced internally from past histories of estimates.

##### Calibration Parameters

The truth wavefront sensor will provide long-term average wavefront data designed to normalize out systematic biases due to either non-common path optical aberration or Hartmann sensor biases due to variations in the sodium layer thickness and altitude. The RTC will process these wavefront sensor data like any other wavefront sensor and use the results to adjust zero-set points in the overall reconstructor.

In a like manner, prior measurements will have determined calibration set points for each wavefront sensor, giving the definition of a “flat” wavefront for each sensor. The set points for LGS wavefront sensors will depend on field position and zenith angle. Thus the multi-system command sequencer, with knowledge of the telescope and AO system configuration, will periodically update the RTC wavefront sensor sub-processors as to which parameter set to apply to the wavefront reconstruction.

##### Reconfiguration

The processing units and algorithm will be made reconfigurable to allow for each of the observing modes envisioned for NGAO. Configuration parameters include:

- Number and field-positions of laser guide stars.

- Number and field-positions of tip-tilt guide stars.

- Field position of TTFA (tip/tilt/focus/astigmatism) sensor.

Furthermore, the scalloped pupil of the Keck primary mirror will rotate with respect to the wavefront sensors and DMs in some science observing scenarios. The wavefront and tomography reconstructors utilizes a model pupil as a “valid data” mask, so this model will be set and updated at the appropriate rate within the RTC.

#### Interfaces

##### Offloading

The RTC will provide offload signals to the telescope so that the high speed wavefront controllers don’t saturate. The offload signals flow to the non-RTC supervisory controller at a relatively low data rate, on the order once per second. Offloading signals include:

- Tip-tilt to the telescope guider.

- Focus to the secondary piston.

- Other low order modes TBD to the telescope primary segment control system.

##### Diagnostics and Telemetry

Diagnostic data is defined as data intended for monitoring the health of the RTC and AO system, and for display to the operator. Centroid data from wavefront sensors, signals going to DMs, and other indicators are transmitted at relatively low, human readable, data rates to the external systems.

Telemetry data is defined as up to full-frame rate streaming of portions or all of the intermediate data to high-speed data capture units. This data is useful for a number of post processing tasks such as

- Debugging or tuning of parameters.

- Analysis of seeing conditions and performance of the AO system.

- Point spread function determination.

Data that would be streamed for data capture include:

- All wavefront sensor centroids, intensities, and wavefront sensor reconstructed phases.

- All tip-tilt and TTFA sensor centroids and intensities.

- All commands to the DMs and tip/tilt mirrors.

- All tomography volume estimate data.

- Ancillary information associated with the operations so as to be able to reconstruct the state of the RTC at the time, including internal data tables, Cn2 numbers, wind numbers, calibration sets etc.

Additional data storage capability will be needed to record full frame rate raw pixel data from the wavefront and tip/tilt sensors.

##### Command State

The RTC at any time will be operating in one of a number of possible states. Examples of such states include:

- Narrow field science LGS AO control (hybrid closed loop on the woofer and open loop on the narrow field tweeter and tip-tilt and TTFA tweeters).

- Narrow field science NGS AO control (closed loop on the woofer and tweeter).

- Control on tip-tilt only.

- Calibration modes (for alignment/registration, push matrix generation, linearity calibrations).

- Uncontrolled or idle, with static values as loaded for the DMs and tip/tilt mirrors.

The supervisory control system will transmit the state transitions to the RTC which will configure accordingly (and also report back its state on demand). The maintenance of state transition rules will be the responsibility of the multi-system command sequencer.

Additional flags will be maintained for turning on and off various diagnostic and telemetry streams.

#### Implementation

##### Algorithms

Algorithms for wavefront phase reconstruction from Hartmann slope data have been analyzed since the beginning days of AO. We anticipate using a modern fast-iterative technique such as the ones described in references 1 and 2. Such techniques can take advantage of parallelism if they are implemented in the Fourier domain. Regularizations taking into account the signal-to-noise of the measurement and filters for suppressing the waffle mode can also be implemented in the Fourier domain. The pupil boundary conditions (outside of which the measurements must not be assumed as zero but allowed to be free variables) force the algorithm to be iterative as described in the above references, but 3-5 iterations using a Fourier-domain pre-conditioned conjugate gradient (FD-PCG) method have been shown to be adequate for meeting our error budget.

Inverse tomography algorithms using wavefront measurements from multiple directions have been developed recently (see references 2 and 3). These methods are also made parallel through the use of the Fourier domain but again must be iterated because of the finite spatial extent of the pupil-apertured data. Again, the FD-PCG method has proven adequately stable and rapidly converging in simulation studies (KAON 475).

Finally, fitting the deformable mirror to the desired wavefront correction can be accomplished with parallel processor implementations that carry an inverse model of each DM.

- MEMS open loop control is decoupled into a linear cross-coupling, which is solvable in the Fourier domain, and independent nonlinear functions for each actuator, solvable with nonlinear lookup tables in parallel. The MEMS are repeatable go-to devices and this open-loop model has been proven to be quite accurate (see reference 5).

- The woofer DM, likely a piezo-actuator device with cross-coupling and hysteretic effects, will be controlled via a linear Fourier domain deconvolution only. We will rely on the fact that this mirror is in “closed loop” (upstream of the wavefront sensors) and so any residual mis-fitting will be measured and sent to the more accurately responding tweeters. Bandwidth shouldn’t suffer because the woofer is correcting the lower order, and hence slower evolving, atmospheric modes.

More details on algorithm implementation are given in KAON 553.

##### Hardware

The multi-processor units are implemented as banks of field-programmable gate arrays (FPGAs) arranged on custom circuit boards. The technology of FPGA programming has advanced to the point that the design and configuration of these boards, intimately coupled to the algorithm distribution on the processor chips themselves and data flow needs, is accomplished entirely using standardized computer aided design and simulation tools. The details of distributing the NGAO RTC architecture onto these processor units are given in KAON 533, sections 4 and 5.

The processor units end up being many repetitions of identical processing elements, making them interchangeable and therefore easy to spare. Except for specialized I/O interfaces, the boards can be configured to process wavefront sensor data, do a piece of the inverse tomography, or process DM commands.

##### Hardware Interfaces

High throughput I/O must be used to get data from wavefront sensors to processor units and DM command data to the D/A converter hardware associated with each DM or tip/tilt mirror. Similarly, high throughput I/O must be used to get telemetry data to data storage units. For the most part, industry standard hardware is now commonly available that will handle our anticipated data rates, and an industry standard protocol (LVDS) is called out in the conceptual design. These data interconnects will be implemented on reliable high speed interconnects, such as fiber optic links.

##### Programming and Design Process

There are a number of FPGA manufacturers and each has commercial design packages to aid in the design of the programming and interconnections. MPP programming is in common practice today in industry and the required skills are taught in university computer and electrical engineering courses.

##### Physical Implementation

Space, power usage, and thermal load considerations are taken into account in the design. We have estimates of these for the conceptual NGAO RTC implementation (KAON 533 Table 5-6) which will be refined as we make trades and design choices in the later system design phases. The physical parameters are expected to be compatible with locating the RTC in a separate electronics enclosure located on the Nasmyth platform.

## Science Operations

This section discusses the hardware and software needed to control the overall NGAO facility for science operations at both the operator and astronomer levels and the pre- and post-observing support tools.

### Science Operation Model

The overall goal of NGAO science operations is to maximize the science return from the allocated observing time, given i) the science cases, ii) a performance budget for the instrument suite, iii) an operation-cost for the Observatory and iv) a scientific skill set for the astronomers. There exists a wide range of science operations models to accomplish this overall goal, as a function of the instrument functionalities, the Observatory budget and the modus operandi and size of the scientific community.

#### Observing Model: classical with built-in flexibility tools

A trade study of possible observing models was performed in KAON 476: it recommended that NGAO science operations be following the Keck classical observing model. NGAO nights, particularly LGS nights are scheduled and allocated 6-month in advance.  Astronomers, assisted by Keck Observatory support personnel, are performing the observations remotely either from Keck HQ or from a partner institution: the astronomers-observers are therefore fully engaged in their observations and can make on-the-fly decisions for the observing strategy.

The suite of NGAO pre-observing tools including simulation and observations planning tools should allow the astronomer to easily and quickly assess the feasibility of a scientific program during the observing proposal submission phase or any phase prior to the observations, and make the best use of the allocated time. Astronomers will want to adapt the scientific program with the observing conditions for the scheduled observing night(s). Using the planning tools, they can make on-the-fly decision on the observing strategy and take advantage of the various observing configurations with NGAO: NGS/LGS switch, AO science instrument switch, non-AO instrument switch during any night.

One of the risks encountered with the classical observing model is that the data collected be incomplete (e.g., due to bad weather or low observing efficiency) preventing the astronomers from fully exploiting the data and publishing, resulting in a lower science return and visibility for the AO instruments. Our model trade study proposes a scenario that can be phased in with NGAO science operations with low impact on the Observatory support: Each TAC may decide to encourage its astronomers’ pool to collaborate for a subset of TAC-allocated nights: the scientific programs could be ranked as a function of required observing conditions, and be given observing priorities till the data is complete. This level of schedule flexibility would likely benefit the overall science return while maintaining Observatory operation costs. The flexibility and scheduling burden would be distributed among the astronomers within the partner institutions. The experiment could be stop at any time should it be not satisfying.

#### Science Operation Requirements: Observing Efficiency

The requirements from the NGAO science cases (KAON 455) and the observing scenarios for these science cases (KAON 571) led to a set of requirements for the science operations from the astronomer point-of-view that are detailed in the System Requirement Document - SRD (Sect. 6.1.4 in KAON 456). In addition, we have reported on the lessons learned from the LGS science operations at Keck (KAON 463) including weather impact on LGS and observing efficiency budget. From this report and other sources, we have developed a second set of Observatory Operational requirements for the science operations in the SRD (Sect. 6.2.5 in KAON 456).

One of the most important requirements is the percent of time collecting science quality data. Our goal is to achieve at least 80% open shutter science time for “faint field” observing program (programs requiring 1 to 4 hours of total integration time with individual integration time of > 20 min) and 70 % for “bright field” observing  programs (programs requiring less than an hour of total integration time and including many fields through the observing night).

In accounting for the open shutter science time, we make the following assumptions:

- Weather impact is not included in the calculation of the open shutter science time. Time loss due to weather in LGS mode accounts for ~25% of the total allocated time (KAON 463). We will track the statistics from time losses due to weather in both LGS and NGS mode. Yet given the Observatory option for the classical observing model, this loss cannot be accounted against the NGAO science operation efficiency. The weather statistics will be included in more general discussion on observing model.

- Open shutter time spent on science acquisition, centering the object, checking the SNR, etc is considered overhead.

- Open shutter time spent for on-sky telluric, photometry, astrometry, PSF calibration is considered science time but we will keep track of its contribution to the total time.

While developing the observing scenarios (KAON 571), we have created a simple efficiency budget tool (http://www.oir.caltech.edu/twiki_oir/bin/view/Keck/NGAO/NGAOObservingScenarios) that can be used for each science case and provide a preliminary assessment on the observing efficiency. A snapshot of the tool is presented in Figure 67. The estimates for the overhead during the course of an observing program are detailed in KAON 571 for the general observing sequence and in KAON 567 for the acquisition sequence. We have considered minimum, median and maximum estimate for each of these contributions and calculate a weighted average equivalent to (min + 4*med + max) / 6. We estimate for the current study that the maximum values represent instances of technical difficulties. Therefore we have not allocated any additional time for technical problems. These estimates have also been checked against current performance.

We can reach ~83% observing efficiency on the high-z galaxies science case, including calibrators. There are still a few contributors to the total overhead whose impact is difficult to mitigate.  Any dedicated time for calibration standards has a strong impact on observing efficiency since these objects are “bright field” observed for a few minutes (< 5 to 10 min), with  ~100% time overheads (slew, acquisition, SNR check, etc). In the Figure 67 example we have estimated ~27 min for any overhead due to the Laser Traffic Control System (LTCS). LTCS interrupts are due to either 1) a plane flying in the vicinity of the beam, 2) beam collision with other telescopes, 3) planned request for no-propagation (closure event) from the Laser Clearinghouse (LCH), and 4) on-the-fly phone call request for no-propagation at all from the LCH. A recent change in the LCH operations could lead to additional time losses.

The number of interrupts due to planes is estimated to ~2 per year, making it a non-issue. The number of interrupts due to beam collision with other telescopes will be reduced once the new “first on target” LTCS rule is agreed upon and applied for all Mauna Kea telescopes (currently the new rule is used between the Keck telescopes). Under this rule, the first telescope on target gets priority to keep observing (currently telescopes projecting a laser have lower priority and the laser is shuttered for any collision). One gets the most benefit from this rule if it used in parallel with the collision preview tool that can predict the collisions before the telescope slew to a new target, hence allowing the observer to select a target that is clear of “planned” collisions. The benefit from this new rule has yet to be fully assessed.

Figure 67.  Efficiency estimate for the high-z galaxies science case.

The planned LCH requests for closure on a specific target direction can be included the observing planning tool and can result in minimal impact on the observing time losses as long as they are less than 10 min and rare. LCH closure requests were rare and insignificant from 2003 to 2007. LCH has recently released its new “SPIRAL 3” software that uses new rules for possible laser impact (not documented), a half-cone angle of 1.5º for the no-propagation zone and estimates no-propagation time windows for a particular direction. This has resulted in a dramatic increase of up to hundreds of events per night. The preliminary assessment of the new operation mode for the LCH is documented in KAON 578. Tools have been developed by the WMKO AO operations team to minimize the impact. As it stands, this new LCH closures rate would significantly impact NGAO observing efficiency for extragalactic targets. This issue is being addressed by WMKO in collaboration with other Observatories and will require more attention for NGAO.

Last minute phone call request for no-propagation from LCH have a huge impact on efficiency for the given night since this stops all LGS operations for a certain time period. This happens ~ 5 times per year when using LGS 140 nights/year. Last but not least, the ability to abort a science exposure quickly and either get ready for a new exposure or move to a new target faster should contribute to reduce the impact from LTCS events.

### Conceptual Design for System Operations

#### Operation Control Infrastructure

For a given observing model, the observing efficiency is the important design requirement for the individual components (e.g., reading out the camera) nut mostly for the integrated system (e.g., offset to sky). The current Keck II LGS system feeding NIRC2 or OSIRIS performs routinely with ~ 30 - 50% overhead depending on the science program (KAON 463). Its limited efficiency as an integrated system is primarily due to the serial architecture for the command interfaces between subsystems (AO/laser/telescope/science instruments) and the lack of multi-system coordination sequences.

To address the efficiency requirement with NGAO as an integrated system, we are proposing a new integrated design. Our conceptual design includes 1) a multi-system sequencer for commanding the sub-systems in parallel (e.g., offset the telescope as the science instrument write the FITS file to disk) and 2) a sequencer for each subsystem (AO, laser, science instrument) to quickly and reliably handle complex command for a given subsystem (e.g., set AO subsystem for NGS field acquisition).

The overall control infrastructure is documented in KAON 569. The three main components of the NGAO science operations are:

- The Pre- and Post- Observing Tools

- The Operation Control GUIs

- The Multi-system Command Sequencer

In Figure 68, we present a block diagram for the science operations architecture using a view that complements the architecture information from KAON 569.  The configuration for the NGAO and the science instrument depends on the science program and the observing strategy and is determined during the pre-observing phases. Using a set of planning tools, the astronomer will develop the detailed observing plan and save all relevant parameters in configuration files. These configuration files can be loaded by the Operation Control GUIs. From the Operation Control GUIs, the operator and the observer will command & control the observation sequences: AO & science acquisition, system tune-up, observing sequences (snapi, dither, offset, filter, etc). The observation sequences are managed by the Multi-system Command Sequencer (MCS): complex sequences for one subsystem are handled by the subsystem sequencer (e.g., “setup AO bench for NGS” is performed by the AO sequencer) or executed directly from the MCS for simple command.

Figure 68.  Science operations tools block diagram.

The post-observing tools have been omitted in Figure 68. The pre- and post- observing tools are described in more detail in the next section.

#### System Configurations Matrix

The purpose of the system configuration matrix is to help map requirements to components. The NGAO system configuration is shown in Figure 69. It represents a total of 5 different configurations in NGS mode and 6 in LGS mode for acquisition, calibrations and science observations with the science instruments (interferometer, imager, IFS). Some of the configurations include more options (e.g., rotator mode in fixed field or fixed pupil). This matrix is also key to the design the sequences of commands to the subsystems and individual components during calibrations, setup and observing sequences.

Figure 69.  NGAO system configurations.

#### System Calibration: Routine and Maintenance Calibrations

The calibrations include 1) routine calibrations, and 2) maintenance calibrations. The routine calibrations are calibrations that are required on run-to-run or night-to-night basis such as fine laser alignment and power calibrations, DM to lenslet registration, non-common path aberrations, etc. The maintenance calibrations are performed following a schedule and may include detector response, noise and offsets calibrations, TT and DM interaction matrices (poke matrices), motion control tune-ups, throughput, etc.

We anticipate that the daily calibrations will be performed by the observing support team using the high-level science operation tools. The maintenance calibrations may be implemented at the sub-sequencer level when applicable. The corresponding calibration sequences will be coded and implemented at the MCS and/or at the subsystem sequencer level. Note that the use of the keyword architecture as currently implemented at Keck will allow the scientists to easily prototype and validate the calibration algorithm using their programming language of choice during the I&T phases.

#### System Operations: Acquisition

The NGS and LGS acquisition requirements and conceptual design are discussed in KAON 567.  This includes a trade study between near-IR and visible detector technologies that found that a commercial CCD is sufficient for the NGS acquisition task. The NGS acquisition will also rely on data retrieval from multi-color astronomical catalogs (USNO-B, GCS-II and SDSS).  KAON 567 lists and studies the possible risks during the acquisition process. The specifications for the acquisition conceptual design are presented in Table 6.

Table 6.  Acquisition conceptual design level specifications.

| Title | Specifications |
| --- | --- |
| Field of view | ≥ 120" |
| IR field identification | a) Image sources in the near-IR (1.0-2.0 µm) b) Image sources in the visible (0.5-1.0 µm) In both cases, use supplementary information about target locations from catalogs and surveys |
| Point source sensitivity | V=22 or J=19, exposure ≤ 10 s, SNR ≥ 10 |
| Position accuracy | ≤ 0.050" rms, random errors in determining source positions in an acquisition camera image |
| Minimal time overheads | Total acquisition process time typically < 50 s, worst case < 120 s. Includes time for telescope moves, camera exposure, and analysis. |
| Photometric imagery | Photometric error of 0.2 magnitudes, in standard astronomical bands such as Johnson, UKIDDS, or SDSS |
| Registration accuracy | ≤ 0.020" rms, random error in determining positions of acquisition camera with respect to telescope optical axis |
| Diagnostics and troubleshooting tools | Report metrics for automatic acquisition and to aid observer decision-making, including manual override by astronomer or observing assistant |
| Data products | Store acquisition images as FITS files, and appropriate diagnostics, in the NGAO data server |
| Interface to observer planning tools | Acquisition software will receive target information from the NGAO observer planning tools |
| Guiding mode | Used for testing when wavefront sensors not available |

The telescope pointing accuracy is currently the largest risk for the observing efficiency. The observing efficiency budget depends on the brightness of the NGS and acknowledges the difficulty of acquiring fainter stars. A single camera design is feasible for LGS and NGS acquisition using a CCD sensor. High level requirements and interfaces to other NGAO subsystems are also discussed in KAON 567.

Table 7 presents a generic description for the acquisition sequence for NGAO with an emphasis on the parallel steps. The NGAO planning tools will assist the astronomer to select the next science target. All relevant configuration information will be loaded by the Operation Control (OC) tools.

Table 7.  Generic NGAO Acquisition Scenario.

| Step | Observing Step | Parallel Steps | Remarks |
| --- | --- | --- | --- |
| 0 | Select next target: assess science priority check target elevation range check observing conditions check LTCS conditions | Complete integration on current science target or calibrator. When target selected from Planning Tools, then information is loaded in OC tools. | It is not clear yet whether the astronomer will have to run these checks manually or whether it will be automated. |
| 1 | Upon completion of readout of science array, LGS is shuttered, AO loops open and key-system feedback parameters are saved then the operation control tools trigger the telescope slew. | OC tools parses information, and get ready for execution: NGS parameters for acquisition AO configuration Instrument configuration |  |
| 2 | Telescope slews | The OC tools send commands to the multi-system sequencer. Setup sequences are executed as appropriate by the AO, laser & science instrument sequencers. |  |
| 3 | Telescope Pointing Adjustment on one of the NGS (brightness allowing). This step is automatically performed by the NGS acquisition subsystem with the visual check of the Observing Assistant (OA). Upon success, pointing corrections are applied and next telescope slew is commanded from the OC tools. | There is no need to use the acquisition camera for the LGS acquisition: LGS pointing model is accurate enough to get all laser spots centered within the capture range for the HO WFS. | This step may be required only when the NGS V>18 mag. (TBC) or when the telescope slews by more than xº in elevation/azimuth range. |
| 4 | Telescope coarse registration on the science field. NGS acquisition subsystem runs an automated routine to record and process image, ID the NGS in the field with respect to catalog data then compute required offset. Visual check of process by OA. Upon success, position offsets are applied to telescope. | LGS propagation and acquisition steps initiated. Laser pointing correction and uplink TT correction loops closed with very low gain. Pickoff mirror positioning and LOWFS setup complete including background. | Need to implement the acquisition for the vibration/wind shake reference. Need additional study for telescope guiding. Not clear if the HOWFS will require a background. |
| 5 | Telescope fine registration on the science field: If photons not detected at the expected SNR on the LOWFS (or NGS not on Pointing Origin), then NGS acquisition subsystem runs a 2nd iteration. Visual check of process by OA. Iterate if necessary (to be detailed). Upon completion adjust telescope pointing model. | Pick-off mirrors for science and TWFS in position | Need to check the conditions for the dichroic during this step. Need to be able to adjust pointing model for telescope even though PO != REF. |
| 6 | AO subsystem control: 1) low gain on woofer & MEMs, 2) increase gain on UT, 3) start telescope guiding, 4) adjust woofer & MEMs gain, 5) initiate TWFS + tomography optimization | Science instrument is setup: optics and read modes are set and confirmed. May record first exposure to check centering with point-source and expected SNR/coadd. Monitor image quality and assess optimization progress. | UTT acquisition requires more design. Assuming redundant information from USNO-B, GSC-II & SDSS uncertainty in field centering should be < 0.2". |
| 7 | Science integration starts |  |  |

The main contributions to the centering error budget during NGAO acquisition in LGS mode are:

- The accuracy for the knowledge of the separation distance and position angle between the stars and the galaxies from the literature. This information is provided by the astronomer, and can be < 0.01" if the field has been observed (recently) with HST cameras. The USNO-B on-line catalog  provides an astrometric accuracy of 0.2", and the astrometric solution for the USNO-B, GSC-II and SDSS catalogs are improved as the proper motions are being calibrated using GSC-I (KAON 467).

- The pickoff arm positioning accuracy for each science target with respect to the TT closed-loop reference position for the LOWFS, which is the total of:

  - The internal positioning accuracy and position stability for each individual pick-off  arm (science and LOWFS) – the requirement is ≤ 0.005" (KAON 548)

  - Registration accuracy and stability between LOWFS and science arms including TT stage positioning accuracy.

- The differential atmospheric refraction between the LOWFS and the science instrument.

- The total contribution from the optical distortions due to thermal gradient, alignment error, woofer and MEMs positioning between the science array and the LOWFS.

The LOWFS and LGS object selection mechanism study (KAON 559) shows that the positioning accuracy requirement can be met.

#### System Operations: Dithering and Offsetting

Several approaches to dithering and offsetting were proposed and discussed in KAON 558. The rationale for reviewing the dithering and offsetting scenarios comes from the important overhead (~30 seconds per move) it currently takes to perform these important observing steps.

The selected approach recommends avoiding any telescope move and AO pause/resume sequence, unless necessary. Most field repositioning on the science array is performed to account for pixel/spaxel response, background emission or super-sampling and are of relatively small amplitude (< 2"). They could be performed by a tilt on the second-relay MEMS. This implementation would leave the LOWFS, TWFS and LGS WFS closed during the entire observing sequence, and would allow for maximum flexibility and efficiency for centering the science target, tracking, correcting for DAR, etc. We believe that these internal optics have the required pointing accuracy and could result in minimal overhead (< 5 second).

An alternate scenario that still does not require the telescope to move would require a global tilt on the woofer, and a counter motion for the LOWFS/TWFS, LGS WFS probe arms. This requires pausing and resuming the AO operations and may require ~ 5 to 10 seconds.

Alternatively, offsets of larger amplitude are performed by requesting a telescope offset, repositioning the probe arms at a different field location and re-acquiring the guide stars on the AO sensors. This may take about ~ 15 to 30 seconds depending on the detailed implementation.

We are confident that the combination of these three scenarios with the possibility of parallel commands to different subsystems will address the efficiency requirement for dithers and offset for the key science cases.

### System Control

The high-level control of the system is performed through the Operation Control GUIs and executed by the Multi-system Command Sequencer (MCS). A schematic view for these controls was presented in Figure 68.

#### Multi-System Command Sequencer

The MCS is the main interface between the Operation Control GUIs (configured and controlled the by AO operator, the expert user and the observer) and the control of each subsystem. The important design concept we have opted for, is to have all complex observing sequences under a central supervisory control system that will send and coordinate commands with the AO, Laser, science instrument(s) and other subsystems. The architecture for the MCS follows the design for the subsystem sequencer (see KAON 569 and section Error! Reference source not found.).

The MCS has four main components: a library of multi-system coordination sequences, a command interface, a data interface and a system health monitor. The functions of these four main components are as follows:

      - Multi-system coordination sequences. The multi-system coordination sequences are a collection of functions which implement complex sequences of commands for the underlying control subsystems (AO, Laser, etc). A multi-system coordination sequence allows the user to send a simple command to the MCS, while it commands and coordinates all of the many tasks required by this command and returns the status to the user. The coordination sequence receives a command from the user and then sends multiple commands appropriate for the task to be accomplished to the underlying multi-systems using the main command interface discussed below. Examples are: the LGS setup sequence that is used during slew to startup, initialize and setup AO, Laser and science instrument for the next LGS acquisition sequence. A key task during the PD phase will be to identify all of the coordination sequences required for the MCS and to specify their requirements. Note that we will likely require some flexibility in the management of this sequence library as we plan to add sequences to the library, mostly diagnostic and troubleshooting sequences, during the I&T and early operation phases of the system.  The reliability and efficiency of the NGAO operations strongly rely on the successful implementation of the multi-system coordination sequences.

      - Command interface (see Section Error! Reference source not found.).

      - Data interface (see Section Error! Reference source not found.).

      - System health monitor. The system health monitor is a task that monitors the status of the MCS functions and tasks.

#### Operation Control (Graphical) User Interfaces

The operation control GUI is the main interface between the Users (AO operator, expert user and observer) and the control of components and execution of sequences with the NGAO and science instrument.

The detailed design for the operation control GUIs for the science instruments will be defined in the science instrument manual. We will work with the science instrument teams to define a common design for the interface between the NGAO science operations GUI and the science instrument GUIs.

We have opted for the following preliminary set of design choices:

- The GUIs will be modular (as shown in Figure 68) and include three main parent components: 1) NGAO controls, 2) science instrument controls and views, and 3) system-view and performance monitoring displays.

- The implementation of these tools should be fully compatible with the pre- and post- observing tools.

- The standard practice in the observatories (Gemini, ESO, STScI, Keck) for the implementation of these operation tools is to use Java and XML programming languages.  We would recommend using these standard practices and other similar ones being developed in the context of Virtual Observatories (VO) and National VO.

- Several GUIs may be required during the operations per parent component. We will attempt to limit the total numbers of GUIs. Due to the limited integrated software development, our current LGSAO control includes as many as 30 displays and leads to some confusion during LGS operations.

- The control GUIs will include two types of command controls: controls for direct commands with no parameters e.g., open AO loops, (re-)close AO loops and controls for more complex commands requiring some parameters e.g., an acquisition sequence using a configuration file.

- The operation control GUIs will be designed to be users-friendly and include/display the minimal complexity. All complex commands will be implemented at the lower levels in the MCS and subsystem sequencers. Additional complex commands could be controlled using from specific call to a different set of GUIs (e.g., a somewhat complex calibration widget could be called from the NGAO GUI).

- The user can select the parameters for complex command either by loading a previously saved configuration file (these configuration files are also the outputs of the planning tools) or by manually entering values in the configuration fields.

### Pre and Post-Observing Tools

#### Pre-Observing Tools

The pre-observing tools will allow the observer to simulate, evaluate and plan for an observing program using the NGAO and the science instrument(s) any time prior to the observations, particularly during the observing time proposal submission process. The astronomer will likely go through a second phase of observation planning in the month prior to, and days leading to the observations. During the observing night, the observer may use the same sets of tools to check and refine the observing strategy, if necessary.

The pre-observing tools are:

- The AO Guide Star Tool to search adequate astronomical catalogs for natural guide sources, identify and select them, and save all relevant information on the NGS and the science field required to simulate and acquire the target.

- The NGAO Simulation tool to estimate the NGAO performance in terms of Strehl ratio, encircled energy, full-width at half-maximum, etc as a function of the NGAO mode and setup.

- The Exposure Time Calculator to estimate the SNR / seconds and dominant noise regime for the science instruments.

- The Observation Preparation tool to prepare, review and save the observing sequences and estimate the observing efficiency.

- The Laser Clearinghouse Planning tool to automate the coordination tasks with the laser clearinghouse.

The requirements for these tools are a combination of derived-requirements from the science cases (KAON 456) and operational requirements (KAON 456). A block diagram for the pre-observing tools architecture design was shown in Figure 68. KAON 577 presents the System Design Report for the pre-observing tools.

Figure 70.  AO guide star tool workflow.

During the proposal phase, the AO Guide Star, the Performance Estimator, the Exposure Time Calculator and the Observation Preparation tools needs to assist the astronomer in identifying suitable Guide Stars and providing a first order estimate for the image quality, the exposure time and expected SNR and the observing strategy, given a basic science instrument setup. The information saved by the user might be inserted in the technical justification of the proposal. The tools need to be user friendly and easily portable on most computer’s OS.

During the detailed observation planning, the same tools will be used to evaluate, optimize and prepare the observations sequences. The output parameters for the guide stars and instrument configurations will be saved in a format shared by the NGAO observing tools. The information will be loaded by the observing tools during night time operations.

Finally, during the observations, these tools may be used to preview and assist the on-going observations and for any on-the-fly change to the observing strategy.

Figure 70, Figure 71 and Figure 72 succinctly present the workflow for the AO guide star tool, the performance simulation and exposure time calculator, and the observation preparation tools, respectively.

The AO Guide Star Tool is used for both LGS and NGS cases. It is a versatile tool that will make request to astronomical catalogs, resolve target names, find and select AO guide stars for the NGAO science cases based on their derived NIR brightness and save the results. It is required to find a single star for NGS and sets of triplets for LGS. The sets of triplets will be ranked according to the estimated total residual error on the estimation of the TT mode and quadratic null modes. The results will be saved in the valid format for the telescope and the tools.

Figure 71.  NGAO performance estimation tool and exposure time calculator workflow.

The NGAO performance estimation tool will take as inputs the AO Guide Star(s) information, the AO mode, the selected instrument and the (anticipated) observing conditions. As it will run on the host computer, or through a web-server, it will not be able to (re-)run a full NGAO simulation for each new observing program. Instead, it will make use of a combination of PSF libraries, performance lookup tables and analytical formulae to estimate AO quantities such as SR, EE, FWHM and possibly a 2-D NGAO model PSF for the science field(s). The tool will allow the user to compare performance results from different AO Guide Star(s) and different LGS asterisms configuration.  The output results and the parameters used for the simulation will be saved in a file. The parameters and the algorithm for the simulation tools are yet to be defined.

Once the AO performance has been estimated it is then possible to calculate the exposure time to achieve a desired SNR given the instrument selection and setup, the detector read mode, a model for the noise and background emission, as well as a (simple) flux distribution model for the target. The tool will also estimate the background limited performance time and check that the detector is used in its linear range.

Figure 72.  Observation preparation tool workflow.

The observation preparation tool will take as inputs the information from the selected AO guide star(s), the NGAO mode, the instrument selection and when required, the observability of the target. The astronomer will define the parameters for the observing sequences that are possible for this observing mode. The tool will check the NGAO configuration e.g., dichroic configuration and expected NGS flux on the LOWFS compatible with the selected observing wavelength. The parameters to be set for the observing sequences are yet to be defined. The tools are anticipated to allow for flexible and versatile use of the instrument. The configuration for the observing sequences will be saved in files that will be loaded at the time of the observations. We have yet to define how these files will be managed. A manual management for these various configuration files (guide star and science targets information, NGAO configuration, instrument configuration, observing sequence information, etc) could lead to confusion.  We will consider implementing an automated file management from the observing proposal phase to the final execution at the telescope.

#### Post-observing Tools

The post-observing tools and interfaces are:

- Data quality metrics: the purpose of this tool is to reduce and analyze data collected during the observations and output quantities such as total residual wavefront error, seeing, photometric stability, Na return, observing efficiency, etc. These quantities have yet to be defined during the PD and DD phases. The results will be saved and stored with the final data product.

- Data product management tool: the observer and the support staff will use this tool to define which data needs to be saved and stored with the science data. This data product management may also help manage the data that does not need to be stored and can be deleted.

- PSF reconstruction tool: based on the WFC data stored on the data server, the Cn2 information, and other system parameters the PSF reconstruction tool will provide an estimate for the PSF in specific locations in the science field. The algorithms for the PSF reconstruction are yet to be defined. We have started the development of a prototype algorithm for the current NGS and LGS system for the on-axis and off-axis cases.

## Science Instruments

### Science Passbands

The NGAO system passbands are shown in Figure 73 along with the NGAO nominal observing bands.  The cut-on and cut-off (50% points) wavelengths are summarized in Table 8.  Additional details on the NGAO passband definitions may be found in KAON 530.

Figure 73: NGAO Passbands

Table 8: NGAO system passband and observing band characteristics

| Passband name | Cut-on ( ((m) | Cut-off ( ((m) | Notes |
| --- | --- | --- | --- |
| NGAO Visible | 0.68 (0.62 goal) | 1.07 | Goal is useful Strehl at Hα |
| NGAO rl | 0.620 | 0.689 | rl = “r band long”, cut-on may be set higher depending on filter characteristics |
| NGAO i' | 0.702 | 0.853 | SDSS i' band |
| NGAO z' | 0.818 | 0.922 | SDSS z' band |
| NGAO z spec | 0.855 | 1.050 | Custom NGAO z band for spectroscopy |
| NGAO Near-IR | 0.97 | 2.40 |  |
| NGAO Y | 0.970 | 1.07 | UKIDSS photometric |
| NGAO Y spec | 0.970 | 1.120 |  |
| NGAO J | 1.170 | 1.330 | UKIDSS/Mauna Kea photometric |
| NGAO J spec | 1.100 | 1.400 |  |
| NGAO H | 1.490 | 1.780 | UKIDSS/Mauna Kea photometric |
| NGAO H spec | 1.475 | 1.825 |  |
| NGAO K | 2.030 | 2.370 | UKIDSS/Mauna Kea photometric |
| NGAO K spec | 2.000 | 2.400 |  |

### DAVINCI

### Interferometer

It is a requirement for the Interferometer to be supported by AO on both telescopes in the NGAO era.  A trade study was performed on the issue of Keck Interferometer support during the system design that is documented in KAON 483.  The primary requirements are to achieve at least the current level of performance while maintaining a common field orientation and polarization from both telescopes.

The NGAO configuration and control loops in Interferometer mode are provided in KAON 550 and KAON 705 (see also section 3.5.2 of this document), respectively.

An assessment of how well the Interferometer needs are met by NGAO was performed near the end of the preliminary design in KAON 728.  The conclusion is that the angles and geometry between Keck I AO and NGAO are quite well matched leaving only the issues of matching material dispersions and dichroic phases.  These can be matched by the identified addition of similar windows and dichroic coatings in the Keck I AO system.

### ‘OHANA

Both existing Keck AO systems accommodate an ‘OHANA fiber injection module at the output of the AO systems.  NGAO should provide an output port where this or a similar fiber injection module could be located, and whose output could be successfully interfered with the light from another telescope.  The ‘OHANA needs are also addressed in KAON 728 and should be met best by locating the ‘OHANA module at the 2nd NGAO instrument location (at least initially).

### Thermal NIR Imager

A thermal NIR imager has not been given a high priority and therefore no significant evaluation has occurred for this instrument.  An evaluation of the reuse of NIRC2, which extends out to L and M-bands, was performed as part of KAON 493.

# Performance Budgets

In support of the flowdown of requirements from the Science Case and high-level Functional Requirements to component specification, eight system performance metrics were identified in the Science Requirements Document.  For three of these metrics, background and transmission, wavefront error and ensquared energy, and high-contrast performance, we have produced associated quantitative performance budgets to identify key performance drivers.  For photometric precision, astrometric accuracy, and polarimetry we have identified key drivers and documented these in technical reports that have informed the NGAO design.  The final two metrics, observing efficiency and observing uptime, have been given only preliminary consideration and will be further developed in the preliminary design phase.

A concise summary of the various performance budgets developed during the SD phase is presented in KAON 491.  The wavefront error / encircled energy budget summary, as modified by the 2009 ‘build-to-cost’ design changes, is documented in KAON 644.

## Background and Transmission

The background and transmission performance budget is developed in KAON 501.

Both AO relays must efficiently transmit the science wavelength light from 0.8 to 2.4 (m (with a goal of 0.656 to 2.4 (m, so as to include H().  The first relay must also efficiently transmit sodium wavelength light (589 nm) and the additional L-band light (3.4 to 4.2 µm) for the interferometer.  This wavelength range must be efficiently divided between the various sensors (LGS and tip-tilt) and the instruments.

The transmission budgets developed in TBD take into account all surface counts in the various NGAO system paths.  As some resultant NGAO (only) transmissions are:

- K-band Narrow-Field Science Transmission	TBD%

Where the science path considered is from before the telescope M1 to the interior of an instrument entrance window, including atmospheric dispersion corrector surfaces.  For the high-order LGS wavefront sensor path, we have NGAO (only) transmission:

- 589 nm LGS WFS Transmission TBD%

based on TBD.  Excellent coatings and cleanliness will be required for all surfaces.

TBD also contains a detailed analysis of thermal background, particularly for K-band science where the current Keck AO system is known to contribute detrimentally to overall background.  The basic result in TBD is that all of the architectures considered for NGAO required approximately the same system cooling, between TBD and TBD to meet science requirements.  The design choice we have adopted to achieve the K-band background requirement is to cool the AO optics to TBD K.

The sensitivity delivered by the NGAO system is significantly affected by the total background seen by the instruments.  In the present Keck telescope AO systems background is recognized as a significantly limiting sensitivity, particularly for the K-band.

Part of the solution to reducing background is the control of scattered light through careful design and implementation, and the use of hexagonal, rotating cold stops matched to the shape of the telescope pupil in the near-IR instruments.  However, thermal emission is a significant factor for near-IR observations, particularly longward of 2 µm.  Using data from the current Keck II telescope AO system we have developed a model of the background contributed by sky + telescope + AO system that indicates the AO system optics should be cooled to TBDK.

## Wavefront Error and Ensquared Energy

A wavefront error budget for NGAO has been developed using Excel spreadsheet tools developed over several years for the engineering evaluation of AO system performance.  The primary purpose of the spreadsheet is to compute AO and instrumental wavefront error budgets for different architectures and science cases, along with Strehl ratios computed using the Marechal approximation.  The spreadsheet also computes ensquared energy fractions using a core/halo model for the point spread function, and calculates sky coverage estimates for tip-tilt guide stars employed in LGS architectures from common star density models.  The spreadsheet has been validated by comparing the spreadsheet predictions to the current performance of the Keck II LGS AO system with good agreement.

The wavefront error budget is described in KAON 644.  The primary tool is an excel spreadsheet.  This budget is supported and anchored by a number of KAONs.  The atmospheric assumptions summarized in KAON 503 are based on previous seeing studies (KAON 303) and new TMT site monitoring data (KAON 415 and 496).  The sodium return assumptions are based on sodium density from Keck LGS photometry (KAON 416), long term LIDAR measurements on Haleakala (KAON 417) and comparisons to measured returns from Gemini and Keck (KAON 419).  The wavefront error budget tool has been anchored to the performance of the existing Keck AO system in KAON 461.  The contribution of Keck telescope segment figure errors is determined in KAONs 468 and 469, and the overall contribution of the telescope to the wavefront errors is determined in KAON 482.  Finally, several tomography codes were compared (KAON 475) in order to validate the tomography assumptions used in the wavefront error budget and the null and quadratic mode tomography errors were evaluated (KAON 492).

Related analyses include sky coverage modeling (KAON 470) and performance versus field of view for low order wavefront sensor guide stars (KAON 504).

In order to test and anchor the NGAO error budget tool, a detailed assessment of the Keck II AO performance was performed in KAON 461.  Table 9 from this KAON demonstrates the capability of the NGAO tool to model the Keck II AO performance, albeit under somewhat different conditions and with some unknowns (such as d0).  More recently we have demonstrated that the NGAO tool can be used to accurately model the demonstrated performance of the Keck II AO system after the Next Generation Wavefront Controller upgrade as shown in Table 10.  The NGAO tool has also been used in this Table to support predictions of the performance of the Keck I LGS AO upgrade that is currently underway.

|  | NGS bright star | LGS (10th mag) |  | LGS (18th) |
| --- | --- | --- | --- | --- |
|  |  | Meas-ured | NGAO tool |  | Meas-ured | NGAO tool |  | Meas-ured | NGAO tool |
| Atmospheric fitting |  | 139 | 110 |  | 128 | 110 |  | 128 | 110 |
| Telescope fitting |  | 60 | 66 |  | 60 | 66 |  | 60 | 66 |
| Camera |  | 113 | 110 |  | 113 | 110 |  | 113 | 110 |
| DM bandwidth |  | 103 | 115 |  | 157 | 146 |  | 157 | 146 |
| DM measurement |  | 17 | 16 |  | 142 | 150 |  | 142 | 150 |
| TT bandwidth |  | 75 | 91 |  | 109 | 94 |  | 300 | 243 |
| TT measurement |  | 9 | 5 |  | 23 | 11 |  | 300 | 349 |
| LGS focus error |  | 0 | 0 |  | 36 | 36 |  | 36 | 91 |
| Focal anisoplanatism |  | 0 | 0 |  | 175 | 208 |  | 175 | 208 |
| LGS high-order error |  | 0 | 0 |  | 80 | 80 |  | 80 | 80 |
| Miscellaneous |  | 120 | 0 |  | 120 | 0 |  | 120 | 0 |
| Miscellaneous (NGAO) |  | 0 | 106 |  | 0 | 72 |  | 0 | 72 |
| Calibrations |  | 0 | 30 |  | 0 | 30 |  | 0 | 30 |
| Total wavefront error |  | 258 | 250 |  | 378 | 372 |  | 557 | 563 |
| K-band Strehl |  | 0.58 | 0.57 |  | 0.31 | 0.30 |  | 0.08 | 0.08 |
| Percentile Seeing |  | 75% | 65% |  | 75% | 65% |  | 75% | 65% |

Table 9.  NGAO error budget tool anchoring to Keck II AO performance.

| Error Term | KII NGWFC upgrade | K I (linear pol.) | KI (circular pol.) |
| --- | --- | --- | --- |
| Atm. Fitting | 118 | 118 | 118 |
| Tel. Fitting | 66 | 66 | 66 |
| Camera | 110 | 110 | 110 |
| DM Band | 125 | 96 | 88 |
| DM Measure | 152 | 104 | 96 |
| TT band | 102 | 102 | 102 |
| TT measurement | 23 | 23 | 23 |
| LGS focus error | 46 | 19 | 19 |
| Focus Aniso. | 164 | 164 | 164 |
| LGS HO error | 80 | 50 | 50 |
| Miscellaneous | 70 | 70 | 70 |
| Calibrations | 30 | 30 | 30 |
| Total Wavefront Error | 348 | 312 | 306 |
| K band Strehl | 0.37 | 0.45 | 0.46 |

Table 10.  The NGAO error budget tools accurately models the upgraded Keck II AO performance.

### Key Flowdowns from the Wavefront Error Budget

The AO system architecture is driven by the required wavefront error and related performance budgets to incorporate a number of innovative subsystems that work together to achieve NGAO science goals for optimized cost and technological risk.  Key new features of NGAO include multiple LGS beacons and a corresponding number of LGS wavefront sensors, multiple tip-tilt stars, a tomographic wavefront reconstructor and high order correction.

Although a shallow optimization, we find that TBD actuators are required across the telescope pupil diameter to overcome both atmospheric turbulence and residual figure errors in the Keck telescope primary mirror (see, for example, KAON’s 468 and 469).  We believe this is most practically achieved using a small MEMS deformable mirror to correct over a narrow field of view.  (A comparison with a large classical DM architecture is presented in KAON 499.)  Our requirement for high sky coverage fraction leads us to require a large technical field of view.  We considered an entirely open-loop control architecture wherein the LGS beams would see no correction, but determined this to be too risky as we would require extremely linear LGS WFS’s possessing a very large dynamic range To address the problem we adopted a two-stage correction architecture, with a first DM with 20 x 20 actuators providing low order correction for the LGS in a closed loop.  A second, MEMS DM is operated in a feed forward or “go to” control mode.  We have allocated 40 nm rms to residual go-to control errors (driven primarily by imperfect knowledge of the woofer mirror position).  To meet sky coverage goals, we further employ separate, lower order MEMS in each of the tip-tilt sensors.

Our study of the performance of the selected AO system architecture shows that it is quite robust, permitting optimization of the residual wavefront error for a wide range of observing conditions.  The spreadsheet tool was configured to optimize the H band Strehl ratio, and certain parameters such as LGS constellation radius, high order update rate, and tip-tilt update rate were allowed to vary within appropriate constraints in order to optimize the Strehl ratio.  By allowing for reconfigurable science and LOWFS star laser asterism, we find performance reductions can be mitigated even in poor seeing, low sodium abundance, or in the event of sub-optimal laser power output.  An example report from our wavefront error budget tool is shown in Figure 74.  Additional examples are provided as an Appendix to this report (section 9).

Figure 74.  Science target wavefront error budget for the Kuiper Belt Object Companion Survey Key Science Case. (TBR)

In addition the science target WFE budget, we also maintain a separate WFE error budget for the sharpening of the LOWFS NGS stars.  An example of this budget, corresponding to the science case in Figure 74 is shown in Figure 75.

Figure 75. LOWFS NGS wavefront error budget for the KBO Companion Survey Science Case.

The NGS is 35" off-axis.  We expect such a star to be sharpened to about 35% J-Strehl using MOAO correction based on multi-LGS tomography. (TBR)

### Laser Power considerations

Our error budget analysis indicates that an equivalent of 75W of sodium laser power (assuming an SOR-type laser return per Watt) is sufficient to meet the narrow-field science performance objectives.  This power will be divided to form between 7 laser beacons (4 science beacons and 3 point-and-shoot LOWFS beacons).

### Performance Summary

A summary of wavefront error performance is presented in Table 11.

Table 11. Wavefront error budget summary for several NGAO science cases.

The performance metric for the high-redshift Galaxies science cases is ensquared energy in a 70 x 70 mas spaxel.  For all other cases, it is Strehl ratio. (TBR)

The first column of the table indicates the observing scenario.  The second column indicates the integration time assumed for the science exposure.  The third column indicates the tip-tilt reference used, and the fourth column gives the diameter of the LGS variable radius constellation.  The fifth column indicates the tip-tilt error that results from the assumed angular offset of the tip-tilt star.  The sixth column gives the sky coverage fraction over which the tip-tilt error will be less than or equal to the error given in column five.  This estimate results from the use of common sky coverage models (Spagna and Bachall-Soneira).  The last three columns give the high order wavefront error, the total wavefront error with tip-tilt errors, and the H band Strehl.  For the extragalactic case, the figure of merit is ensquared energy rather than residual wavefront error, for the 50 mas spatial sampling of the IFU the ensquared energy is TBD % in K-band.

These results show that the fixed radius LGS constellation and the performance levels assumed for the tomographic wavefront reconstruction, LGS wavefront sensors and near-IR tip-tilt sensors are capable of providing performance that is generally at the level required by the science cases.  Initial estimates of NGAO system performance based on laser tomography AO resulted in the adoption of three representative values of residual wavefront error for the science case simulations: 140 nm, 170 nm and 200 nm.  This has led to further work to develop additional techniques for performance improvement including the additional three freely positionable LGS and the additional tip-tilt sensors.

The sky coverage fractions required by the extragalactic and Galactic science cases requires optimizing the offset and brightness of the tip-tilt stars.  This is accomplished by increasing the faint magnitude limit for tip-tilt stars through the use of tip-tilt sensors operating at near-IR wavelengths combined with MOAO correction using deployable LGS beacons specifically for tip-tilt reference sharpening, and by providing a 120" field of view for tip-tilt star selection.

## Photometric Precision

Requirements for photometric measurements in the NGAO science cases range from 0.05 to 0.1 magnitudes in relative photometry, and ≤ 0.05 magnitudes for absolute photometry.  The fundamental condition for high photometric accuracy is stability of the PSF.  Because of the high Strehl delivered by the NGAO system, a more stable PSF is expected.  Many of the science cases that require the highest photometric accuracy are observing a science target of sufficient brightness (H < 16) to permit use of the science target as an on-axis tip-tilt reference, further improving Strehl performance.

Detailed consideration of the physical effects that can degrade NGAO system photometric precision is documented in KAON 474, including AO system performance, stellar crowding, scintillation, atmospheric attenuation, and detector non-uniformities.  The key result of KAON 474 is that in order to meet the scientifically required photometric precision, NGAO will need to provide the astronomical user with detailed and reliable information regarding the NGAO point spread function (PSF) on an exposure-by-exposure basis.

We envision ‘on-axis’ PSF information provide by AO system control and sensing telemetry, in the absence of an appropriate stellar point source reference (which if known will always provide a more accurate, direct measure of the PSF).  NGAO will also provide an estimate of the field-dependent PSF based upon integrated recording of Cn2(h,t) information from the called-for atmospheric profilometer on the Mauna Kea summit ridge.  Work at Palomar (Britton 2006) has shown that real time turbulence monitoring giving Cn2 data during the observation is also useful in improving the results of PSF post processing.  This post processing will also be supported by facility PSF deconvolution software.

## Astrometric Precision

Astrometry is important for a number of the Galactic and Solar System science cases.  The most demanding requirements are for observations of the Galactic Center where precision of 100 (as is required.  The current Keck II LGS AO system with the NIRC2 instrument is able to achieve best-case precision of 200 (as.  The high Strehl of the NGAO system (~3 times that of the current LGS AO system under similar conditions) will make a significant contribution to improved accuracy of astrometric measurements by reducing source confusion.  In addition, studies of the astrometric precision of the current Keck II LGS AO system indicate that geometric distortion, differential tilt anisoplanatism between the science target and off axis tip-tilt stars (increasing with increasing distance between the two), and differential atmospheric refraction all contribute to the error in astrometric measurements.

Detailed consideration of the physical effects degrading astrometric accuracy for NGAO was documented in KAON 480, including differential atmospheric tilt jitter, geometric distortion, atmospheric refraction, and stellar confusion.  Better Strehl ratio and point source contrast from NGAO will help overcome astrometric errors due to stellar confusion in crowded fields, as well as improving point source sensitivity for all observations, thus providing a richer reference field for astrometric calibration.

The same features provided to monitor the PSF and monitor atmospheric turbulence for photometric accuracy would contribute to NGAO astrometric precision.  Geometric distortion in the AO system and instruments will be minimized during design and facilities will be incorporated for mapping residual distortion during commissioning.  The optical design choice of having mutual optical conjugation of the 1st and 2nd relay DM’s is an intention strategy of mitigating NGAO-inducing plate scale distortions into the science focal planes. (Because the systematic error floor will be rapidly reached, we are more concerned about long-term stability and place less emphasis on the potential correction of differential atmospheric tilt jitter afforded by MCAO architectures.)   Improved mechanical stability is also a fundamental part of the design of the NGAO system and instruments.

The NGAO system will also incorporate an ADC to reduce the effects of atmospheric refraction, and differential tilt anisoplanatism will be reduced by the use of multiple, optimally located tip-tilt stars.  Alignment tools for these multiple tip-tilt stars will minimize plate scale changes due to the AO correction.

## Companion Sensitivity

Another important area for NGAO science is high contrast observations.  The Strehl proposed for NGAO is lower than extreme AO systems such as the Gemini Planet Imager, but at the same time, NGAO will provide higher sensitivity and sky coverage that greatly exceeds that of an NGS-only extreme AO system.

Details of the high-contrast error budget development are presented in detail in KAON 497.  One product of this effort is a preliminary numerical budgeting tool (similar in some ways to the wavefront error spreadsheet tool) that allocates contributions to the residual high-contrast ‘dark hole’ halo to various physical effects, such as atmosphere fitting error, spatial aliasing, control servo lag, measurement noise, and residual tip/tilt errors.  In addition, numerical simulations were performed to evaluate the impact of segment gaps (using the grey pixel approximation), segment vibrations, telescope wind-shake, and coronagraph residual diffraction effects.  Partial consideration has been made of the residual spatial power spectrum of tomography error, quasi-static LGS calibration errors, telescope static residual errors, and instrument static errors.  By taking separate account of the expected residual speckle lifetimes associated with each physical effect, we can predict the achievable contrast for a certain observation in a given integration time.

An example of the high-contrast simulation capability employed in KAON 497 is shown in Figure 76.

Figure 76.  Simulated NGAO J-band science observations with secondary objects inserted.

Top row: AO without coronagraph; middle row: AO + coronagraph with 6 /D occulation; bottom row: AO + coronagraph with 10 /D occulation.  The numbers in the lower left corner of each image indicate the primary /secondary / delta magnitudes, i.e. the format is J1 / J2 (J).  The images are stretched (asinh) and individually scaled.

The fundamental conclusion of KAON 497 is that NGAO can indeed serve as a powerful high-contrast science engine, particularly in the uniqueness space associated with faint science targets (where the NGS-only GPI system will not be usable and where NGAO surpasses in contrast (by an order of magnitude) the LGS-capable PALM-3000 system.)

We found that even with the high-order 64x64 actuator NGAO deformable mirror, residual telescope figure errors lead to speckles with troublesome spatial and temporal scales with the greatest contribution to the high-contrast error budget.

While our analysis of the contrast performance needed indicates that a conventional occulting spot coronagraph with an apodized (hexagonal, rotating) Lyot stop will meet the needs of the majority of the NGAO high contrast science cases, we will also in the preliminary design phase investigate the use of more advanced techniques such as non-redundant aperture masking. To help address specific needs identified in our high-contrast error budget initial analysis, we are expecting further analysis in the preliminary design phase of a variable diameter spatial filter as the field stop for the NGAO NGS WFS.

The level of contrast achieved with NGAO will ultimately depend on the control of systematic errors such as non-static, non-common path aberrations, servo lag error and various sources of speckle.  Speckle suppression techniques including spatially resolved spectroscopy will be available for NGAO observations and we intend to incorporate to the extent possible the calibration “best practices” discovered by the GPI project.

## Polarimetric Precision

Polarimetric precision was considered only superficially in the system design phase.  We identified the K-mirror rotator as a potential detriment to polarimetric precision, but adopted this in our architecture for its other system advantages (simplicity and cost).

We do not yet know how stable or calibratable polarimetry will be with NGAO.

One potential strategy for polarimetry for further consideration is the use of the K-mirror rotator in a fixed orientation, allowing the science image to rotate on the sky.  For high-contrast polarimetry, this may be an acceptable observing mode, but this will require more careful analysis of all the system implications.

## Observing Efficiency and Uptime

KAON 463 discusses the observing efficiency and uptime of the existing Keck LGS AO system for reference.  Observing efficiency has already been discussed in section 3.6.1.2.  More detailed efficiency and uptime budgets will be produced in the preliminary design phase. (TBR)

# Requirements Development and Compliance

The requirements development process is discussed in KAON 573 and is illustrated schematically in Figure 77.  The process began by understanding the goals that the Keck community had for a next generation AO capability at WMKO.  This was followed by the development of science cases to understand the science drivers and requirements on this NGAO capability.  The Science Case Requirements Document (KAON 455) discusses and documents this process and the resultant science requirements.  These requirements were developed in parallel with initial performance budgets and analysis to determine feasibility.  The science requirements and additional observatory and user requirements were subsequently documented in the System Requirements Document (KAON 456).  Both of these documents were intended to be architecture independent.  As the team developed an architecture and subsystem designs to satisfy the system requirements the next level of implementation dependent requirements were documented in the Functional Requirements Document (KAON 573).  Appendix B of KAON 573 is a printout from the requirements database.  The Operations Concept Document and Interface Control Documents will be developed during the Preliminary Design.  The document you are currently reading is the System Design Manual shown in the V-diagram as a product of the subsystem architecture definition.

Figure 77.  NGAO project V-diagram including the design and development process.

Processes are shown in blue and associated documentation in tan.

In all levels of the requirements documents, steps were taken to assure that each documented specification is traceable back to its origin or driver. The most relevant sources are the top level NGAO science requirements and essential observatory standards but in many cases requirements are generated based on architectural design decisions, engineering best judgments, or for other reasons. Maintaining requirements traceability enables reasonable change control, so that the systems engineer is able to understand and manage the impact of descopes, engineering “push backs,” error budget redistribution, etc.

The science case requirements were summarized in a spreadsheet that was used in the architecture selection process (KAON 499 describes this selection process).  The current version of this spreadsheet can be found in KAON 548 or as an Appendix to the System Design Report (KAON 575).  The cascaded relay architecture we have selected and developed has been demonstrated in our performance budget analyses (see section 4) to meet the background, wavefront error, encircled energy and sky coverage science case requirements.

Although not yet demonstrated by performance budgets or analysis we are developing the functional requirements and designs to ensure that the astrometric and photometric requirements will be met.  A major element of meeting these requirements will be providing a good calibration of the PSF.

The key elements of the selected architecture flowed directly from the science case requirements.  At the highest level these can be summarized as follows:

- Dramatically improved performance at near infrared wavelengths.

- Improved IR sensitivity.

- High Strehls (≥ 80% at K-band) are required over narrow fields. The flowed down requirements are derived from the wavefront error performance budget and assumption about how these error terms can be met.  These flowed down requirements include number of actuators in the narrow field, required system bandwidth, number of LGS, number of NGS, required laser power, etc.

- Lower backgrounds.  This is particularly driven by the high redshift galaxy science.  This requirement has driven the need for a cooled AO system and the required temperature.

- Improved astrometric, photometric and companion sensitivity performance.

- Improved IR sensitivity is required (see above).

- It will also be critical to improve the PSF stability and knowledge.  The requirements on the PSF stability and knowledge to achieve the astrometric, photometric and companion sensitivity requirements will be developed during the Preliminary Design.  The astrometric error budget and PSF reconstruction tools will be developed during the Preliminary Design.

- Increased sky coverage.

- Wide field required.  This requirement drove us to the 120" diameter field needed to find suitable NGS for tip-tilt sensing.  The field requirement was determined via the analysis documented in KAON 504.

- Ability to use faint NGS.  This requirement drove us to the architecture where we provide AO correction of the tip-tilt stars.

- AO correction in the red portion of the visible spectrum.

- This drove the need to transmit these wavelengths to the visible science instruments and to share visible light with the LGS and NGS wavefront sensors via appropriate dichroics.

- Science instruments that will facilitate the range of science programs.

- This drove the selection and conceptual design of the science instruments described in section 3.7.

- This drove the providing of locations for these science instruments in the design.

We have also mapped each science case to a configuration of the NGAO system as shown in Table 12 to ensure that the NGAO architecture and subsystems can operationally support each science case (the configurations are maintained in KAON 550).  The numbers in the NGS and LGS configuration columns refer to NGAO system configurations.  A partial view of the configuration spreadsheet is provided in Figure 69.

Table 12.  Science case mapping to NGAO configurations.

# Alternate System Architectures

During the selection of the system architecture described in this document several alternate architectures were also evaluated and ranked. Each of these architectures, along with our adopted cascaded relay, are described and evaluated in KAON 499.

- Split relay.  The LOWFS, NIR deployable IFU and LGS wavefront sensor are fed directly from the telescope (and therefore must rotate).  The narrow field science instruments are fed by a refractive AO relay including a K-mirror and ADC.  Some technical evaluation details for this architecture are discussed in KAON 506.

- Adaptive secondary mirror.  All of the science instruments and wavefront sensors are fed directly by the telescope.  An adaptive secondary trade study was performed in KAON 485.  The existence of an adaptive secondary could potentially improve the performance on seeing limited instruments, and would offer the optimal approach to a ground layer AO system (see KAON 472).

- Large relay.  A large rotator and AO relay feed all of the science instruments and wavefront sensors.  This is the architecture that was described in the NGAO proposal (KAON 400).

- Keck I upgrade.  Quite similar to the selected cascaded relay approach.  The NIR deployable IFU and LGS WFS both follow the existing AO relay.  A second, higher order relay feeds the narrow field science instruments.  The difference is that this is an upgrade to the existing system, rather than a fresh start.  KAONs 500 and 502 describe this upgrade in some detail.  During preliminary design, we will look more closely at interim benefits to the Keck I LGS system that could be realized as part of our NGAO risk mitigation.

# Trade Studies

A number of trade studies were performed early in the SD phase to inform the system architecture down select and design choices.  A list of these trade studies is provided in Table 13 and their results were briefly summarized in the SDM (KAON 511).  These trade studies were key inputs to the architecture down selection process described in KAON 499.

Table 13.  List of trade studies performed.

| Trade Study Title | KAON # |
| --- | --- |
| MOAO & MCAO | 452 |
| NGAO Versus Keck AO Upgrades | 462 |
| Adaptive Secondary Mirror Option | 485 |
| Keck Interferometer Support | 483 (& 428) |
| GLAO for non-NGAO Instruments | 472 |
| Instrument Reuse | 493 |
| Telescope Wavefront Errors | 482 |
| Observing Model | 476 |
| Rayleigh Rejection | 490 |
| LGS Wavefront Sensor Type & number of subapertures | 465 |
| Low Order Wavefront Sensor number & type | 470 |
| Low Order Wavefront Sensor Architecture | 487 |
| LGS Asterism Geometry and Size | 429 |
| Variable Versus Fixed LGS Asterism Geometry | 427 |
| Uplink Compensation | 509 |

A few trade studies were performed during the preliminary design to support design decisions:

- As part of the build-to-cost exercise several alternate optical relay designs were considered in KAON 628.  The conclusion was to continue with the baseline cascaded relay design.

- A number of motion control architectures were evaluated against the NGAO needs in KAON 643.  The conclusion was to use a combination of centralized control for high precision devices and distributed control, with smart motors, for devices with less demanding requirements.

- KAON 680 looked at options for vibration mitigation and recommended a parametric oscillator approach similar to that being used with the Keck Interferometer.

# Glossary

Table 14. defines the acronyms and specialized terms used in this document.

Table 14.  Glossary of Terms

| Term | Definition |
| --- | --- |
| ACS | Active Control System |
| ADC | Atmospheric Dispersion Corrector |
| AO | Adaptive Optics |
| API | Application Programmer Interface |
| DCS | Drive and Control System |
| DM | Deformable Mirror |
| DOF | Degrees Of Freedom |
| EPICS | Experimental Physics Industrial Control System |
| FAA | Federal Aviation Administration |
| FOV | Field Of View |
| FPGA | Field Programmable Gate Array |
| FRD | Functional Requirements Document |
| FWHM | Full Width at Half Maximum |
| HODM | High Order Deformable Mirror |
| HOWFS | High Order WaveFront Sensor |
| IBRD | Instrument Baseline Requirements Document |
| IFU | Integral Field Unit |
| KAON | Keck Adaptive Optics Note |
| KI | Keck Interferometer |
| KOTN | Keck Observatory Technical Note |
| LGS | Laser Guide Star |
| LODM | Low Order Deformable Mirror |
| LOWFS | Low Order WaveFront Sensor |
| mas | milli-arcsecond |
| MEMS | Micro Electro-Mechanical System |
| MTBF | Mean Time Between Failures |
| NGAO | Next Generation Adaptive Optics |
| NGS | Natural Guide Star |
| NIR | Near InfraRed |
| NIRC2 | NIR Camera 2 |
| NIRSPEC | NIR SPECtrometer |
| OA | Observing Assistant |
| OAP | Off-Axis Parabola |
| ‘OHANA | Optical Hawaiian Array for Nanoradian Astronomy |
| OMU | Opto-Mechanical Unit |
| OSIRIS | OH-Suppression InfraRed Integral field Spectrograph |
| OSM | Object Selection Mechanism |
| PSF | Point Spread Function |
| rms | root mean square |
| SCRD | Science Case Requirements Document |
| SRD | System Requirements Document |
| TBC | To Be Completed |
| TBD | To Be Determined |
| WFE | WaveFront Error |
| WFS | WaveFront Sensor |
| WMKO | W. M. Keck Observatory |

# Appendix: NGAO PD Phase Detailed Wavefront Error Budgets

The following are detailed wavefront error / ensquared energy budgets developed using the median turbulence condition Mauna Kea Ridge Cn2(h) model (KAON 503).  This model has:

r0 (0.5 microns) = 16 cm

0 (0.5 microns) = 2.7 arcseconds

d0 (0.5 microns) = 4.85 m

L0 = 50 m

with a Cn2(h) distribution given by:

| Altitude (m) | Mauna Kea Ridge Cn2 Fractional Turbulence |
| --- | --- |
| 0 | 0.517 |
| 500 | 0.119 |
| 1000 | 0.063 |
| 2000 | 0.061 |
| 4000 | 0.105 |
| 8000 | 0.081 |
| 16000 | 0.054 |

KAON 503 also defines a wind velocity model for the Mauna Kea Ridge resulting in:

Greenwood frequency = 27.91 Hz

Figure 78. Science target wavefront error budget for Io Science Case. (TBR)

Figure 79. Science target wavefront error budget for Galactic Center Science Case. (TBR)

Figure 80.  Science target wavefront error budget for ExoJupiter LGS Case. (TBR)

Figure 81.  Science target wavefront error budget for Galaxy/Galaxy Lensing Science Case. (TBR)

Figure 82. LOWFS NGS wavefront error budget for the Galaxy / Galaxy Lensing Survey Science Case.

NGS 54” off-axis.  We expect such a star to be sharpened to about TBD% J-Strehl using MOAO correction based on multi-LGS tomography. (TBR)

Figure 83. Science target Ensquared Energy error budget for High-Redshift Galaxies.

Extended Groth Strip Science Case (TBR)

# Comments

Just providing information to personnel is not fail safe.  There should be interlocks to prevent accidental entry to hazardous areas.

Why is there a choice?

# Text boxes

NGAO near-IR

NGAO visible

NGAO rl

NGAO i'

NGAO z'

NGAO

z spec

K

Y

J

H