### Specifications

2-tier layout

- FoV

  - 150 arcsec. NGS field, 175 arcsec LGS field at zenith

  - 30 arcsec narrow field

- MCAO

  - Fold-up mirror located after OAP1, at around 10km conjugate, can be replaced by Low-order DM for MCAO capabilities.

- Woofer DM

  - 5 mm or 7 mm pitch woofer DM, 5mm pitch shown

  - 9.125 incident angle on woofer DM

- LGS WFS unit

  - LGS WFS fed by 589nm dichroic between woofer DM and OAP2

  - 12 degree LGS dichroic shown

- OSM/d-IFS orientation

  - Horizontal OSM and dIFS when using folded 2nd relay system

  - Vertically fed OSM and dIFS possible when using transmitted 2nd relay

- OSM/dIFS beamsplitter bank

  - 20 degree incident angle on 2nd relay fold dichroic.

  - This is the same as for 1-tier champion when using folded 2nd relay.

  - Does not appear to present difficulties when transmitting 2nd relay.

- Tweeter DM

  - Large area available for tweeter packaging

  - 10 degree incident angle on tweeter

- ADCs

  - We can put Brian’s JHK ADC before OSM/dIFS, after fold to 2nd relay.

  - There is room for a narrow field ADC before the instrument pickoffs, but it makes sense to me to have each instrument handle ADC’ing independently.

- ACQ Camera

  - No different than 1-tier champion, with acquisition camera pickoff upstream of OSM/dIFS.