NGAO System Design Phase: Work Scope Planning Sheet

WBS Element Title:	Laser

WBS Element Number:	3.3.3

Work Package Lead:	Viswa Velur

Work Package Participants:	Jason Chin

Revision	 1.0 	Initial

1.1 	After EC input.

# Work Scope

WBS Dictionary Entry: 	Based on system requirements and error budgets, determine the power requirements for existing lasers technology.  Specify a laser or set of lasers to produce guide stars. Take into consideration the current state of the art and availability of lasers.  Produce as output: a summary of the laser options versus requirements.

Requirements: 	FRD v1.0

# Inputs: Assumptions:

- FRD v 1.0

- Science Requirements Summary spreadsheet

- The NGAO error budget spreadsheet and assumptions thereof.

- LAO laser documentation

- Laser Architecture(s) from WBS 3.3.1.

- Emphasis will be placed on the SOR and LMCTI laser formats.

# Products:	Final Report

1.  Check and ensure that the # of the LGS Flux pages are consistent with experimental (or theoretical) parameters from relevant sources.

2.  Documentation summarizing the amount of laser power that will result in the necessary return will be presented for the laser architecture(s) and lasers considered.

FRD 2.0

Feed into requirements and compliance matrix for FRD 2.0 (laser section).

# Methodology:	-

# Estimate of effort:	20 hrs.

# Approvals:			20 hours

| Control | Name | Date |
| --- | --- | --- |
| Authored by: | Viswa Velur | 09/12/07 |
| Approved by: | Jason Chin | 10/2/07 |
|  | Don Gavel | 10/11/07 |
|  | Peter Wizinowich | 10/11/07 |

# Comments

This WSPS had 80 hrs allocated for this task. The XLS sheet shows 20 hrs allocated.