Palomar Adaptive Optics Test Plan

| Title | Switching Reflecting Spot |
| --- | --- |
| Date |  |
| Lead | J. Roberts |
| Time requested | 1h |
| Required conditions | Optics down, in lab or on the telescope (daytime) |

Purpose Shift the dichroic spot between the all dichroic and the NGS reflecting spot

Required equipment Lamp and extension cord Gloves

Test procedure – LGS to NGS Register and lock on white light Move acq_z to 15800 (focused on dichroic beamsplitter) Illuminate the beamsplitter with a lamp Turn up the white light power to 100 (white_light on, pwr=100) Shift the spot location by noting the current location of the rotary mount and rotating 10.6mm from there (1 full turn = 1mm) Visually check the location on the video monitor It helps to set the video camera to integrate (30s) Adjust the spot as necessary Y centration can be adjusted using the rotary mount; X centration can be adjusted using the linear stage directly under the dichroic mount Remove lamp and turn the white light down to 50. Register and lock on the white light Turn up the white light power to 100 (white_light on, pwr=100) Visually check again if the spot appears centered If an adjustment is necessary, repeat steps 7-9 With all the loops open, move ttm_a in .25” steps until the white light spot shows up on the edge of the reflecting spot in the acquisition camera. Note the number of steps. Close the TT loop to recenter, then open it. Move ttm_a in -.25” steps until the white light shows up on the opposite edge of the reflecting spot in the acquistion camera. Note the number of steps If the number of steps on each side differ by more than 2, repeat steps 7-9 and retest with the TTM Check ttm_b in the same way After the final adjustment, check both ttm_a and ttm_b Note the final difference in steps in X and Y.

Test procedure – NGS to LGS Register and lock on white light Move acq_z to 15800 (focused on dichroic beamsplitter) Illuminate the beamsplitter with a lamp Turn up the white light power to 100 (white_light on, pwr=100) Shift the spot location by noting the current location of the rotary mount and rotating 10.6mm from there (1 full turn = 1mm) Visually check the location on the video monitor Adjust the spot as necessary Y centration can be adjusted using the rotary mount; X centration can be adjusted using the linear stage directly under the dichroic mount Using acqview, grab and save a frame with the dichroic illuminated. From this frame, note the center pixel of the dichroic spot (use fitsread and atv in idl) Note the pixel locations of the edges of the spot and use these to find the center Remove lamp and turn the white light down to 50. Register and lock on the white light Turn the white light back up and using acqview, grab and save a frame of the spot From this frame, note the center pixel of the spot (use fitsread and atv in idl) Note the pixel locations of the edges of the spot and use these to find the center If the centers differ by more than 3 pixels, repeat steps 7-13 Note the final center locations

Number of 0.25” steps

| ttm_a + |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| ttm_a - |  |  |  |  |  |  |
| ttm_b + |  |  |  |  |  |  |
| ttm_b - |  |  |  |  |  |  |

Spot Pixel Coordinates

|  | Top | Bottom | Left | Right | Center |
| --- | --- | --- | --- | --- | --- |
| Dichroic 1 |  |  |  |  |  |
| WL 1 |  |  |  |  |  |
| Dichroic 2 |  |  |  |  |  |
| WL 2 |  |  |  |  |  |
| Dichroic 3 |  |  |  |  |  |
| WL 3 |  |  |  |  |  |
| Dichroic 4 |  |  |  |  |  |
| WL 4 |  |  |  |  |  |