Palomar Adaptive Optics Test Plan

| Title | LOWFS Perfomance and Optimization |
| --- | --- |
| Date | 9/6/06 |
| Lead | J. Roberts |
| Time requested | 3 hours |
| Required conditions | Nighttime, NGS |

Purpose To look at the closed loop bandwidth of the LOWFS at various frame rates To optimize the servo gains for the LOWFS

Previous analysis Wavefrot Error Budget LOWFS Calculated optimal frame rates for various magnitudes Magnitude Frame Rate Flux Predicted Bandwidth Frame Rate Flux Predicted Bandwidth 8th 1275 28720 * 51 2000 18308* 80 10th 683 8490 27 700 8290 28 12th 358 2565 14 400 2299 16 14th 177 823 7 200 729 8 16th 78 296 3 100 231 4 18th 30 124 1.2 30 122 1.2 * saturated!

Test procedure Depending on the sky brightness, acquire either an 18th mag star or a 10th mag star in the LOWFS (first center star on dichroic spot). Set log wfp=lo, data=all Set the frame rate to the first listed in Table 1 for this magnitude star. Check that the flux is approximately what is expected. If not, adjust the frame rate. Steer off and take a LOWFS sky from TAO. Take a PHARO sky as well. Set the log interval as given in Table 2. Turn on the LOWFS and take data for approximately 30sec. Take a PHARO image. Set the TT servo gain to the first value in Table 3 for this star. Lock the LOWFS on the star and take 30sec of data and take a PHARO image. Continue to change the gains. Take 30sec of data and a PHARO image for each. Open the loop and repeat steps 3-9 for the rest of the frame rates (take PHARO skys as needed) Repeat steps 1-10 on each of the following magnitudes: 14th, 12th, 16th, (10th or 18th) Table 1 Magnitude Rate 1 Flux 1 Rate 2 Flux 2 Rate 3 Flux 3 Rate 4 Flux 4 10th 500 11606 700 8290 1000 5803 1250 4642 12th 200 4599 400 2299 600 1533 800 1150 14th 100 1457 200 729 300 486 400 364 16th 30 770 50 462 100 231 150 154 18th 30 122 50 73 100 36 Table 2 Frame Rate 30-400 500-800 900-1000 1250-1500 Log Interval 1 2 3 4 Table 3 Frame Rate Gain 1 Gain 2 Gain 3 Gain 4 30-400 0.2 0.4 0.8 1 500 0.1 0.2 0.4 0.6 600 0.08 0.17 0.35 0.6 700 0.07 0.15 0.3 0.5 800 0.06 0.12 0.25 0.4 1000 0.05 0.1 0.2 0.3 1250 0.02 0.05 0.15 0.2

Results and conclusions