Action Items   Decisions

Introduction

- Questions for Directors (PW)

  - Need to make sure Shri agrees with NGAO project not holding funding contingency (or agree on the cases for which we need to hold contingency).

  - How many of the Federal dollars can we assume are from TSIP?  Is there a limit?

  - Still need to figure out whether non-TSIP proposals need to include indirect costs and whether they are part of our cost cap.  UC & CIT will ask for their share of indirect costs.

- B2C Review Success Criteria

- Change “believable” to “credible”.  Need to better quantify.

- Determine what level of re-costing we need to do for review.

- Determine to what level a design is needed versus just an approach for the review.

- Costing

- Consider others for a cost review (ideas: Palmer, McLean)

- Ask people how confident they are in their cost estimates

- Consider some mods to costing approach (i.e., cost totals on cost sheets)

- Consider other cost comparisons (i.e., GPI; GPI might be able to help with comparison)

- Observation: RD feels that we may only be able to compare ~ ¼ of our items with NFIRAOS.

Core Science Requirements

- Draft set:

  - 1) High sensitivity & sky coverage with 50% EE in < 70 mas (driven by high-z galaxies?)

  - 2) Strehl > 20% at 850 nm (driven by black holes in nearby galaxies – need kinematics?)

  - 3) Astrometric accuracy < 100 uas at K-band for SO-2 (driven by GC)

  - 4) Backup NGS mode (no worse than K2 NGS)

  - 5) IFU multiplicity is below a line

- Doesn’t include high performance IR imaging case (may be implied by 2 and 3)

- Need to think about science at J

- Can we have high sensitivity in narrow field?

- Should also take a look at science drivers to see if they impact the core science requirements.

- Decision to reduce high contrast requirements to just first requirement (just nearby, low mass brown dwarf case)

- Need a methodology for cost/benefit trade.  Focus on a few cases to understand the trades and then look at the impact on other cases.

What requirements drive cost?

- Need to also consider sensitivity.

- Agreed to take a more conservative approach to sodium density.  3E9 atoms/cm2 instead of the median of 4E6 atoms/cm2.

- Agreed not to change from median seeing conditions.

- What is cost of NGS mode?  Could we use instrument on other Nasmyth platform as backup.

- Consider the following changes:

  - N = 40 or 48, versus 64, actuators

  - Lower power PnS lasers in combination with ~50W in a modest 40-60” diameter asterism.

- Use new multi WFS tomographic error propagator for now (until we can better understand).

Cost Savings Ideas (also look at Don’s slides)

- Visible IFU, SWIFT, for Palomar cost ~$3.5M.  Could we bring to Keck in exchange for nights?  (SWIFT size ~ 18x54x36”).

- Upgrade Keck I 20W laser to CW for $2M.

- May be able to get more return from LMCT laser by being on peak of sodium line (at most a factor of 2).

- Put NGAO on K1 instead of K2.

- Consider a single relay option.

- What can we do to improve OSIRIS sensitivity?  Better grating (42% thruput).  Hawaii R2G.

- Backup visible imager option: 1kx1k MAGIQ camera with 16 bits ~$37k

- Refrigerate bench instead of enclosure.

- If we only have one movable IFS then is a field of 60 or better 40” diameter sufficient?  This could allow for a fixed modest field asterism.

- Consider getting some special filters from users.

Instrumentation

- One ADC may be worth reconsidering if we have a modest diameter field for movable IFS (same ADC could feed OSIRIS, d-IFS & NIR camera).

- Consider more of the IR imager in refrigerated space (as opposed to in the dewar).

- IR imager pixel size trade study must consider desired spatial resolution, sky background and saturation, all of which favor smaller pixels, versus read noise.  Field of view probably not a major driver.

- 30” diameter not necessary for visible imager.  15” may be sufficient.

- Need R=3000-4000 for visible IFU (driven by nearby black hole kinematics).

- The two visible IFU R~100 science cases (asteroids & brown dwarfs) shouldn’t be considered as drivers.

- Don’t need coronagraph for visible imager.

- The wavelength overlap between the IR and visible imagers allows you to have two plate scale options around 1 um.

- Default for visible imager/IFU should be a 2k (vs 4k) detector (unless we are forced to go to 1k).  Need good science arguments to go to 4k (2k fine to achieve pixel scale and field).

- Visible imager/IFU costs need to be revised.  Remove coronagraph, include full IFU costs & DRP.