NGAO Preliminary Design Phase Performance Budget Flowdown Reconciliation

Version 0.5

R. Dekany, 8/27/09

# Introduction

A number of high-level performance budget allocations and underlying assumptions, initially developed during the NGAO System Design phase, have been flowed down into a significant set of derivative subsystem performance and functional requirements.  These flowdown budgets are captured in the MS Excel workbook:

NGAO PD Phase Flowdown Budgets 2003.xls

available at the NGAO TWiki page:

http://www.oir.caltech.edu/twiki_oir/bin/view/Keck/NGAO/FlowdownSummary

The flowdown process has in some cases resulted in inconsistent subsystem requirements, revision of original allocations, and identification of new requirements heretofore unidentified.  The purpose of this memorandum is to describe the key flowdown issues and to propose feasible resolutions consistent with the NGAO science requirements.

Additional issues have been identified and will be tracked in subsequent revision to the version-controlled flowdown budgets .xls file.

# Key issues

## Surface Optical Transmission

The predicted reflectivity and transmissivity of all NGAO optical surfaces is captured in worksheets prefaced by “Trans”, for various optical paths.  To make these internally consistent, we propose the following be used consistently:

| Proposed resolution | Unresolved issue for later |
| --- | --- |
| Keck 1 M1 reflectivity = RM1() = RAL() * (1 – 5% (dust loss)) where RAl is the reflectivity of Al Keck 1 M2 reflectivity = RM1() = RAL() * (1 – 2% (dust loss)) where RAl is the reflectivity of Al Keck 1 M3 reflectivity = RM1() = RAL() * (1 – 4% (dust loss)) where RAl is the reflectivity of Al 1st window transmission = TW1() = TAR() * (1 –2% (dust loss)) where TAR is the anti-reflection coated transmission All 589 nm ‘laser enhanced’ reflections = RNa = 99.4% All 589 nm ‘laser enhanced’ transmissions = TNa = 98.9% Dust / degradation loss on LGSF optical surfaces = (1 – 0.5% (dust loss)) Dust / degradation loss on all AO system optical surfaces = (1 – 0.5% (dust loss)) Cold stop losses = (1 – 2% (undersizing loss)) for all wavelengths | Gaussian beam losses arising from LGS uplink finite apertures Losses due to near-field propagation of initial optical surface phase errors scattering to vignette angles at later NGAO optical surfaces Laser system power division (depending upon # of lasers and ultimate power distribution into the 7 LGS beacons) Will there be requirements flowed down for optical ghost brightness, particularly from optical filters? |

## System Optical Transmission

Based on coating data believed to be reliable, the system transmission requirements are proposed to be modified as follows:

| Optical path | Old value | New value |
| --- | --- | --- |
| LGSF | 0.75 | 0.60 |
| Fixed Asterism LGS HOWFS | 0.35 | 0.50 |
| PnS Asterism LGS HOWFS | 0.35 | 0.50 |
| LOWFS | 0.32 | 0.30 |

## System Emissivity

Inclusion of coating data to the emissivity budget, updating of the surface counts to reflect the B2C design, and possible other changes to the emissivity calculation have resulted in a change optical surface temperature required to meet the requirement to not exceed the sky+telescope in K-band by more than 30%:

| Term | Old value | New value |
| --- | --- | --- |
| Internal enclosure temperature | -15C (TBC) | -18C |

## Servo Bandwidth Error

The flowdown for compute latency differs significantly between performance budgets:

| Term | WFE budget | High-contrast budget | Proposed resolution |
| --- | --- | --- | --- |
| Allowable servo lag error | 59 nm rms | 30 nm rms | -- |
| Compute latency (non-readout) | 300 microsecond centroiding 400 microsecond tomography 200 microsecond DM cmd calc 950 microseconds total | 300 microseconds total | 600 microseconds total |
| ½ DM hold latency | ½ frame integration time included in servo latency calculation | ½ frame integration time not included | TBD |

## Tomography Error

The B2C tomography error is unchanged by the flowdown process, but it remains one of our most difficult requirements (due to the large disconnect with proven, on-sky tomography error performance)

| Term | Requirement |
| --- | --- |
| Residual tomography error from fixed 3+1 Na LGS beacon asterism | 37 nm, rms |

## Tracking and Dither Errors

| Term | Old value | New value |
| --- | --- | --- |
| Dither precision | -- | TBD; not yet flowed down |
| Non-common-path tracking error for T = 3600 second exposure | 5 mas / hr | 13.6 mas / hr implying optical bench temperature variation less than 1C per hr |

## Calibration

| Term | Previous value | Proposed value / comment |
| --- | --- | --- |
| AO system optical surface figure quality |  /10 to  /50 |  /20 for most surfaces with /10 allowed for cost drivers |
| LODM stroke allocated to correcting telescope, AO system, and instrument aberrations | 0.7 microns peak-to-valley | 1.4 microns peak-to-valley |
| Stale reconstructor error | 15 nm, rms | Same, but flowdown implication for the NGAO high-level control and RTC software has not been performed. |
| Quasi-static WFE | -- | 50 nm rms before AO correction (all frequencies) 20 nm rms low-spatial-freq error after correction 10 nm rms mid-spatial freq error after correction |
| Dynamic WFS Zero-point Calibration Error | 40 nm, rms | The implication of this requirement has not yet been flowed down to calibration and design requirements on the WFS. It is believe the current 4x4 pixel per subap design, with center projection, will enable this but it remains unproven. |

## TTFA Focus and Astigmatism Errors

The accuracy requirement for the measurement of focus and astigmatism terms in by the TTFA has not yet been flowed down:

| Term | Requirement |
| --- | --- |
| TTFA focus and astigmatism measurement error | TBD |

## Laser Beacon Spot Size

| Term | Old value | New value |
| --- | --- | --- |
| Laser beam FWHM due to inherent laser beam quality and BTO and LLT optics | 900 mas due to laser, BTO, and LLT only | The flowdown based on BTO surface quality assumptions resulted in a much smaller value (600 mas, including atmospheric errors) We propose to leave this at 900 mas pending better understanding |
| LGS beacon FWHM measured on the HOWFS | 1300 mas from all sources |  |

## Anti-aliasing

The implication to the high-contrast error budget of wavefront aliasing in the fixed asterism HOWFS is not well understood:

| Term | Issue |
| --- | --- |
| Aliasing of high spatial frequency errors into mid-spatial frequency errors | Approximately 77 nm * 0.33 = 25 nm, rms of aliasing error is expected |

## WFE Budget Reorganization

To better reflect the design of the NGAO system, we propose renaming several of the high-level WFE budget terms:

| Term | Former | Proposed / Comment |
| --- | --- | --- |
| Leaky integrator zero-point calibration error | 15 nm allocation | The relevance of this terms will depend on the details of the servo control implementation; for now retain as is but resolve before flowdown v2 |
| HOWFS Pupil Misregistrations | DM-to-lenslet Misregistration and DM-to-lenslet Pupil Scale Error | Propose to replace two former errors allocated a total of 21 nm, rms with a single term at 21 nm, rms (further flowdown requiring detailed modeling) |
| PnS HOWFS Pupil Misregistrations | DM-to-lenslet Misregistration and DM-to-lenslet Pupil Scale Error in LOWFS sharpening budget | Propose to replace two former errors allocated a total of 21 nm, rms with a single term at 35 nm, rms |
| Non-common-path tracking errors | Science Instrument Mechanical Drift & Long-exposure Field Rotation Errors | Propose to replace two former errors with an allocation based on a more comprehensive NCP tracking budget |

## Relative Astrometric Accuracy

An initial flowdown of relative astrometric accuracy has been developed for both spares and crowded (e.g. galactic center) fields.  We continue to struggle with the construction of a clean flowdown that captures the various real-world observing issues (various observations at the GC, for example, require different calibrations, different observing cadences, etc.)  The draft flowdowns should be reviewed for feedback at the Sept 2, 2009 team meeting.

## System Uptime

The implication of the initial flowdown of the system uptime high-level requirement is not yet understood.  The initial interpretation is that numerous systems will require MTBF of 2000 hours or more.  Identification of the driving reliability issues in the NGAO system should be a high priority, starting with this flowdown.

## Observing Efficiency

The time allocations for setting up both LGS AO observations and NGS AO observations have been flowed down, but the relatively challenge of meeting these allocations and the implied speed and latency requirements on software and mechanisms remains unknown.

# Footnotes

The flowdown emissivity calculations should be made consistent with the same dust level assumptions established for optical transmission calculations.

Excepting the NGAO first window (see above).

For zenith pointing.

Based only as a performance compromise – requires detailed design consideration and understand of implementation costs

Implied by the high-level requirement on non-correctable AO system aberrations.

Even at this level, DM stroke error is negligible, even in 37.5th percentile seeing conditions.

The efficacy of an anti-aliasing spatial filter for the fixed asterism HOWFS field stop is unclear.  The LGS will generally not be sharpened strongly in the fixed asterism HOWFS.