MRI: Development of an Improved Keck II Laser Launch Facility

Enhancing the Scientific Return of Keck Laser Guide Star Adaptive Optics

A proposal to the National Science Foundation

Major Research Instrumentation Program

Program Solicitation: NSF 09-502

Closing Date: January 22, 2009

Principal Investigator:

Peter Wizinowich, W. M. Keck Observatory

Scientific Collaborators:

Andrea Ghez, University of California Los Angeles

Michael Liu, University of Hawaii

Claire Max, University of California Santa Cruz

Authorized Organizational Representative:

________________________

Sean Adkins

W. M. Keck Observatory

The AOR of each organization involved in this proposal is aware of this submission.

# Project Summary

This instrument development proposal is intended to provide a new laser launch capability for the W. M. Keck Observatory’s (WMKO) laser guide star (LGS) adaptive optics (AO) facility on the Keck II telescope.  Our proposed approach is to replace the existing side launch laser facility with a new center launch facility which will produce notably improved scientific performance.

Background:  The twin 10 m Keck telescopes were the first of a new generation of ground-based, large optical/infrared telescopes, offering major improvement in light gathering power and angular resolution.  WMKO was also the first to implement both natural guide star (NGS) and LGS AO systems in order to achieve angular resolutions in the near-infrared that match the capabilities of the Hubble Space Telescope in the visible.  Over two hundred refereed science papers have been produced using the Keck AO systems, including fifty-five with the more recently installed LGS AO system.  Astronomy with LGS AO is still very new, with less than 10 peer-reviewed papers from other observatories.  The WMKO 2002 Strategic Plan identified “Maintaining world leadership in high angular resolution astronomy” as a 20-year strategic goal paramount to the Observatory’s mission.  The WMKO 2008 Strategic Plan reiterates the importance of AO to the Observatory’s future with a strong priority given to the Observatory’s Next Generation AO (NGAO) facility: “NGAO will reinvent Keck”.  In this proposal we describe a new laser launch facility for the Keck II LGS AO system that will significantly increase the existing system’s scientific return in the near-term and which will directly support NGAO in the longer term.

Intellectual Merit:  In addition to providing the first NGS and LGS AO facilities on a large telescope, WMKO has endeavored to continually improve the scientific performance and capabilities of these systems.  The resultant scientific attractiveness of these facilities has been commented on by many observers, including the following recent quote from Dr. Bruce Macintosh: “As I get more access to data from other observatories, it’s clear that Keck unambiguously has the best AO system of any telescope in the world.” Every significant new AO improvement has triggered new discoveries by our observers from the structure of the rings of Uranus, to the search for extrasolar planets, to the size and nature of the environment around the black hole at the center of our galaxy, to the morphology of high-redshift galaxies.  All Keck II LGS AO science would benefit from the proposed upgrade which is predicted to provide sensitivity improvements of up to 65% and factors of up to two in both photometric and astrometric accuracy (e.g., 2x in astrometry leads to 8x in dynamical mass determination accuracy).

Technical Improvements: The Keck II LGS AO facility currently projects the laser from the side of the telescope.   This results in significant perspective elongation as seen by the AO wavefront sensor due to the finite thickness of the sodium layer.  We will significantly improve the resultant wavefront sensor measurement error by projecting the laser from behind the telescope’s secondary mirror.  This requires the procurement and installation of a compact reflective launch telescope and the implementation of a beam transport system between the existing laser and the launch telescope.  In addition to providing improved scientific productivity in the near-term, we will also design and implement the overall system so that it is easily upgradeable to our future NGAO multiple LGS system.

Broader Impacts:  The significantly improved science capabilities of the Keck II AO facility produced through this proposal will be directly available to a broad community of astronomers including those in the Caltech, University of California and University of Hawaii communities through their time allocation committees.  The entire U.S. community will have access through NASA membership in the WMKO partnership and the NSF-funded National Optical Astronomy Observatory’s Telescope System Instrumentation Program.  WMKO will reinforce its role in the training of world experts in the field of LGS AO.  WMKO will also continue to offer educational programs and services to work with local residents, educators and especially students, including its strong participation in the Akamai Workforce Initiative aimed at local Hawaii university and community college students.

# Table of Contents

Project Summary	i

Table of Contents	ii

Project Description	1

Section A - Research Activities	1

A.1	Background and Past Science Achievements with Keck Adaptive Optics	1

A.2	Future Science Opportunities with a New Laser Launch Facility at Keck II	1

A.3	Personnel	5

A.4	Results from Prior NSF MRI Support	5

Section B - Description of Research Instrumentation and Needs	5

B.1	Current Keck II Laser Launch Facility	5

B.2	Planned Keck I Laser Launch Facility	6

B.3	Proposed Keck II Laser Launch Facility Upgrade	7

B.4	Predicted Performance	8

B.5	Science Instruments	10

B.6	Next Generation Adaptive Optics	10

Section C - Impact of Research and Training Infrastructure	11

Section D - Management Plan	13

D.1	Project Plan	13

D.2	Schedule	14

D.3	Project Structure, Organization and Management	14

D.4	Risk Assessment and Management	15

References Cited	16

Biographical Sketches	19

Other Personnel	31

Budget and Budget Justification	32

Current and Pending Support	35

List of Suggested Reviewers	50

# Project Description

## Research Activities

### Background and Past Science Achievements with Keck Adaptive Optics

Galileo’s (1610) application of the telescope to astronomy led to a number of revolutionary discoveries. These discoveries, including the phases of Venus and the resolution of the Milky Way into stars, were enabled by the roughly ten-fold increase of angular resolution compared to the naked eye. Over time progressively larger and larger optical telescopes, culminating with the Keck I 10 m telescope in 1992, afforded the detection of progressively fainter objects.  However, significant improvements over Galileo’s angular resolution for most objects had to wait until the successful implementation of Adaptive Optics (AO) to correct for the optical distortions introduced by turbulence in the earth’s atmosphere.

The first implementation of AO on a large (8 to 10 m) telescope was made on the Keck II telescope (Wizinowich et al., 2000) and has produced a greater than 10 fold improvement in angular resolution over seeing-limited observations.  While this early implementation relied on a bright natural guide star (NGS) to measure the atmospheric turbulence, and therefore was limited to only a small fraction of the sky, it has produced many dramatic results including the first image of a planetary system (Figure 1) beyond our own (Marois et al., 2008).

Figure 1: The first image of a planetary system beyond our own: HR 8799 imaged with Keck II AO

The first implementation of laser guide star (LGS) AO on a large telescope was also made on the Keck II telescope (Wizinowich et al., 2006; van Dam et al., 2006).  LGS AO provided the W. M. Keck Observatory (WMKO) science community with the ability to achieve high angular resolution observations over most of the sky and has enabled a wide range of science that was previously not feasible from ground-based and/or space-based observatories (Keck II’s LGS AO resolution in the near-infrared exceeds that of HST by a factor of four, the ratio of the two telescopes’ diameters).

Scientific productivity has steadily increased since the LGS AO system became available for science in 2004.  In 2008 a total of 23 refereed science papers were published with data from the Keck II LGS AO facility and a total of 99 science nights were allocated by the various WMKO time allocation committees for LGS AO science.  The performance of this system has steadily improved over the last three years as the system reliability and observing efficiency has been improved.  A $2M grant from the W. M. Keck Foundation to upgrade the AO system’s real-time controller and camera was completed in 2007 and provides a significant performance improvement for both NGS and LGS AO science.

### Future Science Opportunities with a New Laser Launch Facility at Keck II

The next logical step in performance improvement is to install a laser launch telescope behind the Keck II telescope’s secondary mirror so that it is centered on the telescope aperture.  This would reduce the perspective elongation of the LGS image by a factor of two.  All science with the Keck II LGS AO facility is expected to significantly benefit from this upgrade as discussed in section B.4.  The topics discussed in the remainder of this section provide an overview of a few of the key science areas that will benefit from the improvement of the Keck II LGS launch facility.

#### Brown Dwarfs and Low Mass Stars in Binary Systems

Residing at the extremes of luminosity (Lbol <~ 10-4Lsun) and temperature (Teff <~ 2000 K), brown dwarfs are key laboratories for understanding the continuum of physics that governs objects from low-mass stars down to gas-giant planets.  About 15% of brown dwarfs are small-separation (<~ 0.3") binaries and thus require high angular resolution imaging to study.  While at face value these are relatively simple systems, in fact ultracool binaries have proven to be unusually rich laboratories for probing the formation and physical properties of brown dwarfs.

Keck II LGS AO has proven to be a very powerful and unique tool for understanding the properties of brown dwarfs and thereby test theoretical models of their evolution and atmospheres, constituting about ¼ of all Keck II LGS refereed papers published so far, including six in 2008.  Recent studies have probed the spectral properties of brown dwarfs as they evolve from the warmer L-type dwarfs to cooler T-type dwarfs (e.g. Liu et al 2006; Leggett et al 2008).  Keck II LGS has also lead the way in searches for the very coolest brown dwarfs as binary companions to known brown dwarfs, achieving sensitivity to objects as cool as 400 K (Chiu et al., 2008; Delorme et al., 2008).

Perhaps the most promising direct tests of the theory will come from precise measurements of the fundamental properties of low mass stars and brown dwarfs (e.g. see review by Liu et al 2008a).  Many of these measurements are coming directly from Keck II LGS AO.  The first dynamical mass measurement for a binary T dwarf, the coolest class of brown dwarfs, was carried out using Keck II LGS AO (Figure 2; Liu et al., 2008b).  This is the second directly confirmed field brown dwarf binary and the coolest, lowest mass binary (Mtotal = 59 Jupiter masses; Teff = 1000 K) with a dynamical mass determination to date. The mass determination accuracy strongly depends on the accuracy with which the orbital positions and relative size of the binary components can be measured (Mtotal ~ (3). Therefore, the predicted factor of two accuracy improvement with the new launch facility (section B.4) will be a major gain for this science.

Figure 2: Orbit and dynamical mass determination for a field brown dwarf binary using Keck II LGS AO data and HST data (Liu et al., 2008)

#### The Galactic Center: Black Holes and Young Stars

The proximity of our Galaxy’s center presents a unique opportunity to study a massive black hole and its environs with much higher spatial resolution than can be brought to bear on any other galaxy.  Keck  telescope Galactic Center (GC) observations began with speckle imaging and then moved onto NGS AO and finally LGS AO observations (Figure 3). Keck high resolution observations have allowed the case for a super massive black hole (SBMH) at the GC to go from a possibility to a certainty, thanks to the recent determinations of individual stellar orbits (e.g., Ghez et al., 1998, 2005, 2008).  Furthermore, with each subsequent performance improvement new discoveries have been made.  Within the past year GC publications obtained with Keck II LGS AO have included studies of the puzzling problem of how young stars form in the immediate vicinity of the central SBMH (Stolte et al., 2008; Lu et al., 2009), measurements of the distance to the black hole and understanding the Galaxy’s central gravitational potential (Ghez et al., 2008), and understanding the characteristics of the under-luminous emission associated with the central black hole (Marrone et al., 2008; Meyer et al., 2008; Do et al., 2009).

Figure 3: Left: Color composite (H, K’, L’) Keck II LGS AO 10" x10" image of the Galactic Center.  Three times more stars are visible close to the black hole (i.e., Sgr A*) than with NGS AO.  Right: The positions of several stars orbiting the black hole are plotted proceeding from light to dark.  Several new short-period stars (Ghez et al., in prep.) have been discovered with Keck II LGS AO, doubling the number of stars that give independent estimates of the black hole’s properties and that can control for source confusion.  Among the new stars is the shortest orbital period measured to date (11 years for S0-37).  Stars discovered with speckle imaging are detected between 1995 and 2008, while those discovered with LGS AO have a time baseline of 2005 to 2008.  The new laser launch facility will detect even more sources and further reduce source confusion, which is still the dominant source of uncertainty.

By delivering higher Strehl ratios (see section B.4), the new center launch facility offers a promising new era of discovery in GC research by reducing stellar confusion, which limits the current astrometric measurements in this region.  Our scientific goals are to (1) obtain a precision measurement of the Galaxy's central potential with stellar orbits, which will provide, in the near-term, the first measurement of the distance to the Galactic center (Ro) to 1% accuracy as well as strong constraints on, or possible measurements of, an intermediate-mass black hole companion to the SBMH and, in the long-term, a test of general relativity and a detection of the extended dark matter distribution around the SMBH, (2) test and discriminate between theories of star formation in the extreme environment of the center of our Galaxy, using stellar kinematics, and (3) measure the detailed structure of a dynamically relaxed stellar cusp around a SMBH, an essential input into models for the growth of nuclear black holes.

#### Extragalactic Astronomy: Galaxy Morphology and Supernovae

LGS AO has greatly expanded the application of high angular resolution to the realm of extragalactic astronomy.  Prior to the advent of LGS AO only a modest number of extragalactic sources located near sufficiently bright NGS could be studied.  In the Deep Fields generally used for multi-wavelength observations of high-redshift galaxies (GOODS, COSMOS, EGS, etc.) there are not enough stars brighter than 14th magnitude to make use of NGS AO to complement observations at other wavelengths.  As a result, a total of only 15 extragalactic science papers were published based on Keck II AO observations between 2000 and 2006.  The publication rate ramped up to 10 papers in 2007 and 13 in 2008 alone, as extragalactic astronomers have begun to make use of the power of Keck II LGS AO to observe targets anywhere in the sky.  The new laser launch facility will enable LGS AO to be even more productive for extragalactic science.

Studies of the morphology of galaxies published with Keck II LGS AO data in the past year have included the morphology for a wide variety of galaxies at z ~ 1.5 to 2.5 (Stockton et al., 2008; van Dokkum et al., 2008; Melbourne et al., 2008a), star formation and stellar populations in galaxies (Melbourne et al., 2008b; Ammons et al., 2009), bulge and disk colors (Steinbring et al., 2008) and properties of a gravitationally lensing galaxy (Auger et al., 2008).  In the CfAO Treasury Survey (Steinbring et al., 2008) over 400 galaxies at 0.5 < z < 1.5 have been observed and their morphologies analyzed. The higher Strehl of the proposed center launch laser facility will allow quantitative determination of features such as the evolution of the bulge-to-disk ratio in galaxies at Z < 2, as well as spatially resolved kinematics of star-forming galaxies at higher signal-to-noise ratio than is currently possible.

The ability of Keck II LGS AO to look nearly anywhere in the sky with high angular resolution has also enabled the near-IR characterization of supernovae and gamma ray bursts.  For example, LGS AO was used to great effect for identification of the progenitor stars of Type II supernovae by combining Keck II LGS imaging of the supernova with pre-explosion HST archive images (Gal-Yam et al., 2007).  Five papers on related topics were published in 2008 using Keck II LGS AO.  One example is shown in Figure 4. The higher point source sensitivity available with the new center launch facility (see section B.4) will be key to broader application of LGS AO for high-z supernovae and gamma ray bursts.

Figure 4: False-color IR image of the core of NGC 1260 and Supernova 2006gy generated from Keck II LGS H and K(-band observations (Smith et al., 2008)

#### Solar System Astronomy

Keck II LGS AO observations have enabled the identification of small moons around Jupiter’s Trojan asteroids and Kuiper Belt Objects and subsequent direct density determinations (Marchis et al., 2006; Brown et al., 2005 and 2006).  The predicted improvements in sensitivity and positional accuracy with the new center launch facility (see section B.4) will greatly assist in the detection and characterization of these small moons.  This science is important in understanding the nature of the early solar system.

### Personnel

The Keck II LGS AO system with the new launch facility will be available to a large fraction of the U.S. astronomical community as described in section C.  The scientific collaborators on this proposal are frequent users of the Keck II LGS AO facility and will work with the WMKO team to characterize and document the scientific performance of the improved LGS AO facility for their research.  For example, Liu has utilized his brown dwarf imaging survey to characterize the scientific performance of the Keck II LGS AO system (Liu, 2008) and Ghez’s team has worked to understand and improve the factors limiting the astrometric performance of the system on the Galactic Center (Lu et al., 2009).

### Results from Prior NSF MRI Support

Wizinowich is the PI, and Ghez is a collaborator, for the NSF MRI awarded proposal entitled ‘Development of the Keck Interferometer with Laser Guide Star Adaptive Optics for Microarcsecond Astrometry – from Exoplanets to Black Holes’ that was awarded in 2006.  The first scientific results at high spectral resolution (R ~ 1800) using self phased referenced interferometry are currently being written up for publication, including observations of the dust and gas within 1 AU of young stars (Eisner et al., 2009) and the disk around a Be star (Woillez et al., 2009).  The interferometer upgrade is continuing with the implementation of dual field phase referencing and astrometry modes (Pott et al., 2008a,b), with both modes planned to be in place by the end of the four year award period.

## Description of Research Instrumentation and Needs

### Current Keck II Laser Launch Facility

In an LGS system like that of the Keck  II telescope (Wizinowich, 2005) a laser tuned to the wavelength of the D2 line of atomic sodium is used to excite sodium atoms in the earth’s mesosphere, located at an altitude of ~90 km.  These atoms re-emit 589 nm light to produce a LGS that can be used as an artificial source for measurements of the atmospheric turbulence by a wavefront sensor.  Due to its double pass through the atmosphere the LGS does not properly sense tip and tilt, and due to the changing altitude of the sodium layer it does not adequately sense focus.  A NGS for tip, tilt and (slow) focus correction is therefore still needed for LGS operations, but it can be significantly fainter than the ~14th magnitude guide star required for NGS AO (by ~ 4 magnitudes).

Figure 5: Left: Schematic showing 1st stage of Keck II laser in room on dome floor, dye laser table on the telescope, and launch lens side-mounted at the top of the telescope.  Right: Side launch of laser.

The final stage of the Keck II laser, the dye laser table, is mounted to the elevation ring of the telescope as shown in Figure 5 and Figure 6.  The first element of the laser launch telescope is mounted on the dye laser table.  The second element of the laser launch telescope is a 50 cm launch lens mounted at the top of the telescope.  Due to the finite thickness of the sodium layer (~20 km thick), side projection of the laser results in the elongated LGS images obtained by the Keck II telescope shown in Figure 7.  Reduction of this perspective elongation, which significantly degrades performance, is the primary purpose of this proposal.

Figure 6: Left: Dye laser table mounted on the telescope elevation ring. Right: Tube leading from the top of the dye laser table to the 50 cm launch lens at the outer edge of the top of the telescope

Figure 7: Left: The LGS image has a FWHM of 1.6" x 2.0".  Middle: The LGS image with the 36 primary mirror segments unstacked.  The individual segments closest to the projector can have FWHM as small as 1.0" , while the segment images further away are elongated toward the projection point.  Right: The circled segment image was used to produce this relative density structure versus altitude plot for the sodium layer.

### Planned Keck I Laser Launch Facility

We are in the process of upgrading the Keck I NGS AO facility to LGS capability.  Toward this end a mode-locked CW laser (Lee et al., 2008) will be installed on the Nasmyth platform of the Keck I telescope in 2009 and a center launch laser facility will be implemented.  This launch facility includes a beam injection module on the laser table, a single mode photonics crystal fiber to transport the beam to the top end of the Keck I telescope, a beam transport optical bench (BTOB) to extract the beam from the fiber and reformat it for the launch telescope, and a launch telescope.  A schematic of the launch telescope mounted to the back end of the Keck telescope secondary mirror module is shown in Figure 8; the beam transport optical bench is mounted to top of the launch telescope in this Figure.  The launch telescope was fabricated by Galileo Avionica and will be shipped to WMKO in January, 2009.

Figure 8: Schematic of the Keck I launch telescope mounted to the rear of the secondary module

### Proposed Keck II Laser Launch Facility Upgrade

This section describes the development activity we propose to perform with MRI funding.  The primary differences between the proposed Keck II launch facility upgrade and the Keck I launch facility are:

- On Keck II the laser is mounted on the part of the telescope that moves (tilts) in elevation.  On Keck I the laser will be mounted such that it is stationary with respect to gravity.

- Free space propagation must be used on Keck II since the pulse format of the Keck II laser cannot be handled by a single mode fiber.  Keck I will use a fiber for laser beam transport.

- We will design the part of the beam transport system mounted to the launch telescope (the BTOB for Keck I) and the launch telescope so that they are compatible with a future upgrade to multiple LGS in support of NGAO.

- We propose to improve the launch telescope so that its focus is less sensitive to temperature.

The major activities of this development effort are the following:

- Procurement of the launch telescope.

- Modifications to the existing secondary mirror module to accommodate the launch telescope.

- Design and implementation of a new beam transport system between the existing dye laser table and the launch telescope, including a beam transport optical bench mounted to the launch telescope, and associated laser steering hardware and software to control laser pointing and focus, including flexure and temperature compensation.

- Modifications to the existing laser safety system and laser traffic control system to accommodate the center launch facility.

- Laboratory integration and test of as much of the system as practical, including the launch telescope, beam transport system and motion control.

- Removal of the existing laser side launch system hardware.

- Telescope integration and test of the new hardware with the existing laser and AO control system, including on-sky performance characterization.

- Handover of the new system to daytime and nighttime operations personnel.

We estimate that three telescope nights will be required over one observing semester to perform on-sky integration and test of the new launch facility and to characterize the performance of the upgraded LGS AO facility.  These nights will be provided from Observatory engineering time.

### Predicted Performance

Scientific productivity depends on such items as sensitivity, photometric accuracy, and astrometric accuracy.  These parameters are in turn dependent on the wavefront quality, traditionally reported as wavefront error or as Strehl ratio (the Strehl ratio is the ratio of the energy in the diffraction-limited core of an image to that in a perfect diffraction-limited image), delivered to the science detector.  In this section we first show how the wavefront error and Strehl will be improved with the center launch system and then discuss how this will impact the science.  We predict performance improvement by factors of up to 1.65 in point-source sensitivity and factors of two in both photometric and astrometric accuracy.

Table 1 shows the wavefront error budget for the existing Keck II LGS AO system and the predicted performance with the new center launch laser for two cases: the case of a bright NGS and median seeing conditions, and the LGS AO T dwarf binary case (with a faint off-axis NGS for tip-tilt) discussed in section A.2.1.  The DM (Deformable Mirror) measurement and bandwidth errors are interrelated and together make up the largest term in the error budget.  The reduction in the LGS elongation by a factor of two results in a significant reduction in the measurement error.  This reduced measurement error allows the bandwidth error to be reduced by running the system faster until the two terms are roughly matched.

Table 1: Keck II LGS AO wavefront error budget for side and center launch for two science cases

The asymmetric LGS elongation of the existing side launched laser, shown in Figure 7, rotates as a function of telescope elevation and AO image rotator angle.  The length and structure of the LGS images depend on variations in the sodium layer thickness and structure.  These changes result in variations in the optimal gain and centroid position for each wavefront sensor subaperture.  Reduced LGS elongation will result in less sensitivity to these changes.  In addition, axial symmetry will make the wavefront sensor subaperture optimal gains and centroids rotation independent. Currently we correct for the optimal centroid variations by observing a natural star with a low bandwidth wavefront sensor.  Center launching would allow fainter NGS to be used for low order correction since lower update rates should now be acceptable for this purpose (the low bandwidth wavefront sensor is also needed for focus corrections as the altitude of the sodium layer changes).  These impacts of a centrally projected laser are included in the error budget by reducing the LGS focus and higher order errors introduced by the elongated laser spots.

The resultant Strehl ratio is increased by ~20% by moving the laser from off-axis to on-axis for the case of a bright tip-tilt star and by ~50% for the T dwarf binary case discussed in section A.2.1 (i.e., 50( zenith angle and a faint off-axis tip-tilt star). This produces a corresponding increase in signal to noise ratio, SNR, for AO observations of point sources for both photon-limited or background limited observations (or a Strehl2 reduction in integration time to reach the same SNR).  For LGS studies of extended sources or faint sources next to bright sources the contrast is the key requirement and will be increased by Strehl / (1 – Strehl) or ~34% in the bright NGS case and ~65% in the T dwarf binary case.  This will significantly reduce the source confusion that limits astrometric accuracy for the Galactic Center science case (section A.2.2).

Figure 9: Positional (top) and photometric (bottom) errors (diamonds) versus Strehl from six nights of Keck II LGS AO binary T dwarf observations between May 2005 and April 2008 (Liu et al., 2008).  Predictions (squares) are extrapolations based on the improvement in Strehl ratio with a center launch laser.

The accuracy of the T dwarf binary measurements shown in Figure 2 is strongly dependent on the Strehl ratio delivered by the AO system as can be seen from the data plotted in Figure 9.  The predicted Strehl improvement for the T dwarf binary case (Table 1) should result in the significantly reduced (factor of two!) relative astrometric and photometric errors shown as squares in Figure 9.  A reduction in the astrometric uncertainty by a factor of 2 will mean an improvement in the uncertainty in the total mass of a binary system by a factor of 8 from Kepler’s laws (Mtotal ~ (3); a major gain for testing theoretical models!

Even greater astrometric improvements (a factor of ~1.3) are feasible because the higher performance of the new center launch facility will allow measurements to be made at shorter wavelengths (i.e., H-band instead of K), offering higher spatial resolution, on a routine basis.  Improved measurements in crowded fields (e.g., the Galactic Center) will also result because one can more easily distinguish one source from another and from the unresolved background of faint sources.

These improvements to AO performance will positively impact science productivity for all types of science.  This was clearly demonstrated by a $2M W. M. Keck Foundation funded upgrade to the AO wavefront controller (Johansson et al., 2008) completed in 2007.  This upgrade achieved its predicted 10% Strehl improvement for Keck II LGS AO observations using a bright NGS.  The scientific results have been spectacular and the WMKO user community has been extremely satisfied.

Note that focal anisoplanatism will be the largest error term for the center launch facility.  We are currently working with other observatories to implement an atmospheric turbulence profiler.  Once this profiler is in place we will look at implementing a tomography portion to our real-time controller to use profile data to determine the optimal correction to apply to the wavefront sensor centroid offsets.  Preliminary estimates indicate this could reduce the focal anisoplanatism on average by a factor of 1.3.

### Science Instruments

The new Keck II center launch LGS system will support three science instruments: a near-IR camera (NIRC2), a near-IR spectrograph (NIRSPEC) and the Keck Interferometer (KI).  (A near-IR integral field spectrograph (OSIRIS) will be supported with the Keck I LGS AO system.)  NIRC2 has been the workhorse science instrument for Keck II AO having been used for 75% of the published Keck AO papers in the last three years. It contains a 1024 x1024 pixel InSb array for science from 1 to 5 (m and offers three imaging plate scales and a grism with R ~ 4000 spectral resolution.  One of NIRC2’s key features is that it has been very well characterized with the AO system for high precision astrometric measurements such as those on the Galactic Center, binary star systems and binary asteroids.  NIRSPEC offers a high spectral resolution (R ~ 20,000) capability with AO that is unique in the world.

The KI is currently being upgraded for higher sensitivity and to implement an astrometry mode with a $2M NSF MRI grant (award 0619965) which builds on the existing significant investment by NASA.  LGS AO is currently being implemented on the Keck I telescope partially in support of this sensitivity improvement; center launching both lasers will also make the KI a more powerful facility.

### Next Generation Adaptive Optics

The proposed new laser launch facility will directly produce significant science returns.  In the longer term, we intend to make use of this new facility in our future NGAO system (Wizinowich et al., 2008).  This hybrid multi-object AO facility will consist of a multi-laser beacon system designed for high Strehl over narrow fields in the near-IR, modest Strehl at optical wavelengths, and high sky coverage.  The WMKO 2008 Strategic Plan identifies the importance of AO to the Observatory’s future with the highest priority given to the Observatory’s planned NGAO facility: “NGAO will reinvent Keck”.

NGAO is currently in the preliminary design phase with funding from the NSF Telescope System Instrumentation Program (TSIP).  The WMKO-funded system design phase was successfully completed in April, 2008.  The report of the review panel (consisting of Brent Ellerbroek, Robert Fugate, Andrea Ghez, Norbert Hubin, Gary Sanders and Nick Scoville) said: “The review panel believes that Keck Observatory has assembled an NGAO team with the necessary past experience … needed to develop the Next Generation Adaptive Optics facility for Keck.  It is a sound, though aggressive, strategy to be among the first observatories to develop and depend on advanced laser guide star AO systems as a means to maintain Keck’s leadership in ground-based observational astronomy for the immediate future.  The panel also believes that NGAO is an important pathfinder for the 2nd generation of AO based instruments for future Extremely Large Telescopes as emphasized in the ‘Roadmap for the Development of United States Astronomical Adaptive Optics’ report issued April 18th 2008.”

This proposal therefore represents an investment in an even more powerful future LGS AO science capability.  Our assessment of the recently completed Keck I launch telescope is that it will meet all of the NGAO requirements.  We will ensure that the beam transport optical bench mounted to the side of the new center launch telescope will be upgradeable to accommodate multiple laser beacons.

## Impact of Research and Training Infrastructure

A 2002 Visiting Committee of distinguished U.S. astronomers, reviewing the performance and standing of the Observatory, wrote: “The Keck Observatory has dominated ground-based...astronomy for a decade.  It is scientifically extremely productive.”  The Observatory maintains a leadership position by innovating and deploying pioneering instrumentation.  This proposal seeks to continue this trend by developing a new center launch laser facility for the Keck II LGS AO system.

The center launch Keck II LGS AO facility will enable improved observations by a large and creative astronomical community.  Access to science observing time with the Keck telescopes is determined by Time Allocation Committees (TACs) representing the institutions with direct interests in the Observatory: the California Institute of Technology (Caltech) and the University of California (UC) each with 35%, NASA with a 16.5% share and the University of Hawaii with a 12.5% share.  Through participation in TSIP, WMKO has made available 64 nights over the last three years to the National Optical Astronomy Observatory (NOAO).  In addition, exchanges with the Gemini Observatory over the last 3 years have totaled 25 nights.  The NASA, NOAO and Gemini time are directly available to the entire U.S. community. The recent ALTAIR survey to understand the needs of the U.S. community for observing resources on large telescopes identified “The highest priority was for more open access time on non-federal facilities, for both groups with and without institutional access to large telescopes,” reflecting the demand for Keck telescope access among others.  Table 2 summarizes the WMKO 2005 observing team statistics.  The observers making scientific use of WMKO in 2005 represented about 10% of the active membership of the American Astronomical Society as judged by the 3133 attendees at the January, 2006 AAS meeting, or ~ 30% of the U.S. optical/IR observer community.

Table 2: Breakdown of WMKO observers in 2005

| Affiliation | Faculty | Students & Postdocs | Total |
| --- | --- | --- | --- |
| UC/Caltech | 72 | 144 | 216 |
| UH | 21 | 29 | 50 |
| NASA community | 24 | 28 | 52 |
| NSF community | 45 | 27 | 72 |
| Total | 162 | 228 | 390 |

The demand for LGS AO has been high with an average of 98 nights assigned to LGS AO science each of the last three years (06B to 09A).  The resultant rate of refereed publications is shown in Figure 10 where the publications are divided amongst those performed with Keck II NGS AO, Keck II LGS AO and the interferometer which uses NGS AO on both Keck telescopes.  A total of 200 refereed science papers using the Keck AO facilities were published between 2000 and the end of 2008.  LGS AO science results have increased rapidly since the first LGS publication in 2005.  The impact has been significant on all fields of astronomy.  Most notably the field of extragalactic astronomy has been opened up by LGS AO with 23 publications on extragalactic science in the last two years, versus seven in the previous two years.  The variety of Keck II LGS AO science published to date can be seen in Table 3.

Figure 10: Refereed Keck AO papers published each year (note the rapid LGS AO increase)

Table 3: Types of refereed science obtained with the Keck II LGS AO system

The educational impact of a more powerful Keck LGS AO Facility can be seen by the impact of the existing AO facilities on the science research of students and postdocs.  A sampling of PhD students who participated in the 2005 papers includes: Matthew Barcys, Jay Farihi, Tiffany Glassman, Seth Hornstein, Denise Kaisler, Quinn Konopacky, Jessica Lu, Caer McCabe, Angelle Tanner & Shelley Wright (UCLA); Tracy Beck, Chad Bender & Gail Schaefer (SUNY); Antonin Bouchez, Josh Eisner, Ben Lane, Stan Metchev & Emily Schaller (Caltech); Alexis Brandeker (Stockholm Observatory), Scott Dahm (UH), James Lloyd, Shuleen Martin & Henry Roe (UCB); Jason Melbourne (UCSC); Nick Siegler (U. Arizona).  A similar sampling of postdocs who participated in these papers includes: Antonin Bouchez, Olivier Lai, David Le Mignant & Marcos van Dam (WMKO); Gaspard Duchene & Lisa Prato (UCLA); Ray Jayawardhana, Paul Kalas, Franck Marchis & Michael Wong (UCB); Michael Liu (UH); Kevin Luhman, John Monnier & Rafael Millan-Gabet (CfA), Eduardo Martin, Henry Roe, Jean-Luc Margot & Maria Rosa Zapatero Osorio (Caltech); Anne Metevier & Eric Steinbring (UCSC).

On the local level WMKO offers many educational programs and services to work with residents, educators and especially students.  Of special note is the NSF-funded Center for Adaptive Optics (CfAO) sponsored Akamai Observatory Internship Program led by WMKO, which we propose to continue past the end of the CfAO. Keck personnel will continue to participate in the Akamai short course and to mentor Hawaiian college students during their internships.

This proposal is made possible on a reasonable timescale and budget by building on significant existing and ongoing investments and expertise.  The W. M. Keck Foundation provided funding for the telescopes, the Keck II LGS AO system and the recent Keck I and II wavefront controller upgrades.  NSF is funding the Keck I laser.  WMKO operation funds are paying for the Keck I LGS AO upgrade.  The CfAO has funded two postdocs to work on Keck AO development.  The WMKO AO group led by Wizinowich has been responsible for the development of the Keck AO facilities.  The science portion of this proposal includes a very strong base of high angular resolution science expertise in the areas we wish to address (funded by other grants to individual faculty members and researchers).

The WMKO AO facilities have proven to be a powerful science research facility and an excellent training ground.  Great science, and access to the facilities to do this great science, is what will make LGS AO an increasingly critical part of the U.S. astronomy community’s toolbox.

## Management Plan

### Project Plan

The activities planned for the new Keck II center launch facility described in this proposal correspond to the elements shown in the top-level work breakdown structure of Figure 11.

Figure 11: Top level WBS

Cost estimates for this facility are based on significant current experience at WMKO in the development of complex instrumentation systems especially those used in the existing Keck AO facilities.  Project personnel were involved in making the labor estimates, which were arrived at by starting with detail level tasks and then aggregating detail level estimates into labor totals.  Costs for materials and equipment are based on recent costs for similar items for the Keck I LGS upgrade.  A quoted price is used for the launch telescope assembly.  The total proposed budget is $1,936k, 30% of which will be covered by WMKO.

WMKO’s standard development process will be followed with small revisions.  The system design phase will be absorbed into the preliminary design phase since most of the performance requirements can be taken from previous design work for both Keck I LGS AO and NGAO.  This will be followed by a detailed design phase.  The launch telescope contract will be issued early in the preliminary design phase and the contract will include a design review for modifications to the Keck I launch telescope design.

The implementation phase will include hardware fabrication and assembly and software coding and testing culminating with a laboratory testing phase that will integrate as much of the hardware and software as practical off of the telescope.  Modifications to the Keck II telescope to support the installation will also be performed during this phase.  A pre-telescope readiness review will be held prior to installing the new launch system at the telescope.  Most of the new hardware will be installed and tested prior to removing the old launch system in order to minimize LGS AO down-time.  The final phase will include performance characterization and system support during a shared-risk science observing semester.

Operations personnel will participate in the laboratory and telescope integration and test, and especially the commissioning phase, in support of knowledge transfer to the people with operational responsibility.  Operational system changes will go through engineering review by the WMKO AO configuration control board.

### Schedule

The schedule for the new center launch facility is shown in Figure 12.  The top-level elements in this schedule correspond directly to the WBS shown in Figure 11.  This is a 26 month program with a planned start date of August, 2009 and completion in September 2011.  The focus of the first nine months will be on completing the design phases and starting the launch telescope contract (Sept., 2009 with delivery in Jan., 2011).  The focus of the second nine months will be on fabricating and assembling the hardware and software and completing the lab integration and test phase.  After an April, 2011 pre-telescope readiness review, implementation of the hardware will begin at the telescope with on-sky integration, test and characterization occurring in the last three months of observing semester 11A (May to July).  TAC-allocated shared-risk science observing will occur in the first three months of 11B (August to October).

Figure 12: Proposed Project Schedule

### Project Structure, Organization and Management

WMKO will be the lead institution.  Galileo Avionica is the preferred vendor for the launch telescope contract. The organization chart for the project is shown in Figure 13, and Table 4 provides a detailed description of the project staff. This is the same team that has been successfully working to implement the Keck I LGS AO upgrade including the Keck I launch facility. Much of this team was also heavily involved in the successful completion and commissioning of the Keck II LGS AO facility.

WMKO’s normal management process will provide oversight for this project.  This includes regular status reports to WMKO’s management and Science Steering Committee. WMKO’s Office of Sponsored Programs will monitor project compliance with NSF terms and conditions, including timely reporting. Regular project meetings will be held to manage activities, discuss progress and address problems.

Figure 13: Project Organization

Table 4: Project Staff

| Position | Name | Notes |
| --- | --- | --- |
| Principal Investigator | Peter Wizinowich | As PI & AO project manager Wizinowich is responsible for the overall project success in coordination with other WMKO activities. |
| Project Scientist | Michael Liu | Liu leads the management of the science requirements for the upgrade & oversees the performance characterization phase of the project. |
| Project Manager | Jason Chin | Chin is responsible for managing the engineering team & project to meet the budget and schedule. |
| Systems Engineer | Thomas Stalcup | Stalcup manages the design process to ensure proper design choices, maintains the performance budgets, & leads the performance characterization. |
| AO Operations Manager | Randy Campbell | Campbell ensures an operational system is produced through management of the AO configuration control board & as a project review participant. |
| Leads: Medeiros (mech.), Panteleev (optical), TBD (software), Wetherell (electr.) | Engineering leads design modifications to the hardware & software systems and design/specify additional components required for the upgrade. They also lead the implementation of the upgrades. |

### Risk Assessment and Management

Table 5 summarizes the significant risk areas.  Since this is largely a repeat of the Keck I launch telescope implementation we do not anticipate surprises beyond those already encountered and addressed.  If funded this work will follow the Keck I work in a timely fashion while the lessons learned are still fresh.

Table 5: Significant risk areas

| Category | Risk Area | Likelihood | Impact | Mitigation |
| --- | --- | --- | --- | --- |
| Technical | Launch telescope does not achieve required image quality | Low | High | On-telescope Keck I launch telescope I&T will occur in 2009. Lessons learned will be fed into the Keck II launch telescope. Focus vs temperature variations will be reduced & retrofitted to Keck I. |
| Schedule | Launch telescope delivery | Med | Low | Keck I launch telescope was delivered late. Lessons learned will be applied by the vendor & Keck. Delivery slips would be known in time so as not to impact the observing schedule. |
| Budget | Budget increases due to technical problems & schedule delays | Med | Med | Track schedule & budget vs plan, anticipate problems & re-plan as needed. Reassign personnel if schedule slips & bring back as needed. |

# References Cited

[A complete bibliography of refereed Keck Adaptive Optics science papers can be found at: http://www2.keck.hawaii.edu/library/keck_papers.html]

- Ammons, S.M., Melbourne, J., Max, C.E., Koo, D.C., Rosario, D.J.V.  Spatially Resolved Stellar Populations of Eight GOODS-South Active Galactic Nuclei at z ~ 1.  AJ 137, 470-497 (2009).

- Auger, M.W., Fassnacht, C.D., Wong, K.C., Thompson, D., Matthews, K., Soifer, B.T.  Lens Galaxy Properties of SBS 1520+530: Insights from Keck Spectroscopy and AO Imaging.  ApJ 673, 778-786 (2008).

- Brown, M.E. Bouchez, A.H., Rabinowitz, D., Sari, R., Trujillo, C.A., van Dam, M., Campbell, R., Chin, J.,  Hartman, S., Johansson, E., Lafon, R., Le Mignant, D., Stomski, P., Summers, D., Wizinowich, P.  Keck Observatory Laser Guide Star Adaptive Optics Discovery and Characterization of a Satellite of the Large Kuiper Belt Object 2003 EL_61.  ApJ 632, L45-L48 (2005).

- Brown, M.E., van Dam, M., Bouchez, A., Le Mignant, D., Campbell, R., Chin, J., Conrad, A., Hartman, S., Johansson, E., Lafon, R., Rabinowitz, D., Stomski, P., Summers, D., Trujillo, C., Wizinowich, P.  Satellites of the Largest Kuiper Belt Objects.  Apj 639, L43-L46 (2006).

- Chiu, K., Liu, M.C., Jiang, L., Allers, K.N., Stark, D.P., Bunker, A., Fan, X., Glazebrook, K., Dupuy, T.J.  Four Faint T Dwarfs from the UKIRT Infrared Deep Sky Survey (UKIDSS) Southern Stripe.  MNRAS, 385, L53-L57 (2008).

- Delorme, P., Delfosse, X., Albert, L., Artigau, E., Forveille, T., Reyle, C., Allard, F., Homeier, D., Robin, A., Willott, C.J., Liu, M., Dupuy, T.  CFBDS J005910.90-011401.3: reaching the T-Y Brown Dwarf Transition.  A&A 482, 961-971 (2008).

- Do, T., Ghez, A.M., Morris, M.R., Yelda, S., Meyer, L., Lu, J.R., Hornstein, S.D., Matthews, K.  A near-IR variability study of the Galactic black hole: a red noise source with no detected periodicity.  ApJ in press (2009).

- Eisner, J., et al.  High-dispersion Interferometric Spectroscopy of Dust and Gas within 1 AU of Young Stars: Early Science from the Keck ASTRA Project.  In preparation (2009).

- Gal-Yam, A., Leonard, D.C., Fox, D.B., Cenko, S.B., Soderberg, A.M., Moon, D.S., Sand, D.J., Li, W., Filippenko, A.V., Aldering, G., Copin, Y.  On the Progenitor of SN 2005gI and the Nature of Type IIn Supernovae.  ApJ 656, 372-381 (2007).

- Ghez, A.M., Klein, B.L., Morris, M., & Becklin, E.E. High Proper Motion Stars in the Vicinity of Sgr A*: Evidence for a Supermassive Black Hole at the Center of Our Galaxy. ApJ 509, 678-686 (1998).

- Ghez, A. M., Salim, S., Hornstein, S. D., Tanner, A., Morris, M., Becklin, E. E., Duchene, G. Stellar Orbits around the Galactic Center Black Hole. ApJ, 620, 744-757 (2005).

- Ghez, A.M., Hornstein, S.D., Lu, J., Bouchez, A., Le Mignant, D., Wizinowich, P., Matthews, K., Morris, M., Becklin, E.E., Campbell, R.D., Chin, J.C.Y., van Dam, M.A., Hartman, S.K., Johansson, E.M., Lafon, R.E., Stomski, P.J., Summer, D. The First Laser Guide Star Adaptive Optics Observations of the Galactic Center: Sgr A*'s Infrared Color and the Extended Red Emission in its Vicinity.  ApJ 635, 1087-1094 (2005).

- Ghez, A.M., Salim, S., Weinberg, N.N., Lu, J.R., Do, T., Dunn, J.K., Matthews, K., Morris, M., Yelda, S., Becklin, E.E., Kremenek, T., Milosavljevic, M., Naiman, J.  Measuring Distances and Properties of the Milky Way’s Central Supermassive Black Hole with Stellar Orbits.  ApJ 689, 1044-1062 (2008).

- Johansson, E., van Dam, M., Stomski, P., Bell, J., Chin, J., Sumner, R., Wizinowich, P., Biasi, R., Andrighettoni, M., Pescoller, D.  Upgrading the Keck AO wavefront controllers.  SPIE 7015, 7015-121 (2008).

- Lee, I.,  Jalali, M., Vanasse, N., Prezkuta, Z., Groff, K., Roush, J., Rogers, N., Andrews, E., Moule, G., Tiemann, B., Hankla, A., Adkins, S., d'Orgeville, C. 20 W and 50 W guidestar laser system update for the Keck I and Gemini South telescopes. SPIE 7015, 70150N (2008).

- Leggett, S.K., Saumon, D., Albert, L., Cushing, M.C., Liu, M.C., Luhman, K.L., Marley, M.S., Kirkpatrick, J.D., Roellig, T.L., Allers, K.N.  HN Peg B: A test of models of the L to T dwarf transition.  ApJ 682, 1256-1263 (2008).

- Liu, M.C., Leggett, S.K., Golimowski, D.A., Chiu, K., Fan, X., Geballe, T., Schneider, D.P., Brinkmann, J. SDSS J1534+1615AB: A Novel T Dwarf Binary Found with Keck Laser Guide Star Adaptive Optics and the Potential Role of Binarity in the L/T Transition. ApJ 647, 1393-1404 (2006).

- Liu, M.C. LGS AO Science Impact: Present and Future Perspectives.  SPIE Proc. 7015, 7015-7 (2008).

- Liu, M.C., Dupuy, T.J., Ireland, M.J. Keck Laser Guide Star Adaptive Optics Monitoring of 2MASS J15344984-2952274AB: First Dynamical Mass Determination of a Binary T Dwarf.  ApJ 689, 436-460 (2008).

- Lu, J.R., Ghez, A.M., Hornstein, S.D., Morris, M.R., Becklin, E.E., Matthews, K. A Disk of Young Stars at the Galactic Center as Determined by Individual Stellar Orbits.  ApJ 690, 1463-1487 (2009).

- Marchis, F., Hestroffer, D., Descamps, P., Berthier, J., Bouchez, A., Campbell, R.D., Chin, J.C.Y., van Dam, M.A., Hartman, S.K., Johansson, E.M., Lafon, R.E., Le Mignant, D., de Pater, I., Stomski, P., Summers, D., Wizinowich, P., Wong, M.H.  Multiplicity in the Jupiter Trojan Population: Low density of 617 Patroclus with Keck LGS AO and Perspective.  Nature 439, 565-567 (2006).

- Marois, C., Macintosh, B., Barman, T., Zuckerman, B., Song, I., Patience, J., Lafreniere, D., Doyon, R. Direct Imaging of Multiple Planets Orbiting the Star HR 8799. Science (Nov., 2008)

- Marrone, D.P., Baganoff, F.K., Morris, M.R., Moran, J.M., Ghez, A.M., Hornstein, S.D., Munoz, D.J., Bautz, M.W., Ricker, G.R., Brandt, W.N, Garmire, G.P., Lu, J.R., Matthews, K., Zhao, J.-H., Rao, R., Bower, G.C.  An X-Ray, Infrared, and Submillimeter Flare of Sagittarious A*.  ApJ 682, 373-383 (2008).

- Melbourne, J., Ammons, M., Wright, S.A., Metevier, A., Steinbring, E., Max, C., Koo, D.C., Larkin, J.E., Barcyz, M.  Triggered or Self-Regulated Star Formation within Intermediate Redshift Luminous Infrared Galaxies. I. Morphologies and Spectral Energy Distributions.  AJ 135, 1207-1224 (2008).

- Melbourne, J., Desai, V., Armus, L., Dey, A., Brand, K., Thompson, D., Soifer, B.T., Matthews, K., Jannuzi, B.T., Houck, J.R.  Morphologies of High-Redshift, Dust-Obscured Galaxies from Keck Laser Guide Star Adaptive Optics.  AJ 136, 1110-1117 (2008).

- Myer, L., Do, T., Ghez, A., Morris, M.R., Witzel, G., Eckart, A., Belanger, G., Schoedel, R. A 600 minute near-infrared lightcurve of Sagittarius A*.  ApJ 688, L17-L20 (2008).

- Pott, J-U., Woillez, J., Wizinowich, P., Eckart, A., Glindemann, A., Ghez, A., Graham, J. First spectro-interferometry on galactic center sources in the infrared: results and science prospects at the sensitivity limit of current large aperture arrays.  SPIE Proc. 7013-73 (2008).

- Pott, J-U., Woillez, J., Akeson, R., Berkey, B., Colavita, M., Cooper, A., Eisner, J., Ghez, A., Graham, J., Hillenbrand, L., Hrynevych, M., Medeiros, D., Millan-Gabet, R., Monnier, J., Morrison, D., Panteleeva, T., Quataert, E., Randolph, B., Smith, B., Summers, K. Tsubota, K., Tyau, C., Weinberg, N., Wetherell, E., Wizinowich, P. Astrometry with the Keck Interferometer: the ASTRA project and its science.  Astrometry and Imaging with the Very Large Telescope Interferometer, Keszthely, Hungary (2008).

- Smith, N., Foley, R.J., Bloom, J.S., Li, W., Filippenko, A.V., Gavazzi, R., Ghez, A., Konopacky, Q., Malkan, M., Marshall, P.J., Treu, T., Woo, J-H.  Late-Time Observations of SN 2006gy: Still Going Strong.  ApJ 686, 485-491 (2008).

- Steinbring, E., Melbourne, J., Metevier, A.J., Koo, D.C., Chun, M.R., Simard, L., Larkin, J.E., Max, C.E. CATS: Optical to Near-Infrared Colors of the Bulge and Disk of Two Z = 0.7 Galaxies using Hubble Space Telescope and Keck Laser Guide Star Imaging.  AJ 136, 1523-1532 (2008).

- Stockton, a., McGrath, E., Canalizo, G., Iye, M., Maihara, T.  Morphologies of Two Massive Old Galaxies at z ~ 2.5.  ApJ 672, 146-152 (2008)

- Stolte, A., Ghez, A.M., Morris, M., Lu, J.R., Brandner, W., Matthews, K.  The proper motion of the Arches cluster with Keck Laser-Guide Star Adaptive Optics.  ApJ 675, 1278-1292 (2008).

- van Dam, M. Bouchez, A., Le Mignant, D., Johansson, E., Wizinowich, P., Campbell, R., Chin, J. Hartman, S., Lafon, R., Stomski, P., Summers, D..  The W. M. Keck Observatory Laser Guide Star Adaptive Optics System: Performance Characterization.  PASP 118, 310-318 (2006).

- van Dokkum, P.G., Franx, M., Kriek, M., Holden, B., Illingworth, G.D., Magee, D., Bouwens, R., Marchesini, D., Quadri, R., Rudnick, G., Taylor, E.N., Toft, S.  Confirmation of the Remarkable Compactness of Massive Quiescent Galaxies at z ~ 2.3: Early-Ype Galaxies Did not Form in a Simple Monolithic Collapse.  ApJ, 677, L5-L8 (2008).

- Wizinowich, P., Acton, D.S., Shelton, C., Stomski, P., Gathright, J., Ho, K., Lupton, W., Tsubota, K., Lai, O., Max, C., Brase, J., An, J., Avicola, K., Olivier, S., Gavel, D., Macintosh, B., Ghez, A., Larkin, J. First Light Adaptive Optics Images from the Keck II Telescope: A New Era of High Angular Resolution Imagery.  PASP 112, 315-319 (2000).

- Wizinowich, P.  Adaptive optics and Keck Observatory.  Instrumentation & Measurement Magazine, IEEE Vol. 8, Issue 2, 12-19 (2005)

- Wizinowich, P., Le Mignant, D., Bouchez, A., Campbell, R., Chin, J., Contos, A., van Dam, M., Hartman, S., Johansson, E., Lafon, R., Lewis, H., Stomski, P., Summers, D., Brown, C., Danforth, P., Pennington, D.  The W. M. Keck Observatory Laser Guide Star Adaptive Optics System: Overview.  PASP 118: 297-309 (2006).

- Wizinowich, P., Dekany, R., Gavel, D., Max, C., Adkins, S., Bauman, B., Bell, J., Bouchez, A., Britton, M., Chin, J., Flicker, R., Johansson, E., Kupke, R., Le Mignant, D., Lockwood, C., Medeiros, D., McGrath, E., Moore, A., Neyman, C., Reinig, M., Velur, V. W.M. Keck Observatory’s next-generation adaptive optics facility.  SPIE Proc. 7015-36 (2008).

- Woillez, J., et al. Self Phase Referencing for High Spectral Resolution with the Keck Interferometer: Implementation, Performance and First Science.  In preparation (2009).

# Biographical Sketches

###### Jason Chin (Project Manager)

Professional Preparation

Undergraduate Institution

University of Southern California				Major: Electrical Engineering	B.Sc. 	1987

Graduate Institutions

University of Southern California				Major: Electrical Engineering	M.A.Sc.	1988

Appointments

1995 – Present.	Senior Electronics Engineer, W. M. Keck Observatory, Hawaii.

1986 – 1995	Systems Engineer, Hughes Aircraft Company, Reconnaissance Systems Division, El Segundo, California

1986 – 1988	Teaching Assistant, University of Southern California, Los Angeles, California

Publications

Publications related to the project

- W.M. Keck Observatory’s next-generation adaptive optics facility.  P. Wizinowich, R. Dekany, D. Gavel, C. Max, S. Adkins, B. Bauman, J. Bell, A. Bouchez, M. Britton, J. Chin, R. Flicker, E. Johansson, R. Kupke, D. Le Mignant, C. Lockwood, D. Medeiros, E. McGrath, A. Moore, C. Neyman, M. Reinig, V. Velur.  SPIE Proc. 7015-36 (2008).

- The W. M. Keck Observatory Laser Guide Star Adaptive Optics System: Overview. P. Wizinowich, D. Le Mignant, A. Bouchez, R. Campbell, J. Chin, A. Contos, M van Dam, S. Hartman, E. Johansson, R. Lafon, H. Lewis, P. Stomski, D. Summers, C. Brown, P. Danforth, D. Pennington.  PASP 118, 297-309 (2006).

- The W. M. Keck Observatory Laser Guide Star Adaptive Optics System: Performance Characterization. M. van Dam, A.H. Bouchez, D. Le Mignant, E.M. Johansson, P.L. Wizinowich, R.D. Campbell, J.C.Y. Chin, S.K. Hartman, R.E. Lafon, P.J. Stomski, Jr., D.M. Summers.  PASP 118, 310-318 (2006).

- The First Laser Guide Star Adaptive Optics Observations of the Galactic Center: SGR A*’s Infrared Color and the Extended Red Emission in its Vicinity. A. Ghez, S. Hornstein, J. Lu, A. Bouchez, D. Le Mignant, P. Wizinowich, K.  Matthews, M. Morris, E. Becklin, R. Campbell, J. Chin, M. van Dam, S. Hartman, E. Johansson, R. Lafon, P. Stomski, D. Summers.  ApJ 635, 1087-1094 (2005).

- Multiplicity in the Jupiter Trojan Population: Low density of 617 Patroclus with Keck Laser Guide Star Adaptive Optics and Perspective.  F. Marchis, D. Hestroffer, P. Descamps, J. Berthier, A. Bouchez, R. Campbell, J. Chin, M. van Dam, S. Hartman, E. Johansson, R. Lafon, D. Le Mignant, I. de Pater, P. Stomski, D. Summers, P. Wizinowich, M. Wong.  Nature 439, 565-567 (2006).

Other publications

- Satellites of the Largest Kuiper Belt Objects.  M. Brown, M. van Dam, A. Bouchez, D. Le Mignant, R. Campbell, J. Chin, A. Conrad, S. Hartman, E. Johansson, R. Lafon, D. Rabinowitz, P. Stomski, D. Summers, C. Trujillo, P. Wizinowich.  ApJ 639, L43-46 (2006).

- Keck Observatory laser guide star adaptive optics discovery and characterization of a satellite to large Kuiper belt object 2003 EL61.  M.E. Brown, A.H. Bouchez, D. Rabinowitz, R. Sari, C.A. Trujillo, M. van Dam, R. Campbell, J. Chin, S. Hartman, E. Johansson, R. Lafon, D. Le Mignant, P. Stomski, D. Summers, P. Wizinowich. ApJ 632, L45-48 (2005).

- Merging Galaxies in GOODS-S: First Extragalactic Results from Keck Laser Adaptive Optics.  J. Melbourne, S.A. Wright, M. Barcys, A.H. Bouchez, J. Chin, M.A. van Dam, S. Hartman, E. Johansson, D.C. Koo, R. Lafon, J. Larkin, D. Le Mignant, J. Lotz, C.E. Max, D. Pennington, P.J. Stomski, D. Summers, P.L. Wizinowich.  ApJ 625, L27-L30 (2005).

Synergistic Activities

Responsibilities at W. M. Keck Observatory have included the following:

- Electronics engineering for the Keck I and II telescopes, adaptive optics systems and interferometer.

- Project management and systems engineering for the Keck I LGS AO system upgrade and for the Keck II laser completion, telescope integration and commissioning for operations.

- Electronics group lead for the development and operations of the adaptive optics systems and interferometer.

Collaborators & Other Affiliations

Collaborators

Antonin Bouchez		Caltech				Domenico Bonaccini	European Southern Obs.

Mark Colavita		Jet Propulsion Lab		Richard Dekany		Caltech

Yutaka Hayano		Subaru Telescope			James Larkin		UCLA

David Le Mignant	LAM, Marseille

Graduate Advisors

M.A.Sc. Prof. John Choma, University of Southern California

###### Andrea M. Ghez (Scientific Collaborator)

            - Professional Preparation

Undergraduate Institution

Massachusetts Institute of Technology			Major: Physics			B.S. 	1987

Graduate Institutions

California Institute of Technology				Major: Physics			Ph.D.	1992
Steward Observatory, University of Arizona		Hubble Postdoctoral Research Fellow	     1992-1993

Appointments

2000 – Present.	Full Professor, Physics & Astronomy, UCLA

1997-2000.	Associate Professor, Physics & Astronomy, UCLA

1994-1997.	Assistant Professor, Physics & Astronomy, UCLA

Publications

Publications related to the project

- Ghez, A.M., Klein, B.L., Morris, M., & Becklin, E.E. 1998, “High Proper Motion Stars in the Vicinity of Sgr A*: Evidence for a Supermassive Black Hole at the Center of Our Galaxy,” ApJ, 509, 678.

- Ghez, A. M., Morris, M., Becklin, E. E., Kremenek, T., and Tanner, A. 2000, “The Accelerations of Stars Orbiting the Milky Way’s Central Black Hole,” Nature, 407, 349.

- Ghez, A. M., Duchene, G., Matthews, K., Hornstein, S. D., Tanner, A., Larkin, J., Morris, M., Becklin, E. E., Salim, S., Kremenek, T., Thompson, D. J., Soifer, B. T., Neugebauer, G., McLean, I. 2003 “The First Measurement of Spectral Lines in a Short-Period Star Bound to the Galaxy’s Central Black Hole: A Paradox of Youth,” ApJ, 586, L127.

- Ghez, A. M., Salim, S., Hornstein, S. D., Tanner, A., Morris, M., Becklin, E. E., Duchene, G. 2005, “Stellar Orbits Around the Galactic Center Black Hole,” ApJ, 620, 744.

- Ghez, A. M., Salim, S., Weinberg, N. N., Lu, J. R., Do, T., Dunn, J. K., Matthews, K., Morris, M., Yelda, S., Becklin, E. E., Kremenek, T., Milosavljevic, M., Naiman, J., 2008, “Measuring Distance and Properties of the Milky Way’s Central Supermassive Black Hole with Stellar Orbits,” ApJ, 689, 1044.

Other publications

- Ghez, A.M., Neugebauer, G., Gorham, P., Haniff, C., Kulkarni, S., Matthews , K., Koresko, C., & Beckwith, S. 1991, “Diffraction Limited Infrared Images of the Binary Star T Tauri,” AJ, 102, 2066

- Ghez, A.M., Neugebauer, G., & Matthews, K. 1993, “The Multiplicity of T Tauri Stars in the Taurus-Auriga & Ophiuchus-Scorpius Star Forming Regions: A 2.2 μm Imaging Survey,” AJ, 106, 2005

- Ghez, A. M., McCarthy, D. W., Patience, J.L., and Beck, T.L. 1997, “The Multiplicity of T Tauri Stars in Southern Star Forming Regions,” ApJ, 481, 378

- Ghez, A. M., White, R. J., and Simon, M. 1997 “High Spatial Resolution Imaging of Pre-Main-Sequence Binary Stars: Resolving the Relationship Between Disks and Close Companions,” ApJ, 490, 353

- Ghez, A. M., Wright, S. A, Matthews, K., Thompson, D., Le Mignant, D., Tanner, A., Hornstein, S. D., Morris, M., Becklin, E. E., & Soifer, B. T. 2003, “ Variable Infrared Emission from the Supermassive Black Hole at the Center of the Milky Way,” ApJ, 601, L159

Synergistic Activities

- Supervised 18 undergraduate and 3 high school student’s (12 women, 2 Hispanic, & 1 African-American) research projects (1994-present)

- Member of several National Research Council Committees responsible for setting priorities for Astronomical Community (O/IR Panel of 2000 Decadal Survey, Committee on Astronomy & Astrophysics, Board on Physics & Astronomy; 1999-present)

- Member of several UCLA committees on day care (a key issue for retaining women scientist; 2006-present)

- Contributed to science education for the general public (65 general public talks, 11 documentaries, figures for 11 textbooks; 1996-present)

- Has served as a highly visible role model for under-represented groups by conducting high impact research, which has been recognized with several honors and awards, including:

2009	Women in Space Science Award, Adler Planetarium

2008	MacArthur Fellowship

2008	Helen Hogg Distinguished Visitorship Award

2007	UCLA Academic Advancement Program Faculty Recognition Award

2007	Sackler Lecturer, Leiden University

2007	Sackler Lecturer, Harvard University

2006	Aaronson Award, University of Arizona

2004	National Academy of Sciences

2004	American Academy of Arts and Sciences

2004	Sackler Prize, University of Tel Aviv

2004	UCLA Gold Shield Prize

2004	UCLA Faculty Research Lecturer Award

Collaborators & Other Affiliations

List of all collaborators within the last 48 months

P. Andre (Saclay) R. Akeson (JPL) E. Becklin (UCLA) F. Baganoff (MIT) G. Basri (UCB) C. Beichman (JPL) A. Boden (IPAC) J. Bouvier (Grenoble) H. Bouy (UCB) G. Bower (UCB) W. Brandner (MPIA) N. Brandt (Penn State) J. Carpenter (IPAC) A. Eckart (U. Cologne) G. Garmire (Penn State) J. Graham (UCB) W. Herbst (Wesleyan) L. Hillenbrand (Caltech) J. Johnston (USNO) S. Kraus (MPIfR) D. Latham (Harvard) B. Macintosh (LLNL) D. Marrone (U Chicago) K. Matthews (Caltech) K. Menen (MPIR) S. Metchev (Stony Brook) S. Mohanty (Harvard) M. Morris (UCLA) J. Moran (Harvard) J.-U. Pott (Keck) L. Prato (Lowell) G. Ricker (MIT) A. Sargent (Caltech) R. Schoedel (IAA) M. Simon (Stony Brook) D. Thompson (UofA) G. Torres (Harvard) G. Weigelt (MPIfR) P. Wizinowich (Keck) J. Woillez (Keck) J. Zhao (CfA)

Graduate Advisors

Gerry Neugebauer (Caltech)

Graduate Students (9)

Tuan Do (UCLA) Quinn Konopacky (UCLA) Jessica Lu (Caltech) Seth Hornstein (U of Colorado) Caer McCabe (Spitzer), Jennifer Patience (University of Exeter) Angelle Tanner (JPL) Russel White (Georgia State University) Sylvana Yelda (UCLA)

Postgraduate-Scholar Sponsor (5)

Gaspard Duchene (UCB) Will Clarkson (UCLA) Nate McCrady (UCLA) Andrea Stolte (University of Cologne), Jorg-Uwe Pott (University of Cologne).

###### Michael C. Liu (Scientific Collaborator)

Professional Preparation

Undergraduate Institution

Cornell University				Major: Physics		B.A. summa cum laude 	1992

Graduate Institutions

University of California, Berkeley				Major: Physics			M.A.	1993
University of California, Berkeley				Major: Physics			Ph.D.	2000

University of Hawaii, Institute of Astronomy	Star and planet formation Postdoc		2000-2003

Appointments

2007 – Present.	Associate Astronomer, Institute of Astronomy, University of Hawai‘i

2003-2007.	Associate Astronomer, Institute of Astronomy, University of Hawai‘i

2000-2003.	Beatrice Watson Parrent Fellow, Institute of Astronomy, University of Hawai‘i

1993-2000.	Graduate Research Assistant, Department of Astronomy, UC Berkeley

Publications

Publications related to the project

- Dupuy, T. J., Liu, M. C., & Ireland, M. J. 2008, “The Dynamical Mass of the Substellar Benchmark Binary HD 130948BC,” ApJ, in press (accepted July 2008)

- Liu, M. C., Dupuy, T. J., & Ireland, M. 2008, “Keck Laser Guide Star Adaptive Optics Monitoring of 2MASS J15344984-2952274AB: First Dynamical Mass Determination of a Binary T Dwarf”, ApJ, 689, 436

- Liu, M. C., Leggett, S., & Chiu, K. 2007, “The Late-T Dwarf Companion to the Exoplanet Host Star HD 3651: A New Benchmark for Gravity and Metallicity Effects in Ultracool Spectra,”ApJ, 660, 1507

- Liu, M. C. et al. 2006, “A Novel T Dwarf Binary from Keck Laser Guide Star Adaptive Opticsand the Potential Role of Binarity in the L/T Transition,” ApJ, 647, 1393

- Liu, M. C., & Leggett, S., 2005, “Kelu-1 is a Binary L Dwarf: First Brown Dwarf Science from Laser Guide Star Adaptive Optics,” ApJ, 636, 616

Other publications

- Tarter, J. et al. 2006, “A Re-Appraisal of the Habitability of Planets Around M Dwarf Stars,” Astrobiology, in press

- Liu,M. C. 2004, “Substructure in the Circumstellar Disk around the Young Star AUMic (GJ 803),”Science, 305, 1442

- Liu, M. C., Matthews, B., Williams, J. & Kalas, P. 2004, “A Sub-Millimeter Search of Nearby Young Stars for Cold Dust: Discovery of Debris Disks around Two Low-Mass Stars,” ApJ, 608, 526

- Liu, M. C., Najita, J., & Tokunaga, A. T. 2003, “A Survey for Circumstellar Disks around Young Substellar Objects,” ApJ, 585, 372

- Liu, M. C., Charlot, S., & Graham, J. R. 2000, “Theoretical Predictions for Surface Brightness Fluctuations and Implications for Stellar Populations of Elliptical Galaxies,” ApJ, 543, 644

Synergistic Activities

- HST Cycle 16 Science Review panel, 2007

- AURA Giant Segmented Mirror Telescope, Science Working Group 2005 –

- Active public outreach speaker (e.g., Univ of Hawaii forum, IfA Friends of Astronomy, National Public Radio, Hilo AstroDay)

- Keck Adaptive Optics Science Working Group, 2002 – present (Co-Chair 2005 – present) (involves Keck, U. Hawaii, UC, Caltech & NASA communities)

- Undergraduate mentor for University of Hawaii NSF REU program, 2001 & 2005

Collaborators & Other Affiliations

List of all collaborators within the last 48 months

Related to current proposal: Loic Albert (CFHT), Sean Andrews (CfA/Harvard), Katelyn Allers (Hawaii), Adam Burgasser (MIT), Michael Cushing (Hawaii), David Golimowski (JHU), Xiaohui Fan (Arizona), Thierry Forveille (Grenoble), Tom Geballe (Gemini), Bertrand Goldman (MPIA), David Golimowski (JHU), Davy Kirkpatrick (IPAC/Caltech), Sandy Leggett (Gemini Obs), Jamie Lloyd (Caltech), Kevin Luhman (Penn State), Mark Marley (NASA/Ames), Brenda Matthews (Berkeley), Eduardo Martin (IAC/Central Florida), David Pinfield (Hertsfordshire), Neill Reid (STScI), Tom Roellig (NASA/Ames), Didier Saumon (LANL), Evgenya Shkolnik (Carnegie/DTM), Jill Tarter (SETI), Richard Wainscoat (Hawaii), Steve Warren (Imperial), Jonathan Williams (Hawaii).

Unrelated to current proposal: Ken Chambers (Hawaii), Rosa Gonzalez (UNAM), Joseph Jensen (NOAO), David Sanders (Hawaii), Alan Stockton (Hawaii), John Tonry (Hawaii).

Graduate Advisors

James R. Graham (University of California, Berkeley)

George R. Herbig (University of Hawai´ı)

Graduate Students (9)

Mark Willman (Masters)

Mark Pitts (Masters)

Dagny Looper (Masters)

Brendan Bowler (Masters)

Trent Dupuy (PhD thesis)

Postgraduate-Scholar Sponsor (4)

Katelyn Allers, Zahed Wahhaj, Evgenya Shkolnik, Beth Biller

###### Claire E. Max (Scientific Collaborator)

            - Professional Preparation

Undergraduate Institution

Harvard University		Major: Astronomy		A.B. magna cum laude 	1968

Graduate Institution

Princeton University		Major: Astrophysical Sciences	PhD			1972

Post-Doctoral Fellowship Institution

University of California, Berkeley	Physics Department				      1972-1974

            - Appointments

2008–	Director, University of California Center for Adaptive Optics

2004–	Director, National Science Foundation Center for Adaptive Optics

2001–	Astronomer, University of California Observatories/Lick Observatory and Professor, Department of Astronomy and Astrophysics, University of California at Santa Cruz

1995–2000	Director of University Relations, Lawrence Livermore National Laboratory

1993–1995	Director of Institutes, Physical Sciences Directorate, Lawrence Livermore Nat’l Laboratory

1984–1993	Founding Director, Livermore Branch, Inst. Geophysics & Planetary Physics, Univ. Calif.

1974–2004	Physicist, Lawrence Livermore National Laboratory, University of California

            - Publications

Publications related to the project

- "Design, layout, and early results of a feasibility experiment for sodium-layer laser-guide-star adaptive optics," C.E. Max, K. Avicola, J.M. Brase, H.W. Friedman, H.D. Bissinger, J. Duff, D.T. Gavel, J.A. Horton, R. Kiefer, J.R. Morris, S.S. Olivier, R.W. Presta, D.A. Rapp, J.T. Salmon and K.E. Waltjen. Optical Society of America Journal A, 11, 813-824, 1994.

- “Image Improvement from a Sodium-Layer Laser Guide Star Adaptive Optics System,” C.E. Max, S.S. Olivier, H.W. Friedman, J. An, K. Avicola, B.V. Beeman, H.D. Bissinger, J.M. Brase, G.V. Erbert, D.T. Gavel, K. Kanz, M.C. Liu, B. Macintosh, K.P. Neeb, J. Patience and K.E. Waltjen. Science, 277, 1649–1652, 1997.

- "Merging Galaxies in GOODS-S: First Extragalactic Results from Keck Laser Adaptive Optics," J. Melbourne, S.A. Wright, M. Barczys, A.H. Bouchez, J. Chin, M.A. van Dam, S. Hartman, E. Johansson, D.C. Koo, R. Lafon, J. Larkin, D. Le Mignant, J. Lotz, C.E. Max, D.M. Pennington, P.J. Stomski, D. Summers and P.L. Wizinowich. ApJ Letters, 625, L27-L30, 2005.

- “Locating the Two Black Holes in NGC 6240,” C. E. Max, G. Canalizo, & W. H. de Vries, 2007, Science, 316, 1877.

- “Spatially Resolved Stellar Populations of Eight GOODS-South AGN at z~1,” S. Mark Ammons, Jason Melbourne, Claire E. Max, David C. Koo, David J. V. Rosario, 2008, AJ, 137, 470.

Other publications

- "Cloud Structures on Neptune Observed with Keck Telescope Adaptive Optics," C. E. Max, B. A. Macintosh, S. G. Gibbard, D. T. Gavel, H. G. Roe, I. de Pater, A.M. Ghez, D. S. Acton, O. Lai, P. Stomski and P. L. Wizinowich. AJ, 125, 364-375, 2003.

- "Adaptive Optics Imaging and Spectroscopy of Cygnus A. I. Evidence for a Minor Merger," G. Canalizo, C. Max, D. Whysong, R. Antonucci and S.E. Dahm. ApJ, 597, 823-831, 2003.

- “Super-resolving distant galaxies with gravitational telescopes: Keck-LGSAO and Hubble imaging of the lens system SDSSJ0737+3216,” Marshall, P. J.; Treu, T.; Melbourne, J.; Gavazzi, R.; Bundy, K.; Ammons, S. M.; Bolton, A. S.; Burles, S.; Larkin, J. E.; Le Mignant, D.; Koo, D. C.; Koopmans, L. V. E.; Max, C. E.; Moustakas, L. A.; Steinbring, E.; & Wright, S. A., ApJ, 671, 1196, 2007.

- “Rest-Frame R-band Light Curve of a z ~ 1.3 Supernova Obtained with Keck Laser Adaptive Optics,” Melbourne, J.; Dawson, K. S.; Koo, D. C.; Max, C.; Larkin, J. E.; Wright, S. A.; Steinbring, E.; Barczys, M.; Aldering, G.; Barbary, K.; Doi, M.; Fadeyev, V.; Goldhaber, G.; Hattori, T.; Ihara, Y.; Kashikawa, N.; Konishi, K.; Kowalski, M.; Kuznetsova, N.; Lidman, C.; Morokuma, T.; Perlmutter, S.; Rubin, D.; Schlegel, D. J.; Spadafora, A. L.; Takanashi, N.; & Yasuda, N., AJ, 133, 2709, 2007.

- “The W. M. Keck Observatory Laser Guide Star Adaptive Optics System: Overview,” Wizinowich, Peter L.; Le Mignant, David; Bouchez, Antonin H.; Campbell, Randy D.; Chin, Jason C. Y.; Contos, Adam R.; van Dam, Marcos A.; Hartman, Scott K.; Johansson, Erik M.; Lafon, Robert E.; Lewis, Hilton; Stomski, Paul J.; Summers, Douglas M.; Brown, Curtis G.; Danforth, Pamela M.; Max, Claire E.; & Pennington, Deanna M., PASP, 118, 297-309, 2006.

            - Synergistic Activities

- Other leadership positions: Project Scientist, Keck Observatory Next Generation Adaptive Optics

- Originator and project leader for the Akamai Short Course and Internship on the Big Island of Hawaii.  This is a Center for Adaptive Optics program aimed at increasing the participation of Hawaiian community college-age students in the scientific and technical workforce. Optics and observatory operations are at the core of this summer internship experience.

- Co-founder of the Institute for Scientist and Engineer Educators at UC Santa Cruz.  This program is a spin-off from the Center for Adaptive Optics, with the goal of introducing science and engineering graduate students on our campus to modern knowledge and practice of teaching and learning, and then using these new skills in outreach programs to students from groups that are under-represented in science and engineering.

- Member, Astro 2010 Committee, National Research Council, National Academy of Sciences

- Has served as a highly visible role model for under-represented groups by conducting high impact research, which has been recognized with several honors and awards, including honors and awards including:

2009	Madison Medal, Princeton University

2008	National Academy of Sciences

2004	E. O. Lawrence Award (Department of Energy)

2002	American Academy of Arts and Sciences

            - Collaborators & Other Affiliations

List of all collaborators and co-editors within the last 48 months

Ammons, S. M. (UCSC), Antonucci, R. (UCSB), Barczys, M. (no current affiliation), Bouchez, A.H. (Caltech), Brown, M.E. (Caltech), Brown, C.G. (LLNL), Campbell, R.D. (Keck), Canalizo, G. (UC Riverside), Chin, J. (Keck), Chun, M.R. (U. Hawaii), Danforth, P.M. (LLNL), de Pater, I. (UC Berkeley), de Vries, W.H. (UC Davis), Gates, E.L. (Lick Obs.), Gavel, D. (UCSC), Ghez, A.M. (UCLA), Gibbard, S.G. (LLNL), Graham, J.R. (UC Berkeley), Johansson, E.M. (Keck), Kalas, P. (UC Berkeley), Koo, D.C. (UCSC), Larkin, J. (UCLA), Le Mignant, D. (Keck), Lewis, H. (Keck), Lloyd, J.P. (Cornell), Macintosh, B.A. (LLNL), Marshall, P. J. (UCSB), McKay, C.P. (NASA Ames), Melbourne, J. (Caltech), Metevier, A. (Sonoma State), Pennington, D.M. (LLNL), Perlmutter, S. (UC Berkeley), Perrin, M.D. (UCLA), Pollack, L.K. (Apple), Raschke, L. (UCSC), Roe, H.G. (Lowell Obs.), Rosario, David J. V. (UCSC), Schlegel, D. J. (LBNL), Schneider, G. (U Ariz.), Simard, L. (HIA), Steinbring, E. (HIA), Stomski, P.J. (Keck), Summers, D. (Keck), Treu, T. (UCSB), van Dam, M.A. (in New Zealand), Whysong, D. (NRAO), Wiberg, D.M. (UCSC), Wizinowich, P.L. (Keck), Wright, S.A. (UC Irvine)

Graduate Advisors:  Francis Perkins (retired, formerly of Princeton University).

Postdoctoral Sponsor: Alan Kaufman (retired, formerly of University of California, Berkeley).

Graduate Students (3): Lynne Raschke (UC Santa Cruz), Jason Melbourne (California Inst. of Technology), S. Mark Ammons (finishing PhD in June 09).

Postgraduate-Scholar Sponsor in past 5 years:  Elizabeth McGrath (UC Santa Cruz).

###### Thomas Stalcup (Systems Engineer)

            - Professional Preparation

Undergraduate Institution

University of Missouri-Rolla			Major: Electrical Engineering	B.S. 	1999

Graduate Institutions

University of Missouri-Rolla			Major: Electrical Engineering	M.S.	2002
University of Arizona, Optical Sciences Center	Major: Optical Science		M.S.	2003

University of Arizona, Optical Sciences Center	Major: Optical Science		Ph.D.	2006

            - Appointments

2008 – Present.	Adaptive Optics Scientist, W. M. Keck Observatory, Hawaii.

2005 – 2008.	Adaptive Optics Scientist, MMT Observatory, University of Arizona, Arizona.

2004 – 2005.	Principal Engineer, Steward Observatory, University of Arizona, Arizona.

            - Publications

1. T. Stalcup, R. Angel, M. Lloyd-Hart, M. Rademacher, “Status of the MMT Observatory multiple laser beacon projector,” in Astronomical Adaptive Optics systems and Applications III, eds. R. K. Tyson, M. Lloyd-Hart, Proc. SPIE 6691, 66910M (2007).

2. T. Stalcup, Design and Construction of a Multiple Beam Laser Projector and Dynamically Refocused Wavefront Sensor, Doctoral dissertation, University of Arizona (2006).

3. T. Stalcup, K. Powell, “Image motion correction using accelerometers at the MMT Observatory,” in Advanced Optical and Mechanical Technologies in Telescopes and Instrumentation, eds. E. Atad-Ettedgui and D. Lemke, Proc. SPIE 7018, 70181H (2008).

            - Synergistic Activities

Responsible for commissioning the LGS system for Keck I as well as ongoing performance and operational improvements to the Keck I and II AO systems in the roles of system engineering and optical engineering.

Committee secretary for the SOAR telescope SAM ground layer LGS system design review.

            - Collaborators & Other Affiliations

Collaborators

Laird Close		U. of Arizona		Michael Hart		U. of Arizona

Phil Hinz		U. of Arizona		Don McCarthy		U. of Arizona

Richard Green		LBT Observatory		J. Roger P. Angel		U. of Arizona

Keith Powell		U. of Arizona		Oliver Durney		U. of Arizona

Tom Connors		U. of Arizona		Matthew Rademacher	U. of Arizona

Miguel Snyder		U. of Arizona		N. Mark Milton		U. of Arizona

Christoph Baranec	Caltech			Vidhya Vaitheeswaran	U. of Arizona

Faith Vilas		MMT Observatory	Grant Williams		MMT Observatory

Guido Brusa-Zappellini	LBT Observatory		Doug Miller		LBT Observatory

Grover Swartzlander	U. of Arizona		Nick Siegler		JPL

Mike Meyer		U. of Arizona		Daniel Eisenstein		U. of Arizona

Matthew Kenworthy	U. of Arizona		Mary Anne Peters	U. of Arizona

Erin Ford		U. of Arizona		Rukiah Abdul-Malik	U. of Arizona

Ryeojin Park		U. of Arizona		Eric Nielsen		U. of Arizona

John Codona		U. of Arizona		Craig Kulesa		U. of Arizona

Keith Hege		U. of Arizona

Graduate Advisors

M.S. Prof. Steve Watkins, University of Missouri-Rolla

PhD. Prof. J. Roger P. Angel, University of Arizona

###### Peter Wizinowich (Principal Investigator)

Professional Preparation

Undergraduate Institution

University of Toronto					Major: Physics & Astronomy	B.Sc. 	1978

Graduate Institutions

University of Toronto, Institute for Aerospace Studies	Major: Applied Physics		M.A.Sc.	1980
University of Arizona, Optical Sciences Center		Major: Optics			PhD.	1989

Appointments

1991 – Present.	Optical Systems Manager, W. M. Keck Observatory, Hawaii.

1989 – 1991.	Staff Scientist, Steward Observatory, University of Arizona, Arizona.

1982 – 1985.	Instrumentation Technician, Canada-France-Hawaii Telescope, Hawaii.

1980 – 1981.	Resident Astronomer, University of Toronto Southern Observatory, Chile.

Publications

Publications related to the project

- W.M. Keck Observatory’s next-generation adaptive optics facility.  P. Wizinowich, R. Dekany, D. Gavel, C. Max, S. Adkins, B. Bauman, J. Bell, A. Bouchez, M. Britton, J. Chin, R. Flicker, E. Johansson, R. Kupke, D. Le Mignant, C. Lockwood, D. Medeiros, E. McGrath, A. Moore, C. Neyman, M. Reinig, V. Velur.  SPIE Proc. 7015-36 (2008).

- Quasi-static aberrations induced by laser guide stars in adaptive optics.  M.A. van Dam, A.H. Bouchez, D. Le Mignant, P.L. Wizinowich. Optics Express 14, 7535-7540 (2006).

- The W. M. Keck Observatory Laser Guide Star Adaptive Optics System: Overview. P. Wizinowich, D. Le Mignant, A. Bouchez, R. Campbell, J. Chin, A. Contos, M van Dam, S. Hartman, E. Johansson, R. Lafon, H. Lewis, P. Stomski, D. Summers, C. Brown, P. Danforth, D. Pennington. PASP 118, 297-309 (2006).

- The W. M. Keck Observatory Laser Guide Star Adaptive Optics System: Performance Characterization. M. van Dam, A.H. Bouchez, D. Le Mignant, E.M. Johansson, P.L. Wizinowich, R.D. Campbell, J.C.Y. Chin, S.K. Hartman, R.E. Lafon, P.J. Stomski, Jr., D.M. Summers.  PASP 118, 310-318 (2006).

- The First Laser Guide Star Adaptive Optics Observations of the Galactic Center: SGR A*’s Infrared Color and the Extended Red Emission in its Vicinity. A. Ghez, S. Hornstein, J. Lu, A. Bouchez, D. Le Mignant, P. Wizinowich, K.  Matthews, M. Morris, E. Becklin, R. Campbell, J. Chin, M. van Dam, S. Hartman, E. Johansson, R. Lafon, P. Stomski, D. Summers.  ApJ 635, 1087-1094 (2005).

Other publications

- Astrometry with the Keck Interferometer: the ASTRA project and its science.  J-U. Pott, J. Woillez, R. Akeson, B. Berkey, M. Colavita, A. Cooper, J. Eisner, A. Ghez, J. Graham, L. Hillenbrand, M. Hrynevych, D. Medeiros, R. Millan-Gabet, J. Monnier, D. Morrison, T. Panteleeva, E. Quataert, B. Randolph, B. Smith, K. Summers, K. Tsubota, C. Tyau, N. Weinberg, E. Wetherell, P. Wizinowich.  Astrometry and Imaging with the Very Large Telescope Interferometer, Keszthely, Hungary (2008).

- Recent progress at the Keck Interferometer: operations and V2 science.  S. Ragland, P. Wizinowich, R. Akeson, M. Colavita, E. Appleby, B. Berkey, A. Booth, A. Cooper, S. Crawford, W. Dahl, C. Felizardo, J. Garcia-Gathright, J. Gathright, J. Herstein, M. Hrynevych, C. Koresko, R. Ligon, D. Medeiros, B. Mennesson, R. MillanGabet, D. Morrison, C. Paine, B. Parvin, T. Panteleeva, E. Serabyn, B. Smith, K. Summers, K. Tsubota, C. Tyau, E. Wetherell, J. Woillez.  SPIE Proc. 7013-10 (2008).

- First Light Adaptive Optics Images from the Keck II Telescope: A New Era of High Angular Resolution Imagery. P. Wizinowich, D.S. Acton, C. Shelton, P. Stomski, J. Gathright, K. Ho, W. Lupton, K. Tsubota, O. Lai, C. Max, J. Brase, J. An, K. Avicola, S. Olivier, D. Gavel, B. Macintosh, A. Ghez & J. Larkin. PASP 112, 315-319 (2000).

Synergistic Activities

Responsible for the following major projects at W. M. Keck Observatory (in the combined roles of project management, personnel management, system engineering and optical engineering):

- Keck I and II telescope optics

- Keck I and II NGS AO systems

- Keck I and II LGS AO system

- Keck Interferometer and ASTRA Upgrade

Committee chair for the:

- SPIE Adaptive Optical Systems Symposium, Munich (2000), Waikoloa (2002) & Marseille (2008)

- TMT Performance Review (2008)

- Gemini Multi-Conjugate Adaptive Optics CoDR & PDR, Hawaii (2000 & 2001)

- Mauna Kea Laser Guide Star Technical Working Group, Hawaii (1996-2000)

- Gemini Altair Adaptive Optics System PDR & CDR, Victoria (1996 & 1998)

- OSA Summer Topical Meeting on Adaptive Optics, Maui (1996)

Plus: program committee member for adaptive optics conferences; committee member for instrument reviews; AO working group member for Gemini and HIA; referee for science journals, NSF & NASA proposals; and invited speaker.

Collaborators & Other Affiliations

Collaborators and Co-Editors

Rachel Akeson	 	MSC, Caltech			Antonin Bouchez		Caltech

Domenico Bonaccini	European Southern Obs.		Mark Colavita		Jet Propulsion Lab. Michelle Creech-Eikman	New Mexico Tech.		Richard Dekany		Caltech

Josh Eisner		U. of Arizona			Brent Ellerbroek		TMT Project

Don Gavel		UCSC				Andrea Ghez		UCLA

James Graham		UCB				Michael Hart		U. of Arizona

Lynne Hillenbrand	Caltech				Norbert Hubin		European Southern Obs.

Olivier Lai		CFHT				James Larkin		UCLA

David Le Mignant	LAM, Marseille			Mike Liu		University of Hawaii

Franck Marchis		UCB				Claire Max		UCSC

Rafael Millan-Gabet	Caltech				John Monnier		U. of Michigan

Guy Perrin		Observatoire de Paris		Eliot Quataert		UCB

Nevin Weinberg 		UCSB

Graduate Advisors

M.A.Sc. Prof. Ray Measures, University of Toronto		PhD. Prof. J. Roger P. Angel, University of Arizona

Postgraduate-Scholar Sponsor (total of 9; 5 within last five years)

Antonin Bouchez, PhD Caltech 2003			Ralf Flicker, PhD Lund University 2003

Stephan Kellner, PhD Max Planck Institute Heidelberg 2005	Jorg-Uwe Pott, PhD University of Cologne 2006

Julien Woillez, PhD University of Paris 2003

# Other Personnel

Other key personnel at WMKO that will be significantly involved in this project:

Drew Medeiros.  Medeiros will be the mechanical engineer for this project.  He is currently performing a similar role for the Keck I LGS AO upgrade.

Sergey Panteleev.  Dr. Panteleev will be the optics engineer responsible for the launch telescope optics acceptance.  He performed this same role for the Keck I launch telescope.

Ed Wetherell.  Wetherell will be responsible for the electronics in collaboration with Chin.  He has performed a similar role on the Keck I LGS AO upgrade.

# Budget and Budget Justification

The W. M. Keck Observatory is submitting this proposal for the development of a significant enhancement to the Keck II LGS AO facility.

The project duration is 26 months with a planned start date of August 1, 2009 and a completion date of September 30, 2011.  The detailed project budget is shown in Table 6.  The total budget for the project is $1936k.  WMKO will contribute 30% or $581k (including overhead) for the two-year period.  The request to the NSF MRI program is for $1355.5k.

Budget Justification

- Senior personnel assigned to the project represent the essential leadership required for the project activities.  Adaptive optics is a highly specialized field, and the senior personnel listed here represent the key leadership for the project.  Their participation in this project is essential to ensure its success.  As indicated in the notes to the budget salaries for senior personnel are based on WMKO fiscal year 2009 rates with the addition of 3.5% inflation per year.

- The engineers (other professionals) required by this project represent the engineering skills needed to design and implement the upgrades.  As indicated in the notes to the budget salaries for other personnel are based on WMKO fiscal year 2009 rates with the addition of 3.5% inflation per year.  The engineering staff details are shown in Table 7.

- Fringe benefits are included at the standard WMKO rate.

- The equipment purchases for this project are required for the implementation of the center launch facility. The cost estimate is based on past experience with similar components and fabrications.

- Travel costs are based on requirements for travel by project staff to the launch telescope acceptance and for travel to design reviews.

- There are no participant support costs in this proposal budget.

- Materials and supplies are components and fabrications for the implementations of the center launch telescope and are detailed in Table 8.  No publication costs, consultant services, computer services or subawards are included.  Other includes the cost of laser spotters for on-sky integration and test.

- WMKO has a federally approved indirect cost rate of 55%.  This is applied to a modified total direct cost base consisting of the total direct costs less equipment and subawards, plus the first $25K of each subaward.

Table 6: Detailed Project Budget

Table 7: Other Professionals

Table 8: Materials and Supplies (unit cost under $5k)

Cost Sharing

The W. M. Keck Observatory is committed to providing a cost share of $580,928 for this proposal to the NSF Major Research Instrumentation Program titled “MRI: Development of an Improved Keck II Laser Launch Facility”. This cost sharing commitment is included in the Observatory's development budget for fiscal 2010 and 2011, consistent with the timeline and the proposed yearly budgets submitted with the proposal. The Observatory’s fiscal year begins on October 1 of each year, and the Observatory’s operations are funded by the University of California and NASA. The cost sharing commitment will be supported by non-Federal funds and will be available at the start of each fiscal year.

In year 1 of the project WMKO has budgeted $239,743 as shown in the year 1 proposal budget. These funds will be applied to the cost of equipment in year 1. In year 2 of the project WMKO has budgeted $327,826 as shown in the year 2 proposal budget. These funds will be applied to the cost of equipment in year 2. In year 3 of the project WMKO has budgeted $13,359 as shown in the year 3 proposal budget.  These funds will be applied to salaries and benefits in year 3.

# Current and Pending Support

Peter Wizinowich – Current Support:

Keck Interferometer Project

Period: February 1, 2005 – June 30, 2009

Funding: JPL cost reimbursement subcontract #1264288 of $14.54M

Location: W. M. Keck Observatory

Effort: 1 month/yr

NSF Laser for Keck I

Period: September 27, 2005 – June 30, 2009

Funding: NSF of $2.81M

Location: W. M. Keck Observatory

Effort: 0.5 month/yr

ASTRA Project to upgrade the Keck Interferometer

Period: July 10, 2006 – June 30, 2010.

Funding: NSF MRI award 0619965 of $1.958M.

Location: W. M. Keck Observatory

Effort: 2 month/yr

NGAO Preliminary Design

Period: March 1, 2008 – February 28, 2010

Funding: NSF award (TSIP) AST0132798, AURA sub-award C10591T of $2.047M

Location: W. M. Keck Observatory

Effort:  6 month/yr

Peter Wizinowich – Pending:

Sodium-Wavelength Lasers for Astronomical Adaptive Optics

Period: January 1, 2009 – January 31, 2010

Funding: AURA Sub-award No. C66003A of $300k in support of NSF GSMT award AST-0443999

Location: Managed from W. M. Keck Observatory

Effort: 0.5 month/yr

MRI: Development of an Improved Keck II Laser Launch Facility – Enhancing the Scientific Return of Keck Laser Guide Star Adaptive Optics (this proposal)

Period: 8/1/09 – 9/30/11

Funding: National Science Foundation MRI award of $1,355,500

Effort: 0.75 month/yr

Jason Chin – Current Support:

NGAO Preliminary Design

Period: March 1, 2008 – February 28, 2010

Funding: NSF award (TSIP) AST0132798, AURA sub-award C10591T of $2.047M

Location: W. M. Keck Observatory

Effort:  1 month/yr

Jason Chin – Pending:

MRI: Development of an Improved Keck II Laser Launch Facility – Enhancing the Scientific Return of Keck Laser Guide Star Adaptive Optics (this proposal)

Period: 8/1/09 – 9/30/11

Funding: National Science Foundation MRI award of $1,355,500

Effort: 2 month/yr

Thomas Stalcup  – Current Support:

NGAO Preliminary Design

Period: March 1, 2008 – February 28, 2010

Funding: NSF award (TSIP) AST0132798, AURA sub-award C10591T of $2.047M

Location: W. M. Keck Observatory

Effort:  1 month/yr

Thomas Stalcup – Pending:

MRI: Development of an Improved Keck II Laser Launch Facility – Enhancing the Scientific Return of Keck Laser Guide Star Adaptive Optics (this proposal)

Period: 8/1/09 – 9/30/11

Funding: National Science Foundation MRI award of $1,355,500

Effort: 6 month/yr

Statement of Current and Pending Support

Claire E. Max

Current Support

Title:  Center for Adaptive Optics, an NSF Science and Technology Center

Funding Source:  National Science Foundation

Award Number:  AST-9876783

Project Period:  11/1/99-10/31/09

Award Amount:  $35,581,329

Time Commitment per year:  5.5 months/year

Title:  The Laboratory for Adaptive Optics

Funding Source:  Gordon and Betty Moore Foundation

Award Number:  #181

Project Period: 7/1/02-6/30/09

Award Amount: $9,100,000

Time Commitment: 0.5 months/year

Title: Preliminary Design Phase, Keck Next Generation Adaptive Optics System

Funding Source: W.M. Keck Observatory

Award Number: PO#28388

Project Period: 05/01/08-02/10/10

Award Amount: $812,246

Time Commitment:  2 months/yr

Pending Support

Title: Active Galactic Nuclei in Merging Galaxies Viewed with Laser Guide Star 	Adaptive Optics

Funding Source: National Science Foundation

Award Number: Pending

Proposed Project Period: 6/1/09-5/30/12

Award amount: $288,326

Time Commitment: 1.5 months/yr in Year 1; 2 months/yr in Years 2 and 3

Title: MRI: Development of Enhanced Adaptive Optics System and Infrared Instrumentation for the Shane 3-meter Telescope

Funding Source: National Science Foundation

Award number: Pending

Proposed Project Period: 10/01/09 -09/30/12

Award amount: $2,000,000

Time commitment: 0 hours/year

Title: MRI: Development of an Improved Keck II Laser Launch Facility  – Enhancing the Scientific Return of Keck Laser Guide Star Adaptive Optics (this proposal)

Funding source: National Science Foundation

Award number: pending

Proposed Project Period: 8/1/09 – 9/30/11

Award amount: $1,355,500

Time commitment: 0 hours/year

# Supplementary Documents

Organizational Classification

The California Association for Research in Astronomy, DBA the W.M. Keck Observatory, is a non-degree granting organization.  The California Association for Research in Astronomy, operator of the W. M. Keck Observatory, is a 501(c)(3) corporation organized to conduct scientific research.  The California Association for Research in Astronomy is incorporated in the state of California.

# Letters from unfunded participants

# List of Suggested Reviewers

- Dr. Laird Close, Steward Observatory, University of Arizona, 933 N. Cherry Ave., Tucson, AZ 85721.  lclose@as.arizona.edu.  (520) 626-5992.

- Dr. Heidi Hammel, Co-Director, Research Branch, Space Science Institute, Connecticut Office, 72 Sarah Bishop Road, Ridgefield, CT 06877.  hbh@alum.mit.edu.  (203) 438-3506.

- Dr. Yutaka Hayano, Assistant Professor, Subaru Telescope, National Astronomical Observatory of Japan, 650 North A’ohoku Place, Hilo, HI 96720.  hayano@subaru.naoj.org.  (808) 934-5941.

- Dr. Francois Rigaut, Senior Scientist, Gemini Observatory, Southern Operations Center, c/o AURA, Casilla 603, La Serena, Chile.  FRigaut@gemini.edu.  +56 (51) 205784.

# Footnotes

http://www.keckobservatory.org/education.php

http://www.keckobservatory.org/article.php?id=89