NGAO System Design Phase: Work Scope Planning Sheet

WBS Element Title:	Number and Type of Low Order WFS TS

WBS Element Number:	3.1.2.2.10

Work Package Lead:	Richard Clare

Work Package Participants:	Chris Neyman

# Work Scope

WBS Dictionary Entry: 	Perform a cost/benefit analysis for the optimal type, waveband, and number of tip/tilt and tip/tilt/focus low-order WFS.  Complete when LOWFS requirements and sky coverage estimates have been documented.

Requirements: 	Due to the limited availability of Stephan Kellner for NGAO during the first quarter of FY07, this trade study was turned over to Neyman/Clare/Flicker. Some modifications to the scope of 3.1.2.2.10 have been made, which tie in with corresponding modifications in 3.1.2.2.9 (cf. that WSPS). Modifications in 3.1.2.2.10 include

- WFS type (SH vs PYR) trade study moved to 3.1.2.2.9

- Costing of WFS relating to architecture moved to 3.1.2.2.9

# Inputs:	Sources for this TS include:

# Existing simulation code authored by Richard Clare, described in Clare & Ellerbroek, “Sky coverage estimates for adaptive optics systems from computations in Zernike space,” JOSAA Vol. 23, February 2006.

# Turbulence model based on CN-M2 (NGAO proposal), and the baseline system parameters are imported from the benchmark science cases (key observing scnearios) as reported in Section 14, Appendix: Wavefront Error Budget, NGAO proposal, June 2006.

# Products:	Deliverables of this TS include:

# Sky coverage calculations for SH-type LOWFS, as a function of LOWFS configuration (number of sensors, degree of image sharpening, number of sensed modes) and sensing wavelength (e.g. V, J, H and K).

# Costing estimates of elements that do not pertain to the LOWFS architectural choice (which are counted to WBS 3.1.2.2.9 – this item may be deferred until after meeting 4)

# KAON of results written up, viewgraphs and presentation at m4

- Support for the development of the wavefront error budget (in particular the understanding of the focus blind modes).

# Methodology:	Using Richard Clare’s sky coverage code as-is for SH WFSs, having moved the pyramid sensor comparison to WBS 3.1.2.2.9. The code is a covariance based calculation over a low-order Zernike turbulence model, and it assumes the Spagna model for star density and luminosity calculations.

# Estimate of effort:	Estimated work: 60 hours (SEMP = 60 hours).  20 hours added for support of the wavefront error budget.

# Approvals:

| Control | Name | Date |
| --- | --- | --- |
| Authored by: | Ralf Flicker | 01/02/07 (revised 1/19/07) |
| Approved by: | Richard Dekany | 2/2/07 |
|  | Peter Wizinowich | 2/2/07 |

Proposed Table of contents

- Abstract

- Introduction

- Analysis

- Conclusions

- References