Keck Adaptive Optics Note 461

Wavefront Error Budget Predictions and Measured Performance

for Current and Upgraded Keck Adaptive Optics

P. Wizinowich, R. Dekany, M. van Dam

January 26, 2007

# Introduction

The purpose of this note is multifold:

- To summarize the measured versus predicted performance for the existing Keck AO systems and our understanding of the reasons for the differences.

- To provide an anchor for the Next Generation AO (NGAO) wavefront error budget tool.

- To predict the performance of the planned and potential upgrades to this system.

Note that item 2 is in support of NGAO System Design phase WBS 3.1.1.2.3 Anchor to Keck II LGS AO PSFs and item 3 is in support of WBS 3.1.2.1.2 NGAO versus Keck AO Upgrades trade study.

# Measured versus Predicted Performance for Current Keck AO

  - Measured versus Predicted Comparison

The originally predicted performance, and assumptions, for the Keck AO systems are defined in the Keck AO Blue Book (Keck Observatory Report 208).  The measured performance of the Keck NGS and LGS AO systems are summarized in two refereed publications by van Dam et al.  Table 1 compares the predicted and measured performance from these two sources for the NGS bright star case and the LGS case with a 10th magnitude NGS.  For the LGS case a column is also included for the NGAO tool predictions that will be discussed in section 3.  The final column shows the measured LGS AO performance for an 18th mag NGS.

The various error terms in the rows of this table are explained in the Blue Book and two van Dam et al. papers.  The “Miscellaneous” row was included for the measured NGS case to include terms that could not be explicitly assigned to the other rows such as dynamic calibration errors, additional telescope errors, poorly sensed modes and atmospheric dispersion.  The “Miscellaneous (NGAO)” row was included to represent the sum of seven additional small error sources in the NGAO error budget tool, each of about 20 nm in magnitude.  The percentile seeing should be interpreted using the following example: 75% means that 75% of the nights have worse seeing and the listed performance can be achieved or exceeded on the 25% of the nights with the best seeing. The reason we use percentiles rather than atmospheric parameters is that the LGS AO performance depends on a large number of atmospheric parameters, such as r0, τ0, Cn2 profile and the sodium density structure.

It is clear from the “Total wavefront error” and “K-band Strehl” rows that the measured performance is significantly lower than the Blue Book predicted, or rather planned, performance.  This discrepancy is discussed in the next section.  The Strehl in the measured column is in reality higher than the value calculated by adding the terms in quadrature, since the the high spatial frequency terms are double counted (focal anisoplanatism and atmospheric and fitting error).

One point should be made before we move to this explanation.  That is that the impact of the tip/tilt errors is different than that of the higher order terms.  The tip/tilt errors broaden the diffraction-limited core while the higher order errors move energy from the diffraction-limited core into the seeing limited halo.

Table 1 Keck AO Wavefront Error Budget: Planned (Blue Book), Measured and Predicted (NGAO tool)

  - Measured versus Predicted Explanation

The discrepancy between the Blue Book values and the measured performance is explained by the delivered system not achieving some of its requirements and the Keck environment being different than the assumptions in the Blue Book.  These factors are further explained as follows:

- The science instrument did not achieve its wavefront quality requirements.  Note that the image quality can be improved by image sharpening, but only over narrow fields and wavelengths. In addition, scattering and vibrations on the AO bench limit the ability to obtain diffraction-limited images with a calibration source.

- The delivered AO system did not achieve its bandwidth requirement.  Both the DM and TT bandwidth terms are significantly higher than the predicted performance due to the fact that the achieved bandwidth (30 Hz for NGS AO, 20 Hz for LGS AO) is significantly less than the expected bandwidth (90 Hz).  The DM bandwidth error discrepancy is due to latency in the real-time control system and our overly optimistic expectations about the ratio of sample rate to bandwidth.  The same latencies impact the NGS tip/tilt bandwidth.  Tip/tilt bandwidth latencies and errors are reduced in the LGS case (the higher numbers in this case are due to a fainter star).  The DM measurement error discrepancy in the LGS case is also partly due to the lower bandwidth since these two terms are traded against each other in operation (the system is run slower to reduce the measurement error at the expense of the bandwidth error). In addition, the tip-tilt mirror exhibits a large resonance when driven at large bandwidths, limiting the ability to correct for high frequency aberrations.

- The delivered laser system did not achieve the planned laser power.  A 20 W system was planned versus the actually achieved ~ 13 W system (only 10 W at the time that the Strehl ratios presented in Table 1 were measured). This results in increased DM bandwidth and measurement errors, as the frame rate is reduced due to the reduced power.

- The Keck telescopes contribute significant tip/tilt vibrations in the 20-40 Hz range that was not accounted for in the Blue Book.  The low bandwidth of the delivered system does not allow for significant correction of these vibrations.

- The value for the focal anisoplanatism parameter, d0, assumed (based on very little data) in the Blue Book appears to have been too optimistic.  More recent measurements of the Cn2 profile above Mauna Kea indicate that this parameter is smaller and the resultant amount of focal anisoplanatism is therefore significantly larger.

# Anchoring the NGAO Wavefront Error Budget Tool

The measured Keck II LGS AO performance is being used as an anchor to test and improve the NGAO wavefront error budget spreadsheet developed by Dekany et al.  The comparison of the NGAO tool predictions to the measured performance in the above table show good agreement with one exception: the tip/tilt bandwidth error.  This is due to the fact that the NGAO tool does not yet include the realities of the telescope tip/tilt vibration environment.  This will be rectified by incorporating the results from some measured tip/tilt power spectra in the NGAO tool assumptions.

# Predicted Performance for Keck AO Upgrades

  - Next Generation Wavefront Controller (NGWFC)

  - Keck I LGS AO

  - Potential Upgrades

# References

Adaptive Optics for Keck Observatory.  Keck Observatory Report 208 (January, 1996).

van Dam, M.A., Le Mignant, D., & Macintosh, B.A., Performance of the Keck Observatory adaptive-optics system.  Applied Optics, 43: 5459-5467 (2004).

van Dam, M.A. et al., The W.M. Keck Observatory Laser Guide Star Adaptive Optics System: Performance Characterization.  Publications of the Astronomical Society of the Pacific, 118: 310-318 (2006).