Keck Adaptive Optics Note

Next Generation Adaptive Optics:

Functional Requirements Document

Version 0.0

April 17, 2007

1	Introduction	1

2	Scope and Applicability	1

3	References	1

3.1	Related Documents	1

3.2	Referenced Drawings	1

4	Revision History	1

5	Overall System Architecture & Assumptions	2

5.1	Purpose	2

5.2	Overview	2

5.3	Performance Budget Flowdown	3

6	Overall Functional Requirements (Requirements for all Subsystems)	4

6.1	Architectural Assumptions	4

6.2	Optical Requirements	4

6.3	Mechanical Requirements	4

6.4	Electronic/Electrical Requirements	4

6.5	Safety Requirements	4

6.6	Software Requirements	4

6.7	Interface Requirements	4

6.8	Reliability Requirements	4

6.9	Spares Requirements	4

6.10	Service and Maintenance Requirements	4

6.11	Documentation Requirements	4

7	AO System Functional Requirements	5

7.1	Architectural Assumptions	5

7.2	Optical Requirements	5

7.3	Mechanical Requirements	9

7.4	Electronic/Electrical Requirements	10

7.5	Safety Requirements	10

7.6	Software Requirements	10

7.7	Interface Requirements	12

7.8	Reliability Requirements	13

7.9	Spares Requirements	13

7.10	Service and Maintenance Requirements	13

7.11	Documentation Requirements	13

8	Laser Facility Functional Requirements	14

8.1	Architectural Assumptions	14

8.2	Optical Requirements	14

8.3	Mechanical Requirements	14

8.4	Electronic/Electrical Requirements	14

8.5	Safety Requirements	14

8.6	Software Requirements	14

8.7	Interface Requirements	14

8.8	Reliability Requirements	14

8.9	Spares Requirements	14

8.10	Service and Maintenance Requirements	14

8.11	Documentation Requirements	14

9	Science Operations Facility Functional Requirements	15

9.1	Architectural Assumptions	15

9.2	Optical Requirements	15

9.3	Mechanical Requirements	15

9.4	Electronic/Electrical Requirements	15

9.5	Safety Requirements	15

9.6	Software Requirements	15

9.7	Interface Requirements	15

9.8	Reliability Requirements	15

9.9	Spares Requirements	15

9.10	Service and Maintenance Requirements	15

9.11	Documentation Requirements	15

10	Telescope Facility Functional requirements	16

10.1	Architectural Assumptions	16

10.2	Optical Requirements	16

10.3	Mechanical Requirements	16

10.4	Electronic/Electrical Requirements	16

10.5	Safety Requirements	16

10.6	Software Requirements	16

10.7	Interface Requirements	16

10.8	Reliability Requirements	16

10.9	Spares Requirements	16

10.10	Service and Maintenance Requirements	16

10.11	Documentation Requirements	16

11	Science Instruments Functional Requirements	17

11.1	Architectural Assumptions	17

11.2	Optical Requirements	17

11.3	Mechanical Requirements	17

11.4	Electronic/Electrical Requirements	17

11.5	Safety Requirements	17

11.6	Software Requirements	17

11.7	Interface Requirements	17

11.8	Reliability Requirements	17

11.9	Spares Requirements	17

11.10	Service and Maintenance Requirements	17

11.11	Documentation Requirements	17

12	Deployable IFU Science Instrument Functional Requirements	18

12.1	Architectural Assumptions	18

12.2	Optical Requirements	18

12.3	Mechanical Requirements	18

12.4	Electronic/Electrical Requirements	18

12.5	Safety Requirements	18

12.6	Software Requirements	18

12.7	Interface Requirements	18

12.8	Reliability Requirements	18

12.9	Spares Requirements	18

12.10	Service and Maintenance Requirements	18

12.11	Documentation Requirements	18

13	Imagers Science Instrument Functional Requirements	19

13.1	Architectural Assumptions	19

13.2	Optical Requirements	19

13.3	Mechanical Requirements	19

13.4	Electronic/Electrical Requirements	19

13.5	Safety Requirements	19

13.6	Software Requirements	19

13.7	Interface Requirements	19

13.8	Reliability Requirements	19

13.9	Spares Requirements	19

13.10	Service and Maintenance Requirements	19

13.11	Documentation Requirements	19

14	Single Object IFU Science Instrument Functional Requirements	20

14.1	Architectural Assumptions	20

14.2	Optical Requirements	20

14.3	Mechanical Requirements	20

14.4	Electronic/Electrical Requirements	20

14.5	Safety Requirements	20

14.6	Software Requirements	20

14.7	Interface Requirements	20

14.8	Reliability Requirements	20

14.9	Spares Requirements	20

14.10	Service and Maintenance Requirements	20

14.11	Documentation Requirements	20

15	Glossary	21

Figure 1 Keck telescope structure	3

Table 2 Glossary of Terms	15

# Introduction

This document describes the functional requirements for W.M. Keck Observatory’s (WMKO) Next Generation Adaptive Optics (NGAO) system.  The Functional Requirements Document (FRD) flows down the requirements from the design-independent System Requirements Document (SRD) to a few high level systems (AO system, laser facility, science operations facility and science instruments).  These systems were chosen to divide the NGAO system into functions that would be required independent of the selected architecture.  The flow down of the requirements on the other hand is frequently a design choice that could be revisited.

# Scope and Applicability

This document establishes functional requirements for all of the AO system aspects of NGAO.

# References

## Related Documents

- Instrumentation Baseline Requirements Document.

- KAON 456.  NGAO System Requirements Document.

## Referenced Drawings

Table X lists the drawing numbers, revisions and date, source and title for all drawings referenced in this document.

# Revision History

| Version | Date | Author | Reason for revision / remarks |
| --- | --- | --- | --- |
| 0.0 | Apr. 17, 2007 | Wizinowich | Initial version |

# Overall System Architecture & Assumptions

## Purpose

The purpose of the background section of this document is to provide context and related information for the functional requirements defined in later sections of this document.

## Overview

The scientific and technical requirements for NGAO result in the following basic systems:

- AO system.  The AO system will likely consist of an AO enclosure, an opto-mechanical system, and software and electronics for both non real-time and real-time control.

- Laser facility.  The laser facility will likely consist of a laser enclosure, the laser(s), the launch facility including a beam transport system and launch telescope, safety systems and laser system control electronics and software.

- Science operations facility.  The science operations facility will primarily include the software and computers required to support operation of the AO system and science instruments.  This includes operating the systems for nighttime observing as well as pre- and post-observing activities.

- Science instruments.  The three highest priority instruments are currently a near-IR imager, a visible imager and a deployable near-IR integral field unit (IFU).  Three lower priority instruments have also been identified including a near-IR IFU, a visible IFU and an L and M-band imager.  There is also a requirement that the NGAO project be designed so as to allow the continued AO support of the Interferometer and the fiber injection module used for the ‘OHANA (Optical Hawaiian Array for Nanoradian Astronomy) project.

- Telescope facility.

The AO and laser facilities and the science instruments will have to interface with the telescope structure.  Figure 1 shows a schematic view of a Keck telescope.  The most likely location for the NGAO system and science instruments is on one of the Nasmyth platforms of the telescope.  Nominally we have chosen the left Nasmyth platform of the Keck II telescope as our starting point.  The most likely location for the projection telescope is behind the f/15 secondary mirror in the top end of the telescope.

Figure 1 Keck telescope structure

## Performance Budget Flowdown

# Overall Functional Requirements (Requirements for all Subsystems)

The purpose of the overall requirements section is to convey requirements that apply generally to the overall .

Note that the Observatory’s standard requirements for all new instrumentation are summarized in the Instrumentation Baseline Requirements Document.  Additional Observatory requirements specific to NGAO are listed in the following sections.

## Architectural Assumptions

The following architectural assumptions have been made in preparing this FRD:

- AO system located on the left Nasmyth platform of Keck II.

- Existing f/15 secondary mirror used to feed NGAO.

## Optical Requirements

## Mechanical Requirements

## Electronic/Electrical Requirements

## Safety Requirements

## Software Requirements

## Interface Requirements

## Reliability Requirements

## Spares Requirements

## Service and Maintenance Requirements

## Documentation Requirements

# AO System Functional Requirements

## Architectural Assumptions

The following architectural assumptions have been made regarding the AO system:

- An enclosure is required to perform the following functions:

  - Clean room

  - Humidity control

  - Background light suppression

  - Optics area temperature control

  - Separate electronics enclosure with glycol cooling

  - Input and output shutters

  - Ventilation for personnel

- An optics support structure is required.

- An optical relay is required to perform the following functions:

- A deformable mirror is required

- A tip/tilt stage is required to perform the following functions

- An optical switchyard is required to perform the following functions

- Atmospheric dispersion correction is required to perform the following functions

- LGS wavefront sensors

- Three fast low order wavefront sensors are required to perform the following functions

- A slow NGS wavefront sensor is required to perform the following functions

- NGS wavefront sensor

- One or more acquisition cameras are required to

- A calibration unit is required to

- The following alignment and diagnostic functions are required

## Optical Requirements

| # | Optical Performance Requirements | Discussion |
| --- | --- | --- |
| 1 | The telescope plus NGAO throughput to the science instruments shall be ≥ 70% at 0.6-5.5 µm |  |
| 2 | The telescope plus NGAO throughput to the interferometer shall be ≥ 60% at 5.5-14.0 µm |  |
| 3 | The telescope plus NGAO emissivity to the science instrument shall be ≤ the sky emissivity at K and L-bands |  |
| 4 | The rms wavefront error for the combined telescope, NGAO system and visible and NIR imagers shall be TBD for the following TBD conditions |  |
| 5 | The rms wavefront error for the combined telescope, NGAO system and visible and NIR IFUs shall be TBD for the following TBD conditions |  |
| 6 | The rms wavefront error for the combined telescope, NGAO system and deployable NIR IFU shall be TBD for the following TBD conditions |  |
| 7 | The rms wavefront error for the combined telescope, NGAO system and thermal NIR imager shall be TBD for the following TBD conditions |  |
| 8 | The rms wavefront error for the combined telescope and NGAO system delivered to the Interferometer shall be TBD for the following TBD conditions |  |
| 9 | The residual static wavefront errors from the NGAO system shall be ≤ 50 nm rms as delivered to the visible and NIR imagers |  |
| 10 | The NGAO system shall introduce ≤ TBD % polarization in the path to the TBD science instruments |  |
| 11 | The stability of the field produced by the NGAO system shall be TBD as delivered to the TBD science instruments |  |
| 12 | The rms residual tilt from the NGAO system output to the interferometer should be ≤ 0.007” |  |
| 13 | Instability must not decrease the Strehl on the visible and NIR imagers by more than 5% during any 1-hour period or over a 3 ºC temperature change | The image improvement provided by the facility must be stable over periods of hours, under stable atmospheric conditions. The wavefront sensor calibrations must be stable with time, temperature and telescope position. This requirement does not include performance degradations due to changing atmospheric conditions, or different magnitude and location of NGS or LGS |
| 14 | Instability must not decrease the Strehl on the visible and NIR imagers by more than 10% during any 24-hour period or over a 5 ºC temperature change |  |

| # | Optical Implementation Requirements | Discussion |
| --- | --- | --- |
| 1 | The field of view provided to the science instruments must be centered on the telescope elevation axis to within 2” |  |

| # | Optical Design Requirements | Discussion |
| --- | --- | --- |
| 1 | The focal ratio provided to the science instruments should be TBD |  |
| 2 | The exit pupil location provided to the science instruments should be TBD |  |
| 3 | The NGAO system should be capable of correcting TBD level of non-common path aberration in the science instruments | Image sharpening can be used to correct for aberrations in the science instruments. New science instruments should be designed to have small optical aberrations. The interferometer and possible legacy instruments such as NIRC2 or OSIRIS may be allowed larger aberration budgets. |
| 4 | The peak-to-peak range of tip/tilt correction provided by NGAO shall be ≥ 3” | The existing Keck AO systems have a peak-to-peak range of 1.6” which has proven to be inadequate in windy conditions. |

| # | Science Instrument Optical Design Requirements | Discussion |
| --- | --- | --- |
| 1 | A wavelength range of 0.6 to 1.0 µm must be provided to the visible science instruments (imager and IFU) |  |
| 2 | A wavelength range of 1.0 to 2.45 µm must be provided to the NIR science instruments (imager, IFU and deployable IFU) |  |
| 3 | A wavelength range of 3.0 to 5.3 µm must be provided to the thermal NIR imager |  |
| 4 | A field of view of ≥ 20”x20” must be provided to the science imagers (visible and NIR) |  |
| 5 | A field of view of ≥ 12” diameter must be provided to the visible IFU |  |
| 6 | A field of view of ≥ 16” diameter must be provided to the NIR IFU |  |
| 7 | A field of regard of ≥ 1.5’ diameter must be provided to the NIR deployable IFU |  |
| 8 | A field of view of 25”x25” must be provided to the L and M-band imager |  |

The following design requirements are imposed by the Interferometer and/or ‘OHANA support requirements.

| # | Interferometry Optical Design Requirements | Discussion |
| --- | --- | --- |
| 1 | A wavelength range of 1.1 to 14 µm must be provided to the Interferometer |  |
| 2 | A wavelength range of 1.1 to 2.45 µm must be provided to the OHANA injection module |  |
| 3 | A field of view of ≥ 1’ diameter must be provided to the Interferometer |  |
| 4 | A field of view of 5” diameter must be provided to the OHANA injection module |  |
| 5 | NGAO must be able to support a chopping mode for the interferometer. | The nuller requires small amplitude chopping with the AO loops closed at each end of the chop for alignment purposes. |
| 6 | The interferometer output of NGAO must be polarization matched to the interferometer output of the AO system on the other telescope in order to produce ≤ 3º of differential s-p phase shift | The current KI achieves polarization matching by keeping the number, angle and coatings of all reflections the same in the beam trains from each telescope. The differential s-p phase shift in the current KI is measured at 6º resulting in a loss in V2 of 0.003. |
| 7 | The interferometer output of NGAO must have the same image rotation as the interferometer output of the AO system on the other telescope |  |
| 8 | The interferometer output of NGAO must have the same pupil rotation as the interferometer output of the AO system on the other telescope |  |
| 9 | The interferometer output of NGAO must have the same longitudinal chromatic dispersion as the interferometer output of the AO system on the other telescope | Transmissive optics fabricated from different materials can have different amounts of longitudinal chromatic dispersion resulting in the loss of fringe visibility |
| 10 | The ratio of the Strehls from the interferometer output of NGAO and the interferometer output of the AO system on the other telescope must be ≤ 1.2 and ≥ 0.9. | A Strehl mismatch of 22% or an intensity ratio of 1.22 results in a V2 loss of 0.010. |
| 11 | NGAO must be able to accommodate the accelerometers needed to support the Interferometer | On the current AO bench one accelerometer is placed near the telescope focus and another near the output to the DSM. These are used to measure vibration along the optical path and are used in the fringe tracker control system. The accelerometer acquisition system is housed in an electronics rack in the AO electronics vault. |
| 12 | NGAO or NGAO in combination with a modified DSM must be capable of supporting the laser metrology beams from the interferometer | These metrology beams are a potential source of background light on the wavefront sensors |
| 13 | NGAO must incorporate the required tools and tolerances to support alignment to the interferometer | For example, the current AO bench hosts a corner cube to aid in aligning the interferometer to the optical axis of the AO system and telescope |
| 14 | NGAO or NGAO in combination with a modified DSM must provide a collimated 100 mm diameter beam to the interferometer | In the current AO system a removable (on a translation stage) dichroic beamsplitter, located between the deformable mirror and second off-axis parabola, folds the collimated beam to the DSM |

## Mechanical Requirements

| # | Mechanical Performance Requirement | Discussion |
| --- | --- | --- |
| 1 | The NGAO AO system shall not exceed a thermal dissipation budget, into the dome environment, of 100 W |  |

| # | Mechanical Implementation Requirement | Discussion |
| --- | --- | --- |
| 1 | The NGAO facility must allow a means to install new science instruments | For example, if a new instrument can only be installed with the overhead crane then a means of removing the appropriate portion of the AO enclosure roof would be required. |

| # | Mechanical Design Requirement | Discussion |
| --- | --- | --- |
| 1 | The maximum weight of the AO system on the Nasmyth platform shall not exceed 10,000 kg | The weight requirements are imposed by limits on what the telescope can support at various locations without changing its performance. |
| 7 | The NGAO facility must fit within the mechanical constraints of a Nasmyth platform (nominally the Keck II left Nasmyth platform) |  |
| 8 | The NGAO facility must provide access and space for the installation of each science instrument and a mechanical interface on which to mount each instrument |  |
| 9 | The NGAO facility must provide access for routine maintenance of the elevation bearing, elevation wrap, bent Cassegrain platform and mirror cell stairwell |  |
| 10 | The required glycol flow rate and pressure for cooling the NGAO facility shall not exceed TBD and TBD, respectively |  |

## Electronic/Electrical Requirements

| # | Electrical Performance Requirement | Discussion |
| --- | --- | --- |
| 1 | The AO system must not exceed a total electrical power requirement of 10 kW | From a total NGAO budget of 30 kW |
| 2 | The NGAO facility cabling through the azimuth wrap must not require an area of more than TBD |  |

## Safety Requirements

The general Observatory safety requirements that are also applicable to NGAO are already contained in the Instrumentation Baseline Requirements Document.  This section covers the additional laser safety and laser projection safety requirements.

Adequate earthquake restraints are also required for all systems.

## Software Requirements

Unless otherwise indicated all of the requirements of this section apply to all software components of NGAO.

| # | Software Design Requirements | Discussion |
| --- | --- | --- |
| 1 | The NGAO system must be able to support the external interfaces supported by the existing AO systems | The external keywords and EPICS channels used by the existing AO systems are documented in KAON 315, Summary of External Interfaces in the Current WFC and Implications for the NGWFC Design” |
| 2 | The NGAO system must be able to accept tip/tilt offloads from the science instrument |  |
| 3 | The NGAO system must be able to acquire and configure the AO system based on the star magnitude and spectral type provided in the target list |  |
| 4 | NGAO must be able to support a chopping mode for the Nuller mode of the interferometer |  |

## Interface Requirements

| # | Mechanical Interface Requirements | Discussion |
| --- | --- | --- |
| 1 | An agreed upon kinematic interface between the NGAO opto-mechanical systems and the telescope structure must be provided | Kinematic interfaces are proposed so that thermal changes do not distort optical benches. |
| 2 | NGAO must be compatible with the interferometer dual star module (DSM) or replicate its functionality | The current Keck AO systems interface to the interferometer via an opto-mechanical system known as the DSM. |
| 3 | An agreed upon mechanical interface between the NGAO electronics and the telescope must be provided |  |
| 4 | An agreed upon mechanical interface between any NGAO enclosures and the telescope must be provided. |  |
| 5 | An agreed upon mechanical interface between any NGAO glycol cooled systems and the telescope instrument and/or facility glycol systems must be provided |  |
| 6 | An agreed upon mechanical interface between any NGAO CCR-cooled systems must be provided |  |

| # | Electrical Interface Requirements | Discussion |
| --- | --- | --- |
| 1 | An agreed upon electrical interface for power between NGAO systems and the Observatory/telescope must be provided | The Observatory is responsible for providing power to the various NGAO system locations. |
| 2 | An agreed upon interface for communication between NGAO systems and the Observatory/telescope must be provided | The Observatory is responsible for the implementation of all cables between NGAO system locations. The Observatory must in particular approve all cabling required to go in the elevation or azimuth wraps. |

| # | Software Interface Requirements | Discussion |
| --- | --- | --- |
| 1 | An interface should be provided to offload tip/tilt errors to telescope pointing through the telescope drive and control system (DCS) |  |
| 2 | An interface should be provided to offload focus errors to the secondary mirror piston through DCS |  |
| 3 | An interface should be provided to offload coma errors to the secondary mirror tilt through DCS |  |
| 4 | An interface should be provided to offload segment stacking errors to the active control system (ACS) |  |
| 5 | An interface should be provided to write all appropriate NGAO keywords to the science instrument FITS header |  |
| 6 | An interface should be provided to allow NGAO to read/write NGAO science instrument keywords |  |

## Reliability Requirements

TBD

## Spares Requirements

TBD

## Service and Maintenance Requirements

TBD

## Documentation Requirements

TBD

# Laser Facility Functional Requirements

## Architectural Assumptions

## Optical Requirements

## Mechanical Requirements

## Electronic/Electrical Requirements

## Safety Requirements

## Software Requirements

## Interface Requirements

## Reliability Requirements

## Spares Requirements

## Service and Maintenance Requirements

## Documentation Requirements

# Science Operations Facility Functional Requirements

## Architectural Assumptions

## Optical Requirements

## Mechanical Requirements

## Electronic/Electrical Requirements

## Safety Requirements

## Software Requirements

## Interface Requirements

## Reliability Requirements

## Spares Requirements

## Service and Maintenance Requirements

## Documentation Requirements

# Telescope Facility Functional requirements

## Architectural Assumptions

## Optical Requirements

## Mechanical Requirements

## Electronic/Electrical Requirements

## Safety Requirements

## Software Requirements

## Interface Requirements

## Reliability Requirements

## Spares Requirements

## Service and Maintenance Requirements

## Documentation Requirements

# Science Instruments Functional Requirements

## Architectural Assumptions

## Optical Requirements

## Mechanical Requirements

## Electronic/Electrical Requirements

## Safety Requirements

## Software Requirements

## Interface Requirements

## Reliability Requirements

## Spares Requirements

## Service and Maintenance Requirements

## Documentation Requirements

# Deployable IFU Science Instrument Functional Requirements

## Architectural Assumptions

## Optical Requirements

## Mechanical Requirements

## Electronic/Electrical Requirements

## Safety Requirements

## Software Requirements

## Interface Requirements

## Reliability Requirements

## Spares Requirements

## Service and Maintenance Requirements

## Documentation Requirements

# Imagers Science Instrument Functional Requirements

## Architectural Assumptions

## Optical Requirements

## Mechanical Requirements

## Electronic/Electrical Requirements

## Safety Requirements

## Software Requirements

## Interface Requirements

## Reliability Requirements

## Spares Requirements

## Service and Maintenance Requirements

## Documentation Requirements

# Single Object IFU Science Instrument Functional Requirements

## Architectural Assumptions

## Optical Requirements

## Mechanical Requirements

## Electronic/Electrical Requirements

## Safety Requirements

## Software Requirements

## Interface Requirements

## Reliability Requirements

## Spares Requirements

## Service and Maintenance Requirements

## Documentation Requirements

# Glossary

Table 2 defines the acronyms and specialized terms used in this document.

Table 2 Glossary of Terms

| Term | Definition |
| --- | --- |
| ACS | Active Control System |
| ANSI | American National Standards Institute |
| AO | Adaptive Optics |
| DCS | Drive and Control System |
| DSM | Dual Star Module |
| FAA | Federal Aviation Administration |
| FOV | Field Of View |
| FWHM | Full Width at Half Maximum. |
| IFU | Integral Field Unit |
| KAON | Keck Adaptive Optics Note |
| KI | Keck Interferometer |
| LGS | Laser Guide Star |
| MTBF | Mean Time Between Failures |
| NGAO | Next Generation Adaptive Optics |
| NGS | Natural Guide Star |
| NIR | Near InfraRed |
| NIRC2 | NIR Camera 2 |
| NIRSPEC | NIR SPECtrometer |
| ‘OHANA | Optical Hawaiian Array for Nanoradian Astronomy |
| OSHA | Occupational Safety and Health Administration |
| OSIRIS | OH-Suppression InfraRed Integral field Spectrograph |
| TBC | To Be Completed |
| TBD | To Be Determined |
| WMKO | W. M. Keck Observatory |