## Slide 1: BTO layout and definitions
LLT assembly
M1a
M1b
M2
M3
M4
M5
(FSM)
M6
Q3
Q2
Q1
Q0?
LLT2
LLT1
Underlined = Pointing control already installed
Dashed = Not yet installed
White = Mirror or beamsplitter; Green = Dichroic
Total: 12 reflections, 6 transmissions.
Trolley
BS1
BS3
Chicago Sum-Frequency Laser
M0
SFG module
L1
L2
L3
Coude
window

## Slide 2: Requirements
Laser safety
  Co-aligned He-Ne
    Shutter can be opened only if Q3/Q0 ratio is above threshold.
    Q0 and Q3 must have sufficient dynamic range.
  No He-Ne
    Shutter is closed within 20ms if Q3/Q0 falls below threshold.
    Baffling is required to keep wayward beam in dome.
    Override needed to align BTO with dome closed.
Pulsed laser
  Signal on quad cells must be sampled during the laser pulse, with inter-pulse background sampled and subtracted.
Beam wander (~1 Hz)
  Closed-loop bandwidth of 10 Hz sufficient.
High-speed vibrations (~63 Hz)
  If vibrations cannot be damped, then closed-loop bandwidth of >80 Hz over Q0-M0 servo loop may be needed.