## Slide 1: Lasers for MCAO
Celine d’Orgeville (Gemini)
Iain McKinnie (CTI)
Edward Kibblewhite (UoC)
James Murray (Lite Cycles)
John Telle (SOR)

## Slide 2: Outline
Laser requirements for MCAO
Technology options
Laser system procurement
  schedule
  strategies
Gemini laser R&D program on Sum-Frequency Lasers (SFL):
  Coherent Technologies Inc. CW mode-locked SFL
  Univ. of Chicago/Lite Cycles macro-micro-pulsed SFL
  Starfire Optical Range CW SFL
Notes: Overview follows section 5.2 outline

## Slide 3: Laser performance requirements
Total power | “50-W class” laser
Power per LGS beacon | 6W-15W depending on: laser location (on center section/in pier) sodium abundance (low-average~2-3x109at/cm2) zenith angle (0-45°) Same as for conventional LGS AO system
Beam quality | Better than 1.2 times diffraction limited
Wavelength | 589.0nm 3S1/23P3/2 peak transition of Na D2 line
Polarization | Circular
Beam pointing | Excellent
Months
Na abundance (109 atoms/cm2)
Annual mean = 4.3 109 atoms/cm2
2
6
4
Notes: 4-5W: laser on center section, N=3 109 at/cm2, at zenith, PDE=80 PDE/cm2/s
6W: laser in pier, N=3 109 at/cm2, at zenith
15W: laser in pier, N=2 109 at/cm2, at 45deg zenith angle

## Slide 4: Laser performance requirements
Total power | “50-W class” laser
Power per LGS beacon | 6W-15W depending on: laser location (on center section/in pier) sodium abundance (low-average~2-3x109at/cm2) zenith angle (0-45°) Same as for conventional LGS AO system
Beam quality | Better than 1.5 times diffraction limited
Wavelength | 589.0nm 3S1/23P3/2 peak transition of Na D2 line
Polarization | Circular
Beam pointing | Excellent
Notes: 4-5W: laser on center section, N=3 109 at/cm2, at zenith, PDE=80 PDE/cm2/s
6W: laser in pier, N=3 109 at/cm2, at zenith
15W: laser in pier, N=2 109 at/cm2, at 45deg zenith angle

## Slide 5: Laser functional requirements
Location | On center section if possible (case A), if not in pier (B) or optics lab (C)
Control System | Fully automated laser system Interfaced with MCAO CS Elementary tasks and sequences include: prior-to-start internal check, automated start-up, automated shutdown, emergency shutdown, wavelength tunability (if applic.)
Diagnostics | Include: Output power, spectral characteristics, temporal profile (if applic.), spatial profile, internal status, enclosure temperature, coolant temperature and flow rate, accumulated hours + data-logging
A
B,C
A
Notes: 4-5W: laser on center section, N=3 109 at/cm2, at zenith, PDE=80 PDE/cm2/s
6W: laser in pier, N=3 109 at/cm2, at zenith
15W: laser in pier, N=2 109 at/cm2, at 45deg zenith angle

## Slide 6: Laser functional requirements
Location | On center section if possible (case A), if not in pier (B) or optics lab (C)
Control System | Fully automated laser system Interfaced with MCAO CS Elementary tasks and sequences include: prior-to-start internal check, automated start-up, automated shutdown, emergency shutdown, wavelength tunability (if applic.)
Diagnostics | Include: Output power, spectral characteristics, temporal profile (if applic.), spatial profile, internal status, enclosure temperature, coolant temperature and flow rate, accumulated hours + data-logging
Notes: 4-5W: laser on center section, N=3 109 at/cm2, at zenith, PDE=80 PDE/cm2/s
6W: laser in pier, N=3 109 at/cm2, at zenith
15W: laser in pier, N=2 109 at/cm2, at 45deg zenith angle

## Slide 7: Laser functional requirements
Environment | Includes: Altitude, temperature, humidity, wind speed, gravity orientation, vibrations, shocks, seismic acceleration, cleanliness Operational for typical MK and CP conditions  Thermally-insulated, temperature-controlled and vibration-free enclosure
Gemini standards | Includes: Mechanics, electronics, cooling, software, safety
Services | Compatible with available electrical and cooling services on telescope center section (case A)
Maintenance | Reasonably low < 3 days/ week of laser technician
Failures | MTBF(critical) >900h  laser specialist or vendor MTBF (minor) >100h  laser technician
Notes: 4-5W: laser on center section, N=3 109 at/cm2, at zenith, PDE=80 PDE/cm2/s
6W: laser in pier, N=3 109 at/cm2, at zenith
15W: laser in pier, N=2 109 at/cm2, at 45deg zenith angle

## Slide 8: Laser technology options
Dye lasers

## Slide 9: Laser technology options
Dye lasers
    Mature technology
    Dyes are messy, potential safety issue
  CW like ALFA
    Modified commercial system
    Limited output power (~ 4-6 W with some efforts)
    ALFA laser currently de-commissionned
  pulsed like Lick and Keck
    Complex to operate, inefficient format, large system
    Satisfying level of performance and reliability achieved at Lick during the past year
    Keck laser about to be mounted on telescope, operational by the end of 2001
    Keck and LLNL already considering solid-state upgrade/replacement for second–generation laser
 Not an option for MCAO

## Slide 10: Laser technology options
Solid-state and fiber lasers

## Slide 11: Laser technology options
Solid-state and fiber lasers
  Comparatively new in the field, but fast developments
  SS lasers can be flash-lamp- or diode-pumped (better electrical efficiency)
  Laser diodes: ever increasing lifetimes and decreasing prices
  Many different formats and many different technologies
  SS lasers (especially DPSS) can be compact and lightweight
 Better candidates for MCAO

## Slide 12: Many ways to generate 589 nm with SS technology...
Laser material
  bulk crystals, fibers
Laser format
  CW, Q-switched, mode-locked, macro-micro pulse
Non linear effects
  OPO, SFG, SHG
  Raman
...but difficult to get the power AND beam quality AND reliability at the same time and at a reasonable cost !
1
2
3
1
2
Optical Parametric Oscillation (OPO)
3
1
2
3
1
2
Sum-Frequency Generation (SFG)
3
1
2
3= 2
1
2
Second Harmonic Generation (SHG)
3
a
p
21
1
2
Raman anti-Stockes
Nd:YAG
Nd:YAG
SFG
589 nm
1.06 m
1.32 m
Sum-frequency laser
Nd:YAG
SHG
OPO
SFG
1.06 m
1.06 m
532 nm
891 nm
1.32 m
589 nm
OPO-based sum-frequency laser
p
s
21
1
2
Raman Stockes
Nd:YAG
Raman
SHG
1.06 m
1178 nm
589 nm
Raman laser (1)
Nd:YAG
Raman
SHG
1.06 m
532 nm
589 nm
Raman laser (2)

## Slide 13: Sodium lasers state of the art
Many existing laser prototypes (SOR, UoC, MMT, Lick, Calar Alto,...)
On-going laser work at other observatories (MMT, Subaru, Keck, ESO,...)
However:
  Only “laboratory tools” so far
  General lack of automation and reliability
  Insufficient output power level with regard to MCAO 50-W specification
NO 10-W FULLY ENGINEERED LASER commercially available

## Slide 14: Existing sodium LGS facilities
ALFA, Calar Alto Observatory, Spain (Max Planck Institüt)
  Ar+ laser pumped modified Coherent ring dye laser (CW, P ~ 4 W)
ALFA, Calar Alto Observatory, Spain (Max Planck Institüt)
  Ar+ laser pumped modified Coherent ring dye laser (CW, P ~ 4 W)
Lick Observatory (and soon to come Keck Observatory)
  Flash-lamp-pumped Nd:YAG-pumped pulsed dye laser built by LLNL (Lick: 11 kHz rep. rate, P ~ 15 W, Keck: 26 kHz rep. Rate, P ~ 20 W)
ALFA, Calar Alto Observatory, Spain (Max Planck Institüt)
  Ar+ laser pumped modified Coherent ring dye laser (CW, P ~ 4 W)
Lick Observatory (and soon to come Keck Observatory)
  Flash-lamp-pumped Nd:YAG-pumped pulsed dye laser built by LLNL (Lick: 11 kHz rep. rate, P ~ 15 W, Keck: 26 kHz rep. Rate, P ~ 20 W)
University of Chicago
  Sum-frequency laser (macro-micro pulse, 400 Hz rep. Rate, P ~ 8 W)
Notes: - ALFA: Calar Alto Obs., Spain
First laser propagation to the sky in JULY 1996
First LGS AO correction DEC 97
Diffraction limit attained: S=23% @ 2.2 micron (K)
- LICK: 3-meter Shane telescope at Lick Observatory located on Mount Hamilton, near San Jose, California
In SEPT, 1996, this system produced the first significant image improvement using high-order adaptive optics with a sodium-layer laser guide star as a reference.
- UoC: Apache Point Observatory: first laser propagation DEC 1995

## Slide 15: Laser procurement
October 1999
  MK laser RFP (10-W class laser)
  No contract awarded
January 2000
  Laser R&D RFP
    risk-reduction experiments in the field of sodium LGS laser technologies for LGS AO and MCAO
    9-12 month programs
    Pre-identified commercialization process
  12 proposals received including 8 worth consideration for
    fiber lasers
    Raman lasers
    sum-frequency lasers: most mature technology
Notes: Sodium laser state of the art
  Many existing laser prototypes (SOR, UoC, MMT, Lick, Calar Alto,...)
  On-going laser work at other observatories (MMT, Subaru, Keck, ESO,...)
  However:
    Only “laboratory tools” so far
    General lack of automation and reliability
    Insufficient output power level with regard to MCAO 50-W specification
  NO 10-W FULLY ENGINEERED LASER commercially available

## Slide 16: Laser procurement
March 2000
  2 contracts awarded
    Coherent Technologies Inc.
    University of Chicago / Lite Cycles (funding shared with NSF and CfAO)
  1 CRADA with AFRL/SOR (vendor would be LightWave Electronics)
  Program kick-off in June 2000
October 2000
  Submitted extensive NSF Proposal: “Facility Class Guide Star Laser Systems for Astronomical Adaptive Optics”
  PI: Brent Ellerbroek (Gemini), co-PIs: Robert Fugate (AFRL), Jerry Nelson (CfAO), Peter Wizinowich (Keck)
March 2001
  Response to NSF reviewers
Notes: Sodium laser state of the art
  Many existing laser prototypes (SOR, UoC, MMT, Lick, Calar Alto,...)
  On-going laser work at other observatories (MMT, Subaru, Keck, ESO,...)
  However:
    Only “laboratory tools” so far
    General lack of automation and reliability
    Insufficient output power level with regard to MCAO 50-W specification
  NO 10-W FULLY ENGINEERED LASER commercially available

## Slide 17: Laser procurement
May 2001
  Completion of CTI program
  Progress review of UoC/Lite Cycles and AFRL activities
Summer 2001
  New RFP for Gemini North laser system
Summer 2002
  Initiate MCAO laser system procurement
  Procurement strategy depends on
    Results from on-going and possible additional risk-reduction experiments, technology state of the art
    Altair laser system procurement
    NSF response to October 2000 proposal
    Choice of pulsed vs. CW laser
  More during Brent’s cost and schedule presentation !
Notes: Sodium laser state of the art
  Many existing laser prototypes (SOR, UoC, MMT, Lick, Calar Alto,...)
  On-going laser work at other observatories (MMT, Subaru, Keck, ESO,...)
  However:
    Only “laboratory tools” so far
    General lack of automation and reliability
    Insufficient output power level with regard to MCAO 50-W specification
  NO 10-W FULLY ENGINEERED LASER commercially available

## Slide 18: Sodium physics
F=2  F=3
D2 line:=589.2 nm
3P
3S
32S1/2
32P3/2
32P1/2

## Slide 19: Laser power requirements related issues
Top level LGS AO Strehl specification
  observation wavelength ?
  at zenith, 45 degree, 60 degree ?
Laser location
  distance to LLT
    highly impact BTO transmission coefficient
    ideally laser is located on telescope
  related issues are
    changing gravity environment, vibrations and temperature
    power supply limitations, cooling limitations

## Slide 20: Laser power requirements related issues
LGS spot size depends on
  seeing (r0)
  LLT aperture and laser beam diameter on LLT
    gaussian or top-hat profile
    should minimize beam clipping
    optimized beam size on LLT is ~ 2 to 3 x r0
Sodium abundance variability
  seasonal variations up to factor of 10
  single night variations up to factor of 3
  sporadic sodium layers as fast as 10 s time frame

## Slide 21: Laser power requirements related issues
Saturation depends on
  laser temporal and spectral format
  LGS spot size (note: you want it to be as small as possible to optimize WFS centroid measurements)
Now ... let’s have a look at the Gemini South laser power requirements per laser beacon

## Slide 22: How do we set laser power requirements?
1/Assume detector quantum efficiency and telescope optical transmission --> derive photon return requirement at the primary mirror of the telescope from number of photo-detection events (PDE’s) in MCAO simulations
2/ Assume (a) BTO, LLT and atmospheric transmission
(b) sodium layer parameters and seeing
(c) spatial, temporal and spectral characteristics of candidate laser
3/ Compute laser/sodium interaction efficiency (a) without, then (b) with saturation and find photon return as a function of laser output power
4/ Derive laser output power requirement from photon return requirement

## Slide 23: Is saturation an issue ?
Photon return (Photon/cm2/s)
Laser power (W)
Photon return vs. laser power (both at sodium layer i.e. TBTO=TLLT=Tatmo=1)
No-saturation limit
500 MHz
3 GHz
5 modes, 30 MHz mode spacing
Mono/multimode lasers give same results at the 10-W level
Not really an issue for CW and quasi-CW lasers, at least at the 10-W level
  10-15 % increase in power requirements when saturation taken into account, assuming small spot sizes
  Saturation effects can be balanced by adjusting spectral bandwidth
Can be a major issue for pulsed lasers with inefficient temporal formats such as the Keck laser when seeing conditions are good
  The spot size assumption has a major influence on laser power requirement, however reducing saturation by increasing spot size would be counter-productive in terms of WFS SNR optimization
Photon return (photon/cm2/s)
No-saturation limit
Pulsed laser (Keck format)
Saturation with r0 = 17 cm @ 589 nm
Saturation with infinite r0
Average power (W)
0
20
40
60
80
100
Not really an issue for CW and quasi-CW lasers, at least at the 10-W level
  10-15 % increase in power requirements when saturation taken into account, assuming small spot sizes
  Saturation effects can be balanced by adjusting spectral bandwidth
Laser power (W)
Laser bandwidth (MHz)
X
Inefficient spectral format (bandwidth > 3 GHz)
Max. efficiency zone
Maximum efficiency at the
10-W level
X
X
Saturation
Photon return per Watt of laser output power
6
14
18
10
Notes: - Contour plot
- 16 ns excitedlevel life time <-> 10 MHz natural (homogeneous) linewidth
-> velocity groups of sodium atoms are 10 MHz wide within the Doppler-broadened 3 GHz absorption line

## Slide 24: Laser propagation assumptions used to derive laser power requirements in the no-saturation limit
Months
Na abundance (109 atoms/cm2)
Annual mean = 4.3 109 atoms/cm2
2
6
4
A
B
Notes: Sodium abundance variation: Papen et al., 1996, Urbana, Illinois, 40 degree N

## Slide 25: Laser power requirements per laser beacon for a 10-MHz CW laser without saturation

## Slide 26: Laser power requirements per laser beacon (assumes 36 cm diameter spot size at sodium layer)
0°-med. Na 0°-low Na 45°-low Na
Notes: Calculations based on Peter Milonni and John Telle’s work to model laser light /sodium atoms interaction
CAUTION: John Telle says “In the simulation, the CW format is the only format for which collisionnal spin relaxation has been included. Without spin relaxation more optical pumping can occur and enhance the guide star radiance. Thus we believe the current small signal slope efficiency for the Macro-Micro pulse format may be too large.”