Palomar Adaptive Optics Test Plan

| Title | LOWFS Perfomance and Optimization |
| --- | --- |
| Date | 10/11/06 |
| Lead | J. Roberts |
| Time requested | 1 1/2 hours |
| Required conditions | Nighttime, NGS |

Purpose To check color sensitivity of the LOWFS

Previous analysis

Test procedure Acquire the first star in the list in the HOWFS Set the HOWFS to 50Hz and take a sky Set log wfp=ho, data=all, interval = 5 set the ttm integral gain to 0.8 Close TT loop Lock the HOWFS on the star and take 30sec of data. Turn off the HOWFS Acquire the star in the LOWFS Set log wfp=lo, data=all, interval = 20 wfs_cam on, id=lo, rate = 200 Steer off and take a LOWFS sky from TAO. set the ttm integral gain to 0.8 Close TT loop Lock the LOWFS on the star and take 30sec of data. Remain locked on the LOWFS and use PHARO to move in 5” steps east to get to ~25” off Take 30sec of data Open the loop, set the ttm integral gain to 0 and repeat steps 1-16 for the other star. Targets: 1. Tycho-2 2759-1527-1 vmag=12.19 b-v=-0.24 2759-1527-1 23 11 0.493 +35 21 12.57 2000.0 2. Tycho-2 2755-1512-1 vmag=12.20 b-v=1.11 2755-1512-1 23 06 58.576 +33 28 58.40 2000.0

Results and conclusions