Palomar Adaptive Optics Test Plan

| Title | LOWFS Perfomance and Optimization |
| --- | --- |
| Date | 10/11/06 |
| Lead | J. Roberts |
| Time requested | 3 hours |
| Required conditions | Nighttime, NGS |

Purpose To look at the closed loop bandwidth of the LOWFS at various frame rates To optimize the servo gains for the LOWFS

Previous analysis Wavefrot Error Budget LOWFS Calculated optimal frame rates for various magnitudes Magnitude Frame Rate Flux Predicted Bandwidth 8th 793 11328 31 10th 419 3397 17 12th 211 1069 8.4 14th 96 372 3.8 16th 38 150 1.5 18th 13 69 0.5 * saturated!

Test procedure Depending on the sky brightness, acquire either an 18th mag star or a 10th mag star in the LOWFS (first center star on dichroic spot). Set log wfp=lo, data=all Set the frame rate to the first listed in Table 1 for this magnitude star. Check that the flux is approximately what is expected. If not, adjust the frame rate. Steer off and take a LOWFS sky from TAO. Take a PHARO sky as well. Close TT loop Set the log interval as given in Table 2. Turn on the LOWFS and take data for approximately 30sec. Take a PHARO image. Set the TT servo gain to the first value in Table 3 for this star. Lock the LOWFS on the star and take 30sec of data and take a PHARO image. Continue to change the gains. Take 30sec of data and a PHARO image for each. Open the loop and repeat steps 3-9 for the rest of the frame rates (take PHARO skys as needed) Repeat steps 1-10 on each of the following magnitudes: 14th, 12th, 16th, (10th or 18th) Table 1 Magnitude Rate 1 Flux 1 Rate 2 Flux 2 Rate 3 Flux 3 Rate 4 Flux 4 10th 200 7123 400 3561 500 2849 700 2035 12th 100 2258 200 1129 300 753 400 564 14th 50 715 100 358 150 239 200 179 16th 30 189 50 113 100 56 150 38 18th 30 30 Table 2 Frame Rate 30-400 500-800 900-1000 1250-1500 Log Interval 1 2 3 4 Table 3 Frame Rate Gain 1 Gain 2 Gain 3 Gain 4 30-100 0.2 0.4 0.8 1.2 150-300 0.2 0.6 1 1.4 400 0.2 0.6 1 1.2 500 0.15 0.3 0.6 0.9 700 0.1 0.2 0.4 0.8

Results and conclusions