Palomar Adaptive Optics Test Plan

| Title | Internal Focusing for LGS operations |
| --- | --- |
| Date | 12/1/2006 |
| Lead | M. Troy |
| Time requested | 2 hr |
| Required conditions | - |

Purpose We outline here the procedure to co-focus the LOWFS, HOWFS and PHARO for night time operation. All work is done with the white light.

Test procedure Setup Reflecting spot should be in Laser mode? LOWFS load zero offsets Set rate to 500Hz HOWFS load zero offsets Set rate to 200 Hz Set log interval to 20 Turn WFS on Acquire white light in HOWFS with power at 40 Make sure LOWFS is off Take of load a white light flat map co-focus LOWFS and HOWFS to white light Lock in dual mode (see procedure XXX) zero LOWFS focus using wfs_z start, lgsfoc, set the LOWFS zero point to zero, set gain to 0.25 Turn lgsfoc “on” Note: insure HOWFS residuals show no focus, may need to decrease DM proportional servo loop term. note the old and new wfs_z position turn off lgsfoc re-focus white light to zero focus on DM (optional) close HOWFS loops on white light Setup TAO to offload focus to telescope, but prompt user (1mm of secondary motion = 22.9 mm of white_z (or wfs_ motion) Use the TAO prompts to move the ‘white_z’ motor to zero the focus on the DM. Note old and new white_z position Make new white light flat map Make DM flat map (ao_make_flat_map,’flat_map_white_light_<date>’ Open TTM and DM loops Re-focus acquisition camera move LOWFS out of the way Set the video camera to run at 1Hz, saving 1 frame a second Check to make sure the peak counts are less then ~100. If necessary decrease the white light power Shut off white light and take and save a background using ao_plot_vid_image in IDL Turn the white light back on and focus using ao_focus_loop, ‘current acq_z position’ -600, 300, 5, ‘acq ,’acq_wl_focus’,’sky name from step 4.3’,’time_to_avg=2 ao_read_focus,data,file=’acq_wl_focus_focus.dat’ move acq_z to optimal position and note new position Save new AO config file PHARO alignment re-focus PHARO lock HOWFS on zero offsets focus PHARO to maximize Strehl/minimize FWHM. re-tune centroid offsets in HOWFS

Results and conclusions 9/7/2006 wfs_z: starting position:10659 um, ending position: 7150 um white_z: starting position: 27500 um, ending position: 30917 um saved as 060908a did not re-focus acq camera, procedure above was not written did re-focus and tune up PHARO 10/11/2006 wfs_z: starting position:10650 um, ending position: 7260 um white_z: starting position: 27500 um, ending position: 29792 um acq_z: starting position: 14600 um, ending position: 14740 um did re-focus and tune up PHARO