Palomar Adaptive Optics Test Plan

| Title | LGS Acquisition and characterization |
| --- | --- |
| Date | 12/1/06 |
| Lead | A. Bouchez,M. Troy |
| Time requested | 1 hr |
| Required conditions | - |

Purpose Acquire LGS, focus LLT, determine LGS magnitude and spot size,

Test procedure Setup Configure AO to look at sky Telescope at zenith, at best NGS focus. Acquisition camera filter not installed. Move LLT mirror to its default position (determined during LLT alignment) [-11,53] Load best available flatmap Acq focused at 90 km altitude (NGS focus-2450) move acq_z 12300 (for NGS use 14740) LLT focused to 90 km altitude (NGS focus - 300). bto_control “move llt_focus 11564” check/set laser focus to correct value bto_control “move laser_focus 9500” Setup acquisition camera: Start up IDL program acqview Set integration time to 2s In an appropriate experiment directory: IDL> ao_plot_vid_image Perform final safety checks and fire laser Acquire LGS on Acq If LGS is not in the Acq. FOV, use ellipticity of dichroic spots (apex points to LGS) and Raleigh gradient (brighter towards LGS) to steer it in: offset llt_a +X=down; offset llt_b +X=left Move LGS onto HOWFS by clicking on “center LGS” Move LGS to clear region of ACQ. field: offset llt_b +30 Focus on Na layer Rough focus laser spot: bto_control “offset llt_focus …” in steps of 100 move acq_z … in steps of 300 Detune laser, take and save a 5s background image. Focus Acq ao_focus_loop, current-600, 300, 5, ‘acq’, ‘save_name’, ‘sky_name’, time=6.0 ao_read_focus, data,file=’save_name’ move acq_z best_focus Focus LLT ao_focus_loop, current-100, 50, 5, ‘llt’, ‘save_name’, ‘sky_name’, time=6.0 ao_read_focus, data,file=’save_name’ bto_control “move llt_focus XXX” Repeat steps 4.3 and 4.4 again if necessary Tune center wavelength This depends…. Take photometry Install V filter in Acq. camera Record and save a final set of detuned and tuned 5s Acq images for measuring photometry and spot size. Image photometric calibrator Go to photometric standard NGS, Landolt ~mV=11.0 Move acq_z to NGS focus Move star to approximate position of LGS Take two images, with a ~10” dither between them

Results and conclusions