Palomar Adaptive Optics Test Plan

| Title | NGS AO Checkout (12/06 v2) |
| --- | --- |
| Date | Every AO engineering night |
| Lead | A. Bouchez |
| Time requested | 20 minutes. Start after 6º twilight. |
| Required conditions | N/A |

Purpose Verify acceptable performance of the NGS AO system for subsequent engineering tests, and measuring seeing, on-axis Strehl and isoplanatic angle.

Test procedure Choose a binary star near zenith from the list below. Acquire the primary with the AO system with an initial frame rate of 500Hz. Adjust the frame rate to get 100-200 cts/subap on the WFS. Take a wavefront sensor sky. Perform both coarse and fine WFS-DM registration. Verify that co_default2 is loaded and that focus offloading is on. Close the TT and DM loops. Create a flat map on the star. IDL> ao_make_dm_flat_map, filename Set the flat map to default when complete. While waiting for the flat map, check signal levels on PHARO: Initial setup: 25mas FOV, filter Ks, ND 1%, standard cross, 2s integration. Adjust the exposure time and filter to get 10-15k peak counts on brighter star. With the loops closed, adjust tel. pointing to center both stars in the PHARO FOV. Open the TT and DM loops. Repeat the lenslet to DM registration. Offset to sky and take a new WFS background. Record 3 PHARO sky frames. Offset back to star and close TT and DM loops. Record 3 images with PHARO. Note the directory, frame numbers, and Strehl. Open the DM loop only. Record 1 image with PHARO, 30s integration. Note frame number and FWHM. Record the telescope focus.

Results (use one column per night) UT date Weather conditions PHARO directory Target WDS # 13. Sky frames 15. Closed-loop frames 15. Closed-loop Strehl 17. Open-loop frame 17. Open-loop FWHM 18. Telescope focus

Star list

Result of a VizieR search of the Washinton Double Star Catalogue (I/237) with the following constraints:  (DE2000: "18:20:00..48:20:00")  AND   (Sep1: "8..15")  AND   (Sep2: "8..15")  AND   (MagA: "5..7.5")  AND   (MagB: ">8")

This list is available in the Palomar format at: /export/home/pharo/lgs/wds2.lst

The digit in the first column provides a link to the Vizier page on the star.

Full    recno    RA2000  DE2000  pa1   Sep1   MagA   MagB

"h:m:s" "d:m:s"  deg arcsec   mag    mag

1      1632  00 32.8  +28 17  160    8.7   6.30  11.26

2      4755  01 41.3  +25 45   32   11.3   6.30  10.90

3      6043  02 09.6  +42 51  183   10.9   7.20  11.00

4      7194  02 38.3  +37 44  260    9.2   6.16  11.30

5      8161  03 01.5  +32 25    8    8.2   6.90   8.40

6     10866  04 09.6  +31 39  174   12.8   6.90  14.10

7     11686  04 28.9  +30 22   36   14.2   6.38   8.28

8     13555  05 09.8  +28 02   27   11.8   6.00   8.65

9     13915  05 15.4  +32 41  342   12.6   5.02  11.10

10     15769  05 43.0  +33 19  204   11.5   6.80  11.80

11     21453  06 51.6  +21 46  355   10.6   5.27  14.00

12     23030  07 06.2  +24 52   50   14.1   7.10  11.10

13     24579  07 22.0  +36 46    9   10.6   5.13  11.70

14     25336  07 29.8  +27 55  289   13.9   5.00  13.60

15     37648  11 38.7  +45 07  266   10.5   6.46   8.39

16     39044  12 17.5  +28 56  275    8.2   5.70  10.20

17     39405  12 28.1  +44 48  161   10.4   7.50   8.12

18     40881  13 10.9  +21 14  316   10.9   6.82  10.80

19     40900  13 11.5  +21 55  288   10.6   6.82  10.90

20     42896  14 06.7  +34 47   71   14.2   7.00  10.20

21     52744  18 01.6  +33 19  202   13.3   6.15  13.30

22     52898  18 03.9  +26 39  193   12.4   7.00  12.00

23     57496  19 03.9  +34 09  295   11.1   7.30  12.80

24     57902  19 08.8  +34 46  271   12.9   7.00   8.60

25     60632  19 41.3  +30 43   29    9.1   7.30  13.40

26     61322  19 49.0  +19 09  311    8.6   5.04   9.03

27     64828  20 24.2  +29 00  134   13.0   7.20  11.20

28     67000  20 47.2  +34 22  194   12.4   5.20  11.50

29     67003  20 47.3  +45 35   75   14.0   6.40  12.40

30     68168  21 03.5  +24 00  299   13.1   7.40  13.40

31     68328  21 05.7  +47 48  315   10.4   7.45  12.00

32     69741  21 24.1  +25 19  330    8.5   6.20  12.20

33     74560  22 46.0  +19 15  270    8.7   7.47  10.80

34     75567  23 07.4  +20 35  335   13.5   6.70  10.40