Palomar Adaptive Optics Test Plan

| Title | LGS and NGS acquisition and lock |
| --- | --- |
| Date | 12/1/06 |
| Lead | M. Troy |
| Time requested | - |
| Required conditions | - |

Purpose Acquire NGS and LGS, Lock all loops and be ready to perform science at this end of this procedure

Test procedure Setup This procedure assumes the LGS acquisition and characterization procedure has been executed Load co_zero centroid offsets for HOWFS Set servo loop gains llt_integral_gain 1.6 dm_proportional_gain 0.02 Focus acquisition camera to NGS, ‘move acq_z 14600’ Set chopper delay and gate on generator using PC delay value = 58400 Gate value = 3998 Move Telescope to a bright star near the TT NGS (follow BTO slew procedure) Move telescope to put NGS on HOWFS Lock on NGS star Register DM Lock TT and DM as normal and offload focus to telescope Make new telescope flat map and load Move telescope back to TT NGS ttm_integral_gain 0.15 dm_integral_gain 0.15 Pre-pare for LOWFS lock Using TAO select LGS mode (Under the Observation menu) Set HOWFS camera frame rate for LGS Focus acquisition camera to LGS, ‘move acq_z 12350’ Propagate laser Verify BTO HS lock on Q3 Center Laser on reflecting spot, using acqview (center LGS button) Set HOWFS z stage start lgsfoc in IDL, set Height to 90km, send HWFS stage by clicking 1-shot, WFS stage should move to 80,840um Find laser in HOWFS to verify location and approximate frame rate Lock LOWFS Focus acquisition camera to NGS, ‘move acq_z 14600’ Start up LOWFS plots, ‘ao_plot_lo_gui’ in IDL Move LOWFS to star using acqview (send LOWFS button) Set LOWFS camera rate, ‘wfs_cam id=lo,rate=XXX’,gain=0 Take sky Move telescope 60” E From TAO menu take LOWFS sky CCC Move telescope back re-start LOWFS, wfs_cam on, id=lo Log all data, log wfp=lo, data=all Startup pixel display, ‘ao_display_latest_lo_pixel’ in IDL Zero LOWFS centroids, using acqview zero_lo_cent button Lock, TTM using button on TAO Check lock performance in plots Lock HOWFS on LGS Start up LGS IDL plots (ao_plot_gui_lgs_hwfp) Start Chopper Using terminal window on PC Set to external reference Set to run Check chopper settings Startup aomonitor in idl to check average counts Startup connection to delay generator (see setup procedure) Detune laser Adjust delay on chopper (channel 3) to see no Rayleigh. Find the limit where Rayleigh is just visible. Retune laser Adjust delay to see maximum signal. Find the limit where signal starts to drop off. Select a delay time between the two limits Set WFS camera to best estimate for framerate (100Hz) Take sky offset llt_a 20 arcseconds From TAO menu take HOWFS sky offset llt_a -20 arcseconds turn howfs on, wfs_cam on, id=ho set log interval to avoid late messages, ‘log wfp=ho, interval=10’ Lock LLT Type “llt on” Check performance in GUIs Lock DM Click on DM button on TAO Start focus offloading from LOWFS In /data/scratch start idl and run “lgsfoc” Verify LOWFS focus offset is 0 With LOWFS locked on TT and the DM loop locked on the laser, set the loop to On.

Results and conclusions