Palomar Adaptive Optics Test Plan

| Title | Internal Focusing for LGS operations |
| --- | --- |
| Date | 1/5/2007 V3.1 |
| Lead | M. Troy |
| Time requested | 2 hr |
| Required conditions | - |

Purpose We outline here the procedure to co-focus the LOWFS, HOWFS and PHARO for night time operation. All work is done with the white light.

Test procedure Setup Reflecting spot should be in Laser mode LOWFS load zero offsets Set rate to 500Hz HOWFS load zero offsets Set rate to 200 Hz Load pixel_gains_lse_sep03 Acquire white light in HOWFS with power at 40, Lock TT and DM loops Make sure LOWFS is off Take and load a white light flat map IDL> ao_make_dm_flat_map,’filename’ co-focus LOWFS and HOWFS to white light Lock in dual mode (see procedure XXX) Lock TT on LOWFS and DM on HOWFS zero LOWFS focus using wfs_z start, lgsfoc, set the LOWFS zero point to zero, set gain to 0.25 Turn lgsfoc “on” Note: insure HOWFS residuals show no focus, may need to decrease DM proportional servo loop term. turn off lgsfoc note the old and new wfs_z position re-focus white light to zero focus on DM (optional) close HOWFS loops on white light Set DM proportional gain to zero Setup TAO to offload focus to telescope, but prompt user (1mm of secondary motion = 22.9 mm of white_z (or wfs_ motion) Use the TAO prompts to move the ‘white_z’ motor to zero the focus on the DM. Open and close DM loop after moving white_z Note old and new white_z position Reset DM proportional gain to 0.02 Make new white light flat map Re-focus acquisition camera move LOWFS out of the way Set the video camera to run at 1Hz, saving 1 frame a second Set white light power to 20 Check to make sure the peak counts are less then ~100. If necessary decrease the white light power Shut off white light and take and save a background using ao_plot_vid_image in IDL, call it acq_wl_bkgd Turn the white light back on and focus using ao_focus_loop, ‘current acq_z position’ -600, 300, 5, ‘acq’ ,’acq_wl_’, sky=’acq_wl_bkgd’, time_to_avg=2 move acq_z to optimal position and note new position Save new AO config file PHARO alignment re-focus PHARO lock HOWFS on zero offsets focus PHARO to maximize Strehl/minimize FWHM. re-tune centroid offsets in HOWFS

Results and conclusions 1/5/07 (V3.1) wfs_z: starting position: 10800, ending position: 10540 white_z: starting position: 29790, ending position: 33256 acq_z: starting position: 14600, ending position: 14600 12/6/06 wfs_z: starting position: 10400, ending position: 10800 white_z: starting position: 29792, ending position 29792 acq_z: starting position: 14600, ending position: 14600 Did tune up on PHARO, no refocus req’d 10/11/2006 wfs_z: starting position:10650 um, ending position: 7260 um white_z: starting position: 27500 um, ending position: 29792 um acq_z: starting position: 14600 um, ending position: 14740 um did re-focus and tune up PHARO 9/7/2006 wfs_z: starting position:10659 um, ending position: 7150 um white_z: starting position: 27500 um, ending position: 30917 um saved as 060908a did not re-focus acq camera, procedure above was not written did re-focus and tune up PHARO