Palomar Adaptive Optics Test Plan

| Title | Dual NGS |
| --- | --- |
| Date | 1/5/07 |
| Lead | J. Roberts |
| Time requested | ½ hour |
| Required conditions |  |

Purpose Acquire white light or star in both LOWFS and HOWFS

Test procedure Acquire source on the HOWFS (register and lock) Start acqview Send LOWFS to the source Turn on LO camera and start up plots Take a LO background Zero LO centroids Close the TT loop Zero HO centroids Close DM loop