## Slide 1: Questions on IFPAC_SCHEMATIC

## Slide 2: Signal Chain Preamplifier
Compensation Capacitor should go to –Vs, not GND
Where is resistor
For compensation
Network?
Does compensation keep the
amplifier from oscillating?
Gain for preamp is ~9.2x and the
signal will hit the amplifier rails with
a full well signal

## Slide 3: Signal Chain Preamplifier
Has large signal gain (~9.2x) and the output voltage range is ~+/- 3.7V. The amplifier will hit the rail at ~57,500 e- which is less than full well.
Has the compensation capacitor been connected to the negative supply voltage?
Datasheet recommends a resistor in the compensation network. Has this been added?
Does compensation capacitor prevent oscillation?

## Slide 4: Analog Second Stage
Need 33pF in parallel to
Make truly differential

## Slide 5: Analog Second Stage
Has a 33pF capacitor been added in parallel to R67?

## Slide 6: Integration Amplifier
Is there a logic to the capacitor values?
Why are there two in parallel?
Open loop is possible in this configuration

## Slide 7: Integration Amplifier
Is there a logical scheme to the values of capacitors chosen?
Why are there two capacitors in parallel in each feedback path?
Putting the amplifier into open loop is possible with this configuration. How is this prevented?

## Slide 8: Amplifier Bypass Capacitors
These are the only bypass capacitors for
All of the op-amps. There should be a pair
near each op-amp.

## Slide 9: Amplifier Bypass Capacitors
Have bypass capacitors been added for each amplifier on board?
Oscillation problems can occur without these capacitors. What have the tests of the board shown?

## Slide 10: Buffer Amplifier
Amplifier has -1 or fractional gain(!?)

## Slide 11: Buffer Amplifier
Multiple resistors in feedback path create a small feedback resistor. This makes the amplifier attenuate the signal. Is this what was intended? Why?

## Slide 12: ADC Questions
Supply voltage same as amplifiers
Need high speed ceramic cap too
On RefIn pin

## Slide 13: ADC Questions
The ADC uses the amplifier supply voltage. Does this voltage need to be regulated or does using this voltage deliver acceptable results?
Does the datasheet call for an additional high speed ceramic capacitor on the RefIn pin?

## Slide 14: ADC Input Question
Please describe the
signal input scheme for
the ADC

## Slide 15: ADC Input Question
Could you please describe/explain the ADC signal input scheme
What is the equation for the input signal?
Do all of the offsets keep the signal within the voltage range of the ADC?

## Slide 16: Bias Amplifier
Values missing
Unstable topology

## Slide 17: Bias Amplifier
What are the values of resistors R551 and R552?
Placing R551 within feedback loop increases output impedance and can cause unstable behavior. Why is R551 placed where it is?

## Slide 18: Number of Bias Lines
All inputs are used, but only two outputs are used

## Slide 19: Number of Bias Lines
All inputs have voltages, but only two outputs are used. Are there more bias lines available on this card?
Have more bias lines been implemented on the already built card?

## Slide 20: Backplane Connector
Backplane connector
Is high density and will
be hard to probe.

## Slide 21: Backplane Connector
The connector is very high density and we are concerned that probing the signals will be difficult.
Is it possible to use a lower density connector?
What percentage of pins in the connector are used?

## Slide 22: Backplane Traces
Backplane traces are small and close together.

## Slide 23: Backplane Traces
Backplane traces are small and close together.
What are the trace widths?
What is the spacing between traces?
Has there been any crosstalk problems?
Has there been any manufacturability problems?

## Slide 24: Improper Trace Clearance
Concerned that there is
not enough clearance
between trace and
mounting hole

## Slide 25: Improper Trace Clearance
There seems to be no clearance between mounting hole and signal trace
What is the spacing between mounting holes and traces?
Has there been manufacturability problems with the current spacing?