## Slide 1: Single Board Controller Comments
Roger Smith
Caltech
2013-05-13

## Slide 2: Single Board Controller
Motivated by the need for high ADC clock rates
  Clocks exceeding 140 MHz (or more)
  FPGA adjacent to ADC is necessary
Eliminates backplane complexity
  High speed signals no longer travel along backplane
Advantage of a single low impedance analog ground plane
Board performance not affected when placed on extenders
Final package has A/C power in and USB out

## Slide 3: Single Board Challenges/Questions
Will everything fit on a single board?
  Would like to use standard size (eg. 6U VME board)
  Custom size board not out of the question
  Custom sizes require a custom enclosure
Power requirements
  Associated power board with single board controller
  Do power requirements allow for a compact power supply board?
Other questions/challenges?

## Slide 4: Electronics box
We are contemplating a single board CCD controller to operate both science and guide CCDs, plugging this directly into a slightly extended vacuum interface board.
Plug-in power supply between board and dewar within same enclosure.
Remove side panel to gain access to test points on controller board.
Board dimensions are TBD.
Box mounts to flat faces of dewar. Its ok to have to remove boards to access bolts.
Cooling by conduction to dewar.
Front panels with ejectors
Power modules
8 ch CCD controller
283 mm
AC power
USB over fiber

## Slide 5: Electronics box mount
PCB dimensions are yet TBD….
Options to consider:
Eurocard 6U = 230mm wide * 160mm deep like VME.
Extended 3U = 100mm wide * 230mm deep like Leach controller.
  This provides less lateral overhang.
  Is this enough board area?
  Do Vicor power modules fit in this space?
Plug in Power
Controller
278 mm

## Slide 6: Electronics box – faceted option
If we go with two 4ch single board controllers, there is the option of placing the boards side by side along the circumference. (Leach controller boards are 100mm wide * 230mm deep)
Advantages:
Easier trace routing through VIB
Direct heat sinking to dewar for all boards.
Very compact.
Disadvantages ?
Unusual enclosure topology? Is this really a problem?
Plug in Power
4ch Controller
92 mm
4ch Controller
114 mm

## Slide 7: Ground plane topology
Four ground planes join here:
Digital
Analog supply return
Analog reference (not shown)
Clock (high current analog)
Digital
USB
DCDS Fast FPGA
Sequencer
Dense FPGA
ADC
ADC
ADC
ADC
ADC buffers
Bias DACs
Connector
Clock DACs
Clock Drivers
Clock Switches
Card ejectors
Front Panel
Power planes mimic grounds but need low impedance paths to connector
Bias Drivers
TBD whether FPGAs are same device or separate.