## Slide 1: Data Handling
Stephen Kaye
Caltech
2013-05-23

## Slide 2: Data Format in Pipeline
16 Bit data from ADC
FPGA combines multiple conversions (subtract 5 reset, add 5 charge, no normalize)
>19 bit data is sent over USB link
  >19 bits * 1MSPS = >19 Mbps for each ADC
  2 CCDs = >38 Mbps
  FPGA must double buffer it can simultaneously send data over USB for previous pixel while coadding data for present pixel
Received data will be compressed before write to disk
  Rice Tile Compression
  Compress data on the fly using FPACK from CFITSIO library.
  Need to benchmark speed but with modern processor compression is probably faster than disk write.

## Slide 3: Testing Data Pipeline
Need to demonstrate full functionality for one data path
  Convert at 10 MSPS
  Sum multiple conversions
  Send >19 bit data to host @ 1 MHz
  Write compressed data to disk
Tests Data Rate from Controller to RAM
  Full speed ADC
  Functional USB link
Test File Write Speed
  Previous test plus…
  Compression algorithm for on the fly data
End to end test with multiple USB ports. How many ports can be serviced per server.

## Slide 4: Deliverables
Would like to make test system part of deliverable
Requires
  ADC (dummy data. E.g. grounded input)
  FPGA
  USB link, with fiber extender.
  Host computer software
Early deliverable since it doesn’t require clocks, biases, or signal chains.
To test multiple USB ports, only need FPGA onwards.
  Whether testing one USB link or more, need artificial data generation in FPGA, sending fixed pattern (eg incrementing pixel counter) in place of ADC output.