## Slide 1: ZTF Observing System
Roger Smith, Systems Engineer
NSF visit to Caltech
2014-07-24

## Slide 2: Outline
Camera comparisons
Technical challenges
Subsystem walk through
  Key strategic choices
  Enabling technologies

## Slide 3
LSST
DECam
ZTF

## Slide 4: Prime focus cameras*
 | DECam | ZTF | LSST | 
Telescope, Location | 4m Chile | 1.2m Palomar | 8.4m Chile | 
Field of View | 2.9 | 47 | 9.8 | degree2
Survey Speed | 130 ? | 3800 | ~900 | deg2/hour
Collecting area | 9.9 | 0.87 | 35 | m2
Image Scale | 0.27 | 1.0 | 0.2 | arcsec/pixel
Science Pixels | 520 | 606 | 3170 | Mpixel
Camera + filter size | 1.6 x 2 | 0.48 x 0.44 | 1.65 | m
Focal Plane Diameter | 480 | 560 | 634 | mm
Overhead per pointing | 20 | 10 | 3+5 | sec
Readout Channels | 124 | 64 | 3024 | 
Pixel/channel | 4 | 9 | 1 | Mpixel
Pixel rate per ch. | 200 | 1000 | 500 | kHz
*PanSTARRS, Skymapper and JPAS are at cass. focus

## Slide 5: Technical Challenges for ZTF
Cost: maximize survey volume per unit time per dollar,
  For objects bright enough for spectroscopic follow up.
Compactness: minimize beam obstruction
   large focal plane at prime focus on relatively small telescope
  Shutter blades and filters stow outside telescope
Minimize dead time:
  15s readout time (10s goal)
  Faster telescope repointing
  Faster dome move
  Fast shutter
Near real time data transfer and analysis

## Slide 6: Strategic decisions
Coarse image scale:
  Big pixels on sky  more sky photons  higher read noise  faster readout  lower channel count = less electronics & lower CCD optimization costs
  Fewer pixels  less silicon to buy, less data to store transport and process.
  Matches Image quality of telescope and site
  DIQ more sensitive to lateral charge diffusion
Conventional CCDs, maximum size
  Lowest cost per unit area
  Fewer parts
  Good fill factor without extreme tolerances

## Slide 7: Key technology choices
Cold field flatteners
  Halves the radiative load  small cheap cooling system
Vacuum interface board
  Eliminate dewar wiring and hermetic connectors
  COTS cables to electronics outside telescope tube.
Differential signal transmission
  Robust, high speed signal transmission to electronics outside telescope  low crosstalk and fast settling; COTS electronics
Pupil plane shutter
  No beam obstruction
  Force balanced (bi-parting)
  Made and tested off-site
Cover these points during walk-through….

## Slide 8: ZTF Walk through

## Slide 9
3 corrector elements, 1.2m pupil
Bi-parting shutter
Forward baffle
3 spider vanes containing cables
Declination axis
Primary mirror
Hexapod hidden within prime focus hub
Dewar window
Enlarged instrument hatch
Unused plate loading hatch
S
N
E
w

## Slide 10: Dome
New speed-controlled drive.
Velocity profiling
  arrive just in time
  Trajectory based on next exposure, as well as present
  cruise through
  accelerate before shutter closes
Reinstate windshield

## Slide 11: Telescope
New baffles in front of shutter and inside tube
Lower gear ratio on declination axis; retune  faster slews
  …Use existing high resolution direct shaft encoder
Enlarge access door and instrument handling fixtures.
Seal, clean and repaint interior
Flush tube with dry (and filtered) to prevent condensation on window (and dust on optics)

## Slide 12: Shutter:
Original shutter behind corrector to be replaced with flat blades in front.
Pupil plane  bi parting  balanced
  Impact on pointing testable in advance
Shutter air extractor to clean blades.
Wind screen to be re-instated

## Slide 13
Bonn Shutter team has extensive experience

## Slide 14
Bonn Shutter team has extensive experience
Dual motor, focal plane shutters
Single motor, pupil shutter, bi-parting
2g acceleration, 3kg/blade, balanced.

## Slide 15: Optics
Powered window supports 2.3 ton force of atmosphere with FoS=6.
3rd corrector element  fixes aberrations caused by thick dewar window.
CCDs faceted on spherical focal surface.
Plano-convex field flatteners
  Compensate for residual field curvature
  Substrate for fixed G and R filters
  act as radiation shield, halving thermal load.
Upgrade to exchangeable (flat) filter can be supported.

## Slide 16: ZTF Dewar
Meniscus window
Frames for field flatteners (previous version)
CCDs faceted on spherical surface
Aluminum mount with integrated flexures
COTS cables connect around perimeter of VIB
Physik Instruments
Hexapod
Polycold Joule Thompson coolers (2)
Charcoal getter container
TechApps flexible thermal link
1mW/K kapton flex circuits from CCDs
Ring girder carrying spiders
Spiders (3)
Vacuum Interface Board
trapped between two O-rings
Designed by LBNL, guided by Caltech

## Slide 17
How ZTF can be so much simpler than LSST:
50 times fewer readout channels, due to…
Half as much silicon
1.5 times pixel size
Twice pixel rate
Faster shutter
1 readout per pointing not 2
5x longer readout time to match slew (unlike LSST)

## Slide 18
ZTF electronics outside telescope:
no custom ASICs,
looser power budget
smaller cooling system
much easier assembly
LSST electronics are in vacuum!

## Slide 19: ZTF Dewar
Meniscus window
Frames for field flatteners (previous version)
CCDs faceted on spherical surface
Aluminum mount with integrated flexures
COTS cables connect around perimeter of VIB
Physik Instruments
Hexapod
Polycold Joule Thompson coolers (2)
Charcoal getter container
TechApps flexible thermal link
1mW/K kapton flex circuits from CCDs
Ring girder carrying spiders
Spiders (3)
Vacuum Interface Board
trapped between two O-rings
Designed by LBNL, guided by Caltech

## Slide 20: Hexapod and Spiders
New spiders reduce beam obstruction
  support new hexapod
  conceal cables
  3 instead of 4 …. shorter diffraction spikes.
Generic hexapod from Physik Instruments provides ample resolution.
Long travel useful for optical diagnostics.
All 6 degrees-of-freedom used:
  Focus, tip, tilt
  XY for optical alignment.
  Field rotation due to atmospheric dispersion and polar axis misalignment.

## Slide 21: Delivered Image Quality
3 extra focal imaging CCDs at edge of focal plane for…
  focus, tilt sensing
  mirror figure and optical alignment diagnostics
2Kx2K auto-guider in 4th corner of focal plane used for long exposures or diagnostics.
Full DIQ budget has been developed.
Guide telescopes no longer used
Edwin Hubble
1889-1953

## Slide 22: Electronics
Commercial CCD controller outside telescope.
STA’s “Archon” is optimized for high pixel rate.
Drives 4 CCDs with ganged clocks.
16 true differential CCD outputs; preamps in dewar drive differential transmission line.
Vacuum interface board eliminates dewar wiring and hermetic connectors.
Rear cover flange

## Slide 23
P48 Control Room
RAID Disk
Server
1 of 5
Communications
Shared
Gbit Ethernet
HPWREN
155Mb/s
0.9 TB/night, compressed.
Daily average ~100 Mb/s
Clk & Sync
RAID Disk
Server
2 of 5
RAID Disk
Server
3 of 5
private Gbit Ethernet
private Gbit Ethernet
<512 Mb/s
Archon 1 of 5
CCD
Clock boards(3)
CCD
CCD
4ch ADC
CCD
Clock boards(3)
8 Clocks (3)
4ch ADCs (4)
4ch ADCs (4)
4 ADCs (4)
Motherboard
30 Biases
Archon 1 of 5
CCD
Clock boards(3)
CCD
CCD
4ch ADC
CCD
Clock boards(3)
8 Clocks (3)
4ch ADCs (4)
4ch ADCs (4)
4 ADCs (4)
Motherboard
30 Biases

## Slide 24: Data transport
Responsibilities and mechanisms same as PTF:
Observing System (COO)
  each controller has separate data link to a server with local disk
  tile-compressed FITS file per CCD; header not compressed.
  monitor disk usage, but no responsibility to notify.
Palomar (POMO)
  maintain physical link (HPWREN)
  trawl for new FITS files (on 5 servers)
  copy images to IPAC
  delete from servers only when successful
IPAC:
  provides repository to receive data
  detects new data and initiates processing.
Tolerant of loss of CCD controller or link outage.

## Slide 25: Observing System Summary
ZTF is optimized for cost effectiveness.
  Leverage existing facilities and expertise.
  High sensitivity (QE, beam obstruction, DIQ)
  Low overheads (shutter, readout, repointing)
  Simple
   Relatively easy to commission and maintain.
   Reliable