## Slide 1: ZTF Filter Mechanism Design Concept Proposal
M. Porter
2016-01-22

## Slide 2: Rail System Architecture
Loading position
Storage position
Jukebox
Carriage
Rails
Courtesy of J. Zolkower

## Slide 3: Rail System Operation
Filter deploy sequence
Jukebox motor actuate to position selected filter
Jukebox carriage to Rail carriage hand-off (TBD actuation)
Rail motor actuate to extend rails
After full extension, +Z stage actuation to dock filter to window
Filter hand-off (to instrument) and latch sequence
-Z stage actuate
Rail motor actuate to retract rails

## Slide 4
Filter
Carriage
Rail
Carriage
Jukebox

## Slide 12: Rail System Operation (Con’t)
Filter retrieve sequence
Jukebox motor actuate to position unoccupied filter carriage
Rail motor actuate to extend rails
After full extension, +Z stage actuation to dock filter to window
Filter hand-off (to rail-side carriage) and latch sequence
-Z stage actuate
Rail motor actuate to retract rails
Rail carriage to Jukebox carriage hand-off (TBD actuation)

## Slide 13: Robotic System Architecture
Filter cartridges
Filter cartridges
Loading position
Storage position
End effector
Filter storage
Kuka KR10 R1100

## Slide 14: Kuka KR10 R1100
Cost: $40k, Weight: 54kg

## Slide 15: Robotic System Operation
Filter deploy sequence
Robot arm maneuver to selected filter
Filter storage to end effector hand-off (TBD actuation)
Robot arm extracts filter and position under instrument window
Filter hand-off (to instrument) and latch sequence
“Handshake” confirmation before end effector release
Robot move to stowed position

## Slide 24: Robotic System Operation (Cont’d)
Filter retrieve sequence
Robot arm position under filter window
End effector engage and latch onto filter
Filter hand-off (to robot) and interlock sequence
Robot arm extract filter and maneuver to selected filter slot
Robot to filter storage (TBD actuation)
“Handshake” confirmation before end effector release
Robot move to stowed position

## Slide 25: Hand-off & latching approaches
Active | Passive
Solenoid driven pin | Potential trap
Rotary latch | Interlocking pawls
Zero point chuck | Internal latch lock pin
Pulley gang latch | Mechalogic
Keeper | 
Multi-dof robot gripper | 

## Slide 26: Example hand-off & latch sequence

## Slide 27: Requirement compliance
REQ | Title | Summary | Goal | Req’t | Rail CBE | Robot CBE
0105 | Operating Modes | Exchangable, full-field spectral defining filter in front of instrument FOV | Y | Y | Y | Y
0110 | Commissioning and Service Modes | Commissioning, alignment, maintenance, and non-science modes should be supported | Y | Y | Y | Y
0115 | Number of Filters | Shall allow 3 usable filters per night without human intervention | 3 | 3 | 3 | 3
0120 | Filter Safety (Environmental) | All filters and optics shall be protected from harm | Y | Y | Y | Y
0125 | Filter Safety (During Service) | Filters shall be protected during human activities in telescope | Y | Y | Y | Y
0130 | Earthquake Safety | Positive margin on ultimate during equivalent quasi-static acceleration | TBD | TBD | TBD | TBD
0135 | Maximum Operating Accelerations | Filters shall not be damaged by exchanger operation | 4g | TBC | TBC | TBC
0140 | Beam Obstruction | Optical transmission loss due to shadowing from exchanger shall not exceed 1% on-axis | 0.50% | 1% | 0.5 | 0.5
0145 | Axial Positional Precision | Axial separation repeatability shall be less than +/- 0.25mm (per filter) and less than 1mm between different filters | TBC | +/-0.25mm | TBD | TBD
0150 | Lateral Positional Precision | Lateral registration repeatability shall be less than +/- 0.25mm (per filter) and less than 1mm between different filters | TBC | +/-0.25mm | TBD | TBD
0155 | Filter Tilt | Deployed filter angle w.r.t. cryostat window normal shall be less than TBD degrees | TBD | TBD deg | TBD | TBD
0160 | Exchange Time | Filter to filter exchange shall be less than 90 seconds | 60s | 90s | 60 | 40
0165 | Exchanger Reliability | Expected lifetime shall be greater than 33,000 cycles | 40000 | 33000 | TBC | TBC
0175 | Exchanger Impact on Tube Seeing | Surface temperature of exchanger mechanism shall not exceed +/- 3C of telescope tube | +/- 3C | +/- 3C | TBC | TBC

## Slide 28: Rail system risk matrix
Likelihood | 5 |  | 005 |  |  | 
 | 4 |  |  |  |  | 
 | 3 |  |  | 003 |  | 
 | 2 |  | 002 | 004 |  | 001
 | 1 |  |  |  |  | 
 |  | 1 | 2 | 3 | 4 | 5
 |  | Consequence |  |  |  | 
ID | Approach/Type | Risk Title
001 | M/I | Dropped filter
002 | M/I | Incomplete actuation
003 | M/I | Incomplete latching
004 | M/I | Impact event
005 | M/R | Late delivery of exchanger
Approach/Type
M: Mitigate
W: Watch
A: Accept
R: Research
I: Implementation
Likelihood
1: Very unlikely
2: Unlikely
3: Likely
4: Very likely
5: Certain
Consequence
1: Minor
2: Moderate
3: Large
4: Severe
5: Catastrophic

## Slide 29: Robot system risk matrix
Likelihood | 5 |  |  |  |  | 
 | 4 |  |  |  |  | 
 | 3 |  | 005 | 003, 004 |  | 
 | 2 |  | 002 |  |  | 001
 | 1 |  |  |  |  | 
 |  | 1 | 2 | 3 | 4 | 5
 |  | Consequence |  |  |  | 
ID | Approach/Type | Risk Title
001 | M/I | Dropped filter
002 | M/I | Incomplete actuation
003 | M/I | Incomplete latching
004 | M/I | Impact event
005 | M/R | End effector design
Approach/Type
M: Mitigate
W: Watch
A: Accept
R: Research
I: Implementation
Likelihood
1: Very unlikely
2: Unlikely
3: Likely
4: Very likely
5: Certain
Consequence
1: Minor
2: Moderate
3: Large
4: Severe
5: Catastrophic

## Slide 30: Technical motivation and recommendation
Subsystem by subsystem comparison – simplicity advantage of robot
COTS system vs. multiple custom systems
  Reliability
  Less testing required
Built-in safety features of robot (collision detection, torque sensing, etc) and mature consumer software
Robust robot system allows misalignment handling
Ability to leverage JPL experience/expertise

## Slide 31: Backup slides

## Slide 32: Potential risks of rail system
Description | Impact(s) | Mitigation
Pulley cable breakage | Back-driven motion | Non-backdrivable actuators
Misalignment when docking w/ instrument | Unable to exchange, instrument misalignment, excessive loads | Alignment MGSE, testing
Cable wear and cyclic relaxation | Incomplete actuation | Bi-annual service, testing
No encoder or telemetry | Incomplete actuation, impact event | Redundant limit switches
Unexpected out of plane loading | Incomplete actuation, impact, misalignment | Testing
Lubricated joint seizing | Incomplete actuation | Bi-annual service, testing
Power loss | Loss of telemetry | Recovery procedure
Jamming at jukebox exchange | Unable to exchange | Bi-annual service, testing
Incomplete latch at exchange | Unable to exchange | Interlocking latches
Insufficient FTE’s | Cost/schedule overrun | Contract out subsystem(s)

## Slide 33: Potential risks of robot system
Description | Impact(s) | Mitigation
Misalignment when docking w/ instrument | Unable to exchange, instrument misalignment, excessive loads | Torque sensors, built-in current limits, built-in collision detection
Loss of encoder or telemetry | Incomplete actuation, impact event | Redundant limit switches, built-in current limits, built-in collision detection
Unexpected out of plane loading | Incomplete actuation, impact, misalignment | Non-backdrivable actuators, 400% payload mass margin
Lubricated joint seizing | Incomplete actuation | Bi-annual service, testing
Power loss | Loss of telemetry | Recovery procedure, non-backdrivable actuators
Jamming at jukebox exchange | Unable to exchange | Bi-annual service, testing
Incomplete latch at exchange | Unable to exchange | Interlocking latches

## Slide 34
20”
24”

## Slide 35
Puzzle https://www.youtube.com/watch?v=LI5cgaF9XVI
Collision detection https://www.youtube.com/watch?v=PX7mT_nTGLg
Human + robotiq https://www.youtube.com/watch?v=tCss_TjSs7Y
Safe handling https://www.youtube.com/watch?v=ymAgKyMF82s
Flex tube assembly https://www.youtube.com/watch?v=3xZWCGP1no8
Pick & place https://www.youtube.com/watch?v=Pt4KzYNRrIk
Machine vision https://www.youtube.com/watch?v=_U4sGRB2peU
Delicate handling https://www.youtube.com/watch?v=EgzL7V9GU-Q
Demo https://www.youtube.com/watch?v=oeYbLFrsTiI
Dynamic human safety https://www.youtube.com/watch?v=sUp3EL-8xgE
Vision + force sensing https://www.youtube.com/watch?v=TPQ0ISwOgb8
Human safety https://www.youtube.com/watch?v=rOIl3EnJhl0
Glass panel cleanroom https://www.youtube.com/watch?v=4SBr4tClbf4
http://blog.robotiq.com/bid/37452/How-To-Handle-Fragile-Parts-With-Robots

## Slide 36: KR10 R1100 spec

## Slide 37: LBR R800 spec