# Document Data

| PROJECT NAME ZTF | DOCUMENT TITLE ZTF FILTER EXCHANGER ROBOT FORCE LIMITING TEST | AUTHOR J. BELICKI | DATE PREPARED (MM/DD/YYYY) 07/20/2017 |
| --- | --- | --- | --- |
| H/W TYPE (Brassboard, Breadboard, Engineering Model, Flight, GDS (DSN), Ground Support, Prototype, Qualification Unit, R&D, Raw Material) | PART OR ASSEMBLY NUMBER ELECTRO-PERMANENT MAGNETS (EPM) | PART REVISION | SERIAL NUMBER 001 |  |
| DESCRIPTION OF WORK BEING PERFORMED THIS PROCEDURE COVERS THE TESTING AND INITIAL CHARACTERIZATION OF THE ELECTRO-PERMANENT MAGENETS (EPM) IN ZTF. NOT INCLUDED IS ENVIRONMENTAL CALIBRATIONS. |
| PARTICIPANTS | ACCEPTED AS A COMPLETED RECORD |
| ENGINEER (Print Name and Sign) | DATE | ENGINEER (Print Name and Sign) | DATE |
| ENGINEER (Print Name and Sign) | DATE | ENGINEER (Print Name and Sign) | DATE |

# IBAT Steps

| STEP ID | INSTRUCTIONS | STEP SIGN-OFF Operator Buddy |
| --- | --- | --- |
| Note | ESD Note This IBAT involves work with ESD sensitive hardware. Use proper caution when handling and adhere to OIR ESD control requirements for all successive steps. |  |  |
| 10 | Serialize all EPMs and EPM Boards in system. Note location of all EPMs in system and location of spares. Record serial number and Inspection Report number for the items listed below: ----- FLIGHT HARDWARE ----- ITEM # P/N REV DESCRIPTION QTY S/N 1. EML25MM-24 A ELECTRO-PERMANENT MAGNETS 22 SN01-22 2. 1300ZTF2004 A WINDOW FRAME FILTER CONTROLLER PCB 1 _____ 3. 1300ZTF-2005 A CARTRIDGE FILTER CONTROLLER PCB 4 _____ ----- NON-FLIGHT HARDWARE ----- ITEM # P/N REV DESCRIPTION QTY S/N N1. - FILTER CONTROLLER TEST BOARD 1 - Note: Before installing any hardware, make sure hardware is visibly clean. Wipe hardware with a clean room wiper wetted with ethyl alcohol as required. Document Name: Document Location: |  |  |
| 20 | Inductance Measurement of EPMs: Using EPM board designated for testing, acquire first set of EPMs calibration data. Next use EPM board in that location to acquire EPM calibration data. Save to text file. Location selected: EMP Serial Numbers: EPM SN Board SN Location Test Number Software Version Used: Software Location: Calibration Distances: Distance (mil) Shim Color TEST 1 TEST 2 TEST 3 TEST 4 0.5 0.75 1.5 2 3 4 5 10 15 20 25 30 35 40 45 50 |  |  |
| 30 | Analyze any differences between two boards and inductance measurements. This will indicate whether all EPMs can be calibrated with single board or if they must be calibrated in situ. Result: Single Board can be used to calibrate all Specific board associated with EPM must be used Code analyzing data: Code Location: Document containing results: Document location: |  |  |
| 40 | Calibrate all EPMs: Calibrate all EPMs with the following shim distances and locations: Distance (mil) Shim Color 0.5 0.75 1.5 2 3 4 5 10 15 20 25 30 35 40 45 50 Test Status: EPM Test Complete Notes SN01 SN02 SN03 SN04 SN05 SN06 SN07 SN08 SN09 SN10 SN11 SN12 SN13 SN14 SN15 SN16 SN17 SN18 SN19 SN20 SN21 SN22 Document Name: Document Location: Software Version Used: Software Location: |  |  |