## Slide 1: ZTF update
Roger Smith
2016-01-05

## Slide 2: 48,000 deg2/night to spectroscopic depth
FoV = 46.7 deg2 @1arcsec/pixel
  4x4 mosaic of 6Kx6K CCDs,
Expose 25 sec, repoint in 10 s.
   faster telescope and dome drives
   new telescope control system.
Readout during re-pointing
    4 ch/CCD at 1 Mpix/sec/ch
    Preamps in dewar; fully differential signal path; digital CDS.
Downlink during next exposure.

## Slide 3: Survey volume vs. exposure time
Goal
Requirement

## Slide 4: Optical design
Classic Schmidt design assumes curved photographic plates and no window.
Plano convex field flattener used for smaller focal planes gets too thick for good broadband image quality.
31 mm window with slight concavity on interior reduces curvature of focal plane to ~ 7m.
CCDs are placed on chords with thin plano convex field flatteners on each CCD.
A 3rd element is added to the corrector to only slightly increase its power.
Optical layout

## Slide 5: Very compact camera
Sensor area (mm2) is 1.09 times DES and 44% of LSST.
Camera area is 8.2 times smaller than LSST camera…
Total obstruction, including spiders, is only 23% of 1.2m beam.

## Slide 6: Exploded view of camera

## Slide 7: Window (32 mm center thickness)
Optics don’t like thick window.
Convex interior surface rests on compliant gaskets with width and compliance tuned for optimal stress distribution and maximum factor of safety.
Edges beveled and polished as precaution.
First window (28mm) rejected due to defect; 2nd window made thicker for greater FoS as shown.
Stress on inner surface (MPa)
Quarter of window
Factor of safety = 6 relative to 36 MPa which would give 1% probability of failure after 20 years, assuming 75 µm initial crack size (conservative).

## Slide 8: Indium Tin Oxide window heater
Conductive gaskets at top and bottom
Make contact with ITO layer in AR coating stack to allow window heating.
Otherwise temperature at center radiatively cooled ~30C below ambient.
Very thin ITO layer keeps transmission loss low (~1%) but requires 160 V drive.
Like Low-E architectural glass but thinner for much lower transmission loss  high resistivity -> higher drive voltage
Same material is used as window demister in luxury cars, and as backside contact for LBNL fully depleted CCDs.

## Slide 9: CCDs delivered ahead of schedule
Mechanical sample
One for P200 prime

## Slide 10: CCD height control
CCDs must be located to 10 µm rms on facets of ~ 7m radius sphere.
To simplify, original design with wire EDM flexures was replaced by tight-hole-and-slot with controlled preload to allow slippage under thermal contraction.
Thick precision ground shims customized to each CCD to control height.
Initial dead reckoning is based on profilometry.
Final adjustment based on through focus scans on telescope.
Special attention to safe and easy installation.

## Slide 11: Cold plate in dewar walls (front)
On optical profilometer, with ceramic tooling balls to allow location of hole centers.
Note CCD landings are on chords of spherical surface.

## Slide 12: Cold plate in dewar walls (rear)

## Slide 13: Final height adjustment to be based on through focus scans
For single star, focus error ~4.6µm
With averaging,
local height error < 1µm
Height measurement accuracy demonstrated on PTF by Gina Duggan:

## Slide 14: CCD handling fixtures
Story board developed; parts design and procured.
Assembly and testing in progress.
ZTF CCDs be removed and reinstalled to change shims, after through focus imaging on telescope, so great care has been taken to make process easy and safe.

## Slide 15: Enlarged vacuum prep facilities
Large ultrasonic cleaner
Large vacuum oven
Rinse tub
Commensurate lifting equipment
Cold trap
Large oil free vacuum pump

## Slide 16: Large vacuum oven
Multiple storage tanks support exchange of water with detergents for ultrasonic-cleaning either metals, optics or large printed circuits

## Slide 17: Rear cover

## Slide 18: Inexpensive Cooling system
Field flattener lenses work like floating radiation shield to halve radiation from window.
Cold heads fully hidden between hexapod legs.
PT16 refrigerant gets charcoal getters cold enough to sustain vacuum for years.
48W available from two high performance heads with PT16 refrigerant

## Slide 19: Rear view of assembly
Joule Thompson Coolers nested within hexapod
Connectors and cables at periphery are hidden behind instrument

## Slide 20: Thermal path
Flexible thermal links
(behind Vacuum Interface Board)
Charcoal getter containers
mounted behind cold head

## Slide 21: Joule Thompson cooler
Counterflow heat exchanger (polycold Compact Cooler)
expansion capillary
Cold head
Charcoal getter on back of cold head
Lateral brace, insulating
Copper thermal straps on front of cold head
Termination penetrating VIB to connect to CCD cold plate in 4 places.

## Slide 22: Vacuum Interface Board
This very large PCB is key to ZTF compactness.
Allows any CCD to be removed/installed independently
Pre-amplifiers transmit differentially for low crosstalk at high speed.
Carries all signals through vacuum seals to COTS cables … no hand wiring.

## Slide 23: CCD Controllers (in hand, under test)
Semiconductor Technology Associates, “Archon”.
5 controllers are fully independent.
80 ch at 1 Mpix/s each
Common master clock: synchronized, low timing jitter.
Data compression in real time prior to first disk write.
Measuring excellent performance and reliability (no crashes).

## Slide 24: New spiders & hub
Raked backwards to accommodate hexapod
  FEA says still stiff enough
Three spider vanes instead of four; tapered section
  Lower off axis beam obstruction
  Less more compact diffraction pattern
Cables and refrigerant lines hidden within profile
Section

## Slide 25: FEA 60° from Zenith  deflections ok
0s to 1s Bolts Pre-tensioned. 198μm deflection.
2s to 3s Gravity Applied. 80μm deflection
Axial Deformation
0s to 1s Bolts Pre-tensioned. 122μm deflection.
2s to 3s Gravity Applied. 28μm deflection
Radial Deformation

## Slide 26: Hexapod (in lab)
Focus, tilt and collimation adjusted during every readout (0.5 mm/s)
Based on predictions from model.
Model updated every exposure using three extra focal CCDs and one in focus, that could be used as guider though probably not required.
Hexapod fully hidden behind instrument; powered down when not moving. … does not back drive.

## Slide 27: Trim plate
Refigured original corrector will serve as 3rd element to supplement doublet
Extensive baffling planned

## Slide 28: Evidence of condensation on corrector
Severe corrosion due to condensation trickling to low side when telescope stowed (pointing south)
Southern edge of single corrector
1950 to ~ mid 1960’s
Southern edge of “new” doublet cell
mid 1990’s to present.

## Slide 29: Radiative cooling of trim plate
For Ttel = 5 C = 278 K and is 5% humidity, equivalent temperature of the atmosphere, Tatm = -11C = 262 K [1],[2]
  Placing the trim plate in front of the doublet moves the doublet closer to that of the telescope tube temperature. This reduces tube seeing due to inverse convection, but does not eliminate it. However the trim plate temperature is lower than the doublet alone, increasing the risk of condensation.
How cold? Solving the Stephan-Boltzman equations for four plane-parallel surfaces, one estimates the doublet corrector temperature to be
3Tcorr4 = 2Ttel4 + Tatm4
Tcorr = 273 K = 5K below ambient … tube seeing is still a concern.
and the trim plate temperature is
3Ttrim4 = 2Tatm4 + Ttel4
Ttrim = 267.7 K = 10.3K below ambient … condensation risk.
References
[1] W.C. Swinbank, "Long‐wave radiation from clear skies," Quarterly Journal of the Royal Meteorological Society 89.381 (1963): 339-348.
[2] Mark A. Goforth, George W. Gilchrist, and Joseph D. Sirianni, "Cloud effects on thermal downwelling sky radiance," AeroSense 2002, International Society for Optics and Photonics (2002).

## Slide 30: Trim plate heater planned
Add resistive ITO layer to AR coating stack.
Uniform electrical heating to replace the ~120W radiated to sky.
  240 V required but hidden in space between trim plate and doublet.
Servo control to keeps corrector at ambient:
  Eliminates tube seeing due to inverse convection.
  Eliminates condensation risk.

## Slide 31: Bonn Shutter is in fabrication
To avoid beam obstruction, pupil plane shutter (in front of telescope)  1.3m aperture
0.5 s to open or close
Operation to 35 mph wind load.
Dual blades move in opposite directions, driven by common belt so self balancing.
Servo motor with velocity profile to minimize image motion.

## Slide 32: Shutter prototype is under test by BonnShutter and DESY (in Berlin)
Reaction force (negligible),
Acoustic noise (acceptable)
Operation to -5 C (pass)
Light leaks (in progress)
Acceleration profile
Reaction force into frame
Vibration is modest and well above ~ 4Hz telescope resonances

## Slide 33: For washing trim plate
Lightweight splash guard is installed to protect shutter
baffle hinges to one side.

## Slide 34: Gutter to collect trim plate wash water
Seals and gutter support frequent washing.
Temporary cover over shutter blade slot

## Slide 35: Telescope resonances studied
Programmable input produced by reaction force from Aerotech linear motor
(direct drive with high resolution encloder)
Charge shifting on PTF CCDs (8 lines every ~ 15ms) turns each star into series of spots to allow centroid motions on both axes to be measured at 67 Hz for ~7 s.

## Slide 36: Telescope resonances (30 N excitation in HA)
Image motion
in HA
Image motion
in Dec
Frequency response
in HA
Frequency response
in Dec

## Slide 37: Resonances evident after slews
Shutter opened with charge shifting before end of slew.

## Slide 38: Telescope and dome upgrades
Dome
RA drive
Dec drive
Windscreen (new, wireless link)
Flat field screen with LED illumination
Electrical distribution and lightning protection.
Air dryer and filtering (higher volume, lower pressure)
Thermal management in/below dome.
Safer handling of flammable refrigerants
  move compressor to thermally regulated shed outside dome
Modern Variable Frequency drives provide flatter torque-speed curve (>0.5 deg/s2)
and higher top speed ((>3 deg/s)

## Slide 39: HA drive bench test
New HA and Dec drives to be installed in Feb

## Slide 40: Dome upgrade components
New variable frequency controller
 Increased acceleration and top speed
Only runs as fast as required
Dynamic braking
Optimal settling (no overshoot)
New dome drive motor to be installed in Feb:
More powerful
Servo controlled to give flat torque vs. speed
New gearbox and tyre

## Slide 41: Other infrastructure
Refurbished windscreen; new drive; wireless control
New oil pump for Dec drive worm gear